3GPP TS 23.234 V6.0.0 (2004-03)

Technical Specification

3rd Generation Partnership Project;

Technical Specification Group Services and System Aspects;

3GPP system to Wireless Local Area Network (WLAN) interworking;

System description

(Release 6)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

UMTS, radio, LAN, interworking

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2004, 3GPP Organizational Partners (ARIB, CCSA, ETSI, T1, TTA, TTC).

All rights reserved.

Contents

Foreword	6

1	Scope	7

2	References	7

3	Definitions, symbols and abbreviations	8

3.1	Definitions	8

3.2	Symbols	9

3.3	Abbreviations	9

4	WLAN Radio networks interworking with 3GPP	10

5	High-level Requirements and Principles	11

5.1	Access Control Requirements	11

5.2	Access Control Principles	12

5.3	User Identity	14

5.3.1	General	14

5.3.2	NAI Username	14

5.3.3	NAI Realm Name	14

5.3.4	Roaming NAI	14

5.4	Network Advertisement and Selection	14

5.4.1	Description of the issue	14

5.4.2	I-WLAN Access Network Advertisement and Selection	16

5.4.2.1	Case of IEEE 802.11 WLANs	16

5.4.2.1.1	General	16

5.4.2.1.2	Network Advertisement	16

5.4.2.1.3	Network Selection	16

5.4.2.2	Case of other WLANs	17

5.4.3	VPLMN Advertisement and Selection	17

5.4.3.1	General	17

5.4.3.2	Network Advertisement	17

5.4.3.3	Network Selection	18

5.5	 Authentication methods	18

5.6	Service Authorization Principles for scenario 3	18

5.6.1	Accessing Home Network provided services	18

5.6.2	Accessing Visited Network provided services	19

5.6.3	External IP Network selection	19

5.7	IP Connectivity for scenario 3	19

5.7.1	Principles	19

5.7.2	Tunnelling Requirements	20

5.8	Roaming requirements for scenario 3	20

5.9	Routing Enforcement and Policy Enforcement in Scenario 3	20

5.9.1	Purpose for routing enforcement and policy enforcement	20

5.9.2	Routing Enforcement in the WLAN AN	21

5.9.3	Routing enforcement and policy Enforcement in the HPLMN	21

5.9.4	Routing enforcement and policy Enforcement in the VPLMN	21

5.10	IP address allocation for the WLAN UE	21

5.11	Charging	22

5.12	AAA Protocol Requirements	22

6	Interworking Architecture	22

6.1	Reference Model	22

6.1.1	Non Roaming WLAN Inter-working Reference Model	23

6.1.2	Roaming WLAN Inter-working Reference Model	23

6.2	Network elements	25

6.2.1	WLAN UE	25

6.2.1.1	WLAN UE classes	26

6.2.2	3GPP AAA Proxy	26

6.2.3	3GPP AAA Server	26

6.2.4	HLR/HSS	27

6.2.5	WLAN Access Gateway	27

6.2.5.1	Routing Enforcement	28

6.2.5.2	Per-tunnel Charging Generation	28

6.2.6	Packet Data Gateway	28

6.3	Reference Points	29

6.3.1	Wa reference point	29

6.3.1.1	General description	29

6.3.1.2	Functionality	29

6.3.2	Wx reference point	30

6.3.3	D'/Gr' reference point	30

6.3.4	Wo reference point	31

6.3.5	Wf reference point	31

6.3.6	Wg reference point	31

6.3.7	Wn reference point	31

6.3.8	Wp reference point	31

6.3.9	Wi reference point	32

6.3.10	Wm reference point	32

6.3.11	Wd reference point	32

6.3.11.1	General description	32

6.3.11.2	Functionality	32

6.3.12	Wu reference point	32

6.3.13	Ww reference point	33

6.3.13.1	General Description	33

6.3.13.2	Functionality	33

6.4	Protocols	33

6.4.1	Remote IP Layer	33

6.4.2	Tunneling layer	33

6.4.3	Transport IP Layer	34

6.5	WLAN user profile	34

7	Procedures	35

7.1	I-WLAN and VPLMN Selection Procedure	35

7.1.1	Initial network selection	35

7.1.2	Network re-selection	35

7.2	WLAN Access Authentication and Authorisation	36

7.3	Subscriber Profile Update	37

7.3.1	Access and service Authorization information update procedure	37

7.4	Cancelling WLAN Registration	39

7.5	Disconnecting a Subscriber by WLAN	39

7.6	Disconnecting a Subscriber by Online Charging System	40

7.7	Charging offline charged subscribers	41

7.8	Charging online charged subscribers	42

7.9	W-APN resolution and Tunnel establishment	43

7.9.1	Redirection	44

7.9.2	Subsequent authentication	46

7.9.3	Use of DNS	46

7.9.4	Subsequent tunnel establishment	46

7.10	Tunnel disconnection procedures	46

7.10.1	WLAN UE initiated tunnel disconnection	47

7.10.2	The network initiated tunnel disconnection	47

7.10.3	Disconnection of the last tunnel for a WLAN UE	48

Annex A (informative):	Refererence Points Signalling Flows	48

A.1	Signalling Sequences examples for Wa Reference Point	48

A.1.1	Authentication, Authorisation and Session Key delivery	48

A.1.2	Immediate purging of a user from the WLAN access	50

A.2	Signalling Sequences examples for Wx Reference Point	50

A.2.1	Authentication Information Retrieval	50

A.2.2	Subscriber Profile Retrieval	51

A.2.3	Subscriber Profile Update	52

A.2.4	WLAN Registration	53

A.2.5	Cancel Registration	54

A.2.6	Purge Function for WLAN interworking	55

A.3	Signalling Sequences examples for D' Reference Point	55

A.3.1	Authentication Information Retrieval	55

A.3.2	Subscriber Profile Retrieval	56

A.4	Gr' Signalling Mechanisms to support WLAN service	56

A.4.1	Introduction	56

A.4.2	InfoRetrieval procedure:	57

A.4.2	GprsLocationUpdate procedure:	57

A.5	Example of Authentication procedures	58

A.5.1	EAP/AKA Procedure	58

A.5.2	EAP SIM procedure	61

A.5.3	Alternative EAP initialisation	64

A.5.4	Re-authentication message sequence chart	65

Annex B (informative):	WLAN radio technologies	67

Annex C (informative):	Possible interworking architectures between WLAN AN and PLMN	69

C.1	WLAN shared by (or connected to) multiple ISPs and PLMNs	69

C.2	Routing packets from WLAN UE when WLAN AN is connected to multiple VPLMNs/ISPs and it provides direct Internet access	69

C.2.1	Separating traffic for different VPLMNs	69

C.2.2	Routing the traffic	70

C.2.3	Separating traffic to different VPLMNs using a combined DNS/NAT approach	71

C.3	WLAN AN exclusively owned by and connected to a single PLMN	73

C.4	WLAN AN connected to a single ISP	73

Annex D (informative):	Support of SMS over WLAN	74

D.1	Architecture for support of SMS over WLAN	74

D.1.1	IP Short Message Gateway (IP-SM-GW)	74

D.1.2	HLR/HSS enhancements	74

D.1.2.1	An indication that the terminal is IP connected	75

D.1.2.2	The address of the IP-SM-GW	75

D.1.3	IP address database	75

D.1.4	Reference points	75

D.1.5	IP Connectivity for SMS over WLAN	75

D.2	Delivery of short messages to WLAN (IP) connected client	75

D.2.1	Message flows for IP terminated short messages	75

D.3	Short messages originated on WLAN (IP) connected client	77

D.3.1	Message flow for IP originated short messages	77

Annex E (informative):	Information on the discussed tunnel switching alternative	78

E.1	Non Roaming WLAN Inter-working Reference Model	78

E.2	Roaming WLAN Inter-working Reference Model	78

E.3	WAG Description	79

E.4	Wu Reference Point	79

E.5	Wn Reference Point	80

E.6	Wp Reference Point	80

Annex F (informative):	Information on re-using the GGSN via the Gn' reference point	81

F.1	Introduction	81

F.2	Mapping between E2E tunnel and GTP tunnel	81

F.3	Interworking procedures over Gn'	82

F.4	Issues to investigate for Gn' reference point	82

Annex G (informative):	Change history	83

# Foreword

This Technical Specification has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# 1	Scope

This document specifies system description for interworking between 3GPP systems and WLAN Local Area Networks (WLANs). The intent of 3GPP–WLAN Interworking is to extend 3GPP services and functionality to the WLAN access environment.the 3GPP WLAN subsystem. The 3GPP WLAN subsystem is assumed to provide bearer services for connecting a 3GPP subscriber via WLAN to IP based services compatible with those offered via PS domain.

This specification defines a 3GPP system and procedures for the following functionalities:

-	Provide the interworking WLAN with a means of Access, Authentication and Authorisation (AAA) through the 3GPP System, which allows WLAN UEs to access WLAN and the locally connected IP network (e.g. Internet)

-	Provide WLAN UEs with IP bearer capability to access PS based services which are provided by PLMN.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.  In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

3GPP TS 21.905: "Vocabulary for 3GPP Specifications".

3GPP TS 22.101: "Service principles".

3GPP TR 22.934: "Feasibility study on 3GPP system to WLAN interworking".

3GPP TS 23.002: "Network architecture".

3GPP TS 23.003: "Numbering, addressing and identification".

3GPP TS 23.040: "Technical Realisation of the Short Message Service (SMS)"

3GPP TS 23.060: "GPRS; Service description".

3GPP TR 23.934: "3GPP system to WLAN Interworking; Functional and architectural definition".

3GPP TS 24.234: "3GPP System to WLAN Interworking; UE to Network protocols; Stage 3".

3GPP TS 29.002: "Mobile Application Part (MAP) specification".

3GPP TS 29.329: " Sh Interface based on the Diameter protocol; Protocol details".

3GPP TS 31.102: "Characteristics of the USIM Application."

3GPP TS 32.225: "Telecommunication management; Charging management; Charging data description for the IP Multimedia Subsystem (IMS)."

3GPP TS 33.234: "WLAN Interworking Security."

3GPP TR 23.825: "Overall Architecture Aspects of IP Flow Based Bearer Level Charging"

RFC2284: "PPP Extensible Authentication Protocol (EAP)"

RFC 2486: "The Network Access Identifier"

J. Caron, "DNS Based Roaming", http://www.ietf.org/internet-drafts/draft-caron-dns-based-roaming-00.txt, April 2002, (work in progress)

IEEE Std 802.1X-2001 IEEE Standard for Local and metropolitan area networks— Port-Based Network Access Control

IETF Internet-Draft: "Network Discovery and Selection within the EAP Framework". draft-adrangi-eap-network-discovery-and-selection-01, work in progress.

IEEE Std 802.11-1999, Local and metropolitan area networks—Specific requirements—Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications, IEEE, Sep. 1999.

IETF Internet-Draft: "EAP AKA Authentication" draft-arkko-pppext-eap-aka-11 (October 2003).

IETF Internet-Draft: "EAP SIM Authentication" draft-haverinen-pppext-eap-sim-12 (October 2003).

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

Available SSID:	It is an SSID that the WLAN UE has found after active and/or passive scanning which meets certain conditions as specified in IEEE 802.11 [19].

3GPP - WLAN Interworking: Used generically to refer to interworking between the 3GPP system and the WLAN family of standards. Annex B includes examples of WLAN Radio Network Technologies.

Environment:	The type of area to be covered by the WLAN network of a 3GPP - WLAN interworking; e.g. public, corporate and residential.

External IP Network/External Packet Data Network: An IP network to which access may be provided through the 3GPP system, rather than directly from the WLAN AN. For example, the Internet, an operator's IP network or a 3rd party IP network such as a corporate IP network.

Home WLAN: The WLAN that is interworking with the HPLMN of the 3GPP - WLAN interworking user.

Interworking WLAN :	WLAN that interworks with a 3GPP system.

I-WLAN selection: Procedure for the selection among the available I-WLAN APs

Offline charging: Offline charging mechanism is provided for collecting and forwarding charging information about occurred WLAN access resource and core network resource usage, etc without affecting the service rendered in real-time.

Online charging: Online charging mechanism is provided where the service rendered is affected in real-time and is required for a direct interaction with session/service control. This allows an online charged subscriber to access WLAN.

Policy Enforcement:	In scenario 3, Policy Enforcement is implemented in a WAG to allow only authorized packets to/from a WLAN AN to pass through.

PS based services:	In WLAN interworking, PS based service is a general term to refer to the services provided by a PLMN using IP bearer capability between WLAN UEs and the PLMN in scenario 3 and upwards. They include all services provided by 3G PS domain that use the IP bearer service, (e.g., IMS, Internet access, Corporate IP network access), and other services (e.g., SMS and LCS).

Requested W-APN:	The W-APN requested by the user

Routing Enforcement:	In scenario 3, Routing Enforcement ensures that all packets sent to/from the WLAN UE for 3G PS based service are routed to the interworking VPLMN (roaming case) or HPLMN (no roaming case). Routing Enforcement is implemented between a WLAN AN and a WAG.

Selected W-APN:	The W-APN selected by the network as a result of the user request

Service Authorization:	Authorization for a user to access the requested service according to the user's subscription.

Supported PLMN:	A PLMN of a roaming partner (i.e. to which the WLAN operator has a direct roaming relationship).

Visited WLAN:	An interworking WLAN that Interworks only with a visited PLMN.

W-APN:	WLAN Access Point Name – identifies an IP network and a point of interconnection to that network (Packet Data Gateway)

WLAN coverage:	an area where wireless local area network access services are provided for interworking by an entity in accordance with WLAN standards.

WLAN roaming:	The ability for a 3GPP - WLAN interworking user (subscriber) to function in a serving WLAN different from the home WLAN

WLAN UE:	The WLAN UE is the UE (equipped with UICC card including (U)SIM) utilized by a 3GPP subscriber to access the WLAN interworking.

WLAN UE's local IP address:	An address that is necessary to deliver the packet to a WLAN UE in a WLAN AN. It identifies the WLAN UE in the WLAN AN. WLAN UE's local IP address may be translated by Network Address Translation prior to being received by the interworking function.

WLAN UE's remote IP address:	An address used in the data packet encapsulated by the WLAN UE-initiated tunnel. It represents the identity of the WLAN UE in the network which the WLAN UE is accessing.

## 3.2	Symbols

For the purposes of the present document the following symbols apply:

D'	Reference point between a pre-R6 HSS/HLR and a 3GPP AAA Server

Gr'	Reference point between a pre-R6 HSS/HLR and a 3GPP AAA Server

Wa		Reference point between a WLAN Access Network and a 3GPP AAA Server/Proxy (charging and control signalling)

Wd	Reference point between a 3GPP AAA Proxy and a 3GPP AAA Server (charging and control signalling)

Wf	Reference point between a CGw/CCF and a 3GPP AAA Server/Proxy

Wg	Reference point between a 3GPP AAA Proxy and WAG

Wi	Reference point between a Packet Data Gateway and an external IP Network

Wm	Reference point between a Packet Data Gateway and a 3GPP AAA Server

Wn	Reference point between a WLAN Access Network and a WLAN Access Gateway

Wp	Reference point between a WLAN Access Gateway and a Packet Data Gateway

Wo	Reference point between a 3GPP AAA Server and an OCS

Wu	Reference point between a WLAN UE and a Packet Data Gateway

Wx	Reference point between an HSS and a 3GPP AAA Server

## 3.3	Abbreviations

AAA	Authentication, Authorisation and Accounting

AKA	Authentication and Key Agreement

AP	Access Point

APN	Access Point Name

CCF		Charging Collection Function

CGw	Charging Gateway

DHCP	Dynamic Host Configuration Protocol

DNS	Domain Name System

EAP	Extensible Authentication Protocol

FQDN	Fully Qualified Domain Name

GGSN	Gateway GPRS Support Node

GTP	GPRS Tunnelling Protocol

HLR	Home Location Register

HPLMN	Home PLMN

HSS	Home Subscriber Server

IEEE	Institute of Electrical and Electronics Engineers

IP	Internet Protocol

IP-SM-GW		IP Short Message Gateway

ISP	Internet Service Provider

I-WLAN	Interworking WLAN

NAI	Network Access Identifier

NAT	Network Address Translation

OCS		Online Charging System

PDA		Personal Digital Assistant

PDG	Packet Data Gateway

PLMN	Public Land Mobile Network

SIM	Subscriber Identity Module

SSID	Service Set ID

UE	User Equipment

UMTS	Universal Mobile Telecommunications System

USIM	UMTS SIM

SSID	Service Set IDentifier

VPLMN	Visited PLMN

WAG	WLAN Access Gateway

W-APN	WLAN APN

WLAN	Wireless Local Area Network

WLAN AN	WLAN Access Network

WLAN UE	WLAN User Equipment

# 4	WLAN Radio networks interworking with 3GPP

This specification defines two new procedures in the 3GPP System:

-	WLAN Access, Authentication and Authorisation, which provides for access to the WLAN and the locally connected IP network (e.g. Internet) to be authenticated and authorised through the 3GPP System

-	Access to External IP networks, which allows WLAN UEs to establish connectivity with an External IP network, such as 3G operator networks, corporate Intranets or the Internet from a suitable IP network.

For scenario 3, access to External IP Networks should, as far as possible, be technically independent of WLAN Access Authentication and Authorisation. However, Access to External IP Networks from 3GPP WLAN interworking systems shall be possible only if WLAN Access Authentication/Authorisation has been completed first.

Note:	The independence requirement does not preclude the possibility that the procedure for access to external IP network may rely on information derived in the procedure for WLAN Access Authorization.

Scenario 2 requires the first of these capabilities only. Scenario 3 requires a combination of both.

Figure 4.1 illustrates WLAN networks from the point of view of 3GPP interworking.

The Packet Data Gateway supports access to External IP networks, including those supporting 3GPP PS Domain based services. Scenario 2 offers direct connection from the WLAN to the Internet/intranet. The WLAN includes WLAN access points and intermediate AAA elements. It may additionally include other devices such as routers. The WLAN User Equipment (WLAN UE) includes all equipment that is in possession of the end user, such as a computer, WLAN radio interface adapter etc.

Figure 4.1: Simplified WLAN Network Model. The shaded area refers to scenario 3 functionality

As 3GPP-WLAN interworking concentrates on the interfaces between 3GPP elements and the interface between the 3GPP system and the WLAN, the internal operation of the WLAN is only considered in order to assess the impact of architecture options/requirements on the WLAN.

3GPP-WLAN interworking shall be independent of the underlying WLAN Radio Technology.

# 5	High-level Requirements and Principles

## 5.1	Access Control Requirements

The following functional requirements have been identified:

-	Legacy WLAN terminals should be supported. However software upgrades may be required for e.g. security reasons.

-	Minimal impact on the user equipment, i.e. client software.

-	Minimal impact on existing WLAN networks.

-	The need for operators to administer and maintain end user software shall be minimized.

-	Existing SIM and USIM shall be supported.

-	Authentication shall rely on (U)SIM based authentication mechanisms.

-	R6 USIM may include new functionality if necessary e.g. in order to improve privacy.

-	Changes in the HSS/HLR/AuC shall be minimized.

-	Methods for key distribution to the WLAN access network shall be supported.

-	The WLAN connection established for a 3GPP subscriber shall have no impact to the capabilities of having simultaneous PS and CS connections for the same subscriber.

-	WLAN Access Authorization shall occur upon the success of the authentication procedure. It shall take into account the user's subscription profile and optionally information about the WLAN AN, such as WLAN AN operator name, WLAN AN location information (e.g., country, telephone area code, city), WLAN AN throughput (e.g., maximum and minimum bandwidth guarantees for both ingress and egress traffic).  This information is used to enable use-case scenarios like location based authentication/authorization, location based billing / customer care, and location based service offerings.

-	It shall be possible to indicate to the user of the results of authorization requests.

-	Results of WLAN Access Authorization requests shall be indicated to the WLAN, so that the WLAN can take appropriate action.

-	The WLAN Access Authorization mechanism shall be able to inform the user and WLAN immediately of any change in service provision.

-	This TS proposes solutions for operators who want to interwork their WLAN with an existing pre-R6 HLR/HSS.

Additional access control requirements for scenario 3:

-	Service Authorization shall occur after the WLAN Access Authentication/Authorization procedure.

-	Service based policy control shall be possible for the services authorized for the user.

-	Access to 3GPP PS based services shall be provided via WLAN. The interworking architecture shall be able to support all 3GPP PS based services.

-	Access to PS based services normally provided by the 3GPP PS Core Network shall be provided via WLAN. WLAN access to these services shall support the same features as those supported via the 3GPP PS Core Network according to operator choice, e.g. private addressing schemes, external address allocation, secure tunneling to private external network. Quality of Service shall be supported when accessing these services via WLAN, although some limitations may exist because of the WLAN AN.

-	A scenario 3 WLAN inter-working system shall be able to support WLAN UEs operating in scenario 2, e.g. according to subscription.

-	A Scenario3 capable user should be able to choose between a scenario2 type of internet access (direct access through local network) or a scenario3 type of access to internet (through the PLMN), when the network allows it.

- 	When the WLAN inter-working system does not support access to 3GPP PS based services, the WLAN UE shall be able to detect it.

-	A scenario 3 WLAN inter-working system shall be able to mandate all flows for 3G PS based services to be routed to the HPLMN or the VPLMN, e.g. according to subscription. This routing enforcement shall not rely on the WLAN UE client.

Note:	This may mandate additional functionality existing in the WLAN AN

-	The technical solution for access control to External IP networks from WLAN shall be decoupled from WLAN Access Control.

## 5.2	Access Control Principles

End to End Authentication:  WLAN Authentication signaling is executed between WLAN UE and 3GPP AAA Server for the purpose of authenticating the end-user and authorizing the access to the WLAN and 3GPP network.

Transporting Authentication signalling over WLAN Radio Interface:  WLAN authentication signalling is carried between WLAN UE and WLAN AN by WLAN Access Technology specific protocols. To ensure multivendor interoperability these WLAN technology specific protocols shall conform to existing standards of the specific WLAN access technology.

Transporting Authentication signalling between WLAN AN and 3GPP network: WLAN Authentication signalling shall be transported between any WLAN AN and 3GPP network by a standard protocol, which is independent of the specific WLAN technology utilised within the WLAN Access network.

Details of end to end authentication and transport of authentication signalling over the WLAN radio interface and between the 3GPP network and WLAN is covered in 3GPP TS 33.234 [10]

WLAN Access Authorization: This defines the process(es) in 3GPP AAA Server verifying whether WLAN Access should be allowed to a subscriber and deciding what access rules/policy should be applied to a subscriber. It is the stage after access authentication, but before service authorisation and WLAN UE's local IP address allocation.

After the authentication process succeeds, there could be additional conditions for the 3GPP AAA Server to decide whether the access is allowed and what access rules/policy should be applied. These conditions may be based on the subscriber's profile, the account status, O&M rules, local agreements or information about the WLAN AN.

The procedure for WLAN Access Authorization between the WLAN UE and the 3GPP AAA Server is combined with the WLAN Access Authentication.

Access rules/policy decided by the 3GPP AAA Server may be deployed in the 3GPP AAA Server, or/and in other entities such as the WAG or the WLAN AN.

Access rules/policy may include access scope limitation, time limitation, bandwidth control values, and/or user priority.

WLAN Access rules/policy should be specified by the home and/or visited operator based on the subscriber's profile, the account status, O&M rules (e.g. blacklist, access limitation list), and local agreements. Factors such as access time and access location could also be considered in these rules.

The access scope limitation could be, for example, only/not/may "access through WAG"; only/not/may "access intranet X".

Access scope limitation can be achieved using IP allocation scheme, VLAN allocation, Filtering, ACLs in the routers and switchers, etc.

Different access priority or the range of priorities may be authorized for different subscribers, and/or for one subscriber based on different access time or location, etc.

3GPP WLAN attach: The WLAN-attach status indicates whether the WLAN UE is now being served by the 3GPP WLAN IW network.

A WLAN UE is "WLAN-attached" after successful authentication and WLAN Access Authorization.

A WLAN UE is "WLAN-detached" in 3GPP network after its disconnection, or its authentication or WLAN Access Authorization being cancelled.

The WLAN-attach status is maintained by the 3GPP AAA server.

The WLAN UE's WLAN attach status should be obtained from the AAA Server directly or through the HSS, by other entities in the 3GPP or 3GPP connected network. Other entities in the 3GPP network obtain the WLAN UE's WLAN-attach status directly from the AAA Server or through the HSS. These entities and the corresponding reference points are not in the scope of this TS.

The description of the corresponding status in the WLAN UE is out of the scope of this TS.

Additional access control principle for scenario 3:

Service Selection and authorisation: The solution shall include means for securely delivering service selection information from the WLAN UE to the 3GPP AAA server in the Home Network. If a scenario3 user chooses to access the internet directly using the local IP network (like a scenario2 user), no service selection information is passed to the PLMN. In all other cases, where a scenario3 type of services is opted by the user, the service selection information shall contain an indication of the requested W-APN to which access is requested. The 3GPP AAA Server in the Home network shall verify the users subscription to the indicated W-APN against the subscriber profile retrieved from HSS. The 3GPP AAA Server selects a W-APN based on the requested W-APN and on the user's subscription/local policy.

The service request shall be indicated by a tunnel establishment request from the WLAN UE to the PDG. The PDG shall then seek authentication/authorisation from the 3GPP AAA Proxy or Server in the same network.

The results of the authorisation decision shall be communicated to the Visited Network. All subscription-based authorisation decisions are made in the Home network.

In the case of a request for access to services provided in the Visited Network, the 3GPP AAA Proxy shall also authorise access based on local policy.

## 5.3	User Identity

### 5.3.1	General

The network authentication procedure is based on the use of EAP method where user identification is based on Network Access Identifier (NAI), whose format is specified in RFC 2486 [12]. A NAI is composed of a username part and a realm part.

### 5.3.2	NAI Username

The NAI username part format shall comply with IETF EAP-SIM [23]and EAP-AKA [22]. The Permanent User Identity, which is specified in IETF EAP-SIM [23] and EAP-AKA [22], shall be derived from IMSI, which resides in the UICC. Details of these are covered in 3GPP TS 33.234 [14], 3GPP TS 24.234 [9] and TS 23.003 [5].

For user identity protection a temporary identity in the username part of the NAI can be used. The use of a temporary identifier is necessary to replace the IMSI in radio transmissions as it protects the user against tracing from unauthorized access networks. As a working assumption, it is considered in this version of the TS that temporary identifiers are allocated in the 3GPP AAA Server. The format and the procedure for deriving the temporary identity are defined in TS 33.234 [14].

For re-authentication, WLAN UE shall use the previously allocated re-authentication identity as specified in the IETF EAP-SIM [23]and EAP-AKA [22] Internet-Drafts as its NAI user identity. The format and the procedure for deriving the re-authentication identity are defined in TS 33.234 [14].

### 5.3.3	NAI Realm Name

The NAI realm name shall be in the form of an Internet domain name as specified in RFC 1035 and shall identify the user's HPLMN, based on its MCC and MNC. Details on NAI realm construction are specified in 3GPP TS 23.003 [5].

### 5.3.4	Roaming NAI

A roaming NAI is constructed when the WLAN UE authenticates through a VPLMN. The WLAN UE shall indicate in the NAI both the user's HPLMN and the chosen VPLMN, based on their MCC and MNC.

The realm portion of the roaming NAI shall be constructed according to Section 5.3.2 based on the chosen Visited Network MCC and MNC.

The details on Roaming NAI construction are specified in 3GPP TS 23.003 [5].

## 5.4	Network Advertisement and Selection

### 5.4.1	Description of the issue

If the WLAN radio technology allows for features enabling radio access network sharing or provider selection these shall be reused for WLAN Access Network (WLAN AN) selection in 3GPP-WLAN interworking.

In addition to WLAN Access Network selection, the WLAN UE may need to select a VPLMN through which to authenticate, if more than one is available through the chosen radio network.

WLAN Access Network advertisement and selection depends on the particular WLAN technology.

VPLMN advertisement and selection should be independent of WLAN technology.

The generic Network Advertising and Selection scenario is illustrated in Figures 5.1 and 5.2.

Figure 5.1: Network Advertising and Selection Scenario

An area is shown covered by a WLAN Access Networks having a set of roaming agreements with different 3G networks (3GPP Visited Network #1,#2,…,#n). A WLAN UE entering the WLAN AN wants to connect to his own 3GPP Home Network to which he is a subscriber (as shown in Figure 5.1).

Referring to the figure the user subscribing to the services provided to the 3GPP Home Network can reach the associated home network in two different ways, e.g. via either of 3GPP Visited Network #1 or 3GPP Visited Network #2.

Figure 5.2: Network Advertising and Selection Scenario

Another scenario is represented by an area covered by some WLAN Access Networks (WLAN AN#1, #2, …, #n) having a set of roaming agreements with different 3G networks (3GPP Visited Network #1,#2,…,#n) and where one of the WLAN Access Network has a directly roaming agreement with the 3GPP Home network or the WLAN Access Network is directly deployed by the 3GPP Home network. A WLAN UE entering the area wants to connect to his own 3GPP Home Network to which he is a subscriber (as shown in Figure 5.2).

Referring to the figure the user subscribing to the services provided to the 3GPP Home Network can reach the associated home network in three different ways, e.g. via WLAN AN#1 then through either of 3GPP Visited Network #1 or 3GPP Visited Network #2, or via WLAN AN#2.

### 5.4.2	I-WLAN Access Network Advertisement and Selection

#### 5.4.2.1	Case of IEEE 802.11 WLANs

##### 5.4.2.1.1	General

The following principles shall apply:

-	Require no modifications of existing legacy APs.

-	Have no impact on existing legacy clients (implies no modification of current broadcast SSIDs).

-	Have low latency and overhead.

In the case of IEEE 802.11 WLANs:

- Modification of current broadcast SSIDs shall not be required;

- Active scanning should be supported by the WLAN UE;

- Passive scanning shall be supported by the WLAN UE;

- Multiple SSIDs may be supported  (i.e. only standard 802.11 capable APs are required).

##### 5.4.2.1.2	Network Advertisement

A WLAN network name is provided in WLAN beacon signal in so-called SSID (Service Set ID) information element. There is also the possibility for a WLAN UE to actively solicit support for specific SSIDs by sending a probe request message and receive a reply if the access point does support the solicited SSID. Active and passing scanning are defined in IEEE 802.11 [21].

A WLAN AN may indicate that it provides 3G interworking without the involvement of any other network than the WLAN AN.

The above requirement may be met through explicit EAP-based procedures or through the generic Preferred SSID list procedures – for example Preferred SSID lists could include SSID formats defined by operators for the above purposes.

##### 5.4.2.1.3	Network Selection

The WLAN UE shall store a list of Preferred SSIDs provided by the Home Network operator and shall also maintain a list of the user's Preferred SSIDs.

The Operator's preferred SSID list would be populated, for example, with the SSIDs commonly used by major hotspot operators with whom the Home Operator has a direct relationship.

In Manual mode the WLAN UE shall scan  (passive scanning) for all available SSIDs in beacon channels it can discover. The WLAN UE may also probe (active scanning) for additional available SSIDs from each of the WLAN networks that it has discovered.  Details on the usage of preferred SSID lists during active scanning are included in 3GPP TS 24.234 [9].

Once a list of all available SSIDs has been obtained, the WLAN UE selects an SSID following the procedure specified in 3GPP TS 24.234 [9] clause 5.2.1 and performs association with the particular access point using the Selected SSID.

The WLAN UE shall obtain a list of available PLMNs from each SSID it associates with according to procedure defined in clause 5.4.3. When a list of PLMNs has been obtained from all SSIDs it shall present them to the user for the user to select one. The WLAN UE shall then associate with the SSID that supports that PLMN.

In the automatic mode the procedure is as follows:

0.	The WLAN UE scans for all available SSIDs. It is not required to continue the scanning after the highest priority SSID is found.

1.	Start association and perform Network Discovery

1a)	If authentication to HPLMN succeeds (i.e. EAP-Success is received), then stop this procedure.

1b)	If Network Advertisement information is received (i.e. EAP-Identity/Request is received), then store the list and start again step 1.

Repeat step1 for all available SSIDs following the order specified in clause 5.2.1 If the scanning in step 0 was stopped due to the discovery of the highest priority SSID, but the HPLMN has not been found (e.g. because the SSID list is not updated or the selected SSID was a fake one), then the user should go back to step 0 and scan for all available SSIDs.

Note that if an AP supporting HPLMN is found in the middle of the procedure, step 1a, then step 1 is stopped and association with the remaining available APs will not take place.

2.	Use the lists of  'Preferred PLMNs for WLAN access' and the lists from step 1b) to find the best match. Select the AP that supports the best match VPLMN.

3.	Associate with the AP selected in step 2 and attempt authentication with the best match PLMN.A WLAN AN may indicate that it provides 3G interworking without the involvement of any other network than the WLAN AN.

If such an indication is provided by the WLAN AN and if the WLAN UE supports the indication, then the WLAN UE shall use it at SSID selection as defined in 3GPP TS 24.234 [9].

The above requirement may be met through explicit EAP-based procedures or through the generic Preferred SSID list procedures – for example Preferred SSID lists could include SSID formats defined by operators for the above purposes.

#### 5.4.2.2	Case of other WLANs

Other WLANs, such as HiperLAN or Bluetooth, are not described in this TS but not excluded.

### 5.4.3	VPLMN Advertisement and Selection

#### 5.4.3.1	General

The following principles shall be used in VPLMN Advertisement and Selection:

-	This procedure takes place after association with an AP

-	The user shall be able to select the Visited Network

-	Use the NAI for routing of AAA messages.

-	Have low latency and overhead.

-	Use existing EAP mechanisms, if possible.

-	Be extensible to permit advertisement of WLAN characteristics other than the PLMNIDs of roaming partners.

#### 5.4.3.2	Network Advertisement

Network advertisement information enumerates the roaming partners and associated NAI realms. This information shall be provided to the WLAN UE when the WLAN is unable to route an authentication request from the WLAN UE based on the initial NAI (e.g. when the WLAN AN receives a NAI with an unknown realm) and when the WLAN UE explicitly requests Network advertisement information. Details on the usage and coding of Network advertisement information are included in 3GPP TS 24.234 [9].

#### 5.4.3.3	Network Selection

The WLAN UE shall indicate its home network through the use of an initial NAI.  The realm part of this initial NAI shall be derived from the IMSI, as described in section 5.3.3.  Optionally, if there is preference for a roaming network, the initial NAI then takes the form of a Roaming NAI, as described in section 5.3.4; e.g., Ffor optimizing user access experience in re-access case, the WLAN UE may include information of preferred roaming network from previous successful authentication while it is associated to the same AP.

For the manual selection case allowed by some operator, initial NAI can include the roaming network decided by the user, e.g. using a preferred PLMN list stored in the UICC.

If the WLAN AN is able to route authentication request based on the initial NAI, then no special processing for network advertisement/selection is needed.

If the WLAN ANis unable to route authentication request from WLAN UE based on the initial NAI, the WLAN AN shall deliver the network advertisement information to the WLAN UE.  The WLAN UE processes this information according to its internal roaming preference policies or prompts the user to select a VPLMN preference. It uses the result to determine how to construct a new NAI indicating the selected VPLMN, according to Section 5.4.2.

After the network advertisement information is delivered and VPLMN selection is performed, the WLAN UE attempts to authenticate with the new NAI determined in the prior step.

The WLAN AN shall use the NAI to route the AAA traffic to the appropriate VPLMN AAA Proxy.

## 5.5		Authentication methods

Authentication methods are discussed in TS 33.234 [6].

## 5.6	Service Authorization Principles for scenario 3

The home network decides whether visited service is allowed or not based on e.g. W-APN, the user subscription information, visited network capabilities and roaming agreement.

### 5.6.1	Accessing Home Network provided services

The following functionality and requirements have been identified:

-	It shall be possible to support multiple service authorizations after a successful WLAN authentication/authorisation (i.e. EAP success).

-	The Service authorisation procedure should, as far as possible, be independent from WLAN Access authentication and authorisation.

-	The routing policy applied at WLAN Access Authentication and Authorisation may include policy determining whether the user has IP connectivity to the PDGs used for access to external IP networks.

-	It shall be possible to permit access to different services simultaneously.

-	Service authorization information shall be protected

-	The Access Point Name (APN) concept defined in 3GPP TS 23.003 shall be used for WLAN interworking authorization (namely W-APN). In a service authorization procedure:

-	W-APN selection and authorization is an end-to-end procedure between the WLAN UE and the HPLMN (the service authorization decision is made by the 3GPP AAA Server based on subscription information retrieved from the HSS/HLR).

Editor's note:	the use of subscription information is FFS.

-	The WLAN UE shall use W-APN to indicate to the network the service or set of services it wants to access.

-	The PDG selection is under control of the 3GPP Home Network. The selection is based on the requested W-APN and user subscription information. The mechanism to select the PDG by the home network is out of scope of this specification, since it depends on the operator's preference.

-	The PDG needs to know the authorized W-APN to select the external network, i.e. Wi interface.

### 5.6.2	Accessing Visited Network provided services

When accessing visited network provided services, additional principles below apply:

-	In order for the WLAN UE to be able to use W-APNs in the VPLMN, the 3GPP AAA Server needs to pass to the 3GPP AAA Proxy the authorized W-APN and service related information which is required by the Visited Network to perform the service.

-	The W-APN needs to be understood by both the Home and the Visited Networks.

-	The V-PDG selection is under control of the 3GPP Visited Network. The selection is based on the authorized W-APN and service related information. The mechanism to select the V-PDG by the Visited Network is out of scope of this specification, since it depends on the operator's preference.

-	The selected PDG in the Visited Network needs to know the authorized W-APN to select the external network, i.e. Wi interface.

### 5.6.3	External IP Network selection

The WLAN UE can connect to different IP networks, including the Internet, an operator's IP network or an external IP network such as a corporate IP network. The user may indicate a preferred IP network with a requested WLAN Access Point Name (W-APN). The Requested W-APN may also indicate a point of interconnection to the external IP network (i.e. PDG).

A W-APN is indicated by the WLAN UE in the tunnel establishment procedure between the WLAN UE and a PDG (whether the request is sent to the WAG or to the PDG is FFS). It is then forwarded to the 3GPP AAA server/proxy in the same network as the PDG..

## 5.7	IP Connectivity for scenario 3

### 5.7.1	Principles

The WLAN UE initiates the establishment of tunnels and is involved in packet encapsulation/decapsulation. The tunnel shall reside between the WLAN UE and the PDG. In the non roaming case, the PDG shall reside in the Home PLMN; in the roaming case, the PDG may reside either in the Home or in the Visited PLMN (both cases shall be supported).

The following steps are performed after WLAN access authentication/authorisation:

1.	W-APN resolution and discovery of the tunnel endpoint (PDG) IP-address is performed using the procedures described in clause 7.9.

2.	Tunnel establishment, including mutual authentication, shall occur between the WLAN UE and the PDG.

Note 1:	Filtering attributes may be needed in order to enable the WLAN to enforce that the WLAN UE tunnels all traffic as required. Filtering attributes may be transmitted from 3GPP AAA Server to WLAN over the Wa reference point. The WLAN Access Network sets up appropriate packet filters.

Note 2:	The PDG is described in section 6.

The tunnel establishment is not coupled to WLAN access authentication/authorisation. The WLAN UE may establish several tunnels in order to access several external IP networks simultaneously. The external IP network selection is performed as part of the establishment of each tunnel.

Editor's note:	Routing towards the Home PLMN in the Visited PLMN, as well as its impacts on the WLAN AN, are for further study.

### 5.7.2	Tunnelling Requirements

The requirements that a WLAN UE-Initiated tunnelling protocol should meet are:

-	Minimal requirements to the underlying IP connectivity network, i.e. WLAN UE initiated tunnelling and tunnel establishment signalling can be deployed on top of generic IP connectivity networks

-	Minimal impacts to the WLAN Access Network

-	Establishment of trusted relationships (e.g. mutual authentication for both tunnel end-points) shall be possible

-	Tunnel IP configuration of the WLAN UE may be obtained from/through the remote tunnel endpoint

-	Set up secure tunnels between WLAN UE and remote tunnel endpoint. Especially support encryption and integrity protection during tunnel establishment and while transporting user data packets, if enabled.

-	Remote IP address (inner IP):

-	The transport of IPv4 packets shall be supported

-	The transport of IPv6 packets shall be supported (e.g. in order to support IPv6 services like IMS)

-	Local IP address (outer IP):

-	The tunnel protocol shall be able to support IPv4 and IPv6 transport addresses

-	The tunnel protocol shall support private WLAN UE's local IP addresses, which are non-routable in the public Internet..

-	The protocol should be fully specified and 3GPP should define its usage to enable multi-vendor inter-operability.

## 5.8	Roaming requirements for scenario 3

For the delivery of 3GPP PS based services in a roaming scenario:

-	The roaming architecture shall ensure that CDRs can be generated e.g. volume and time based by the visited network.

-	The roaming architecture shall ensure that tunnels established are between entities that have a roaming agreement.

-	The roaming architecture shall ensure that the bearer path from the WLAN to Home/Visited 3GPP network conforms to QoS and roaming agreement(s).

-	The roaming architecture shall provide the ability to allow the user to access services provided by the visited network, e.g. local PS services.

-	The roaming architecture shall allow the home network to limit the set of 3GPP services available for a given roaming user.

-	Scenario 3 requires that all packets of PS based services sent to/from a WLAN UE are routed via a VPLMN in a 3GPP network, however basic Internet access may be routed directly from the WLAN.

## 5.9	Routing Enforcement and Policy Enforcement in Scenario 3

### 5.9.1	Purpose for routing enforcement and policy enforcement

In order to ensure operator policies, e.g. QoS, Charging can be applied to user traffic, scenario 3 requires routing enforcement and policy enforcement to be implemented in the 3GPP-WLAN interworking system.

### 5.9.2	Routing Enforcement in the WLAN AN

Routing enforcement shall be used to ensure that all packets sent to/from the WLAN UE for 3G PS based service are routed to the interworking VPLMN (roaming case) or HPLMN (no roaming case). However, this routing enforcement shall not prevent a WLAN AN from routing non 3G PS based service traffic to another network (e.g. the Internet) other than a PLMN, when provision of such services (e.g. direct Internet access from the WLAN) is agreed between the  WLAN and the PLMN.

When subscription limits a WLAN UE to exclusively access only 3GPP PS based service, the PLMN can indicate to the WLAN AN routing enforcement to ensure that all packets sent to/from the WLAN UE are routed to the interworking VPLMN (roaming case) or HPLMN (no roaming case).

If a WLAN UE user subscription allows a Scenario 3 user to access a Scenario 2 type of service (e.g. direct internet access), the WLAN AN should be capable of routing packets directly to the external packet data network.

Routing enforcement in the WLAN AN shall ensure that packets sent to/from the PDG are routed to the right entity in the interworking VPLMN (roaming case) or HPLMN (no roaming case).

Routing enforcement should not prevent the WLAN AN from supporting scenario 2 WLAN UE or a scenario3 capable WLAN UE opting for a scenario2 type of direct internet access, and non 3G interworking WLAN terminals.

Routing enforcement should have minimal impact on the WLAN AN.

### 5.9.3	Routing enforcement and policy Enforcement in the HPLMN

When operating in scenario 3 and access is via a tunnel endpoint (PDG) in the HPLMN, the HPLMN shall be able to provide the VPLMN with suitable policy enforcement information. The HPLMN may also provide suitable routing enforcement information to WLAN.

### 5.9.4	Routing enforcement and policy Enforcement in the VPLMN

When operating in scenario 3, the VPLMN shall be able to implement policy enforcement on traffic sent to/from a WLAN UE according to policy enforcement information provided by the HPLMN.

The VPLMN may also provide suitable routing enforcement information to WLAN.

## 5.10	IP address allocation for the WLAN UE

In Scenario 2, a WLAN UE needs to use its local IP address only. In Scenario 3, a WLAN UE shall use two IP addresses; its local IP address and remote IP address.

A WLAN UE's local IP address identifies the WLAN UE in the WLAN AN. In scenario 2, the WLAN UE's local IP address is assigned by the WLAN AN; in scenario 3, it can be assigned by a WLAN or by a PLMN (a VPLMN in roaming case and a HPLMN in non-roaming case). For the WLAN-assigned local IP address, which belongs to the address space of WLAN AN, there is no additional requirement on the WLAN. WLAN UE's local IP address allocation by the PLMN is for further study.

In scenario 3, a WLAN UE's remote IP address identifies the WLAN UE in the network that the WLAN UE is accessing for the 3G PS service. It shall be used for the inner packet of the WLAN UE-initiated tunnel. It can be assigned by HPLMN, VPLMN or an external IP network. The only case where VPLMN assigns the remote IP address for the WLAN UE is when the WLAN UE-initiated tunnel terminates at the VPLMN's PDG. When the WLAN UE's remote IP address is allocated by the external IP network, the PDG is required to have an interface with an address allocation server, such as AAA or DHCP, belonging to the external IP network. For the WLAN UE's remote IP address, IPv4 addresses shall be supported. When the WLAN UE accesses 3G PS based services using an IPv6 network such as IMS services, IPv6 addresses shall be supported for the WLAN UE's remote IP address.  To avoid any clashes between addresses used in WLAN AN and PLMN and to enable correct routing of packets sent out by the WLAN UE the PLMN operator should allocate public addresses to network nodes, which are addressed by WLAN UEs.

When a WLAN UE accesses several 3G PS based services with different W-APNs simultaneously, the WLAN UE can get several remote IP addresses. There may be several WLAN UE-initiated tunnels for the services.

## 5.11	Charging

The following functionality and requirements have been identified:

-	The WLAN Access Network shall be able to report the WLAN access usage to the appropriate 3GPP system (i.e. VPLMN in the roaming case and HPLMN in the non-roaming case).

-	It shall be possible for the 3GPP system to control a specific ongoing WLAN access session for online charging purposes.

-	It shall be possible for an operator to maintain a single prepaid account for WLAN, PS, CS, and IMS for a user.

-	The 3GPP system shall be able to process the WLAN access resource usage information,and convert it into the format used in 3GPP networks (e.g. CDR).

-	It shall be possible to correlate charging and accounting records generated in WLAN Access related nodes and records generated in 3GPP nodes.

-	It shall be possible to apply offline charging and online charging mechanisms for the WLAN interworking with 3GPP network.

For Scenario 3:

-	It shall be possible to generate per user charging information in the HPLMN and in the VPLMN irrespective of whether the service is provided in the HPLMN or in the VPLMN.

## 5.12	AAA Protocol Requirements

- A common AAA protocol shall be used for Authentication, Authorization and Accounting purposes in the WLAN Interworking Architecture within the 3GPP network.

- The protocol used for Accounting purpose in the WLAN Interworking Architecture in the 3GPP network shall be the same as used by the 3GPP Charging Architecture eg. the AAA protocol used by the 3GPP IMS charging architecture,

- If interworking with a legacy AAA protocol is needed, then it shall be performed at the entry and exit point of the 3GPP network. In the case of roaming, such interworking shall be performed in the visited network. The legacy AAA protocol may not support all features of 3GPP AAA protocol.  Therefore, this interworking might limit the usage of features existent in 3GPP AAA protocol but not existent in legacy AAA protocol(e.g. filtering rules).

# 6	Interworking Architecture

## 6.1	Reference Model

Editor's note:	The term roaming is used here when referring to roaming between 3GPP networks. However, an intermediate aggregator or a chain of intermediate networks may possibly separate the user when accessing the WLAN from the 3GPP home network.

### 6.1.1	Non Roaming WLAN Inter-working Reference Model

Note:	The shaded area refers to scenario 3 functionality.

Figure 6.1: Non-roaming reference model

### 6.1.2	Roaming WLAN Inter-working Reference Model

The home network is responsible for access control. Charging records can be generated in the visited and/or the home 3GPP networks. The Wx and Wo reference points are intra-operator. The home 3GPP network interfaces to other 3GPP networks via the inter-operator Wd reference point.

The 3GPP AAA proxy relays access control signalling and accounting information to the home 3GPP AAA Server using the Wd reference point.

It can also issue charging records to the visited network CGw/CCF when required. The 3GPP network interfaces to WLAN Access Networks via the Wa reference point.

Note:	The shaded area refers to scenario 3 functionality.

Figure 6.2a: Roaming reference model - 3GPP PS based services provided via the 3GPP Home Network

Note:	The shaded area refers to scenario 3 functionality.

Figure 6.2b.: Roaming reference model - 3GPP PS based services provided via the 3GPP Visited Network

## 6.2	Network elements

### 6.2.1	WLAN UE

A WLAN UE is the UE (equipped with UICC card including (U)SIM) utilized by a 3GPP subscriber to access the WLAN network for 3GPP interworking purpose. A WLAN UE may include terminal types whose configuration (e.g. interface to a UICC), operation and software environment are not under the exclusive control of the 3GPP system operator, such as a laptop computer or PDA with a WLAN card, UICC card reader and suitable software applications.

The WLAN UE functions include:

-	Associating to an I-WLAN.

-	WLAN access authentication based on EAP methods.

-	Selection of a suitable VPLMN in the roaming case.

-	Building an appropriate NAI.

-	Obtain a local IP address.

-	Building an appropriate W-APN to be used in scenario 3.

-	Request the resolution of a W-APN in scenario 3 to a PDG address.

-	Establish a secure tunnel in scenario 3 to a PDG.

-	Obtain a remote IP address to be used in scenario 3.

-	Accessing services provided in the operators PS domain.

-	Allowing users to select the type of network access, i.e.between direct access to external IP networks from the WLAN AN and network access through PLMN.

#### 6.2.1.1	WLAN UE classes

According to its capability, a WLAN UE is categorized into three classes.

Class WA WLAN UE:	This class of a WLAN UE has both 3GPP and WLAN radio interfaces. The WLAN UE can be attached to both WLAN and 3GPP systems at the same time, when an interworking WLAN is available. Also it supports simultaneous access to both WLAN and 3GPP cellular network by activating both radio interfaces.

Class WB WLAN UE:	This class of a WLAN UE has both 3GPP and WLAN radio interfaces. But it does not support simultaneous access to both WLAN and 3GPP cellular network because it can operate only one radio interface at a time.

Class WC WLAN UE:	This class of a WLAN UE has only a WLAN radio interface. It is capable of WLAN attach and WLAN access only, when an interworking WLAN is available.

### 6.2.2	3GPP AAA Proxy

The 3GPP AAA Proxy represents a proxying and filtering function that  resides in the Visited 3GPP Network.  The 3GPP AAA Proxy functions include:

-	Relaying the AAA information between WLAN and the 3GPP AAA Server.

-	Enforcing policies derived from roaming agreements between 3GPP operators and between WLAN operator and 3GPP operator

-	Reporting per-user charging/accounting information to the VPLMN CCF/CGw for roaming users

-	Service termination (O&M initiated termination from visited network operator)

-	Protocol conversion when the Wa and Wd reference points do not use the same protocol

For Scenario 3 only:

-	Receiving authorization information related to subscriber requests for W-APNs in the Home or Visited network

-	Authorization of access to Visited network W-APNs according to local policy

The 3GPP AAA Proxy functionality can reside in a separate physical network node, it may reside in the 3GPP AAA Server or any other physical network node.

### 6.2.3	3GPP AAA Server

The 3GPP AAA server is located within the 3GPP network. The 3GPP AAA Server:

-	Retrieves authentication information and subscriber profile (including subscriber's authorization information) from the HLR/HSS of the 3GPP subscriber's home 3GPP network.

-	Authenticates the 3GPP subscriber based on the authentication information retrieved from HLR/HSS. The authentication signaling may pass through AAA proxies.

-		Communicates authorization information to the WLAN potentially via AAA proxies.

-	Registers its (the 3GPP AAA server) address or name with the HLR/HSS for each authenticated and authorized 3GPP subscriber.

-	Initiates the Purge procedure when the 3GPP AAA server deletes the information of a subscriber.

-	May act also as a AAA proxy (see above).

-	Maintains the WLAN UE's WLAN-attach status.

-	Provides the WLAN UE's WLAN-attach status to other entities (which are out of the scope of this TS).

-	Generates and reports per-user charging/accounting information to the HPLMN CCF/CGw.

For scenario 3:

-	Communicates service authorization information (e.g. authorized W-APN, necessary keying material for tunnel establishment and user data traffics) to the PDG. AAA proxies if the PDG is located in VPLMN.

### 6.2.4	HLR/HSS

The HLR/HSS located within the 3GPP subscriber's home network is the entity containing authentication and subscription data required for the 3GPP subscriber to access the WLAN interworking service.

The HSS also provides access to the WLAN UE's WLAN-attach status for other entities, e.g. answers or relays the WLAN-attach status query from other entities (which are out of the scope of this TS).

### 6.2.5	WLAN Access Gateway

The WLAN Access Gateway applies to scenario-3.

The WLAN Access Gateway is a gateway via which the data to/from the WLAN Access Network shall be routed via a PLMN to provide a WLAN UE with 3G PS based services in scenario 3.

The WLAN Access Gateway shall reside in the VPLMN in the roaming case, and in the HPLMN in the non-roaming case.

The WLAN Access Gateway:

-	Allows VPLMN to generate charging information for users accessing via the WLAN AN in the roaming case.

-	Enforces routing of packets through the PDG.

-	Performs collection of per tunnel accounting information, e.g. volume count (byte count) and elapsed time, to be used for inter-operator settlements.

-	Filters out packets based on unencrypted information in the packets.  Packets should only be forwarded if they:

1.	are part of an existing tunnel or

2.	are expected messages from the WLAN UEs. This includes service requests, and tunnel establishment messages.

Since the WAG does not have a full trust relationship with the WLAN UE, it is not able to stop all messages. However, messages from an unknown IP address can easily be discarded. Other approaches may be used as well. Additional types of message screening are left to the operators' control.

Note:	per tunnel accounting generation in the WAG is not required when the WAG and PDG are in the same network, i.e. the non-roaming case.

The WAG shall implement policy enforcement.

If service is provided through a PDG in the HPLMN the WAG:

-	Ensures that all packets from the WLAN UE are routed to the HPLMN.

-	Ensures that packets from the authorised WLAN UEs are only routed to the appropriate PDG in the HPLMN and that packets from other sources than that PDG are not routed to the WLAN UE.

If service is provided through a PDG in the VPLMN the WAG:

-	Ensures that all packets from the WLAN UE are routed to the VPLMN.

-	Ensures that packets from the authorised WLAN UEs are only routed to the appropriate PDG in the VPLMN and that packets from other sources than that PDG are not routed to the WLAN UE.

#### 6.2.5.1	Routing Enforcement

Information regarding the selected PDG, including whether the PDG is in the HPLMN or the VPLMN is provided by the HPLMN to the VPLMN.

In the roaming case, the PDG information is delivered from the 3GPP AAA Server to the 3GPP AAA Proxy.

Within the VPLMN, policy enforcement information is delivered to the WAG.

Note:	Whether information regarding one or all PDGs is provided will likely impact the signalling which supports the activation of a further W-APN. Delivering information of all valid PDGs may limit impacts on signalling for further W-APN establishment.

The policy enforcement delivered during initial authentication will be bound to a user's AAA signalling. The WAG requires functionality to be able to securely bind this information to a user's traffic.

The binding of the policy to a user's traffic allows the WAG to drop un-authorized packets sent to/from a user.

#### 6.2.5.2	Per-tunnel Charging Generation

Editor's Note:	The details of per-tunnel charging generation in the WAG is FFS.

### 6.2.6	Packet Data Gateway

The Packet Data Gateway applies to scenario-3.

3GPP PS based services (Scenario 3) are accessed via a Packet Data Gateway. 3GPP PS based services may be accessed via a Packet Data Gateway in the user's Home Network or a PDG in the selected VPLMN. The process of authorisation and service selection (e.g. W-APN selection) and subscription checking determines whether a service shall be provided by the home network or by the visited network. The resolution of the IP address of the Packet Data Gateway providing access to the selected service will be performed in the PLMN functioning as the home network (in the VPLMN or HPLMN).

Successful activation of a selected service results in:

-	Determination of the Packet Data Gateway IP address used by the WLAN UE;

-	Allocation of a WLAN UE's remote IP address to the WLAN UE (if one is not already allocated);

-	Registration of the WLAN UE's local IP address with the Packet Data Gateway and binding of this address with the WLAN UE's remote IP address.

The Packet Data Gateway:

-	Contains routeing information for WLAN-3G connected users;

-	Routes the packet data received from/sent to the PDN to/from the WLAN-3G connected user;

-	Performs address translation and mapping;

-	Performs de-capsulation and encapsulation;

-	accepts or rejects the requested W-APN according to the decision made by the 3GPP AAA Server;

-	redirects the tunnel establishment request towards another PDG if this is indicated to be done by the 3GPP AAA Server

Allows allocation of the WLAN UE's remote IP address;

-	Relays the WLAN UE's remote IP address allocated by an external IP network to the WLAN UE, when external IP network address allocation is used.

-	Performs registration of the WLAN UE's local IP address and binding of this address with the WLAN UE's remote IP address;

-	Provides procedures for unbinding a WLAN UE's local IP address with the WLAN UE's remote IP address;

-	Provides procedures for authentication and prevention of hijacking (i.e. ensuring the validity of the WLAN UE initiating any binding of the WLAN UE's local IP address with the WLAN UE's remote IP address, unbinding etc.)

-	May filter out unauthorised or unsolicited traffic with packet filtering functions. All types of message screening are left to the operators' control, e.g. by use of Internet firewalls.

-	Generates per user charging information.

-	Generates charging information related to user data traffic for offline and online charging purposes.

-	May apply IP flow based bearer level charging [13], e.g. in order to differentiate or suppress WLAN bearer charging for 3GPP PS based services.

-	Performs the functions of Service-based Local Policy Enforcement Point (controls the quality of service that is provided to a set of IP flow as defined by a packet classifier, control admission based on policy that is applied to the IP bearers associated with the flow, and configuration of the packet handling and "gating" functionality in the user plane.)

-	Communicates with Policy Decision Function (PDF) to allow service-based local policy and QoS inter-working information to be "pushed" by the PDF or to be requested by the PDG. This communication also provides information to support the following functions in the PDG:

-	Control of Diffserv inter-working;

-	Control of RSVP admission control and inter-working;

-	Control of "gating" function in PDG;

-	WLAN bearer authorization;

-	QoS charging related function.

## 6.3	Reference Points

### 6.3.1	Wa reference point

#### 6.3.1.1	General description

The Wa reference point connects the WLAN Access Network, possibly via intermediate networks, to the 3GPP Network (i.e. the 3GPP AAA Proxy in the roaming case and the 3GPP AAA server in the non-roaming case).  The prime purpose of the protocols crossing this reference point is to transport authentication, authorization and charging-related information in a secure manner. The reference point has to accommodate also legacy WLAN Access Networks.

Legacy logical nodes outside of 3GPP scope that terminate or proxy the Wa reference point signalling and do not support 3GPP AAA protocol shall require signalling conversion between the legacy AAA protocol and the 3GPP AAA protocol.

EAP authentication shall be transported over the Wa reference point.

#### 6.3.1.2	Functionality

The functionality of the reference point is to transport AAA frames:

-	Carrying data for authentication signalling between WLAN UE and 3GPP Network.

-	Carrying data for authorization signalling between WLAN AN and 3GPP Network. These data may include a well-defined identification of the WLAN AN.

- Carrying charging signalling per WLAN user.

- Enabling the identification of the operator networks amongst which the roaming occurs.

-	Carrying keying data for the purpose of radio interface integrity protection and encryption.

-	When such functionality is supported by the WLAN AN, purging a user from the WLAN access for immediate service termination

To minimize the requirements put on the WLAN Access Network and to protect the confidentiality of the subscriber's charging status the fact whether a user is offline or online charged by his 3GPP subscription provider shall be transparent for the WLAN AN and thus for the Wa reference point.

### 6.3.2	Wx reference point

This reference point is located between 3GPP AAA Server and HSS. The prime purpose of the protocol(s) crossing this reference point is communication between WLAN AAA infrastructure and HSS.

The functionality of the reference point is to enable:

-	Retrieval of authentication vectors, e.g. for USIM authentication, from HSS.

-	Retrieval of WLAN access-related subscriber information (profile) from HSS

-	Registration of the 3GPP AAA Server of an authorised (for WLAN Access) WLAN user in the HSS.

-	Indication of change of subscriber profile within HSS (e.g. indication for the purpose of service termination).

-	Purge procedure between the 3GPP AAA server and the HSS.

-	Retrieval of online charging / offline charging function addresses from HSS.

-	Fault recovery procedure between the HSS and the 3GPP AAA Server.

-	Retrieval of service related information (e.g. W-APNs that may be selected by the WLAN UE) including an indication of whether the VPLMN is allowed to provide this service.

### 6.3.3	D'/Gr' reference point

This optional reference point is located between 3GPP AAA Server and pre-R6 HLR/HSS. The prime purpose of the protocol(s) crossing this reference point is communication between WLAN AAA infrastructure and HLR.  The protocol crossing this reference point is based upon the D/Gr reference points defined in 3GPP TS 29.002 [7]. Support of the D'/Gr' reference points requires no modifications to the MAP protocol at the HLR.

When the HLR makes it possible the functionality of the reference point is to enable:

-	Retrieval of authentication vectors, e.g. for USIM authentication, from HLR.

-	Registration of the 3GPP AAA Server of an authorised WLAN user in the HLR.

-	Indication of change of subscriber profile within HLR (e.g. indication for the purpose of service termination).

-	Purge procedure between the 3GPP AAA server and the HLR.

-	Fault recovery procedure between the HLR and the 3GPP AAA server.

-	Retrieval of service related information (e.g. APNs that may be selected by the WLAN UE) including indications of whether the service is to be supported by the HPLMN or by an identified VPLMN.

-	Retrieval of online/offline charging function address from HLR.

The functions provided on the D'/Gr' reference points are a subset of the functions provided on the D/Gr reference points described in 3GPP TS 29.002 [7].

If a 3GPP AAA Server supports the D' reference point, it will appear to the HLR/HSS as a VLR and shall behave according to the description of the behaviour of a VLR supporting the D reference point as described in 3GPP TS 29.002 [7].

If a 3GPP AAA Server supports the Gr' reference point, it will appear to the HLR/HSS as an SGSN and shall behave according to the description of the behaviour of an SGSN supporting the Gr reference point as described in 3GPP TS 29.002 [7].

Please refer to Annex A for further details of how this may work for different network scenarios.

### 6.3.4	Wo reference point

The Wo reference point is used by a 3GPP AAA Server to communicate with 3GPP Online Charging System (OCS).  The prime purpose of the protocol(s) crossing this reference point is to transport online charging related information so as to perform credit control for the online charged subscriber.

The functionality of the reference point is to transport:

-	Online charging data.

Wo reference point should be similar to Ro interface currently used in 3GPP OCS.

### 6.3.5	Wf reference point

The Wf reference point is located between 3GPP AAA Server and 3GPP Charging Gateway Function (CGF)/Charging Collection Function (CCF). The prime purpose of the protocols crossing this reference point is to transport/forward charging information towards 3GPP operator's Charging Gateway/Charging collection function located in the visited network or home network where the subscriber is residing.

The information forwarded to Charging Gateway/Charging collection function is typically used for:

-	Generating bills for offline charged subscribers by the subscribers' home operator.

-	Calculation of inter-operator accounting from all roaming users. This inter operator accounting is used to settle the payments between visited and home network operator and/or between home/visited network and WLAN.

The functionality of the reference point is to transport:

-	WLAN access-related charging data per WLAN user.

### 6.3.6	Wg reference point

The Wg reference point applies to scenario-3.

This is an AAA interface between the 3GPP AAA Server/Proxy and the WAG. It is used to provide information needed by the WAG to perform policy enforcement functions for authorised users.

### 6.3.7	Wn reference point

The Wn reference point applies to scenario-3.

This is the reference point between the WLAN Access Network and the WAG. This interface is to force traffic on a WLAN UE initiated tunnel to travel via the WAG. There can be several different ways to implement this interface as shown in Annex C. The specific method to implement this interface is subject to local agreement between the WLAN AN and the PLMN.

### 6.3.8	Wp reference point

The Wp reference point applies to scenario-3.

This is the reference point between the WAG and PDG.

### 6.3.9	Wi reference point

The Wi reference point applies to scenario-3.

This is the reference point between the Packet Data Gateway and a packet data network. The packet data network may be an operator external public or private packet data network or an intra operator packet data network, e.g. the entry point of IMS, RADIUS Accounting or Authentication, DHCP.

Wi reference point is similar to the Gi reference point provided by the PS domain. Interworking with packet data networks is provided via the Wi reference point based on IP. Mobile terminals offered services via the Wi reference point may be globally addressable through the operators public addressing scheme or through the use of a private addressing scheme.

### 6.3.10	Wm reference point

The Wm reference point applies to scenario-3.

This reference point is located between 3GPP AAA Server and Packet Data Gateway. The functionality of this reference point is to enable:

-	The 3GPP AAA Server to retrieve tunneling attributes and WLAN UE's IP configuration parameters from/via Packet Data Gateway.

-	Carrying messages for service authentication between WLAN UE and 3GPP AAA server.

-	Carrying messages for service authorization between PDG and 3GPP AAA server.

-	Carrying authentication data for the purpose of tunnel establishment, tunnel data authentication and encryption.

### 6.3.11	Wd reference point

#### 6.3.11.1	General description

The Wd reference point connects the 3GPP AAA Proxy, possibly via intermediate networks, to the 3GPP AAA Server.  The prime purpose of the protocols crossing this reference point is to transport authentication, authorization and related information in a secure manner.

EAP authentication shall be transported over the Wd reference point.

#### 6.3.11.2	Functionality

The functionality of the reference point is to transport AAA messages including:

-	Carrying data for authentication signalling between 3GPP AAA Proxy and 3GPP AAA Server

-	Carrying data for authorization signalling between 3GPP AAA Proxy and 3GPP AAA Server

-	Carrying charging signalling per WLAN user

- Carrying keying data for the purpose of radio interface integrity protection and encryption

-	Carrying authentication data for the purpose of tunnel establishment, tunnel data authentication and encryption.

-	Used for purging a user from the WLAN access for immediate service termination

-	Enabling the identification of the operator networks amongst which the roaming occurs

### 6.3.12	Wu reference point

The Wu reference point applies to scenario-3.

The Wu reference point is located between the WLAN UE and the Packet Data Gateway. It represents the WLAN UE-initiated tunnel between the WLAN UE and the Packet Data Gateway. Transport for the Wu reference point protocol is provided by the Wn and Wp reference points, which ensure that the data are routed via the WLAN Access Gateway where routing enforcement is applied.

The functionality of the Wu reference point is to enable:

-	WLAN UE-initiated tunnel establishment

-	User data packet transmission within the WLAN UE-initiated tunnel

-	Tear down of the WLAN UE initiated tunnel

### 6.3.13	Ww reference point

#### 6.3.13.1	General Description

The reference point Ww connects the WLAN UE to the WLAN Access Network per IEEE 802.1x [19] specifications.

#### 6.3.13.2	Functionality

The functionality of the reference point is per IEEE 802.1x specifications [19].

Note:	Ww is defined by IEEE 802 and provided here for information only. Any modification to the interface is strictly considered outside the scope of 3GPP.

## 6.4	Protocols

The protocol stack between the WLAN UE and the PDG is shown on figure 6.3

Figure 6.3: Protocol stack between the WLAN UE and the Packet Data Gateway

### 6.4.1	Remote IP Layer

The remote IP layer is used by the WLAN UE to be addressed in the external packet data networks (i.e. on the Wi reference point).

On this layer, the WLAN UE is addressed by its remote IP address and the packets are exchanged between the WLAN UE and an external entity. The PDG routes the remote IP packets without modifying them.

### 6.4.2	Tunneling layer

The tunneling layer consists of a tunneling header, which allows end-to-end tunneling between a WLAN UE and a PDG. It is used to encapsulate IP packets with the remote IP layer.

When encapsulated IP packets are encrypted, the tunneling header contains a field which is used to identify the peer and decrypt the packets.

### 6.4.3	Transport IP Layer

The transport IP layer is used by the intermediate entities/networks and WLAN AN in order to transport the remote IP layer packets.

Between the WLAN UE and the WAG, the transport IP layer is used by the WLAN UE to be addressed within the WLAN AN, the intermediate networks (if any) and 3G networks.

On this layer, the WLAN UE is addressed by its local IP address.

For example this local IP address can be:

-	a private IPv4 address allocated by the WLAN AN; in this case a NAT is required in the WLAN AN and used to make the WLAN UE's local IP address routable in the intermediate networks (if any), the VPLMN and the HPLMN;

-	a public (either IPv4 or IPv6) address allocated by the WLAN AN; in this case no NAT is needed;

-	an IP address allocated by the WAG in an address space that is routable in the WLAN AN as well as in the intermediate networks (if any) and the 3G network; in this case no NAT is needed.

## 6.5	WLAN user profile

The WLAN user profile shall reside in HSS (if the operator is using a legacy HLR, the WLAN user profile may reside in the 3GPP AAA Server) and be retrieved from AAA via Wx reference point. The profile shall contain the following data items: Detailed work on these parameters is expected in stage 3 work.

1.	IMSI

User identification.

2.	MSISDN (optional)

User identification, for example used for charging purposes

3.	Operator determined barring of 3GPP-WLAN interworking subscription

4.	Operator determined barring of 3GPP WLAN tunneling

This allows operator to disable all W-APNs at one time. If there is a conflict between this item and the "access allowed" flag of any W-APN, the most restrictive will prevail.

5.	Maximum session duration (optional)

Used for re-authentication purposes. If this field is not used, the WLAN AN will apply default time intervals.

6.	Charging mode (pre-paid, post-paid, both) and accounting server identifier(s) for every charging mode

Charging mode to be applied and, for every case, the charging node where the accounting information is to be reported.

7.	List of authorized W-APNs (optional)

List of W-APNs for which the user will have services available. These W-APNs may correspond to services in the home network or in the visited network. Each W-APN shall have a flag indicating whether access is allowed in visited PLMNs or in the home PLMN.

8.	Local access allowed

Indicates if the user is allowed to have direct access to external IP networks, e.g. Internet, from the WLAN Access Network.
If this parameter should be further split down to specific services that are allowed or not from the WLAN AN is FFS.

9.	Roaming allowed

Indicates if the user is allowed to use 3GPP-WLAN Interworking in an WLAN AN that have no direct connection to the home PLMN.

# 7	Procedures

Editor's note:	the following procedure is FFS:

-	Subscriber Registers.

## 7.1	I-WLAN and VPLMN Selection Procedure

### 7.1.1	Initial network selection

Figure 7.1: I-WLAN and VPLMN selection procedure

1.	The WLAN UE selects a WLAN AN and establishes the WLAN connection with a WLAN technology specific procedure (e.g. in IEEE 802.11 it starts an association procedure). The details of the selection of the WLAN AN are specified in 3GPP TS 24.234 [9].

2.	The Authentication procedure is initiated in a WLAN technology specific way and as a part of this process, the WLAN UE sends a NAI to the WLAN AN. The NAI shall be constructed as it is specified in 3GPP TS 23.003 [5].

3.	If the WLAN AN is not able to route the authentication request (e.g. in the case where the WLAN AN receives an initial NAI with an unknown realm), the WLAN AN sends a response to the WLAN UE that provides information about the 3GPP networks to which the WLAN AN is able to route authentication requests.

From this point the WLAN UE may continue the access authentication with the selected WLAN AN using a different NAI (step 2) or may start access authentication with another available WLAN AN (step 1) or may stop. The details of the WLAN UE behaviour are specified in 3GPP TS 24.234 [9]. If the WLAN UE continues the access authentication with the selected WLAN AN, it shall select a VPLMN among the 3GPP networks indicated in the response received from the WLAN AN and build the new NAI as a roaming NAI indicating this VPLMN.

4.	The WLAN AN routes the AAA message to the 3GPP AAA Server or 3GPP AAA Proxy based on the NAI and the access authentication is performed as it is specified in 3GPP TS24.234 [9].

### 7.1.2	Network re-selection

When the WLAN UE changes from the current serving PLMN to another PLMN with or without change of the WLAN AN, it needs to use a new NAI corresponding to the new PLMN in a new authentication initiated by the WLAN UE or the WLAN AN.

The 3GPP AAA Server may then receive a new authentication with PLMN selection different from the current active connection. For example, the WLAN UE lost radio in the first WLAN AN, then it changed to another WLAN AN with a different PLMN selection before the previous WLAN AN detected that the user is lost, or the WLAN UE started the new authentication before the disconnection of the previous connection. In this case, the 3GPP AAA Server shall initiate a disconnection to the currently active connection after the success of the new authentication and authorization process.

## 7.2	WLAN Access Authentication and Authorisation

Figure 7.2: Authentication and authorisation procedure

1.	WLAN connection is established with a WLAN technology specific procedure (out of scope for 3GPP).

2.	The EAP authentication procedure is initiated in WLAN technology specific way.

All EAP packets are transported over the WLAN interface encapsulated within a WLAN technology specific protocol.

All EAP packets are transported over the Wa reference point.

A number of EAP Request and EAP Response message exchanges is executed between 3GPP AAA Server and WLAN UE. The amount of round trips depends e.g. on the utilised EAP type. Information stored in and retrieved from HSS may be needed to execute certain EAP message exchanges.

3	Information to execute the authentication with the accessed user is retrieved from HSS. This information retrieval is needed only if necessary information to execute the EAP authentication is not already available in 3GPP AAA Server. To identify the user the username part of the provided NAI identity is utilised.

4	Subscribers WLAN related profile is retrieved from HSS. This profile includes e.g. the authorisation information and permanent identity of the user. Retrieval is needed only if subscriber profile information is not already available in 3GPP AAA Server.

5	If the EAP authentication and authorisation was successful, then 3GPP AAA Server sends Access Accept message to WLAN. In this message 3GPP AAA Server includes EAP Success message, keying material derived from the EAP authentication as well as connection authorisation information (e.g. NAS Filter Rule or Tunnelling attributes) to the WLAN.
WLAN stores the keying material and authorisation information to be used in communication with the authenticated WLAN UE.

6	WLAN informs the WLAN UE about the successful authentication and authorisation with the EAP Success message.

7	3GPP AAA server registers the WLAN users 3GPP AAA Server to the HSS. In registration messages the subscriber is identified by his permanent identity. This registration is needed only if the subscriber is not already registered to this 3GPP AAA Server.

## 7.3	Subscriber Profile Update

Figure 7.3: Subscriber Profile and access authorization info Update Procedure

1.	User is registered to a 3GPP AAA server

2.	Subscribers subscription is modified in the HSS e.g. via O&M.

3.	HSS updates the profile information stored in the registered 3GPP AAA server by Wx reference point procedure "Subscriber Profile".

4.	The WLAN access authorisation information of the associated connection is updated to WLAN as necessary.

### 7.3.1	Access and service Authorization information update procedure

This procedure is for senario3.

Figure 7.4: Authorization information Update Procedure

1.	User is registered to a 3GPP AAA server

2.	User's service subscription is modified in the HSS e.g. via O&M,

3.	HSS updates the profile information stored in the registered 3GPP AAA server by Wx reference point procedure "Subscriber Profile".

4.	The WLAN access authorisation information of the associated connection is updated to WLAN if necessary.

5.	The service authorisation information of the activated services is updated to PDGs if necessary. A deactivation of service may be initiated if the subscriber lost the authorization of the activated service.

6.	The filtering policy information of the activated services is updated to WAG if necessary.

Note:	The de-registration may be initiated by the AAA server to the HSS as necessary, i.e., the AAA server determines that the WLAN UE is unable to access any service upon the updated authorization.

## 7.4	Cancelling WLAN Registration

Figure 7.5: Cancellation of WLAN Registration Procedure

1.	The 3GPP subscribers WLAN subscription is cancelled in HSS.

2.	HSS cancels subscribers WLAN registration in the 3GPP AAA Server by Wx reference point procedure "Cancel WLAN Registration". In the messages subscriber is identified by his permanent identity.

3.	If the subscriber's connection still exists, Wa reference point procedure "Session Abort" procedure is executed towards WLAN.

4.	If the radio connection still exists, WLAN disconnects the radio interface connection by WLAN technology specific mechanisms.

## 7.5	Disconnecting a Subscriber by WLAN

Figure 7.6: WLAN initiated disconnection procedure

1.	WLAN detects that a Session related to a WLAN UE should be terminated towards the 3GPP AAA Server, e.g. when the WLAN UE has disappeared from WLAN coverage.

WLAN initiates Wa Session Termination procedure towards 3GPP AAA server.

2.	In case when the 3GPP AAA server decides to remove the WLAN UEs state from the 3GPP AAA server, the 3GPP AAA server notifies HSS using Wx procedure "Purge" that the WLAN registration in the 3GPP AAA Server has been cancelled. HSS removes the state related to that 3GPP AAA server, e.g., the address of the serving 3GPP AAA server for the identified subscriber.

## 7.6	Disconnecting a Subscriber by Online Charging System

Figure 7.7: OCS Initiated Disconnection Procedure

1.	A subscriber is being online charged by 3GPP AAA server for WLAN access.

2.	OCS (online Charging System) denies credit request from the 3GPP AAA server for WLAN access. The possibly already retrieved online credit runs out.

3.	To disconnect the subscriber's connection, Wa reference point procedure "Session Abort" procedure is executed towards WLAN.

4.	WLAN disconnects the radio interface connection by WLAN technology specific mechanisms.

5.	If no Wx "Purge" procedure was already initiated in step 3, then the 3GPP AAA server notifies HSS that WLAN registration in the 3GPP AAA server has been cancelled, by means of Wx procedure "Purge"

## 7.7	Charging offline charged subscribers

Figure 7.8: Charging Procedure for Offline Charged Subscribers

1.	WLAN user is authenticated and authorized for WLAN access. User profile is downloaded into 3GPP AAA server.  Part of the profile is information that the user is to be offline charged.

2.	WLAN access network collects charging data related to access or services locally consumed.

3.	WLAN access network periodically forwards collected charging information to the 3GPP AAA server over Wb reference point.

4.	3GPP AAA server forwards charging information to the CGw/CCF over the Wf reference point.

Note:	In visited network the 3GPP AAA Proxy may also periodically report the usage of resources to the local CGw/CCF over Wf reference point.

## 7.8	Charging online charged subscribers

Figure 7.9: Charging Procedure for Online Charged Subscribers

1.	WLAN user is authenticated and authorized for WLAN access. User profile is downloaded into 3GPP AAA server. Part of the profile is information that the user is to be online charged.

2.	3GPP AAA server requests online charging credit from the OCS.

3.	OCS returns credit as time and/or volume quota

4.	Allocated quota is indicated to the WLAN AN

5.	WLAN AN monitors the quota consumption

6.	When quota is almost used, WLAN AN issues re-authentication message over Wa reference point. Used quota is indicated in the request

7.	3GPP AAA Server requests more credit from the OCS

8.	OCS returns credit as time and/or volume quota

9.	Allocated new quota is indicated to the WLAN AN

10.	User disconnects from WLAN

11.	WLAN AN reports the used quota to 3GPP AAA Server over Wa reference point.

12.	User account is debited / credit according the usage information in the final message

Note:	In visited network the 3GPP AAA Proxy may also periodically report the usage of resources to the local CGw/CCF over Wf reference point. In home network the 3GPP AAA Server may also report the usage to the CGw/CCF over the Wf reference point using offline charging procedures for statistical or other purposes.

## 7.9	W-APN resolution and Tunnel establishment

This information flow presents the generic message exchange necessary in order to resolve the selected W-APN and establish a WLAN UE-Initiated tunnel for Scenario 3 purposes.

As a prerequisite of these procedures it is necessary to perform the following:

1.	WLAN Access Authentication and Authorisation and provisioning of the WLAN UE's local IP address

Figure 7.10: Example message flow to WLAN UE-Initiated tunnel establishment

When the user decides that he wants to access a service, the WLAN UE selects the W-APN network ID associated to the service requested by the user.

A detailed description of the W-APN resolution and the WLAN UE-Initiated Tunnel Establishment is given below.

2.	Depending on internal configuration, the WLAN UE initiates W-APN resolution and tunnel establishment with a PDG in VPLMN.

Note:	The configuration of the WLAN UE regarding W-APNs can be controlled by e.g. USIM Application Toolkit-based mechanisms.

2.1	UE constructs an FQDN using the W-APN Network Identifier and VPLMN ID as the Operator Identifier and performs a DNS query to resolve it. The DNS response will contain one or more IP addresses of equivalent PDGs that support the requested W-APN in the VPLMN according to standard DNS procedures.
If the VPLMN does not support the W-APN, then the DNS query returns a negative response. In this case, the WLAN UE continues with step 3.

2.2	The WLAN UE selects a PDG from the list received in step 2.1, and the establishment of an end-to-end tunnel is performed between the WLAN UE and this PDGs. The WLAN UE shall include the W-APN and the user identity in the initial tunnel establishment request.

2.3	During the tunnel establishment, the PDG contacts the 3GPP AAA Server in the HPLMN via the 3GPP AAA proxy for authorization of the WLAN UE and to retrieve the information required for the mutual authentication part of the tunnel establishment.
The 3GPP AAA Server verifies that the user requesting the tunnel establishment has been already successfully WLAN Access Authorized. If not, the tunnel establishment request is rejected. 
If the WLAN UE is not allowed to use a visited-PDG to access the given W-APN, then the tunnel establishment shall be rejected by the PDG.

If it is not possible to establish the tunnel with any of the PDG recieved from step2.1, or the tunnel establishment failure reason is that the WLAN UE is not allowed to use a visited-PDG to access the given W-APN, then the WLAN UE continues with step 3.

2.4	During the tunnel establishment procedure, the PDG and the WAG exchange information via the 3GPP AAA Proxy in order to establish a filtering policy to allow the forwarding of tunnelled packets to the PDG. The 3GPP AAA Proxy requests the WAG to apply filtering policy based on information obtained from the PDG. The 3GPP AAA Proxy decides which filtering policy could be applied by the WAG according to local information (e.g. based on number of users, WAG capabilities, roaming agreement policy, etc).

3.	Depending on internal configuration, or due to the failure of step 2.1 or 2.3, the WLAN UE initiates W-APN resolution and tunnel establishment with a PDG in HPLMN.

3.1	UE constructs an FQDN using W-APN Network Identifier and the HPLMN ID as the Operator Identifier, and performs a DNS query to resolve it. The DNS response will contain one or more IP addresses of equivalent PDGs that support the requested W-APN in the HPLMN according to standard DNS procedures.

3.2	The WLAN UE selects a PDG from the list received in step 3.1, and the establishment of an end-to-end tunnel is performed between the WLAN UE and this PDGs. The WLAN UE shall include the W-APN and the user identity in the initial tunnel establishment request.

3.3	During the tunnel establishment, the PDG contacts the 3GPP AAA Server in the HPLMN for authorization of the WLAN UE and to retrieve the information required for the mutual authentication part of tunnel establishment. The 3GPP AAA Server verifies that the user requesting the tunnel establishment has been already WLAN Access Authorized. If not, the tunnel establishment request is rejected. 
If the WLAN UE is not allowed to use a Home PDG to access the given W-APN according to his subscription, then the tunnel establishment shall be rejected by the Home PDG.

3.4	During the tunnel establishment, the PDG and the WAG exchange information via the 3GPP AAA Server and 3GPP AAA Proxy in order to establish a filtering policy to allow the forwarding of tunnelled packets to the PDG. The 3GPP AAA server requests to the WAG to apply filtering policy based on information obtained from the PDG. The 3GPP AAA server decides which filtering policy could be applied by the WAG according to local information (e.g. based on number of user, WAG capabilities, roaming agreement policy, etc). The applied filtering policy is communicated to the Home-PDG.

### 7.9.1	Redirection

In the above procedures, the WLAN UE may not be authorised to access the requested W-APN through the selected PDG. This may occur for the following reasons:

(i)	The requested W-APN is not supported by the network

(ii)	The user is not subscribed to the requested W-APN

(iii)	The PDG is in the VPLMN and the user's subscription indicates that VPLMN access is not allowed for the requested W-APN

(iv)	The operator does not wish to include all PDG addresses in DNS and so (for example) all initial requests are handled by a default PDG which may not be the correct PDG for the requested W-APN

(v)	The user has not supplied an explicit requested W-APN. This is treated as a request for the first appropriate subscribed W-APN, or for a network default W-APN (if a wildcard W-APN is included in the subscription), as per 23.060 Annex A.

In cases (i), (ii) and (iii), the request is simply rejected. In case (iii), the WLAN UE may attempt tunnel establishment to the HPLMN as described in Section 7.8.

In cases (iv) and (v) above, the AAA Server may determine that the user is authorised to access the W-APN through a different PDG. The IP address of the alternative PDG is then returned to the WLAN UE in the rejection message from PDG to WLAN UE. In this case the WLAN UE shall attempt a new tunnel establishment request to the provided PDG address.

Figure 7.11: Message flow of the tunnel establishment with redirection

During the step 2.3/3.3 in the procedure of clause 7.9, the 3GPP AAA Server authorizes the service to the WLAN UE, and sends the authorization information to the requested PDG. If requested PDG is not authorized to provide the service then the AAA server sends a new PDG (Authorized PDG) address and the authorized W-APN, then the following steps performed:

1.	The requested PDG sends tunnel redirection request to the UE with service authorization information (authorized PDG address, authorized W-APN and the re-authentication parameters provided by the AAA server).

2.	The WLAN UE sends an end-to-end tunnel establishment request to the Authorized PDG. Then end-to-end tunnel establishment begins between the Authorized PDG and the WLAN UE. A re-authentication method should be used during this tunnel establishment.

3.	The Authorized PDG provides filtering information to the WAG as it is specified in clause 7.9.

### 7.9.2	Subsequent authentication

In the case that the user attempts a subsequent tunnel establishment to a different PDG, it should be possible to avoid repeating the full authentication process (for example, a shorter re-authentication process should be used). This is ffs in Stage 3 work.

### 7.9.3	Use of DNS

It shall be possible to restrict the propagation of DNS information used for the above mechanism to DNS servers controlled by the PLMNs and to DNS servers available only to authorised 3GPP WLAN UEs (i.e. those WLAN UEs which have successfully connected to a 3GPP Interworking WLAN.)

It shall be possible to configure multiple PDG addresses against a single FQDN in a manner which allows the load to be shared across these PDGs.

Note:	The above shall be achieved by standard DNS mechanisms. The usage of TLD and the DNS query performed by the WLAN UE to resolve the W-APN are left to stage 3. Further details are in [5].

### 7.9.4	Subsequent tunnel establishment

The subsequent tunnel establishment should follow the same procedure as in the first tunnel establishment.

## 7.10	Tunnel disconnection procedures

Tunnel disconnection can be either:

-	Initiated from the WLAN UE, as a result of an explicit deactivation/de-registration from the service.

-	Initiated from the PDG, e.g. due to timeout of the tunnel connection or request from the AAA server or other network entities.

Tunnel disconnection is specified for the following situations:

-	Normal service termination resulting from an end user requesting termination of the end-to-end tunnel connection using tunnel control signalling or deletion of the IP bearers associated with a service,

-	Service termination resulting from network operator intervention,

-	Loss of radio connections which are used to transport the tunnel signalling.

The tunnel disconnection message exchanges between the WLAN UE and the PDG are performed basing on the specific tunnel control signalling protocol. The WLAN UE and the PDG release the control information associated with the tunnel during the exchange, and the PDG should send a tunnel release report to the 3GPP AAA server to update the corresponding subscriber's service connection information and status in the 3GPP AAA server,e.g. the service/tunnel connection activation info, the allocated IP address, etc. The filtering policy information applied on the WAG should also be removed. if necessary.

### 7.10.1	WLAN UE initiated tunnel disconnection

Figure 7.12: WLAN UE initiated tunnel disconnection

1.	The WLAN UE determine to release the tunnel, e.g. due to the normal service termination operation.

2.	The WLAN UE send a Release tunnel request to the PDG.

3.	Upon receiving the Release tunnel request, the PDG sends a Release acknowledgement to the WLAN UE, releases the resources and the associated control information of the tunnel, and sends a Tunnel disconnection report to the 3GPP AAA server.

4.	Upon receiving the Release acknowledgement, the WLAN UE releases the resources and the control information of the tunnel.

5.	Upon receiving the Tunnel disconnection report, the 3GPP AAA server updates the related service information and/or status of the subscriber; and removes the filtering policy related to the disconnected tunnel from WAG if necessary.

### 7.10.2	The network initiated tunnel disconnection

1.	The PDG determines to release the tunnel, e.g. due to timeout of the tunnel connection or a request from the AAA server, or due to a network initiated normal service termination or a service termination resulting from network operator intervention.

2.	The PDG sends a Release tunnel request to the WLAN UE.

3.	Upon receiving the Release tunnel request, the WLAN UE releases the resources and the associated control information of the tunnel, and sends the Release acknowledgement to the PDG.

4.	Upon receiving the release acknowledgement, the PDG releases the resources, the associated control information of the tunnel, and the related service authorization information; and sends a Tunnel disconnection report to the 3GPP AAA server.

5.	Upon receiving the Tunnel disconnection report, the 3GPP AAA server updates the related service information and/or status of the subscriber; and removes the filtering policy related to the disconnected tunnel from WAG if necessary.

Figure 7.13: The network initiated tunnel disconnection

### 7.10.3	Disconnection of the last tunnel for a WLAN UE

If the PDG detects that the disconnected tunnel is the last tunnel between the PDG and the WLAN UE, then all the WLAN UE related authorization and profile information could be removed from the PDG during the tunnel disconnection process.

In case the 3GPP AAA server decides to disconnect the WLAN UE after the disconnection of the tunnel, a disconnection procedure will proceed as described in section 7.6 (step2-4),

After the WLAN UE disconnected, if the 3GPP AAA Server decides to remove the WLAN UE's information from the 3GPP AAA Server, the 3GPP AAA Server notifies HSS using Wx procedure "Purge" that the WLAN registration in the 3GPP AAA Server has been cancelled. The HSS removes the state related to that 3GPP AAA Server, e.g., the address of the serving 3GPP AAA Server for the identified subscriber.

Annex A (informative):
Refererence Points Signalling Flows

Editor's Note: In this annex, references to Diameter should be considered as informative examples.

## A.1	Signalling Sequences examples for Wa Reference Point

### A.1.1	Authentication, Authorisation and Session Key delivery

The purpose of this signalling sequence is to carry WLAN UE - 3GPP AAA Server authentication and authorisation signalling over the Wa reference point. As a result of a successful authentication, authorisation information and session keying material for the autenticated session is delivered from the 3GPP AAA Server to the WLAN.

This Wa signalling sequence is initiated by the WLAN when authentication and authorisation of a WLAN UE is needed. This can take place when a new WLAN UE accesses WLAN, when a WLAN UE switches between WLAN APs or when a periodic re-authentication is performed.

The signalling sequence shown is based on Diameter. For signalling to WLANs using RADIUS the conversion defined in Diameter specification shall be used.

Figure A.1.1: Signalling example on Wa Reference Point for Authentication and Authorisation

1.	The WLAN initiates authentication procedure towards 3GPP network by sending Diameter_EAP_Request message to 3GPP AAA Server. This Diameter message carries encapsulated EAP Response/Identity message to 3GPP AAA Server. This message also carries a Session-ID used to identify the session within the WLAN and optionally a well-defined identification of the WLAN AN (e.g. transported in the NAS-Identifier parameter).

2.	3GPP AAA Server performs the authentication procedure based on information retrieved from HSS/HLR. 3GPP AAA Server sends message Diameter_EAP_Answer to WLAN. This message carries encapsulated EAP Request message.  The content of the EAP Request message is dependent on the EAP type being used.  WLAN conveys the EAP Request message to the WLAN UE.

3.	WLAN UE responds to WLAN by a EAP Response message. WLAN encapsulates it into Diameter_EAP_Request message and sends it to 3GPP AAA Server. The contents of the EAP Response message is dependent on the EAP type being used.

The number of roundtrip Diameter signalling exchanges similar to the signal pair 2 and 3 is dependent e.g. on the EAP type being used.

2N.	When 3GPP AAA server has successfully authenticated and authorised the 3GPP subscriber, the 3GPP AAA Server sends final Diameter_EAP_Answer message carrying encapsulated EAP Success message to WLAN. WLAN forwards the EAP Success message to the WLAN UE.

This Diameter_EAP_Answer message also carries the authorisation information (e.g. NAS Filter Rule or Tunnelling attributes) for the authenticated session. Message also carries the keying material from 3GPP AAA Server to WLAN to be used for the authenticated session by WLAN.

### A.1.2	Immediate purging of a user from the WLAN access

The purpose of this signalling sequence is to indicate to the WLAN that a specific WLAN UE shall be disconnected from accessing the WLAN interworking service.

This signalling sequence is initiated by the 3GPP AAA Server when a WLAN UE needs to be disconnected from accessing WLAN interworking service. For example, a WLAN UE used by a 3GPP subscriber may need to be disconnected when the 3GPP subscriber's subscription is cancelled or when the 3GPP subscriber's online charging account expires.

The signalling sequence shown is based on Diameter. For signalling to WLANs using RADIUS the conversion defined in Diameter specification shall be used.

Figure A.1.2: Signalling example on Wa Reference Point for User Purging

1.	When 3GPP AAA Server needs to disconnect (e.g. after receiving an external trigger) a 3GPP subscriber from the WLAN access service, the 3GPP AAA Server sends a Diameter_Abort_Session_Request to WLAN. This message contains the Session ID by which the session is identified within WLAN.

2.	WLAN responds by Diameter_Abort_Session_Answer as defined in Diameter.

## A.2	Signalling Sequences examples for Wx Reference Point

### A.2.1	Authentication Information Retrieval

This signalling sequence is initiated by a 3GPP AAA Server when a new set of authentication information for a given subscriber is to be retrieved from an HSS/HLR.

Figure A.2.1 Signalling example on Wx Reference Point for Authentication Information Retrieval

1.	3GPP AAA server detects that it requires new authentication vectors for a given 3GPP subscriber. This can happen for example, when a new 3GPP subscriber has accessed 3GPP AAA Server for authentication or when a new set of authentication information is required for one of the 3GPP subscribers already registered in the 3GPP AAA server.

3GPP AAA server sends "AUTH INFO REQUEST" message to the HSS/HLR requesting a set of authentication vectors. In the message the subscriber is identified by the IMSI, which is derived by the 3GPP AAA server from the username part of the NAI

Editor's Note:	For USIM authentication (EAP/AKA) it is ffs whether the temporary identifiers should instead of HSS/HLR be allocated in the 3GPP AAA Server, i.e. whether IMSI or Temporary identifier Is used as user identity over Wx.

2.	HSS/HLR replies by a "AUTH INFO REPLY" message containing the requested authentication vectors.

For USIM authentication (EAP/AKA) HSS/HLR has also allocated a new set of pseudonyms for the subscriber to be given to the subscriber in each subsequent authentication.

Editor's Note: It is ffs whether the temporary identifiers should instead of HSS/HLR be allocated in the 3GPP AAA Server

In case of UMTS AKA authentication, each authentication vector consists of RAND, XRES, AUTN, CK, and IK.

3GPP AAA Server stores the authentication vectors and pseudonyms to be used in future authentication procedures for the subscriber.

### A.2.2	Subscriber Profile Retrieval

This signalling sequence is initiated by a 3GPP AAA Server when a new subscriber has accessed the 3GPP AAA server and the subscription profile information of that subscriber is not available in the 3GPP AAA server. This signalling sequence can also be used if for some reason the subscription profile of a subscriber is lost.  Subscription profile contains e.g. authorisation information.

Figure A.2.2: Signalling example on Wx Reference Point for Subscriber Profile Retrieval

1.	3GPP AAA server detects that it requires the subscription profile for a given 3GPP subcriber. For example. this can happen when a new subscriber has accessed the 3GPP AAA Server for authentication.

3GPP AAA server sends "SUBSCRIBER PROFILE REQUEST" message to the HSS/HLR requesting the subscriber's profile to be downloaded to the 3GPP AAA server. In the message the subscriber is identified by a unique identifier which is used as the username part of the NAI identity.

In case of USIM authentication (EAP/AKA) the utilised unique identifier shall be  the pseudonym (associated with the IMSI)  allocated in the previous authentication or, in case of the very first authentication, the IMSI.

Editor's Note : it is ffs  whether the temporary identifiers should instead of HSS/HLR be allocated in the 3GPP AAA Server, i.e. whether IMSI or Temporary identifier Is used as user identity over Wx.

2.	At reception of "SUBSCRIBER PROFILE REQUEST" message, the HSS/HLR  initiates a Subscriber Profile Update procedure towards the 3GPP AAA Server. The Subscriber Profile Update procedure is explained in the following clause.

### A.2.3	Subscriber Profile Update

This signalling sequence is initiated by the HSS/HLR when subscriber profile needs to be sent to a 3GPP AAA server. This can be due to an explicit request from the 3GPP AAA Server or due to a modification or cancellation of subscription in the HSS/HLR.

Figure A.2.3: Signalling example on Wx Reference Point for Subscriber Profile Update

1.	HSS/HLR initiates the signalling when a subscriber profile needs to be sent to a 3GPP AAA server. This can be due to an explicit request from the 3GPP AAA Server or due to a modification or cancellation of subscription in the HSS/HLR.

HSS/HLR sends "SUBSCRIBER PROFILE" message to 3GPP AAA Server. For example. this message includes
-	Users permanent unique identifier. In case of USIM authentication (EAP/AKA) the utilised unique identifier shall be the IMSI
-	service authorisation information,
-	charging mechanism (offline / online),
-	in case of online charging the DNS name of the subscribers online charging system
3GPP AAA Server stores the subscriber profile information.

2.	3GPP AAA Server acknowledges the reception of the subscriber profile information by sending "PROFILE ACK" message to the HSS/HLR.

### A.2.4	WLAN Registration

This signalling sequence is initiated by the 3GPP AAA Server when a new subscriber has been authenticated and authorised by the 3GPP AAA server. The purpose of this procedure is to register the current 3GPP AAA Server address in the HSS/HLR.

Figure A.2.4: Signalling example on Wx Reference Point for Subscriber Registration

1.	3GPP AAA server initiates the signalling when a new 3GPP subscriber has been authenticated and authorised by the 3GPP AAA server. 3GPP AAA server sends WLAN REGISTRATION message to the HSS/HLR. This message contains the address/name of the 3GPP AAA Server and the permanent subscriber identifier. In case of USIM authentication (EAP/AKA) the unique identifier shall be the IMSI.

2.	HSS/HLR confirms the reception of the WLAN REGISTRATION message by REGISTRATION CONFIRM message.

### A.2.5	Cancel Registration

This signalling sequence is initiated by a HSS when subscription has to be removed from 3GPP AAA Server. This can happen when the subscription is cancelled in HSS.

Figure A.2.5: Signalling example on Wx Reference Point for Registration Cancellation

1.	HSS/HLR initiates the signalling when the registration of a 3GPP subscriber has to be cancelled from a 3GPP AAA server. Subscriber is identified by his permanent user identity.

2.	3GPP AAA Server confirms the reception of the CANCEL WLAN REGISTRATION message by CANCEL REGISTRATION ACK message.

### A.2.6	Purge Function for WLAN interworking

The Purge function allows a 3GPP AAA server to inform the HSS that it has deleted the information of a disconnected (either logged off or exceptionally disconnected from the WLAN interworking service) subscriber. The 3GPP AAA server may, as an implementation option, delete the information of a subscriber immediately after the implicit or explicit logging off of the subscriber. Alternatively, the 3GPP AAA server may keep the information of the disconnected subscriber for some time, such as the subscriber profile and the authentication information retrieved from the HSS, so that the information can be reused at a later connection period without accessing the HSS.

When the 3GPP AAA server deletes the information of a subscriber, it shall initiate the Purge procedure as illustrated in the following figure. Each step is explained in the following.

Figure A.2.6: Signalling example on Wx Reference Point for Purge Procedure

1)	After deleting the information of a disconnected subscriber, the 3GPP AAA server sends a Purge WLAN INFO message to the HSS.

2)	The HSS record a "WLAN INFO Purged" value and acknowledges with a Purge WLAN INFO Ack message.

## A.3	Signalling Sequences examples for D' Reference Point

### A.3.1	Authentication Information Retrieval

Figure A.3.1: Authentication Information Retrieval using D' interface

1.	3GPP AAA server detects that it requires new authentication vectors for a given 3GPP subscriber. This can happen for example, when a new 3GPP subscriber has accessed 3GPP AAA Server for authentication or when a new set of authentication information is required for one of the 3GPP subscribers already registered in the 3GPP AAA server.

3GPP AAA server sends "MAP_SEND_AUTHENTICATION_INFO Request" message to the HSS/HLR requesting a set of authentication vectors. In the message, the subscriber is identified by a unique identifier, IMSI.

2.	HSS/HLR replies by a " MAP_SEND_AUTHENTICATION_INFO Response" message containing the requested authentication vectors.

In case of UMTS AKA authentication, each authentication vector consists of RAND, XRES, AUTN, CK, and IK.

### A.3.2	Subscriber Profile Retrieval

Figure A.3.2: Subscriber Profile Retrieval using D' interface

1.	3GPP AAA server detects that it requires the subscription profile for a given 3GPP subscriber. For example, this can happen when a new subscriber has accessed the 3GPP AAA Server for authentication.

3GPP AAA server sends "MAP_RESTORE_DATA" message to the HSS/HLR requesting the subscriber's profile to be downloaded to the 3GPP AAA server. In the message the subscriber is identified by IMSI.

2.	At reception of "MAP_RESTORE_DATA" message, the HSS/HLR initiates a MAP_INSERT_SUBSCRIBER_DATA procedure towards the 3GPP AAA Server.

Since pre-R6 Subscriber Data records in HLR do not have any standardized information related to WLAN subscription, the choice and interpretation of the retrieved data is left up to the operator.

## A.4	Gr' Signalling Mechanisms to support WLAN service

### A.4.1	Introduction

The following sections describe the use of existing GPRS parameters and signalling mechanisms to support the WLAN services when interworking with legacy HLRs.

The table shows a list of parameters in existing HLR and suggests possible use in context of WLAN operation. However actual use and interpretation is left to the operator.

Table A.4.1: HLR Parameters and use for WLAN Interworking

| Existing GPRS parameter | Possible WLAN use |
| --- | --- |
| IMSI | Subscribers Identity |
| PDP Context subscription record | Services Subscriber has access to |
| VPLMN Address Allowed | Subscriber's ability to use service while roaming |
| SGSN Number, SGSN Address | Indicate the serving 3GPP AAA Server |
| Authentication Vectors | Authentication and ciphering |

Following procedures are relevant between 3GPP AAA Server and HLR with respect to the information identified above. These messages are exchanged over the Gr' interface:

-	Authentication information retrieval via infoRetrieval procedure

-	Subscriber Information retrieval via gprsLocationUpdate procedure

-	Deletion of subscription via cancelLocation procdeure.

It is important to note that use of gprsLocationUpdate procedure from WLAN will detach the subscriber from GPRS.

Further proprietary work with possible impact to existing HLR and/or SGSNs is necessary to support simultaneous connections when Gr' signalling is used for WLAN purposes.

### A.4.2	InfoRetrieval procedure:

Using this procedure the 3GPP AAA server can request for the Authentication Vectors for the user (IMSI) by initiating SEND-AUTHENTICATION-INFO message to HLR. HLR/AuC validates the user (IMSI) and generates Authentication Vectors and responds back with SEND-AUTHENTICATION-INFO-ACK message that contains the generated Authentication Vectors.

The infoRetrieval (Authentication) procedure is illustrated in Figure X below.

Figure A.4.1: infoRetrieval procedure

### A.4.2	GprsLocationUpdate procedure:

Using this procedure the 3GPP AAA server can update the HLR with the local storage area information of the user and request HLR for the subscriber information (services, roaming, etc). 3GPP AAA server initiates this procedure by sending UPDATE-LOCATION message with the local storage area information. HLR sends the subscriber information through INSERT-SUBSCRIBER-DATA, which 3GPP AAA server acknowledges. HLR repeats the above procedure until all the data is sent. On successful completion of above procedure HLR responds with UPDATE-LOCATION-ACK message.

The gprsLocationUpdate (Subscriber Information retrieval) procedure is illustrated in Figure X.1 below.

Figure A.4.2: gprsLocationUpdate procedure

## A.5	Example of Authentication procedures

### A.5.1	EAP/AKA Procedure

USIM based authentication may be based on existing AKA method. In the case of WLAN-3GPP system interworking, this method should be supported by a generic authentication mechanism (independently of the underlying WLAN standard), e.g. EAP. EAP/AKA authentication mechanism is described in Internet Draft draft-arkko-pppext-eap-aka. The current version is 05 (draft-arkko-pppext-eap-aka-05.txt). The following procedure is based on EAP/AKA authentication mechanism:

Figure A.5.1: Authentication based on EAP AKA scheme

1.	After WLAN connection establishment, Extensible Authentication Protocol is started with a WLAN technology specific procedure (out of scope for 3GPP).

2.	The WLAN sends an EAP Request/Identity to the WLAN UE.

EAP packets are transported over the WLAN interface encapsulated within a WLAN technology specific protocol.

3.	The WLAN UE starts EAP AKA authentication procedure by sending an EAP Response/Identity message. The WLAN UE sends its identity complying with Network Access Identifier (NAI) format specified in RFC 2486. NAI contains the temporary identifier allocated to WLAN UE in previous authentication if available and valid. Otherwise, the NAI shall contain the IMSI.

NOTE 1:	generating an identity conforming to NAI format from IMSI is defined in EAP/AKA draft (draft-arkko-pppext-eap-aka-05.txt).

4.	The 3GPP AAA Server is chosen based on the NAI.

NOTE 2:	Diameter/RADIUS proxy chaining and/or Diameter referral can be applied to find the AAA server.

5.	The 3GPP AAA server receives the EAP Response/Identity packet that contains the subscriber identity.

6.	3GPP AAA Server checks that it has an authentication vector available (RAND, AUTN, XRES, IK, CK) for the subscriber from previous authentication. If not, a set of authentication quintuplets is retrieved from HSS/HLR.  If a temporary identifier is provided, it is mapped to the corresponding IMSI.

7.	3GPP AAA server checks that it has the WLAN access profile of the subscriber available. If not, the profile is retrieved from HSS/HLR. 3GPP AAA Server verifies that the subscriber is authorized to use the WLAN service.

Although this step is presented after step 6 in this example, it could be performed at some other point, however before step 14. (This will be specified as part of the Wx interface.)

8.	New keying material is derived from IK and CK. The extra keying material is required in order to pass the encrypted and integrity protected temporary identifier to the WLAN UE. The keying material may also be used for WLAN technology specific confidentiality or integrity protection.

A new temporary identifier is chosen and encrypted. Temporary identifier format is FFS.

9.	3GPP AAA Server sends RAND, AUTN, and encrypted temporary identifier to WLAN in EAP Request/AKA-Challenge message.

10.	The WLAN sends the EAP Request/AKA-Challenge message to the WLAN UE

11.	WLAN UE runs UMTS algorithm on the USIM. The USIM verifies that AUTN is correct and hereby authenticates the network. If AUTN is incorrect, the terminal rejects the authentication (not shown in this example). If the sequence number is out of synch, terminal initiates a synchronization procedure (not shown in this example). If AUTN is correct, the USIM computes RES, IK and CK.

WLAN UE derives required additional keying material from IK and CK. WLAN UE decrypts temporary identifier and saves it to be used on next authentication.

12.	WLAN UE sends EAP Response/AKA-Challenge containing calculated RES to WLAN

13.	WLAN sends the EAP Response/AKA-Challenge packet to 3GPP AAA Server

14.	3GPP AAA Server compares XRES and the received RES.

15.	If the comparison in step 14 is successful, then 3GPP AAA Server sends the EAP Success message to WLAN. The 3GPP AAA Server includes the derived keying material in the message. WLAN stores the keying material to be used in communication with the authenticated WLAN UE.

16.	WLAN informs the WLAN UE about the successful authentication with the EAP Success message. Now the EAP AKA exchange has been successfully completed, and the WLAN UE and the WLAN share session key material.

NOTE 3:	The 3GPP AAA Server that is referred to in this diagram is the one that actually realises the authentication. If AAA Proxies are used between the WLAN Access Network and the AAA Server, they are not referred to in this diagram.

NOTE 4:	Temporary identifier is only used for authentication purpose. User identification on the data path is done by the Access Point in a way that is proper to the WLAN.

### A.5.2	EAP SIM procedure

SIM based authentication shall be based on existing GSM AKA method but shall include enhancements for network authentication. In the case of WLAN-3GPP system interworking, this method should be supported by a generic authentication mechanism (independently of the underlying WLAN standard), e.g. EAP.

EAP SIM authentication mechanism is described in Internet Draft draft-haverinen-pppext-eapsim. The current version is 06 (draft-haverinen-pppext-eap-sim-06.txt).

The following procedure is based on EAP SIM authentication mechanism:

Figure A.5.2: Authentication based on EAP SIM scheme

1.	After WLAN connection establishment, Extensible Authentication Protocol is started with a WLAN technology specific procedure (out of scope for 3GPP).

2.	The WLAN sends an EAP Request/Identity to the WLAN UE.

EAP packets are transported over the WLAN interface encapsulated within a WLAN technology specific protocol.

3.	The WLAN UE starts EAP SIM authentication procedure by sending an EAP Response/Identity message. The WLAN UE sends its identity complying to Network Access Identifier (NAI) format specified in RFC 2486. NAI contains the temporary identifier allocated to WLAN UE in previous authentication if available and valid. Otherwise, the NAI shall contain the IMSI.

NOTE 1:	generating an identity conforming to NAI format from IMSI is defined in EAP/SIM (draft-haverinen-pppext-eap-sim-06.txt).

4.	The 3GPP AAA Server is chosen based on the NAI.

NOTE 2:	Diameter/RADIUS proxy chaining and/or Diameter referral can be applied to find the AAA server.

5.	The 3GPP AAA server receives the EAP Response/Identity packet that contains the subscriber identity.

6.	The 3GPP AAA Server guesses, based on the NAI, that the subscriber is a GSM user; hence it sends the EAP Request/SIM-Start packet to WLAN.

7.	WLAN sends the EAP Request/SIM-Start packet to WLAN UE

8.	The WLAN UE chooses a fresh random number NONCE_MT. The random number is used in network authentication.

The WLAN UE sends the EAP Response/SIM-Start packet, containing NONCE_MT, to WLAN

9.	WLAN sends the EAP Response/SIM-Start packet to 3GPP AAA Server

10.	3GPP AAA Server checks that it has N (usually two or three) available authentication triplets (RAND, SRES, Kc) for the subscriber from previous authentication. Several triplets are required in order to generate longer session keys. If N triplets are not available, a set of authentication triplets is retrieved from HSS/HLR. If a temporary identifier is provided, it is mapped to the corresponding IMSI.

Although this step is presented after step 9 in this example, it could be performed at some other point, for example after step 5, however before step 12. (This will be specified as part of the Wx interface.)

11.	3GPP AAA server checks that it has the WLAN access profile of the subscriber available. If not, the profile is retrieved from HSS/HLR. 3GPP AAA Server verifies that the subscriber is authorized to use the WLAN service.

Although this step is presented after step 10 in this example, it could be performed at some other point, however before step 18. (This will be the specified as part of the Wx interface.)

12.	New keying material is derived from NONCE_MT and N Kc keys. The extra keying material is required in order to calculate a network authentication value and to pass the encrypted and integrity protected temporary identifier to the WLAN UE. The keying material may also be used for WLAN technology specific confidentiality or integrity protection.

A message authentication code (MAC) is calculated over the RAND challenges using a newly derived key. This MAC is used as a network authentication value.

A new temporary identifier is chosen and encrypted.

3GPP AAA Server sends RAND, MAC, and encrypted temporary identifier to WLAN in EAP Request/SIM-Challenge message.

13.	The WLAN sends the EAP Request/SIM-Challenge message to the WLAN UE

14.	WLAN UE runs the GSM A3/A8 algorithms N times, once for each received RAND.

This computing gives N SRES and Kc values.

The WLAN UE derives additional keying material from N Kc keys and NONCE_MT.

The WLAN UE calculates its copy of the network authentication MAC and checks that it is equal with the received MAC. If the MAC is incorrect, the network authentication has failed and the WLAN UE cancels the authentication (not shown in this example). The WLAN UE continues the authentication exchange only if the MAC is correct.

WLAN UE decrypts temporary identifier and saves it to be used on next authentication.

WLAN UE calculates a combined response value MAC_SRES from the N SRES responses.

15.	WLAN UE sends EAP Response/SIM-Challenge containing calculated MAC_SRES to WLAN

16.	WLAN sends the EAP Response/SIM-Challenge packet to 3GPP AAA Server

17.	3GPP AAA Server compares its copy of the MAC_SRES with the received MAC_SRES.

18.	If the comparison in step 17 is successful, then 3GPP AAA Server sends the EAP Success message to WLAN. The 3GPP AAA Server includes the derived keying material in the message. WLAN stores the keying material to be used in communication with the authenticated WLAN UE.

19.	WLAN informs the WLAN UE about the successful authentication with the EAP Success message. Now the EAP SIM exchange has been successfully completed, and the WLAN UE and the WLAN share session key material.

NOTE 3:	The 3GPP AAA Server that is referred to in this diagram is the one that actually realises the authentication. If AAA Proxies are used between the WLAN Access Network and the AAA Server, they are not referred to in this diagram.

NOTE 4:	Temporary identifier is only used for authentication purpose. User identification on the data path is done by the Access Point in a way that is proper to the WLAN

NOTE 5:	the derivation of the value of N is for further study

### A.5.3	Alternative EAP initialisation

The following figure shows an example where the realm identifying the 3GPP AAA server is retrieved by a method linked with the WLAN technology. Once the Diameter connection is initialized, the 3GPP AAA server can start the EAP identity request phase if necessary.

Editor's Note: the application of this procedure to IEEE 802.11 needs to be studied further.

Figure A.5.3 : End-to-end EAP initialisation session

### A.5.4	Re-authentication message sequence chart

The message sequence chart below illustrates the operation on re-authentication.

Figure A.5.4: Re-authentication signalling sequence

1.	Either the WLAN UE or the WLAN initiates the authentication procedure with WLAN technology specific means. The WLAN UE is requested to send its identity

2.	WLAN UE wishes to use the re-authentication procedure and therefore uses a re-authentication identity

3.	3GPP AAA server recognizes the re-authentication identity and agrees on using re-authentication. The 3GPP AAA server sends a re-authentication request (of the EAP type EAP/SIM or EAP/AKA) to the WLAN UE. The request contains an encrypted counter, an encrypted server challenge (NONCE_S) and a Message Authentication Code to cover the whole packet. The packet may also include an encrypted next re-authentication identity for next re-authentication

4.	WLAN UE verifies the Message Authentication Code and checks that the counter value is fresh. If successful, the WLAN UE responds with a re-authentication response packet that includes the counter value encrypted and a Message Authentication Code that covers the EAP packet and the server challenge NONCE_S

5.	3GPP AAA server verifies the Message Authentication Code and the counter. If successful, the 3GPP AAA server sends EAP Success to the WLAN UE.

WLAN UE and 3GPP AAA Server derive new session keys. 3GPP AAA Server sends the session keys to WLAN.

Annex B (informative):
WLAN radio technologies

| Attribute | 802.11b | Bluetooth | 802.11a | HiperLan/2 | 802.11g |
| --- | --- | --- | --- | --- | --- |
| Frequency | 2.4 GHz | 2.4 GHz | 5 GHz | 5 GHz | 2.4 GHz |
| Physical Layer | Direct Sequence Spread Spectrum (DSSS) | Frequency Hopping Spread Spectrum (FHSS) | Orthogonal Frequency Division Multiplexing (OFDM) | OFDM | Orthogonal Frequency Division Multiplexing/Complementary Code Keying OFDM/CCK |
| Channel Width | 22 MHz | 1MHz | 22 MHz | 22 MHz | 22 MHz |
| Range | 150 ft (indoors) 300 ft (outdoors) | 30 ft (with 1mW) | 100 ft (indoors) 200 ft(outdoors) | Expected to be same as 802.11a | 150 ft (indoors) (speed varies as distance from Access Point) |
| Data Throughputs | 1,2,6,11 Mbps | 720 Kbps | 6,9,12,18,36,54 Mbps (speed varies as distance from Access Point) | Same as 802.11a | Up to 54 Mbps |
| MAC | CSMA/CA in Distributed Coordinated Function Mode (DCF) (optional) Polling Based in Point Coordination Function (PCF) | Time Division Duplex (TDD) with a Master/Slave Polling Mechanism | Same as 802.11b | TDMA with TDD | Same as 802.11b |
| Miscellaneous | High Speed Data Applications Susceptible to interference from Bluetooth and other devices | Wire Replacement; Inexpensive Low component count Low Power | Improve Spectral Efficiency over 802.11b | Products not available yet | Backwards compatible with 802.11b |

Table B.1: WLAN technology comparison

Annex C (informative):
Possible interworking architectures between WLAN AN and PLMN

## C.1	WLAN shared by (or connected to) multiple ISPs and PLMNs

This is typically when a WLAN AN is owned by an independent entity such as a hotel and the owner allows subscribers of ISPs to use their WLAN AN by using the ISP network. However, WLAN AN owned by an ISP or a PLMN may also allow other ISP/PLMN subscribers to use the WLAN in a similar way.

In this situation, the WLAN AN may be connected to multiple ISPs and PLMNs in the layer 2 for scenario 3 as shown in Figure C.1.1. Another solution using DNS and NAT is described in C.2.3.

To this end, VLAN or other layer 2 tunnelling capabilities may be implemented in APs or access controller in WLAN AN in order to separate traffic of different networks.

The interface between the WLAN AN and the PLMN may be a Layer 2 tunnel, such as VLAN, Martini, or VPLS, etc. The WAG takes the role of the access router of the WLAN AN. This enables end to end tunnelling for scenario 3, even when the IP address of the PDG is not routable on the Internet.

The local IP address of a WLAN UE in scenario 3 belongs to the PLMN's IP address space. So, all the packets to a WLAN UE shall pass through the PLMN.

Figure C.1.1: Wn Interface when WLAN is connected to multiple ISPs and PLMNs

## C.2	Routing packets from WLAN UE when WLAN AN is connected to multiple VPLMNs/ISPs and it provides direct Internet access

### C.2.1	Separating traffic for different VPLMNs

When a WLAN AN providing direct Internet access has connections to multiple VPLMNs it is necessary to route all the users' non-Internet traffic to the correct VPLMN whilst Internet traffic is routed directly to the Internet. The VPLMN identity is known to the WLAN AN at initial user authentication/authorisation, since the AAA signalling is routed to that VPLMN, and the Access-Accept received from that VPLMN.

Therefore, for each VPLMN there must be a separate (logical) router in the WLAN AN which has a connection to that VPLMN and also to the Internet (note: this is a 'logical' router – it doesn't represent a restriction on WLAN AN's physical architecture). This router will receive all the traffic from WLAN UEs that are authenticated through that VPLMN. We call this the "WLAN AN Border Router for VPLMN X".

Various techniques could be used to ensure that all the WLAN UEs traffic is sent to the correct (logical) router, including:

- VLANs

A separate VLAN is defined for each VPLMN. The WLAN AN Border Router for a given VPLMN is only accessible from that VPLMN's VLAN. Appropriate RADIUS AVPs can be used to place the user onto a particular VLAN. On receiving this instruction, the WLAN AP performs VLAN tagging of all frames from the user. Since the WLAN AN knows the identity of the correct VPLMN at initial authentication/authorisation time, this instruction can be sent to the AP at this time.

As a result, all traffic from the user will be sent to the correct router.

- Compulsory tunnelling

Standard RADIUS AVPs are used to request the WLAN AP to establish a compulsory tunnel for the WLAN UEs frames towards the correct router. Again, this can be done at initial authentication/authorisation time.

Other techniques may also exist, but since there is no requirement for signalling from VPLMN to WLAN AN, the technique chosen is entirely a matter for the WLAN AN operator.

### C.2.2	Routing the traffic

The WLAN AN Border Router for a given VPLMN must distinguish Internet traffic (which should be sent directly to the Internet) from non-Internet traffic (i.e. packets to PDGs – which should be sent to the VPLMN).

One way to achieve this is for the WLAN AN to recognise the addresses of PDGs. Traffic to a known PDG address is routed to the VPLMN and other traffic to the Internet. There are several ways the WLAN AN could discover the PDG addresses:

- Statically – HPLMNs inform VPLMNs of their PDG addresses and VPLMNs inform WLAN ANs of these addresses together with any VPLMN PDG addresses. The addresses are statically configured in the routing tables of the WLAN AN Border Router.

- Dynamically - using standard IP routing protocols – HPLMNs must advertise routes to their PDGs across the inter-operator backbone. VPLMNs simply pass these advertisements to WLAN ANs along with advertisements of their own PDG addresses.

Configuration or advertisement of these addresses into the WLAN AN does not make these addresses routable from the Public Internet.Only users who are Authenticated and Authorised 3GPP WLAN UEs will be able to send packets to the (logical) WLAN AN Border Router, so only these devices can send packets to the configured/advertised addresses.

The above two approaches require that the addresses or prefixes configured or advertised are not also advertised over the public Internet. This is because although an address/prefix may be configured/advertised, there may be firewall rules or policies in the VPLMN which prevent packets being routed over the inter-operator backbone to that address. In that case, packets to that address would be dropped, meaning that any device re-using that address would not be routable at all from the WLAN UEs.

The solution is summarised in the figure below (assuming the VLAN option for dealing with multiple VPLMNs). Note that this is a logical view – the existence of two Border Routers with links to the Internet does not imply two physical elements/links.

Figure C.2.1: Traffic routing based on the use of VLANs in the WLAN AN

### C.2.3	Separating traffic to different VPLMNs using a combined DNS/NAT approach

If the WLAN UE is associated to the WLAN AN and authenticated through EAP, it can access the Internet (scenario 2) or establish a tunnel to a PDG in the VPLMN/HPLMN to access 3GPP PS based services (scenario 3). Both scenarios must be enabled in parallel. The WLAN UE performs a DNS query to resolve a W-APN to a PDG address. This IP address is the tunnel endpoint in the PLMN. If the PDG resides in the HPLMN, it must be possible to route traffic to the PDG through the selected VPLMN. The combined DNS/NAT approach as described in this chapter adds no requirements to the WLAN UE and HPLMN and uses only normal IP routing capabilities in the VPLMN.

The main idea is to use some kind of "reverse NAT" in the VPLMN that maps the PDG address received in the answer to the WLAN UE's DNS request to an address out of the address range of the VPLMN. Each PDG address is mapped to one VPLMN address, which may be a private address, depending on the addresses used in the WLAN AN. For simplicity (no new protocol needed) and performance reasons the VPLMN DNS proxy and the desired reverse NAT function are implemented on the WAG. Thus, inside of the NAT is the HPLMN address space, outside is the WLAN AN address space.

As the WLAN is directly connected to the VPLMN it is aware about the VPLMN IP addresses and can easily route scenario 3 traffic to the correct VPLMN. The VPLMN maps the destination address of the IP packet to the stored PDG address and forwards the packet to the HPLMN. Scenario 2 traffic goes to the default route configured in the WLAN edge router, i.e. to the Internet.

The following figure shows the process of W-APN resolution and NAT in the VPLMN. The figure shows a local DNS server in the WLAN AN while it is also possible that the WLAN UE receives the address of a DNS server in the VPLMN by DHCP or during EAP authentication. If the WLAN UE wants to access a PDG in the HPLMN, the W-APN indicates the HPLMN and optionally the VPLMN, otherwise the W-APN indicates the VPLMN only.

Figure C.2.2: DNS controlled reverse NAT procedure

1.	WLAN access authentication procedure between WLAN UE and AAA server based on EAP.

2.	WLAN UE retrieves PLMN list from WLAN and selects a preferred VPLMN.

3.	WLAN UE gets transport IP address, local name server (optionally) and default router address via DHCP.

4.	WLAN UE builds W-APN FQDN indicating VPLMN (optionally) and HPLMN and sends DNS request to local name server or directly to the name server in the VPLMN.

5.	Local name server inspects W-APN FQDN and forwards DNS request to VPLMN name server. VPLMN name server is implemented together with a "reverse" NAT and probably a Firewall on the WAG.

6.	VPLMN name server inspects W-APN FQDN and forwards DNS request to HPLMN name server through GPRS roaming network.

7.	HPLMN name server resolves W-APN.

8.	HPLMN name server responds to VPLMN name server with an address record of the W-APN.

9.	VPLMN name server (acting as DNS Proxy) optionally changes the PDG address contained in the address record to an address of the WAG address space (this address may be a private address) and stores the mapping between the two addresses. The new address must be routable within the WLAN to the WAG. Changing the addressses may be an option configurable by the operator.

10.	VPLMN name server responds the address record to local name server.

11.	Local name server responds the address record to WLAN UE.

12.	WLAN UE establishes tunnel to the address contained in the address record. This may be an address hosted by the WAG (otherwise it is the PDG address). This address is changed ("NATted") at the WAG to the "real" PDG address.

## C.3	WLAN AN exclusively owned by and connected to a single PLMN

This is when a PLMN operator installs its own WLAN AN without any connections to other ISPs or PLMNs.

In this case, WLAN AN can be regarded as an extension of the PLMN's IP network and no tunnel is required between WLAN AN and PLMN. The local IP address of a WLAN UE in scenario 3 belongs to the PLMN's IP address space.

## C.4	WLAN AN connected to a single ISP

This is when WLAN AN is solely connected to an ISP's backbone network. WLAN AN is regarded as an extension of the ISP's backbone network. Many legacy WLAN ANs can be categorized to this case

The connectivity between the WLAN AN and the PLMN is in layer 3 through the ISP's backbone network as shown in Figure C.4.1.

This kind of WLAN AN supports scenario 2 as defined in the TS 23.234, i.e. the authenticated WLAN UE can access the Internet directly via the ISP.

For scenario 3, the local IP address of a WLAN UE is generally allocated by the ISP and it belongs to the ISP's IP address space. When PLMN allocates WLAN UE's local IP address, a layer 2 tunnel is required.

When the end to end tunnelling is used between a WLAN UE and a PDG and the IP address of the PDG is non-routable in the Internet, an additional means is required for routing the packets to the PDG and to meet the routing enforcement requirement.

It is FFS for methods to enable scenario 3 for this kind of WLAN AN.

Figure C.4.1: Wn Interface when WLAN is connected to a PLMN through an ISP

Annex D (informative):
Support of SMS over WLAN

## D.1	Architecture for support of SMS over WLAN

The architecture for support of IP delivery and origination of SMS messages is illustrated in figure D.1. The SM-SC and GMSC/SMS-IWMSC are defined in TS 23.040 [6]. The IP Short Message Gateway IP-SM-GW communicates between the IP client and the GMSC/SMS-IWMSC. When the WLAN UE is connected to and authenticated with the 3GPP network, the HLR/HSS shall be able to provide the address of the IP-SM-GW in order to enable the SMS message to be routed to the WLAN UE.

Figure D.1:	Architecture for SMS interworking with IP attached terminal

### D.1.1	IP Short Message Gateway (IP-SM-GW)

The IP-SM-GW shall provide the protocol interworking for delivery of the short message between the IP client and the GSM/UMTS network. The functions of this network element are:

- To connect to the GMSC using established MAP protocols over SS7, appearing to the GMSC as an MSC or SGSN using the E or Gd reference points

- To connect to the SMS-IWMSC using established MAP protocols over SS7, appearing to the GMSC as an MSC or SGSN using the E or Gd reference points

- To communicate with the IP client using IP based protocols maintaining the format and functionality of the SMS message

- To associate the MSISDN with the IP address of the terminal

- Support registration and authentication of the WLAN-UE for SMS services

- Support of security associations between WLAN-UE and IP-SM-GW

### D.1.2	HLR/HSS enhancements

In the routeing of an SMS message, the SMS-GMSC performs a MAP request to the HLR/HSS "send routing information for short message" as defined in TS 29.002 [10] to determine the address of the MSC or SGSN to which to route the short message.

When the WLAN UE is connected only to a GSM/UMTS network, the "send routing information for short message" returns the address of the MSC or SGSN for delivery of SMS message. In the event that the WLAN UE is connected via WLAN to the 3GPP network, the HLR/HSS may return the address of the IP-SM-GW in the "send routing information for short message". As such, the HLR/HSS shall support the following functionality:

- An indication that the terminal is IP connected (e.g. an internal flag) for delivery of SMS

- The SS7 MAP address of the IP-SM-GW

- The logic necessary to act on the fact that the terminal is IP connected and return the IP-SM-GW address

The mechanism for prioritizing whether the short message is delivered via a GSM/UMTS or a WLAN connection when the terminal is simultaneously connected to both access networks is outside the scope of this specification.

#### D.1.2.1	An indication that the terminal is IP connected

In order to be able to return the address of the IP-SM-GW in response to a "SendRoutingInfoForShortMsg" request from the GMSC, the HLR/HSS needs to have an indication that the terminal is IP connected and that this is the preferred method for delivery of short messages.

The 3GPP AAA Server maintains the WLAN UE's WLAN attach status. On attachment, the AAA Server shall send a message to the HLR/HSS when the WLAN UE is WLAN IP attached and authenticated and when it is detached.

#### D.1.2.2	The address of the IP-SM-GW

The address of the IP-SM-GW associated with a registered WLAN UE may either be pre-defined as a single address in the HLR/HSS or dynamically configured during the registration process, depending on information received from the 3GPP AAA server or from the IP-SM-GW itself.

### D.1.3	IP address database

The IP address database shall contain the mapping of the IP address of the terminal with the cellular MSISDN. This database may be in the HLR/HSS, in a AAA server or in a ENUM server or it may be contained within the IP-SM-GW.  The database is populated during SMS service registration and authentication of the WLAN UE.

NOTE:	In the context of WLAN, the IP address of the WLAN UE is the remote IP address.

### D.1.4	Reference points

The need for additional reference points is for further study.

### D.1.5	IP Connectivity for SMS over WLAN

For delivery of SMS over WLAN, the WLAN UE needs IP connectivity. WLAN UE gets the IP connectivity by establishing a tunnel to an appropriate home network PDG. The registration of WLAN UE for SMS services occurs over this tunnel. This tunnel shall be maintained for use with SMS services while the WLAN UE is registered with IP-SM-GW. It will be used for sending or receiving of any SMS messages to and from the WLAN UE.

## D.2	Delivery of short messages to WLAN (IP) connected client

An SMS message destined for a particular terminal (with a destination address identified by a MSISDN) is originated by an SME and is sent to the SM-SC associated with that SME in accordance with TS 23.040 [6]).

### D.2.1	Message flows for IP terminated short messages

The message sequence flow for transport of the IP terminated short message from the short message service centre (SM-SC) to the IP client on the WLAN UE is shown in figure D.2.

The SMS may either be delivered directly to the WLAN UE once the IP-SM-GW has received the short message (direct method), or alternatively a notification may be used (notification method). In the notification method, the IP-SM-GW sends a message to the WLAN-UE that a short message is available and awaits a response from the WLAN-UE to determine if the user wishes to receive the message.

Figure D.2: SMS delivery to IP terminal

1)	The tunnel between the WLAN UE and the home PDG is established.

2)	Following establishment of the tunnel, the WLAN UE registers with IP-SM-GW establishing any necessary security association, authenticates for support of SMS services and registers the association between the WLAN UE MSISDN (E.164) and its IP address

3)	The SM-SC forwards the SMS message to the GMSC

4)	The GMSC interrogates the HLR/HSS to retrieve routeing information sendRoutingInfoForShortMsg for the WLAN UE. When a user is registered on a WLAN network for delivery of SMS messages, the HLR/HSS returns the address of IP-SM-GW (rather than address of appropriate MSC or SGSN)

5)	GMSC delivers the SMS to IP-SM-GW using protocols as if it was a message to an MSC or SGSN.

6)	Optionally, the IP-SM-GW interrogates the database to identify the IP address and relevant security parameters associated with the WLAN UE.

7a)	When notification method of delivery is used, the IP-SM-GW sends an SMS notification request to the WLAN UE to inform it that an SMS message is available for delivery.

7b)	When notification method of delivery is used, on receipt of the SMS notification message, the WLAN UE responds with a notification acknowledgement indicating whether it wishes to receive the SMS message.

8.	In the event that the direct method of delivery is used, or that a positive acknowledgement is received from the WLAN-UE in response to the SMS notification request, the IP-SM-GW delivers SMS to IP client using e.g. WAP, SMPP, MMAP, XML, SIP (e.g. IMS client).

9.	IP-SM-GW sends delivery report back to SMS-GMSC (see TS 23.040 [6])

10.	SMS-GMSC sends SM delivery report to HLR/HSS (see TS 23.040 [6])

11.	SMS- GMSC sends SM delivery report to SM-SC (see TS 23.040 [6])

Error handling is performed using the mechanisms defined in TS 23.040 [6].

## D.3	Short messages originated on WLAN (IP) connected client

An SMS message destined for a particular terminal (with a destination address identified by a MSISDN) may be originated by the WLAN (IP) attached client and sent, via the PDG in the case of WLAN, to the IP-SM-GW using an IP based protocol.

### D.3.1	Message flow for IP originated short messages

The message sequence flow for transport of the IP originated short message to the short message service centre (SM-SC) is shown in figure D.3. This is based on the message sequence flow in TS 23.040 [6], maintaining where possible the existing message sequences.

Figure D.3:	SMS origination from IP terminal

1)	The tunnel between the WLAN UE and the home PDG is established.

2)	Following establishment of the tunnel, the WLAN UE registers with IP-SM-GW establishing any necessary security association, authenticates for support of SMS services and registers the association between the WLAN UE MSISDN (E.164) and its IP address

3)	IP client delivers SMS message to the IP-SM-GW, using e.g. WAP, SMPP, MMPP, XML.

4)	IP-SM-GW extracts the SMS message and forwards it to SMS-IWMSC using standard MAP (as TS 23.040) exactly as if it was an MSC or SGSN.

5)	The SMS-IWMSC forwards the SMS message to the SM-SC (see TS 23.040 [6])

6)	SM-SC sends delivery report SMS-IWMSC (see TS 23.040 [6])

7)	SMS-IWMSC sends delivery report to IM-SM-SC (see TS 23.040 [6])

8)	IP-SM-GW sends delivery report to IP-UE using proprietary mechanism and/or protocols.

Error handling is performed using the mechanisms defined in TS 23.040 [6].

Annex E (informative):
Information on the discussed tunnel switching alternative

Editor's Note: The content of this annex does not contain any information relevant to the normative part of this specification and is intended to be removed at a later stage once Stage 3 work is more stable.

## E.1	Non Roaming WLAN Inter-working Reference Model

The 3GPP-WLAN Interworking reference model in the non-roaming case is shown in Figure E.1.1.

Figure E.1.1: Non Roaming Reference Model

## E.2	Roaming WLAN Inter-working Reference Model

Figure E.2.1 shows the 3GPP-WLAN interworking reference model in the roaming case.

The home network is responsible for access control. Charging records can be generated in the Visited and/or the Home 3GPP Networks.  The Wx and Wo reference points are intra-operator. The 3GPP network interfaces to other 3GPP networks, WLANs, and intermediate networks via the Wa reference point.

The 3GPP AAA Proxy relays access control signalling and accounting information to the Home 3GPP AAA Server.

It can also issue charging records to the Visited Network's CGw/CCF when required.

Figure E.2.1	: Roaming Reference Model

## E.3	WAG Description

Support of WAG in scenario 3 is mandatory for both roaming and non-roaming cases.

The WAG shall:

-	Support the setup of a secure tunnel initiated by the WLAN UE, and cooperate with the PDG to supply required parameters (e.g. DNS address, DHCP address, etc) from the destination network to the WLAN UE.

-	Resolve the address of the PDG from the W-APN information supplied by the WLAN UE and verified with the 3G AAA Server.

-	Set up a tunnel to the appropriate PDG(s).

-	Route packets between the WLAN UE initiated tunnel and the tunnel to the PDG.

-	Serve as a firewall for the network connecting the WAG and PDG, allowing only trusted packets into the 3G network.

-	Update user status information in the 3G AAA Server.

-	Generate accounting information, especially when located in the VPLMN.

## E.4	Wu Reference Point

The reference point Wu is located between the WLAN UE and the WAG. The purpose of this reference point is to transport tunnelled user data traffic securely between the WLAN UE and the 3GPP network to provide PS-based services to the WLAN UE. In roaming cases, the Wu reference point is terminated between the WLAN UE and the WAG in the VPLMN. The WLAN may apply a routing enforcement policy, if necessary, to ensure packets are routed only to the WAG.

This reference point is not required to be used when no 3G PS-based Services are provided and a direct connection to external IP network (Internet/Intranet) exists in which case the user data can be directly routed from the WLAN access network without passing 3GPP network, as it is the case with scenario 2.

No specific tunnelling protocol is specified for the Wu reference point, but the current working assumption is that the WLAN UE will be able to use an existing VPN client.

## E.5	Wn Reference Point

Reference point Wn is located between the WAG and the PDG in the HPLMN. This reference point serves the purpose of transporting tunnelled WLAN user data between WAG and the PDG. The tunnel may not need to be encrypted if the transport network (e.g. GRX) is trusted. Since the network entities connected by Wn serves a similar purpose as the connecting network entities of the Gn interface in GPRS; the GTP protocol would be considered as a candidate for the Wn reference point.

## E.6	Wp Reference Point

Reference point Wp is located between the WAG in the VPLMN and the PDG in the HPLMN. This reference point caters for the roaming WLAN traffic by transporting tunnelled WLAN user data between WAG in the VPLMN and the PDG in the HPLMN. Since the network entities connected by Wp serves a similar purpose as the connecting network entities of the Gp interface in GPRS; the GTP protocol would be considered as a candidate for the Wp reference point.

Annex F (informative):
Information on re-using the GGSN via the Gn' reference point

## F.1	Introduction

The Gn' reference point provides an optional means where GPRS mobile operators can reuse existing infrastructure and functionality for a user accessing from a WLAN UE. By standardizing this reference point, interoperability between a decomposed Packet Data Gateways (PDG) and Gateway GPRS Support Nodes (GGSN) is assured. Both the decomposed PDG and the GGSN shall be located in the same PLMN, i.e. HPLMN or VPLMN. The use of Gn' reference point in an operator network is therefore independent of other operators networks. Gn' reference point will provide reuse of GPRS infrastructure. The decomposition of PDG functionality allows to re-use existing GGSN functionality:

- Charging Gateway interfaces

- IP address allocation

- Authentication in external networks

- Single access to 3GPP PS domain services

Traffic Plane Functionality for online and offline service data flow charging (IP bearer flow charging), introduced in Release 6 may also be re-used (although this function could equally be provided at the PDG)

## F.2	Mapping between E2E tunnel and GTP tunnel

The end-to-end tunnel between the WLAN UE and the PDG is setup according to the procedure described in TS 23.234. In a configuration when the Gn' reference point is used with a decomposed PDG, then this procedure triggers the setup of the GTP tunnel between the decomposed PDG and the GGSN. Each end-to-end tunnel is mapped one-to-one to a GTP tunnel. The GTP tunnel between the decomposed PDG and GGSN is established using the two messages Create PDP Context Request and Create PDP Context Response. A GTP tunnel is identified in each node with a TEID (Tunnel End-point Identifier - an integer), an IP address and a UDP port.

Figure F.2: Mapping between E2E tunnel and GTP tunnel

In GPRS different quality-of-service can be assigned to GTP tunnels. WLAN support of layer 2 QoS is being addressed by the IEEE 802.11e study group. Work specifying the interactions with signalling techniques to support the different quality of service techniques needs to be defined. It is unclear at this time how to have a QoS mapping from IEEE 802.11e to IP and hence to the GTP tunnel.

The W-APN provided over the end-to-end tunnel shall be forwarded in the Create PDP Context Request message to GGSN to select external network e.g. PLMN service network, a corporate intranet or the Internet. Internet access can be provided directly from the WLAN Access Network using scenario 2, but of course nothing prevents a PLMN operator from providing Internet access as well via Gi interface using scenario 3. Some mobile operators might have benefits in using one unified access for all kinds of traffic.

The IMSI of the WLAN UE shall be forwarded to GGSN in the Create PDP Context Request message.

For further details on GTP tunnel management please refer to TS 29.060.

## F.3	Interworking procedures over Gn'

Editor's note:	The interworking procedures over the Gn' reference point should be specified. It is expected that these procedures are a true subset of the Gn reference point procedures.

## F.4	Issues to investigate for Gn' reference point

Some issues that needs to be investigated have been identified.

- Does the Gn' reference point have any impact on the GGSN? This shall be avoided.

- The Gn' reference point may introduce packet flows of higher bit rates into the GGSN. Does the current GGSN architecture put any unnecessary capacity constraints on these higher bit rate flows?

- MSISDN is no requirement for WLAN UE's. Is this an issue for GGSN or the GTP protocol?

- Is the UMTS Bearer Level QoS sufficient to support WLAN traffic?

- If parallel WLAN and GPRS sessions are allowed (FFS), the GGSN will serve several "SGSN's" i.e. one GPRS SGSN and one WLAN PDG simultaneously. Is his an issue for the GGSN?

- If Gn' reference point is used, the charging and service specific interfaces in PDG becomes redundant and needs to be handled in the specification in some way. One alternative is to make them conditional, and specify them to be not used if the Gn' reference point is present. Another alternative is to make the Gn' reference point mandatory, whereas the PDG charging and service specific interfaces don't need to be specified at all.

- As an alternative to reusing GPRS charging specifications and infrastructure, it has been proposed to e.g. co-locate the PDG with the GGSN. A mandatory Gn' reference point can however be a "specification tool", i.e. a way to describe, such an arrangement. This would provide PDG and GGSN co-location with a minimum of impact on existing GGSN specifications. In a PDG & GGSN co-location scenario, the Gn' will stay as a reference point only and never be materialized as an interface. This could be a scenario for future evolvement of the architecture.

Editor's note: Functional description of a decomposed PDG is FFS.

Annex G (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| 2002-08 |  |  |  |  | Converted TR23.934v0.5.0 into this TS | 0.0.0 | 0.1.0 |
| 2002-09 |  |  |  |  | Raised to v.1.0.0 for presentation at SA#17 (same content as v.0.1.0) | 0.1.0 | 1.0.0 |
| 2002-10 | SA2#27 | S2-022989 |  |  | Modifications/enhancements for scenarios 2 and 3 | 1.0.0 | 1.1.0 |
| 2002-11 | SA2#28 | S2-023517 |  |  | Modifications/enhancements for scenarios 2 and 3 | 1.1.0 | 1.2.1 |
| 2003-01 | SA2#29 | S2-030295 |  |  | Modifications/enhancements for scenarios 2 and 3 | 1.2.1 | 1.4.0 |
| 2003-02 | SA2#30 | S2-030727 |  |  | Split between scenarios 2 and 3 | 1.4.0 | 1.6.0 |
| 2003-04 | SA2#31 | S2-031514 |  |  | Modifications for scenarios 2 and 3 | 1.6.0 | 1.7.0 |
| 2003-04 |  |  |  |  | Modifications/enhancements for scenarios 2 and 3 | 1.7.0 | 1.8.0 |
| 2003-05 | SA2#32 |  |  |  | Modifications/enhancements for scenarios 2 and 3; sent for information to SA#20; scenario 2 now considered as stable; authentication definitely moved to SA3. | 1.8.0 | 1.10.0 |
| 2003-08 | SA2#34 | S2-033183 |  |  | Editorial clarifications; inclusion of tunnelling solution. Sent to SA for approval | 1.10.0 | 1.14.0 |
| 2003-10 | SA2#35 | S2-033797 |  |  | Enhancements for scenario 3 | 2.0.0 | 2.2.0 |
| 2003-11 | SA2#36 | S2-034357 |  |  | Enhancements for scenarios 2 and 3 | 2.2.0 | 2.3.0 |
| 2004-01 | SA2#37 | S2-040609 |  |  | Enhancements for scenarios 2 and 3 | 2.3.0 | 2.4.0 |
| 2004-02 | SA2#38 |  |  |  | Modifications/enhancements for scenarios 2 and 3; sent for approval to SA#23. | 2.4.0 | 2.5.0 |
| 2004-03 | SA #23 | SP-040049 |  |  | Raised to v.6.0.0 after approval at SA#23 (same content as previous version) | 2.5.0 | 6.0.0 |

# Text boxes

3GPP AAA Server

WLAN

UE

4. Access authorisation information is updated to the WLAN

2. User subscription is modified in HSS

1. User is registered to a 3GPP AAA server

HSS

3. Wx “Subscriber Profile” procedure

3. Wx “Subscriber Profile” procedure

4. Access authorisation information is updated to the WLAN

5．Service authorisation info is updated to the PDGs

6. Filtering policy information update to WAG

WAG

PDG

WLAN

2. User’s service subscription is modified in HSS

1. User is registered to a 3GPP AAA server

HSS

3GPP AAA Server