SPEECHSC                                                   S. Shanmugham

Internet-Draft                                       Cisco Systems, Inc.

Intended status: Standards Track                              D. Burnett

Expires: September 6, 2007                         Nuance Communications

March 5, 2007

Media Resource Control Protocol Version 2 (MRCPv2)

draft-ietf-speechsc-mrcpv2-12

Status of this Memo

By submitting this Internet-Draft, each author represents that any

applicable patent or other IPR claims of which he or she is aware

have been or will be disclosed, and any of which he or she becomes

aware will be disclosed, in accordance with Section 6 of BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF), its areas, and its working groups.  Note that

other groups may also distribute working documents as Internet-

Drafts.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

The list of current Internet-Drafts can be accessed at

http://www.ietf.org/ietf/1id-abstracts.txt.

The list of Internet-Draft Shadow Directories can be accessed at

http://www.ietf.org/shadow.html.

This Internet-Draft will expire on September 6, 2007.

Copyright Notice

Copyright (C) The IETF Trust (2007).

Abstract

The MRCPv2 protocol allows client hosts to control media service

resources such as speech synthesizers, recognizers, verifiers and

identifiers residing in servers on the network.  MRCPv2 is not a

"stand-alone" protocol - it relies on a session management protocol

such as the Session Initiation Protocol (SIP) to establish the MRCPv2

control session between the client and the server, and for rendezvous

and capability discovery.  It also depends on SIP and SDP to

Shanmugham & Burnett    Expires September 6, 2007               [Page 1]

Internet-Draft                   MRCPv2                       March 2007

establish the media sessions and associated parameters between the

media source or sink and the media server.  Once this is done, the

MRCPv2 protocol exchange operates over the control session

established above, allowing the client to control the media

processing resources on the speech resource server.

Table of Contents

1.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   8

2.  Document Conventions  . . . . . . . . . . . . . . . . . . . .   9

2.1.   Definitions  . . . . . . . . . . . . . . . . . . . . . .   9

2.2.   State-Machine Diagrams . . . . . . . . . . . . . . . . .   9

3.  Architecture  . . . . . . . . . . . . . . . . . . . . . . . .  10

3.1.   MRCPv2 Media Resource Types  . . . . . . . . . . . . . .  11

3.2.   Server and Resource Addressing . . . . . . . . . . . . .  12

4.  MRCPv2 Protocol Basics  . . . . . . . . . . . . . . . . . . .  12

4.1.   Connecting to the Server . . . . . . . . . . . . . . . .  13

4.2.   Managing Resource Control Channels . . . . . . . . . . .  13

4.3.   Media Streams and RTP Ports  . . . . . . . . . . . . . .  20

4.4.   MRCPv2 Message Transport . . . . . . . . . . . . . . . .  21

5.  MRCPv2 Specification  . . . . . . . . . . . . . . . . . . . .  21

5.1.   Common Protocol Elements . . . . . . . . . . . . . . . .  22

5.2.   Request  . . . . . . . . . . . . . . . . . . . . . . . .  23

5.3.   Response . . . . . . . . . . . . . . . . . . . . . . . .  24

5.4.   Status Codes . . . . . . . . . . . . . . . . . . . . . .  25

5.5.   Events . . . . . . . . . . . . . . . . . . . . . . . . .  26

6.  MRCPv2 Generic Methods, Headers, and Result Structure . . . .  27

6.1.   Generic Methods  . . . . . . . . . . . . . . . . . . . .  27

6.1.1.   SET-PARAMS . . . . . . . . . . . . . . . . . . . . .  27

6.1.2.   GET-PARAMS . . . . . . . . . . . . . . . . . . . . .  28

6.2.   Generic Message Headers  . . . . . . . . . . . . . . . .  29

6.2.1.   Channel-Identifier . . . . . . . . . . . . . . . . .  30

6.2.2.   Accept . . . . . . . . . . . . . . . . . . . . . . .  31

6.2.3.   Active-Request-Id-List . . . . . . . . . . . . . . .  31

6.2.4.   Proxy-Sync-Id  . . . . . . . . . . . . . . . . . . .  32

6.2.5.   Accept-Charset . . . . . . . . . . . . . . . . . . .  32

6.2.6.   Content-Type . . . . . . . . . . . . . . . . . . . .  32

6.2.7.   Content-ID . . . . . . . . . . . . . . . . . . . . .  32

6.2.8.   Content-Base . . . . . . . . . . . . . . . . . . . .  32

6.2.9.   Content-Encoding . . . . . . . . . . . . . . . . . .  33

6.2.10.  Content-Location . . . . . . . . . . . . . . . . . .  33

6.2.11.  Content-Length . . . . . . . . . . . . . . . . . . .  34

6.2.12.  Fetch Timeout  . . . . . . . . . . . . . . . . . . .  34

6.2.13.  Cache-Control  . . . . . . . . . . . . . . . . . . .  34

6.2.14.  Logging-Tag  . . . . . . . . . . . . . . . . . . . .  36

6.2.15.  Set-Cookie and Set-Cookie2 . . . . . . . . . . . . .  36

6.2.16.  Vendor Specific Parameters . . . . . . . . . . . . .  38

Shanmugham & Burnett    Expires September 6, 2007               [Page 2]

Internet-Draft                   MRCPv2                       March 2007

6.3.   Generic Result Structure . . . . . . . . . . . . . . . .  38

6.3.1.   Natural Language Semantics Markup Language . . . . .  39

7.  Resource Discovery  . . . . . . . . . . . . . . . . . . . . .  40

8.  Speech Synthesizer Resource . . . . . . . . . . . . . . . . .  42

8.1.   Synthesizer State Machine  . . . . . . . . . . . . . . .  42

8.2.   Synthesizer Methods  . . . . . . . . . . . . . . . . . .  43

8.3.   Synthesizer Events . . . . . . . . . . . . . . . . . . .  43

8.4.   Synthesizer Header Fields  . . . . . . . . . . . . . . .  44

8.4.1.   Jump-Size  . . . . . . . . . . . . . . . . . . . . .  44

8.4.2.   Kill-On-Barge-In . . . . . . . . . . . . . . . . . .  45

8.4.3.   Speaker Profile  . . . . . . . . . . . . . . . . . .  45

8.4.4.   Completion Cause . . . . . . . . . . . . . . . . . .  46

8.4.5.   Completion Reason  . . . . . . . . . . . . . . . . .  46

8.4.6.   Voice- Parameters  . . . . . . . . . . . . . . . . .  47

8.4.7.   Prosody-Parameters . . . . . . . . . . . . . . . . .  47

8.4.8.   Speech Marker  . . . . . . . . . . . . . . . . . . .  48

8.4.9.   Speech Language  . . . . . . . . . . . . . . . . . .  49

8.4.10.  Fetch Hint . . . . . . . . . . . . . . . . . . . . .  49

8.4.11.  Audio Fetch Hint . . . . . . . . . . . . . . . . . .  49

8.4.12.  Failed URI . . . . . . . . . . . . . . . . . . . . .  50

8.4.13.  Failed URI Cause . . . . . . . . . . . . . . . . . .  50

8.4.14.  Speak Restart  . . . . . . . . . . . . . . . . . . .  50

8.4.15.  Speak Length . . . . . . . . . . . . . . . . . . . .  50

8.4.16.  Load-Lexicon . . . . . . . . . . . . . . . . . . . .  51

8.4.17.  Lexicon-Search-Order . . . . . . . . . . . . . . . .  51

8.5.   Synthesizer Message Body . . . . . . . . . . . . . . . .  51

8.5.1.   Synthesizer Speech Data  . . . . . . . . . . . . . .  51

8.5.2.   Lexicon Data . . . . . . . . . . . . . . . . . . . .  54

8.6.   SPEAK Method . . . . . . . . . . . . . . . . . . . . . .  55

8.7.   STOP . . . . . . . . . . . . . . . . . . . . . . . . . .  57

8.8.   BARGE-IN-OCCURED . . . . . . . . . . . . . . . . . . . .  58

8.9.   PAUSE  . . . . . . . . . . . . . . . . . . . . . . . . .  60

8.10.  RESUME . . . . . . . . . . . . . . . . . . . . . . . . .  61

8.11.  CONTROL  . . . . . . . . . . . . . . . . . . . . . . . .  63

8.12.  SPEAK-COMPLETE . . . . . . . . . . . . . . . . . . . . .  65

8.13.  SPEECH-MARKER  . . . . . . . . . . . . . . . . . . . . .  66

8.14.  DEFINE-LEXICON . . . . . . . . . . . . . . . . . . . . .  68

9.  Speech Recognizer Resource  . . . . . . . . . . . . . . . . .  68

9.1.   Recognizer State Machine . . . . . . . . . . . . . . . .  70

9.2.   Recognizer Methods . . . . . . . . . . . . . . . . . . .  70

9.3.   Recognizer Events  . . . . . . . . . . . . . . . . . . .  71

9.4.   Recognizer Header Fields . . . . . . . . . . . . . . . .  71

9.4.1.   Confidence Threshold . . . . . . . . . . . . . . . .  73

9.4.2.   Sensitivity Level  . . . . . . . . . . . . . . . . .  73

9.4.3.   Speed Vs Accuracy  . . . . . . . . . . . . . . . . .  74

9.4.4.   N Best List Length . . . . . . . . . . . . . . . . .  74

9.4.5.   Input Type . . . . . . . . . . . . . . . . . . . . .  74

9.4.6.   No Input Timeout . . . . . . . . . . . . . . . . . .  74

Shanmugham & Burnett    Expires September 6, 2007               [Page 3]

Internet-Draft                   MRCPv2                       March 2007

9.4.7.   Recognition Timeout  . . . . . . . . . . . . . . . .  75

9.4.8.   Waveform URI . . . . . . . . . . . . . . . . . . . .  75

9.4.9.   Media Type . . . . . . . . . . . . . . . . . . . . .  76

9.4.10.  Input-Waveform-URI . . . . . . . . . . . . . . . . .  76

9.4.11.  Completion Cause . . . . . . . . . . . . . . . . . .  76

9.4.12.  Completion Reason  . . . . . . . . . . . . . . . . .  78

9.4.13.  Recognizer Context Block . . . . . . . . . . . . . .  78

9.4.14.  Start Input Timers . . . . . . . . . . . . . . . . .  79

9.4.15.  Speech Complete Timeout  . . . . . . . . . . . . . .  79

9.4.16.  Speech Incomplete Timeout  . . . . . . . . . . . . .  80

9.4.17.  DTMF Interdigit Timeout  . . . . . . . . . . . . . .  80

9.4.18.  DTMF Term Timeout  . . . . . . . . . . . . . . . . .  81

9.4.19.  DTMF-Term-Char . . . . . . . . . . . . . . . . . . .  81

9.4.20.  Failed URI . . . . . . . . . . . . . . . . . . . . .  81

9.4.21.  Failed URI Cause . . . . . . . . . . . . . . . . . .  81

9.4.22.  Save Waveform  . . . . . . . . . . . . . . . . . . .  82

9.4.23.  New Audio Channel  . . . . . . . . . . . . . . . . .  82

9.4.24.  Speech-Language  . . . . . . . . . . . . . . . . . .  82

9.4.25.  Ver-Buffer-Utterance . . . . . . . . . . . . . . . .  82

9.4.26.  Recognition-Mode . . . . . . . . . . . . . . . . . .  83

9.4.27.  Cancel-If-Queue  . . . . . . . . . . . . . . . . . .  83

9.4.28.  Hotword-Max-Duration . . . . . . . . . . . . . . . .  84

9.4.29.  Hotword-Min-Duration . . . . . . . . . . . . . . . .  84

9.4.30.  Interpret-Text . . . . . . . . . . . . . . . . . . .  84

9.4.31.  DTMF-Buffer-Time . . . . . . . . . . . . . . . . . .  84

9.4.32.  Clear-DTMF-Buffer  . . . . . . . . . . . . . . . . .  85

9.4.33.  Early-No-Match . . . . . . . . . . . . . . . . . . .  85

9.4.34.  Num-Min-Consistent-Pronunciations  . . . . . . . . .  85

9.4.35.  Consistency-Threshold  . . . . . . . . . . . . . . .  85

9.4.36.  Clash-Threshold  . . . . . . . . . . . . . . . . . .  86

9.4.37.  Personal-Grammar-URI . . . . . . . . . . . . . . . .  86

9.4.38.  Enroll-Utterance . . . . . . . . . . . . . . . . . .  86

9.4.39.  Phrase-Id  . . . . . . . . . . . . . . . . . . . . .  87

9.4.40.  Phrase-NL  . . . . . . . . . . . . . . . . . . . . .  87

9.4.41.  Weight . . . . . . . . . . . . . . . . . . . . . . .  87

9.4.42.  Save-Best-Waveform . . . . . . . . . . . . . . . . .  87

9.4.43.  New-Phrase-Id  . . . . . . . . . . . . . . . . . . .  88

9.4.44.  Confusable-Phrases-URI . . . . . . . . . . . . . . .  88

9.4.45.  Abort-Phrase-Enrollment  . . . . . . . . . . . . . .  88

9.5.   Recognizer Message Body  . . . . . . . . . . . . . . . .  88

9.5.1.   Recognizer Grammar Data  . . . . . . . . . . . . . .  89

9.5.2.   Recognizer Result Data . . . . . . . . . . . . . . .  92

9.5.3.   Enrollment Result Data . . . . . . . . . . . . . . .  93

9.5.4.   Recognizer Context Block . . . . . . . . . . . . . .  93

9.6.   Recognizer Results . . . . . . . . . . . . . . . . . . .  93

9.6.1.   Markup Functions . . . . . . . . . . . . . . . . . .  94

9.6.2.   Overview of Recognizer Result Elements and their

Relationships  . . . . . . . . . . . . . . . . . . .  95

Shanmugham & Burnett    Expires September 6, 2007               [Page 4]

Internet-Draft                   MRCPv2                       March 2007

9.6.3.   Elements and Attributes  . . . . . . . . . . . . . .  95

9.7.   Enrollment Results . . . . . . . . . . . . . . . . . . . 100

9.7.1.   NUM-CLASHES Element  . . . . . . . . . . . . . . . . 100

9.7.2.   NUM-GOOD-REPETITIONS Element . . . . . . . . . . . . 100

9.7.3.   NUM-REPETITIONS-STILL-NEEDED Element . . . . . . . . 100

9.7.4.   CONSISTENCY-STATUS Element . . . . . . . . . . . . . 101

9.7.5.   CLASH-PHRASE-IDS Element . . . . . . . . . . . . . . 101

9.7.6.   TRANSCRIPTIONS Element . . . . . . . . . . . . . . . 101

9.7.7.   CONFUSABLE-PHRASES Element . . . . . . . . . . . . . 101

9.8.   DEFINE-GRAMMAR . . . . . . . . . . . . . . . . . . . . . 101

9.9.   RECOGNIZE  . . . . . . . . . . . . . . . . . . . . . . . 105

9.10.  STOP . . . . . . . . . . . . . . . . . . . . . . . . . . 110

9.11.  GET-RESULT . . . . . . . . . . . . . . . . . . . . . . . 112

9.12.  START-OF-INPUT . . . . . . . . . . . . . . . . . . . . . 112

9.13.  START-INPUT-TIMERS . . . . . . . . . . . . . . . . . . . 113

9.14.  RECOGNITION-COMPLETE . . . . . . . . . . . . . . . . . . 113

9.15.  START-PHRASE-ENROLLMENT  . . . . . . . . . . . . . . . . 115

9.16.  ENROLLMENT-ROLLBACK  . . . . . . . . . . . . . . . . . . 116

9.17.  END-PHRASE-ENROLLMENT  . . . . . . . . . . . . . . . . . 117

9.18.  MODIFY-PHRASE  . . . . . . . . . . . . . . . . . . . . . 117

9.19.  DELETE-PHRASE  . . . . . . . . . . . . . . . . . . . . . 118

9.20.  INTERPRET  . . . . . . . . . . . . . . . . . . . . . . . 118

9.21.  INTERPRETATION-COMPLETE  . . . . . . . . . . . . . . . . 120

9.22.  DTMF Detection . . . . . . . . . . . . . . . . . . . . . 121

10. Recorder Resource . . . . . . . . . . . . . . . . . . . . . . 121

10.1.  Recorder State Machine . . . . . . . . . . . . . . . . . 122

10.2.  Recorder Methods . . . . . . . . . . . . . . . . . . . . 122

10.3.  Recorder Events  . . . . . . . . . . . . . . . . . . . . 122

10.4.  Recorder Header Fields . . . . . . . . . . . . . . . . . 122

10.4.1.  Sensitivity Level  . . . . . . . . . . . . . . . . . 123

10.4.2.  No Input Timeout . . . . . . . . . . . . . . . . . . 123

10.4.3.  Completion Cause . . . . . . . . . . . . . . . . . . 123

10.4.4.  Completion Reason  . . . . . . . . . . . . . . . . . 124

10.4.5.  Failed URI . . . . . . . . . . . . . . . . . . . . . 124

10.4.6.  Failed URI Cause . . . . . . . . . . . . . . . . . . 124

10.4.7.  Record URI . . . . . . . . . . . . . . . . . . . . . 125

10.4.8.  Media Type . . . . . . . . . . . . . . . . . . . . . 125

10.4.9.  Max Time . . . . . . . . . . . . . . . . . . . . . . 125

10.4.10. Trim-Length  . . . . . . . . . . . . . . . . . . . . 126

10.4.11. Final Silence  . . . . . . . . . . . . . . . . . . . 126

10.4.12. Capture On Speech  . . . . . . . . . . . . . . . . . 126

10.4.13. Ver-Buffer-Utterance . . . . . . . . . . . . . . . . 126

10.4.14. Start Input Timers . . . . . . . . . . . . . . . . . 127

10.4.15. New Audio Channel  . . . . . . . . . . . . . . . . . 127

10.5.  Recorder Message Body  . . . . . . . . . . . . . . . . . 127

10.6.  RECORD . . . . . . . . . . . . . . . . . . . . . . . . . 127

10.7.  STOP . . . . . . . . . . . . . . . . . . . . . . . . . . 128

10.8.  RECORD-COMPLETE  . . . . . . . . . . . . . . . . . . . . 129

Shanmugham & Burnett    Expires September 6, 2007               [Page 5]

Internet-Draft                   MRCPv2                       March 2007

10.9.  START-INPUT-TIMERS . . . . . . . . . . . . . . . . . . . 130

10.10. START-OF-INPUT . . . . . . . . . . . . . . . . . . . . . 130

11. Speaker Verification and Identification . . . . . . . . . . . 131

11.1.  Speaker Verification State Machine . . . . . . . . . . . 132

11.2.  Speaker Verification Methods . . . . . . . . . . . . . . 134

11.3.  Verification Events  . . . . . . . . . . . . . . . . . . 135

11.4.  Verification Header Fields . . . . . . . . . . . . . . . 135

11.4.1.  Repository-URI . . . . . . . . . . . . . . . . . . . 136

11.4.2.  Voiceprint-Identifier  . . . . . . . . . . . . . . . 136

11.4.3.  Verification-Mode  . . . . . . . . . . . . . . . . . 136

11.4.4.  Adapt-Model  . . . . . . . . . . . . . . . . . . . . 137

11.4.5.  Abort-Model  . . . . . . . . . . . . . . . . . . . . 137

11.4.6.  Min-Verification-Score . . . . . . . . . . . . . . . 138

11.4.7.  Num-Min-Verification-Phrases . . . . . . . . . . . . 138

11.4.8.  Num-Max-Verification-Phrases . . . . . . . . . . . . 138

11.4.9.  No-Input-Timeout . . . . . . . . . . . . . . . . . . 139

11.4.10. Save-Waveform  . . . . . . . . . . . . . . . . . . . 139

11.4.11. Media Type . . . . . . . . . . . . . . . . . . . . . 139

11.4.12. Waveform-URI . . . . . . . . . . . . . . . . . . . . 139

11.4.13. Voiceprint-Exists  . . . . . . . . . . . . . . . . . 140

11.4.14. Ver-Buffer-Utterance . . . . . . . . . . . . . . . . 140

11.4.15. Input-Waveform-Uri . . . . . . . . . . . . . . . . . 140

11.4.16. Completion-Cause . . . . . . . . . . . . . . . . . . 141

11.4.17. Completion Reason  . . . . . . . . . . . . . . . . . 142

11.4.18. Speech Complete Timeout  . . . . . . . . . . . . . . 142

11.4.19. New Audio Channel  . . . . . . . . . . . . . . . . . 142

11.4.20. Abort-Verification . . . . . . . . . . . . . . . . . 142

11.4.21. Start Input Timers . . . . . . . . . . . . . . . . . 142

11.5.  Verification Message Body  . . . . . . . . . . . . . . . 143

11.5.1.  Verification Result Data . . . . . . . . . . . . . . 143

11.5.2.  Verification Result Elements . . . . . . . . . . . . 143

11.6.  START-SESSION  . . . . . . . . . . . . . . . . . . . . . 147

11.7.  END-SESSION  . . . . . . . . . . . . . . . . . . . . . . 148

11.8.  QUERY-VOICEPRINT . . . . . . . . . . . . . . . . . . . . 149

11.9.  DELETE-VOICEPRINT  . . . . . . . . . . . . . . . . . . . 150

11.10. VERIFY . . . . . . . . . . . . . . . . . . . . . . . . . 151

11.11. VERIFY-FROM-BUFFER . . . . . . . . . . . . . . . . . . . 151

11.12. VERIFY-ROLLBACK  . . . . . . . . . . . . . . . . . . . . 154

11.13. STOP . . . . . . . . . . . . . . . . . . . . . . . . . . 154

11.14. START-INPUT-TIMERS . . . . . . . . . . . . . . . . . . . 155

11.15. VERIFICATION-COMPLETE  . . . . . . . . . . . . . . . . . 156

11.16. START-OF-INPUT . . . . . . . . . . . . . . . . . . . . . 156

11.17. CLEAR-BUFFER . . . . . . . . . . . . . . . . . . . . . . 157

11.18. GET-INTERMEDIATE-RESULT  . . . . . . . . . . . . . . . . 157

12. Security Considerations . . . . . . . . . . . . . . . . . . . 158

12.1.  Rendezvous and Session Establishment . . . . . . . . . . 159

12.2.  Control channel protection . . . . . . . . . . . . . . . 159

12.3.  Media session protection . . . . . . . . . . . . . . . . 159

Shanmugham & Burnett    Expires September 6, 2007               [Page 6]

Internet-Draft                   MRCPv2                       March 2007

12.4.  Indirect Content Access  . . . . . . . . . . . . . . . . 159

12.5.  Protection of stored media . . . . . . . . . . . . . . . 160

13. IANA Considerations . . . . . . . . . . . . . . . . . . . . . 160

13.1.  New registries . . . . . . . . . . . . . . . . . . . . . 160

13.1.1.  MRCPv2 resource types  . . . . . . . . . . . . . . . 160

13.1.2.  MRCPv2 methods and events  . . . . . . . . . . . . . 160

13.1.3.  MRCPv2 headers . . . . . . . . . . . . . . . . . . . 160

13.1.4.  MRCPv2 status codes  . . . . . . . . . . . . . . . . 161

13.1.5.  Grammar Reference List Parameters  . . . . . . . . . 161

13.1.6.  MRCPv2 vendor-specific parameters  . . . . . . . . . 161

13.2.  NLSML-related registrations  . . . . . . . . . . . . . . 162

13.2.1.  application/nlsml+xml MIME type registration . . . . 162

13.3.  NLSML XML Schema registration  . . . . . . . . . . . . . 162

13.4.  MRCPv2 XML Namespace registration  . . . . . . . . . . . 163

13.5.  text/grammar-ref-list Mime Type Registration . . . . . . 163

13.6.  session URL scheme registration  . . . . . . . . . . . . 164

13.7.  SDP parameter registrations  . . . . . . . . . . . . . . 165

14. Examples  . . . . . . . . . . . . . . . . . . . . . . . . . . 166

14.1.  Message Flow . . . . . . . . . . . . . . . . . . . . . . 166

14.2.  Recognition Result Examples  . . . . . . . . . . . . . . 175

14.2.1.  Simple ASR Ambiguity . . . . . . . . . . . . . . . . 175

14.2.2.  Mixed Initiative . . . . . . . . . . . . . . . . . . 176

14.2.3.  DTMF Input . . . . . . . . . . . . . . . . . . . . . 177

14.2.4.  Interpreting Meta-Dialog and Meta-Task Utterances  . 177

14.2.5.  Anaphora and Deixis  . . . . . . . . . . . . . . . . 178

14.2.6.  Distinguishing Individual Items from Sets with

One Member . . . . . . . . . . . . . . . . . . . . . 179

14.2.7.  Extensibility  . . . . . . . . . . . . . . . . . . . 180

15. ABNF Normative Definition . . . . . . . . . . . . . . . . . . 180

16. XML Schemas . . . . . . . . . . . . . . . . . . . . . . . . . 195

16.1.  NLSML Schema Definition  . . . . . . . . . . . . . . . . 195

16.2.  Enrollment Results Schema Definition . . . . . . . . . . 196

16.3.  Verification Results Schema Definition . . . . . . . . . 197

17. References  . . . . . . . . . . . . . . . . . . . . . . . . . 200

17.1.  Normative References . . . . . . . . . . . . . . . . . . 200

17.2.  Informative References . . . . . . . . . . . . . . . . . 203

Appendix A.  Contributors . . . . . . . . . . . . . . . . . . . . 204

Appendix B.  Acknowledgements . . . . . . . . . . . . . . . . . . 205

Authors' Addresses  . . . . . . . . . . . . . . . . . . . . . . . 205

Intellectual Property and Copyright Statements  . . . . . . . . . 206

Shanmugham & Burnett    Expires September 6, 2007               [Page 7]

Internet-Draft                   MRCPv2                       March 2007

1.  Introduction

The MRCPv2 protocol is designed to allow a client device to control

media processing resources on the network.  Some of these media

processing resources include speech recognition engines, speech

synthesis engines, speaker verification and speaker identification

engines.  MRCPv2 enables the implementation of distributed

Interactive Voice Response platforms using VoiceXML [30] browsers or

other client applications while maintaining separate back-end speech

processing capabilities on specialized speech processing servers.

MRCPv2 is based on the earlier Media Resource Control Protocol (MRCP)

[31] developed jointly by Cisco Systems, Inc., Nuance Communications,

and Speechworks Inc.

The protocol requirements of SPEECHSC [1] dictate that the solution

be capable of reaching a media processing server and setting up

communication channels to the media resources, and sending and

receiving control messages and media streams to/from the server.  The

Session Initiation Protocol (SIP) [3] meets these requirements.

MRCPv2 leverages these capabilities by building upon SIP and the

Session Description Protocol (SDP) [4].  MRCPv2 uses SIP to setup and

tear down media and control sessions with the server.  In addition,

the client can use a SIP re-INVITE method (an INVITE dialog sent

within an existing SIP Session) to change the characteristics of

these media and control session while maintaining the SIP dialog

between the client and server.  SDP is used to describe the

parameters of the media sessions associated with that dialog.  It is

mandatory to support SIP as the session establishment protocol to

ensure interoperability.  Other protocols can be used for session

establishment by prior agreement.  This document only describes the

use of SIP and SDP.

MRCPv2 uses SIP and SDP to create the client/server dialog and set up

the media channels to the server.  It also uses SIP and SDP to

establish MRCPv2 control sessions between the client and the server

for each media processing resource required for that dialog.  The

MRCPv2 protocol exchange between the client and the media resource is

carried on that control session.  MRCPv2 protocol exchanges do not

change the state of the SIP dialog, the media sessions, or other

parameters of the dialog initiated via SIP.  It controls and affects

the state of the media processing resource associated with the MRCPv2

session(s).

MRCPv2 defines the messages to control the different media processing

resources and the state machines required to guide their operation.

It also describes how these messages are carried over a transport

layer protocol such as TCP or TLS (Note: SCTP is a viable transport

for MRCPv2 as well, but the mapping onto SCTP is not described in

Shanmugham & Burnett    Expires September 6, 2007               [Page 8]

Internet-Draft                   MRCPv2                       March 2007

this specification).

2.  Document Conventions

RFC2119 [5] provides the interpretations for the key words "MUST",

"MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT",

"RECOMMENDED", "MAY", and "OPTIONAL" found in this document.

Since many of the definitions and syntax are identical to HTTP/1.1

(RFC2616 [6]), this specification refers to the section where they

are defined rather than copying it.  For brevity, [HX.Y] is to be

taken to refer to Section X.Y of RFC2616.

All the mechanisms specified in this document are described in both

prose and an augmented Backus-Naur form (ABNF [9]).

The complete message format in ABNF form is provided in Section 15

and is the normative format definition.

2.1.  Definitions

Media Resource

An entity on the speech processing server that can be

controlled through the MRCPv2 protocol.

MRCP Server

Aggregate of one or more "Media Resource" entities on

a Server, exposed through the MRCPv2 protocol

("Server" for short).

MRCP Client

An entity controlling one or more Media Resources

through the MRCPv2 protocol ("Client" for short).

DTMF

Dual Tone Multi-Frequency; a method of transmitting

key presses in-band, either as actual tones (Q.23

[28]) or as named tone events (RFC2833 [29]).

Hotword Mode

A mode of speech recognition where a stream of

utterances is evaluated for match against a small set

of command words.  This is generally employed to

either trigger some action, or to control the

subsequent grammar to be used for further recognition

2.2.  State-Machine Diagrams

The state-machine diagrams in this document do not show every

possible method call.  Rather, they reflect the state of the resource

based on the methods that have moved to IN-PROGRESS or COMPLETE

Shanmugham & Burnett    Expires September 6, 2007               [Page 9]

Internet-Draft                   MRCPv2                       March 2007

states.  Note that since PENDING requests essentially have not

affected the resource yet and are in queue to be processed, they are

not reflected in the state-machine diagrams.

3.  Architecture

A system using MRCPv2 consists of a client that requires the

generation and/or consumption of media streams and a media resource

server that has the resources or "engines" to process these streams

as input or generate these streams as output.  The client uses SIP

and SDP to establish an MRCPv2 control channel with the server to use

its media processing resources.  MRCPv2 servers are addressed using

SIP URIs.

The session management protocol (SIP) uses SDP with the offer/answer

model described in RFC3264 [7] to set up the MRCPv2 control channels

and describe their characteristics.  A separate MRCPv2 session is

needed to control each of the media processing resources associated

with the SIP dialog between the client and server.  Within a SIP

dialog, the individual resource control channels for the different

resources are added or removed through SDP offer/answer carried in a

SIP re-INVITE transaction.

The server, through the SDP exchange, provides the client with an

unambiguous channel identifier and a TCP port number.  The client MAY

then open a new TCP connection with the server using this port

number.  Multiple MRCPv2 channels can share a TCP connection between

the client and the server.  All MRCPv2 messages exchanged between the

client and the server carry the specified channel identifier that the

server MUST ensure is unambiguous among all MRCPv2 control channels

that are active on that server.  The client uses this channel

identifier to indicate the media processing resource associated with

that channel.

The session management protocol (SIP) also establishes the media

sessions between the client (or other source/sink of media) and the

MRCPv2 server using SDP m-lines.  One or more media processing

resources may share a media session under a SIP session, or each

media processing resource may have its own media session.

Shanmugham & Burnett    Expires September 6, 2007              [Page 10]

Internet-Draft                   MRCPv2                       March 2007

MRCPv2 client                    MRCPv2 Media Resource Server

|--------------------|             |-----------------------------|

||------------------||             ||---------------------------||

|| Application Layer||             || TTS  | ASR  | SV   | SI   ||

||------------------||             ||Engine|Engine|Engine|Engine||

||Media Resource API||             ||---------------------------||

||------------------||             || Media Resource Management ||

|| SIP  |  MRCPv2   ||             ||---------------------------||

||Stack |           ||             ||   SIP  |    MRCPv2        ||

||      |           ||             ||  Stack |                  ||

||------------------||             ||---------------------------||

||   TCP/IP Stack   ||----MRCPv2---||       TCP/IP Stack        ||

||                  ||             ||                           ||

||------------------||-----SIP-----||---------------------------||

|--------------------|             |-----------------------------|

|                             /

SIP                           /

|                           /

|-------------------|              RTP

|                   |              /

| Media Source/Sink |-------------/

|                   |

|-------------------|

Figure 1: Architectural Diagram

3.1.  MRCPv2 Media Resource Types

An MRCPv2 server may offer one or more of the following media

processing resources to its clients.

Basic Synthesizer

A speech synthesizer resource with very limited

capabilities, that can generate its media stream

exclusively from concatenated audio clips.  The speech

data is described using a limited subset of SSML [24]

elements.  A basic synthesizer MUST support the SSML

tags <speak>, <audio>, <say-as> and <mark>.

Speech Synthesizer

A full capability speech synthesis resource capable of

rendering speech from text.  Such a synthesizer MUST

have full SSML [24] support.

Recorder

A resource capable of recording audio and saving it to

a URI.  A recorder MUST provide some end-pointing

capabilities for suppressing silence at the beginning

and end of a recording, and MAY also suppress silence

in the middle of a recording.  If such suppression is

Shanmugham & Burnett    Expires September 6, 2007              [Page 11]

Internet-Draft                   MRCPv2                       March 2007

done, the recorder MUST maintain timing metadata to

indicate the actual time stamps of the recorded media.

DTMF Recognizer

A recognition resource capable of extracting and

interpreting DTMF digits in a media stream and

matching them against a supplied digit grammar It

could also do a semantic interpretation based on

semantic tags in the grammar.

Speech Recognizer

A full speech recognition resource that is capable of

receiving a media stream containing audio and

interpreting it to recognition results.  It also has a

natural language semantic interpreter to post-process

the recognized data according to the semantic data in

the grammar and provide semantic results along with

the recognized input.  The recognizer may also support

enrolled grammars, where the client can enroll and

create new personal grammars for use in future

recognition operations.

Speaker Verifier

A resource capable of verifying the authenticity of a

claimed identity by matching a media stream containing

spoken input to a pre-existing voiceprint.  This may

also involve matching the caller's voice against more

than one voiceprint, also called multi-verification or

speaker identification.

3.2.  Server and Resource Addressing

The MRCPv2 server as a whole is a generic SIP server and is addressed

is by a SIP Contact URI registered by the server through SIP (or via

static configuration of the SIP registrar).

For example:

sip:mrcpv2@example.net

4.  MRCPv2 Protocol Basics

MRCPv2 requires a connection-oriented transport layer protocol such

as TCP or SCTP to guarantee reliable sequencing and delivery of

MRCPv2 control messages between the client and the server.  In order

to meet the requirements for security enumerated in SpeechSC

Requirements [1], clients and servers MUST implement TLS as well.

One or more connections between the client and the server can be

shared among different MRCPv2 channels to the server.  The individual

messages carry the channel identifier to differentiate messages on

Shanmugham & Burnett    Expires September 6, 2007              [Page 12]

Internet-Draft                   MRCPv2                       March 2007

different channels.  MRCPv2 protocol encoding is text based with

mechanisms to carry embedded binary data.  This allows arbitrary data

like recognition grammars, recognition results, synthesizer speech

markup etc. to be carried in MRCPv2 messages.

4.1.  Connecting to the Server

MRCPv2 employs a session establishment and management protocol such

as SIP in conjunction with SDP.  The client finds and reaches an

MRCPv2 server using conventional INVITE and other SIP transactions

for establishing, maintaining, and terminating SIP dialogs.  The SDP

offer/answer exchange model over SIP is used to establish a resource

control channel for each resource.  The SDP offer/answer exchange is

also used to establish media sessions between the server and the

source or sink of audio.

4.2.  Managing Resource Control Channels

The client needs a separate MRCPv2 resource control channel to

control each media processing resource under the SIP dialog.  A

unique channel identifier string identifies these resource control

channels.  The channel identifier is an unambiguous, opaque string

followed by an "@", then by a string token specifying the type of

resource.  The server generates the channel identifier and MUST make

sure it does not clash with the identifier of any other MRCP channel

currently allocated by that server.  MRCPv2 defines the following

IANA-registered types of media processing resources.  Additional

resource types, their associated methods/events and state machines

may be added by future specification proposing to extend the

capabilities of MRCPv2.

+---------------+----------------------+--------------+

| Resource Type | Resource Description | Described in |

+---------------+----------------------+--------------+

| speechrecog   | Speech Recognizer    | Section 9    |

| dtmfrecog     | DTMF Recognizer      | Section 9    |

| speechsynth   | Speech Synthesizer   | Section 8    |

| basicsynth    | Basic Synthesizer    | Section 8    |

| speakverify   | Speaker Verification | Section 11   |

| recorder      | Speech Recorder      | Section 10   |

+---------------+----------------------+--------------+

Resource Types

The SIP INVITE or re-INVITE transaction and the SDP offer/answer

exchange it carries contain m-lines describing the resource control

channel to be allocated.  There MUST be one SDP m-line for each

MRCPv2 resource to be used in the session.  This m-line MUST have a

Shanmugham & Burnett    Expires September 6, 2007              [Page 13]

Internet-Draft                   MRCPv2                       March 2007

media type field of "application" and a transport type field of

either "TCP/MRCPv2" or "TCP/TLS/MRCPv2".  (The usage of SCTP with

MRCPv2 may be addressed in a future specification).  The port number

field of the m-line MUST contain the "discard" port of the transport

protocol (port 9 for TCP) in the SDP offer from the client and MUST

contain the TCP listen port on the server in the SDP answer.  The

client may then either set up a TCP or TLS connection to that server

port or share an already established connection to that port.  The

format field of the m-line is not used by this protocol.  However, to

enable proper generic SDP parsing, it MUST have the arbitrarily-

selected value of "1".  The client must specify the resource type

identifier in the resource attribute associated with the control

m-line of the SDP offer.  The server MUST respond with the full

Channel-Identifier (which includes the resource type identifier and

an unambiguous string) in the "channel" attribute associated with the

control m-line of the SDP answer.

All servers MUST support TLS.  Servers MAY support TCP without TLS in

physically secure environments.  It is up to the client, through the

SDP offer, to choose which transport it wants to use for an MRCPv2

session.  When using TCP the m-lines MUST conform to comedia [10],

which describes the usage of SDP for connection-oriented transport.

When using TLS the SDP m-line for the control pipe MUST conform to

comedia over TLS [11], which specifies the usage of SDP for

establishing a secure connection-oriented transport over TLS.

When the client wants to add a media processing resource to the

session, it issues a SIP re-INVITE transaction.  The SDP offer/answer

exchange carried by this SIP transaction contains one or more

additional control m-lines for the new resources to be allocated to

the session.  The server, on seeing the new m-line, allocates the

resources (if they are available) and responds with a corresponding

control m-line in the SDP answer carried in the SIP response.

The a=setup attribute, as described in comedia [10], MUST be "active"

for the offer from the client and MUST be "passive" for the answer

from the MRCPv2 server.  The a=connection attribute MUST have a value

of "new" on the very first control m-line offer from the client to an

MRCPv2 server.  Subsequent control m-line offers from the client to

the MRCP server MAY contain "new" or "existing", depending on whether

the client wants to set up a new connection or share an existing

connection, respectively.  If the client specifies a value of "new",

the server MUST respond with a value of "new".  If the client

specifies a value of "existing", the server MAY respond with a value

of "existing" if it prefers to share an existing connection or can

answer with a value of "new", in which case the client MUST initiate

a new transport connection.

Shanmugham & Burnett    Expires September 6, 2007              [Page 14]

Internet-Draft                   MRCPv2                       March 2007

When the client wants to de-allocate the resource from this session,

it issues a SIP re-INVITE transaction with the server.  The SDP MUST

offer the control m-line with port 0.  The server MUST then answer

the control m-line with a response of port 0.  This de-allocates the

associated MRCPv2 identifier and resource.  The server MUST NOT close

the TCP, SCTP or TLS connection if it is currently being shared among

multiple MRCP channels.  When all MRCP channels that may be sharing

the connection are released and/or the associated SIP dialog is

terminated, the client or server terminates the connection.

This example exchange adds a resource control channel for a

synthesizer.  Since a synthesizer also generates an audio stream,

this interaction also creates a receive-only RTP media session for

the server to send audio to.

C->S:  INVITE sip:mresources@server.example.com SIP/2.0

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314161 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length: 230

v=0

o=sarvi 2890844526 2890842808 IN IP4 192.168.64.4

s=-

c=IN IP4 10.2.17.12

m=application 9 TCP/MRCPv2 1

a=setup:active

a=connection:new

a=resource:speechsynth

a=cmid:1

m=audio 49170 RTP/AVP 0 96

a=rtpmap:0 pcmu/8000

a=recvonly

a=mid:1

S->C:  SIP/2.0 200 OK

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

Shanmugham & Burnett    Expires September 6, 2007              [Page 15]

Internet-Draft                   MRCPv2                       March 2007

CSeq:314161 INVITE

Contact:<sip:mresources@server.example.com>

Content-Type:application/sdp

Content-Length: 249

v=0

o=- 2890844526 2890842808 IN IP4 192.168.64.4

s=-

c=IN IP4 10.2.17.11

m=application 32416 TCP/MRCPv2 1

a=setup:passive

a=connection:new

a=channel:32AECB234338@speechsynth

a=cmid:1

m=audio 48260 RTP/AVP 00 96

a=rtpmap:0 pcmu/8000

a=sendonly

a=mid:1

C->S:  ACK sip:mresources@server.example.com SIP/2.0

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>;tag=a6c85cf

From:Sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314162 ACK

Content-Length:0

Example: Add Synthesizer Control Channel

This example exchange continues from the previous figure and

allocates an additional resource control channel for a recognizer.

Since a recognizer would need to receive an audio stream for

recognition, this interaction also updates the audio stream to

sendrecv, making it a 2-way RTP media session.

C->S:  INVITE sip:mresources@server.example.com SIP/2.0

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314163 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Shanmugham & Burnett    Expires September 6, 2007              [Page 16]

Internet-Draft                   MRCPv2                       March 2007

Content-Length: 374

v=0

o=sarvi 2890844526 2890842809 IN IP4 192.168.64.4

s=-

c=IN IP4 10.2.17.12

m=application 9 TCP/MRCPv2 1

a=setup:active

a=connection:existing

a=resource:speechsynth

a=cmid:1

m=audio 49170 RTP/AVP 0 96

a=rtpmap:0 pcmu/8000

a=rtpmap:96 telephone-event/8000

a=fmtp:96 0-15

a=sendrecv

a=mid:1

m=application 9 TCP/MRCPv2 1

a=setup:active

a=connection:existing

a=resource:speechrecog

a=cmid:1

S->C:  SIP/2.0 200 OK

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314163 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length:131

v=0

o=sarvi 2890844526 2890842809 IN IP4 192.168.64.4

s=-

c=IN IP4 10.2.17.11

m=application 32416 TCP/MRCPv2 1

a=setup:passive

a=connection:existing

a=channel:32AECB234338@speechsynth

a=cmid:1

m=audio 48260 RTP/AVP 0 96

a=rtpmap:0 pcmu/8000

a=rtpmap:96 telephone-event/8000

a=fmtp:96 0-15

Shanmugham & Burnett    Expires September 6, 2007              [Page 17]

Internet-Draft                   MRCPv2                       March 2007

a=sendrecv

a=mid:1

m=application 32416 TCP/MRCPv2 1

a=setup:passive

a=connection:existing

a=channel:32AECB234338@speechrecog

a=cmid:1

C->S:  ACK sip:mresources@server.example.com SIP/2.0

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>;tag=a6c85cf

From:Sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314164 ACK

Content-Length:0

Add Recognizer example

This example exchange continues from the previous figure and de-

allocates recognizer channel.  Since a recognizer no longer needs to

receive an audio stream, this interaction also updates the RTP media

session to recvonly.

C->S:  INVITE sip:mresources@server.example.com SIP/2.0

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314163 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length: 259

v=0

o=sarvi 2890844526 2890842809 IN IP4 192.168.64.4

s=-

c=IN IP4 10.2.17.12

m=application 9 TCP/MRCPv2 1

a=resource:speechsynth

a=cmid:1

m=audio 49170 RTP/AVP 0 96

a=rtpmap:0 pcmu/8000

a=recvonly

Shanmugham & Burnett    Expires September 6, 2007              [Page 18]

Internet-Draft                   MRCPv2                       March 2007

a=mid:1

m=application 0 TCP/MRCPv2 1

a=resource:speechrecog

a=cmid:1

S->C:  SIP/2.0 200 OK

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314163 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length:131

v=0

o=sarvi 2890844526 2890842809 IN IP4 192.168.64.4

s=-

c=IN IP4 10.2.17.11

m=application 32416 TCP/MRCPv2 1

a=channel:32AECB234338@speechsynth

a=cmid:1

m=audio 48260 RTP/AVP 0 96

a=rtpmap:0 pcmu/8000

a=sendonly

a=mid:1

m=application 0 TCP/MRCPv2 1

a=channel:32AECB234338@speechrecog

a=cmid:1

C->S:  ACK sip:mresources@server.example.com SIP/2.0

Via:SIP/2.0/TCP client.atlanta.example.com:5060;

branch=z9hG4bK74bf9

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>;tag=a6c85cf

From:Sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314164 ACK

Content-Length:0

Deallocate Recognizer example

Shanmugham & Burnett    Expires September 6, 2007              [Page 19]

Internet-Draft                   MRCPv2                       March 2007

4.3.  Media Streams and RTP Ports

Since MRCPv2 resources either generate or consume media streams, the

client or the server needs to associate media sessions with their

corresponding resource or resources.  More than one resource could be

associated with a single media session or each resource could be

assigned a separate media session.  Also note that more that one

media session can be associated with a single resource if need be,

but this scenario is not useful for the current set of resources.

For example, a synthesizer and a recognizer could be associated to

the same media session (m=audio line), if it is opened in "sendrecv"

mode.  Alternatively, the recognizer could have its own "sendonly"

audio session and the synthesizer could have its own "recvonly" audio

session.

The association between control channels and their corresponding

media sessions is established through the "mid" attribute defined in

RFC3388 [12].  If there is more than 1 audio m-line, then each audio

m-line MUST have a "mid" attribute.  Each control m-line MAY have one

or more "cmid" attributes that match the resource control channel to

the "mid" attributes of the audio m-lines it is associated with.

Note that if a control m-line does not have a "cmid" attribute it

will not be associated with any media.  The operations on such a

resource will hence be limited.  For example, if it was a recognizer

resource, the RECOGNIZE method requires an associated media to

process while the INTERPRET method does not.

cmid-attribute = "a=cmid:" identification-tag

identification-tag = token

To allow this flexible mapping of media sessions to MRCPv2 control

channels, a single audio m-line can be associated with multiple

resources or each resource can have its own audio m-line.  For

example, if the client wants to allocate a recognizer and a

synthesizer and associate them with a single 2-way audio pipe, the

SDP offer would contain two control m-lines and a single audio m-line

with an attribute of "sendrecv".  Each of the control m-lines would

have a "cmid" attribute whose value matches the "mid" of the audio

m-line.  If, on the other hand, the client wants to allocate a

recognizer and a synthesizer each with its own separate audio pipe,

the SDP offer would carry two control m-lines (one for the recognizer

and another for the synthesizer) and two audio m-lines (one with the

attribute "sendonly" and another with attribute "recvonly").  The

"cmid" attribute of the recognizer control m-line would match the

"mid" value of the "sendonly" audio m-line and the "cmid" attribute

of the synthesizer control m-line would match the "mid" attribute of

the "recvonly" m-line.

When a server receives media (e.g. audio) on a media session that is

Shanmugham & Burnett    Expires September 6, 2007              [Page 20]

Internet-Draft                   MRCPv2                       March 2007

associated with more than one media processing resource, it is the

responsibility of the server to receive and fork it to the resources

that need to consume it.  If multiple resources in an MRCPv2 session

are generating audio (or other media) to be sent on a single

associated media session, it is the responsibility of the server to

either multiplex the multiple streams onto the single RTP session or

contain an embedded RTP mixer (see RFC3550 [2]) to combine the

multiple streams into one.  In the former case, the media stream will

contain RTP packets generated by different sources, and hence the

packets will have different Synchronization Source identifiers

(SSRCs).  In the latter case, the RTP packets will contain multiple

(CSRCs) corresponding to the original streams before being combined

by the mixer.  An MRCPv2 implementation either MUST correctly process

such RTP sessions, or alternatively MUST avoid associating multiple

resources with a single session.

If a server does not have the capability to mix/multiplex or fork

media, in the latter cases, then the server MUST disallow the client

from associating multiple such resources to a single audio pipe by

rejecting the SDP offer with a SIP 501 "Not Implemented" error.

4.4.  MRCPv2 Message Transport

The MRCPv2 messages defined in this document are transported over a

TCP, TLS or SCTP (in the future) connection between the client and

the server.  The method for setting up this transport connection and

the resource control channel is discussed in Section 4.1 and

Section 4.2.  Multiple resource control channels between a client and

a server that belong to different SIP dialogs can share one or more

TLS, TCP or SCTP connections between them; the server and client MUST

support this mode of operation.  The individual MRCPv2 messages carry

the MRCPv2 channel identifier in their Channel-Identifier header,

which MUST be used to differentiate MRCPv2 messages from different

resource channels (see Section 6.2.1 for details).  All MRCPv2

servers MUST support TLS.  Servers MAY support TCP without TLS in

physically secure environments.  It is up to the client to choose

which mode of transport it wants to use for an MRCPv2 session.

Most examples from here on show only the MRCPv2 messages and do not

show the SIP messages and headers that may have been used to

establish the MRCPv2 control channel.

5.  MRCPv2 Specification

MRCPv2 messages are textual using the ISO 10646 character set in the

UTF-8 encoding (RFC3629 [8]) to allow many different languages to be

represented.  However, to assist in compact representations, MRCPv2

Shanmugham & Burnett    Expires September 6, 2007              [Page 21]

Internet-Draft                   MRCPv2                       March 2007

also allows other character sets such as ISO 8859-1 to be used when

desired.  The MRCPv2 protocol headers (the first line of an MRCP

message) and header names use only the US-ASCII subset of UTF-8.

Internationalization only applies to certain fields like grammar,

results, speech markup etc, and not to MRCPv2 as a whole.

Lines are terminated by CRLF.  Also, some parameters in the message

may contain binary data or a record spanning multiple lines.  Such

fields have a length value associated with the parameter, which

indicates the number of octets immediately following the parameter.

5.1.  Common Protocol Elements

The MRCPv2 message set consists of requests from the client to the

server, responses from the server to the client and asynchronous

events from the server to the client.  All these messages consist of

a start-line, one or more headers, an empty line (i.e. a line with

nothing preceding the CRLF) indicating the end of the header fields,

and an optional message body.

generic-message  =    start-line

message-header

CRLF

[ message-body ]

start-line       =    request-line / response-line / event-line

message-header   =    1*(generic-header / resource-header)

resource-header  =    recognizer-header

/    synthesizer-header

/    recorder-header

/    verifier-header

The message-body contains resource-specific and message-specific data

carried as a MIME entity.  The actual MIME-types used to carry the

data are specified later in the sections defining the individual

messages.

If a message contains a message body, the message MUST contain

content-headers indicating the MIME-type and encoding of the data in

the message body.

Request, response and event messages include the version of MRCP that

the message conforms to.  Version compatibility rules follow [H3.1]

regarding version ordering, compliance requirements, and upgrading of

version numbers.  The version information is indicated by "MRCP" (as

Shanmugham & Burnett    Expires September 6, 2007              [Page 22]

Internet-Draft                   MRCPv2                       March 2007

opposed to "HTTP in [H3.1]) or "MRCP/2.0" ( as opposed to HTTP/1.1 in

[H3.1]).  To be compliant with this specification, clients and

servers sending MRCPv2 messages MUST indicate an mrcp-version of

"MRCP/2.0".

mrcp-version   =    "MRCP" "/" 1*DIGIT "." 1*DIGIT

The message-length field specifies the length of the message,

including the start-line, and MUST be the 2nd token from the

beginning of the message.  This is to make the framing and parsing of

the message simpler to do.  This field specifies the length of the

message including data that may be encoded into the body of the

message.  Note that this value MAY be printed as a fixed-length

integer that is zero-padded in front in order to eliminate or reduce

inefficiency in cases where the message-length value would change as

a result of the length of the message-length token itself.

message-length =    1*DIGIT

All MRCPv2 messages, responses and events MUST carry the Channel-

Identifier header so the server or client can differentiate messages

from different control channels that may share the same transport

connection.

5.2.  Request

An MRCPv2 request consists of a Request line followed by message

headers and an optional message body containing data specific to the

request message.

The Request message from a client to the server includes within the

first line the method to be applied, a method tag for that request

and the version of the protocol in use.

request-line   =    mrcp-version SP message-length SP method-name

SP request-id CRLF

The request-id field is a unique identifier representable as an

unsigned 32 bit integer created by the client and sent to the server.

Consecutive requests within an MRCP session MUST utilize

monotonically increasing request-id's.  The request-id space is

linear, (i.e. not mod(32)) so the space does not wrap and validity

can be checked with a simple unsigned comparison operation.  The

client may choose any initial value for its first request, but a

small integer is RECOMMENDED to avoid exhausting the space in long

sessions.  If the server receives duplicate or out-of-order requests

the server MUST reject the request with a response code of 410.

Shanmugham & Burnett    Expires September 6, 2007              [Page 23]

Internet-Draft                   MRCPv2                       March 2007

The server resource MUST use the client-assigned identifier in its

response to the request.  If the request does not complete

synchronously, future asynchronous events associated with this

request MUST carry the client-assigned request-id.

The mrcp-version field is the MRCP protocol version that is being

used by the client.

The message-length field specifies the length of the message,

including the start-line.

request-id     =    1*DIGIT

The method-name field identifies the specific request that the client

is making to the server.  Each resource supports a subset of the

MRCPv2 methods.  The subset for each resource is defined in the

section of the specification for the corresponding resource.

method-name    =    generic-method

/    synthesizer-method

/    recorder-method

/    recognizer-method

/    verifier-method

5.3.  Response

After receiving and interpreting the request message for a method,

the server resource responds with an MRCPv2 response message.  The

response consists of a response line followed by message headers and

an optional message body containing data specific to the method.

response-line  =    mrcp-version SP message-length SP request-id

SP status-code SP request-state CRLF

The mrcp-version field MUST contain the version of the MRCPv2

protocol running on the server.

The message-length field specifies the length of the message,

including the start-line.

The request-id used in the response MUST match the one sent in the

corresponding request message.

The status-code field is a 3-digit code representing the success or

failure or other status of the request.

The request-state field indicates if the action initiated by the

Request is PENDING, IN-PROGRESS or COMPLETE.  The COMPLETE status

Shanmugham & Burnett    Expires September 6, 2007              [Page 24]

Internet-Draft                   MRCPv2                       March 2007

means that the Request was processed to completion and that there

will be no more events or other messages from that resource to the

client with that request-id.  The PENDING status means that the

request has been placed on a queue and will be processed in first-in-

first-out order.  The IN-PROGRESS status means that the request is

being processed and is not yet complete.  A PENDING or IN-PROGRESS

status indicates that further Event messages may be delivered with

that request-id.

request-state    =  "COMPLETE"

/  "IN-PROGRESS"

/  "PENDING"

5.4.  Status Codes

The status codes are classified under the Success (2XX) codes, Client

Failure (4XX) codes, and Server Failure (5XX).

Success Codes

+------------+--------------------------------------------+

| Code       | Meaning                                    |

+------------+--------------------------------------------+

| 200        | Success                                    |

| 201        | Success with some optional headers ignored |

+------------+--------------------------------------------+

Success 2xx

Client Failure 4xx Codes

+------------+------------------------------------------------------+

| Code       | Meaning                                              |

+------------+------------------------------------------------------+

| 401        | Method not allowed                                   |

| 402        | Method not valid in this state                       |

| 403        | Unsupported Header                                   |

| 404        | Illegal Value for Header.  This is the error for a   |

|            | syntax violation.                                    |

| 405        | Resource not allocated for this session or does not  |

|            | exist                                                |

| 406        | Mandatory Header Missing                             |

| 407        | Method or Operation Failed (e.g., Grammar            |

|            | compilation failed in the recognizer.  Detailed      |

|            | cause codes MAY BE available through a resource      |

|            | specific header.)                                    |

| 408        | Unrecognized or unsupported message entity           |

Shanmugham & Burnett    Expires September 6, 2007              [Page 25]

Internet-Draft                   MRCPv2                       March 2007

| 409        | Unsupported Header Value.  This is a value that is   |

|            | syntactically legal but exceeds the implementation's |

|            | capabilities or expectations.                        |

| 410        | Non-Monotonic or Out of order sequence number in     |

|            | request.                                             |

| 411-420    | Reserved                                             |

+------------+------------------------------------------------------+

Client Failure 4xx

Server Failure 5xx Codes

+------------+------------------------------------------------------+

| Code       | Meaning                                              |

+------------+------------------------------------------------------+

| 501        | Server Internal Error                                |

| 502        | Protocol Version not supported                       |

| 503        | Proxy Timeout.  The MRCP Proxy did not receive a     |

|            | response from the MRCP server.                       |

| 504        | Message too large                                    |

+------------+------------------------------------------------------+

Server Failure 4xx

5.5.  Events

The server resource may need to communicate a change in state or the

occurrence of a certain event to the client.  These messages are used

when a request does not complete immediately and the response returns

a status of PENDING or IN-PROGRESS.  The intermediate results and

events of the request are indicated to the client through the event

message from the server.  The event message consists of an event

header line followed by message headers and an optional message body

containing data specific to the event message.  The header line has

the request-id of the corresponding request and status value.  The

status value is COMPLETE if the request is done and this was the last

event, else it is IN-PROGRESS.

event-line       =  mrcp-version SP message-length SP event-name

SP request-id SP request-state CRLF

The mrcp-version used here is identical to the one used in the

Request/Response Line and indicates the version of the MRCPv2

protocol running on the server.

The message-length field specifies the length of the message,

including the start-line

Shanmugham & Burnett    Expires September 6, 2007              [Page 26]

Internet-Draft                   MRCPv2                       March 2007

The request-id used in the event MUST match the one sent in the

request that caused this event.

The request-state indicates whether the Request/Command causing this

event is complete or still in progress, and is the same as the one

mentioned in Section 5.3.  The final event for a request has a

COMPLETE status indicating the completion of the request.

The event-name identifies the nature of the event generated by the

media resource.  The set of valid event names depends on the resource

generating it.  See the corresponding resource-specific section of

the document.

event-name       =  synthesizer-event

/  recognizer-event

/  recorder-event

/  verifier-event

6.  MRCPv2 Generic Methods, Headers, and Result Structure

MRCPv2 supports a set of methods and headers that are common to all

resources.  These are discussed here; resource-specific methods and

headers are discussed in the corresponding resource-specific section

of the document.

6.1.  Generic Methods

MRCPv2 supports two generic methods for reading and writing the state

associated with a resource.

generic-method      =    "SET-PARAMS"

/    "GET-PARAMS"

These are described in the following sub-sections.

6.1.1.  SET-PARAMS

The "SET-PARAMS" method, from the client to the server, tells the

MRCPv2 resource to define parameters for the session, such as voice

characteristics and prosody on synthesizers, recognition timers on

recognizers, etc.  If the server accepts and sets all parameters it

MUST return a Response-Status of 200.  If it chooses to ignore some

optional headers that can be safely ignored without affecting

operation of the server it MUST return 201.

If one or more of the headers being sent is incorrect, error 403,

404, or 409 MUST be returned as follows:

Shanmugham & Burnett    Expires September 6, 2007              [Page 27]

Internet-Draft                   MRCPv2                       March 2007

o  If one or more of the headers being set has an illegal value, the

server MUST reject the request with a 404 Illegal Value for

Header.

o  If one or more of the headers being set is unsupported for the

resource, the server MUST reject the request with a 403

Unsupported Header, except as described in the next paragraph.

o  If one or more of the headers being set has an unsupported value,

the server MUST reject the request with a 409 Unsupported Header

Value, except as described in the next paragraph.

If both error 404 and another error have occurred, only error 404

MUST be returned.  If both errors 403 and 409 have occurred, but not

error 404, only error 403 MUST be returned.

If error 403, 404, or 409 is returned, the response MUST include the

bad or unsupported headers and their values exactly as they were sent

from the client.  Session parameters modified using "SET-PARAMS" do

not override parameters explicitly specified on individual requests

or requests that are in-PROGRESS.

C->S:  MRCP/2.0 124 SET-PARAMS 543256

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:female

Voice-variant:3

S->C:  MRCP/2.0 47 543256 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

6.1.2.  GET-PARAMS

The "GET-PARAMS" method, from the client to the server, asks the

MRCPv2 resource for its current session parameters, such as voice

characteristics and prosody on synthesizers, recognition-timer on

recognizers, etc.  For every empty header field the client sends in

the request, the server MUST include the corresponding headers and

their values in the response.  If no parameter headers are specified

by the client then the server MUST return all the settable parameters

and their values in the corresponding headers of the response,

including vendor-specific parameters.  Such wild-card parameter

requests can be very processing-intensive, since the number of

settable parameters can be large depending on the implementation.

Hence, it is RECOMMENDED that the client not use the wildcard

"GET-PARAMS" operation very often.  Note that "GET-PARAMS" returns

header values that apply to the whole session and not values that

have a request level scope.

If all of the headers requested are supported, the server MUST return

a Response-Status of 200.  If some of the headers being retrieved are

Shanmugham & Burnett    Expires September 6, 2007              [Page 28]

Internet-Draft                   MRCPv2                       March 2007

unsupported for the resource, the server MUST reject the request with

a 403 Unsupported Header.  Such a response MUST include the (empty)

unsupported headers exactly as they were sent from the client.

C->S:   MRCP/2.0 136 GET-PARAMS 543256

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:

Voice-variant:

Vendor-Specific-Parameters:com.mycorp.param1;

com.mycorp.param2

S->C:   MRCP/2.0 163 543256 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:female

Voice-variant:3

Vendor-Specific-Parameters:com.mycorp.param1="Company Name";

com.example.param2="124324234@example.com"

6.2.  Generic Message Headers

All MRCPv2 headers, which include both the generic-headers defined in

the following sub-sections and the resource-specific headers defined

later, follow the same generic format as that given in Section 3.1 of

RFC2822 [13].  Each header consists of a name followed by a colon

(":") and the value.  Header names are case-insensitive.  The value

MAY be preceded by any amount of LWS, though a single SP is

preferred.  Headers may extend over multiple lines by preceding each

extra line with at least one SP or HT.

message-header = field-name ":" [ field-value ]

field-name     = token

field-value    = *LWS field-content *( CRLF 1*LWS field-content)

field-content  = <the OCTETs making up the field-value

and consisting of either *TEXT or combinations

of token, separators, and quoted-string>

The field-content does not include any leading or trailing LWS (i.e.

linear white space occurring before the first non-whitespace

character of the field-value or after the last non-whitespace

character of the field-value).  Such leading or trailing LWS MAY be

removed without changing the semantics of the field value.  Any LWS

that occurs between field-content MAY be replaced with a single SP

before interpreting the field value or forwarding the message

downstream.

MRCPv2 servers and clients MUST NOT depend on header order.  It is

"good practice" to send general-header fields first, followed by

request-header or response-header fields, and ending with the entity-

Shanmugham & Burnett    Expires September 6, 2007              [Page 29]

Internet-Draft                   MRCPv2                       March 2007

header fields.  However, MRCPv2 servers and clients MUST be prepared

to process the headers in any order.  The only exception to this rule

is when there are multiple headers with the same header name in a

message.

Multiple headers with the same name MAY be present in a message if

and only if the entire value for that header is defined as a comma-

separated list [i.e., #(values)].

It MUST be possible to combine the multiple headers of the same name

into one "header:value" pair without changing the semantics of the

message, by appending each subsequent value to the first, each

separated by a comma.  The order in which headers with the same name

are received is therefore significant to the interpretation of the

combined header value, and thus an intermediary MUST NOT change the

order of these values when a message is forwarded.

generic-header      =    channel-identifier

/    accept

/    active-request-id-list

/    proxy-sync-id

/    accept-charset

/    content-type

/    content-id

/    content-base

/    content-encoding

/    content-location

/    content-length

/    fetch-timeout

/    cache-control

/    logging-tag

/    set-cookie

/    set-cookie2

/    vendor-specific

6.2.1.  Channel-Identifier

All MRCPv2 requests, responses and events MUST contain the Channel-

Identifier header.  The value is allocated by the server when a

control channel is added to the session and communicated to the

client by the "a=channel" attribute in the SDP answer from the

server.  The header value consists of 2 parts separated by the '@'

symbol.  The first part is an unambiguous string identifying the

MRCPv2 session.  The second part is a string token which specifies

one of the media processing resource types listed in Section 3.1.

The unambiguous string (first part) MUST BE unique among the resource

instances managed by the server and is common to all resource

channels with that server established through a single SIP dialog.

Shanmugham & Burnett    Expires September 6, 2007              [Page 30]

Internet-Draft                   MRCPv2                       March 2007

channel-identifier  = "Channel-Identifier" ":" channel-id CRLF

channel-id          = 1*VCHAR "@" 1*VCHAR

6.2.2.  Accept

The Accept header field follows the syntax defined in [H14.1].  The

semantics are also identical, with the exception that if no Accept

header field is present, the server MUST assume a default value that

is specific to the resource type that is being controlled.  This

default value can be changed for a resource on a session by sending

this header in a SET-PARAMS method.  The current default value of

this header for a resource in a session can be set by found through a

GET-PARAMS method.

6.2.3.  Active-Request-Id-List

In a request, this header indicates the list of request-ids to which

the request applies.  This is useful when there are multiple requests

that are PENDING or IN-PROGRESS and the client wants this request to

apply to one or more of these specifically.

In a response, this header returns the list of request-ids that the

method modified or affected.  There could be one or more requests in

a request-state of PENDING or IN-PROGRESS.  When a method affecting

one or more PENDING or IN-PROGRESS requests is sent from the client

to the server, the response MUST contain the list of request-ids that

were affected or modified by this command in its header.

The active-request-id-list is only used in requests and responses,

not in events.

For example, if a "STOP" request with no active-request-id-list is

sent to a synthesizer resource which has one or more "SPEAK" requests

in the PENDING or IN-PROGRESS state, all "SPEAK" requests MUST be

cancelled, including the one IN-PROGRESS.  The response to the "STOP"

request contains in the active-request-id-list the request-ids of all

the "SPEAK" requests that were terminated.  After sending the STOP

response, the server MUST NOT send any SPEAK-COMPLETE or RECOGNITION-

COMPLETE events for the terminated requests.

active-request-id-list  =  "Active-Request-Id-List" ":"

request-id *("," request-id) CRLF

Shanmugham & Burnett    Expires September 6, 2007              [Page 31]

Internet-Draft                   MRCPv2                       March 2007

6.2.4.  Proxy-Sync-Id

When any server resource generates a barge-in-able event, it also

generates a unique tag.  The tag is sent as this header's value in an

event to the client.  The client then acts as a intermediary among

the server resources and sends a BARGE-IN-OCCURRED method to the

synthesizer server resource with the Proxy-Sync-Id it received from

the server resource.  When the recognizer and synthesizer resources

are part of the same session, they may choose to work together to

achieve quicker interaction and response.  Here the proxy-sync-id

helps the resource receiving the event, intermediated by the client,

to decide if this event has been processed through a direct

interaction of the resources.

proxy-sync-id    =  "Proxy-Sync-Id" ":" 1*VCHAR CRLF

6.2.5.  Accept-Charset

See [H14.2].  This specifies the acceptable character set for

entities returned in the response or events associated with this

request.  This is useful in specifying the character set to use in

the NLSML results of a "RECOGNITION-COMPLETE" event.

6.2.6.  Content-Type

See [H14.17].  MRCPv2 supports a restricted set of MIME registered

content types, including speech markup, grammar, and recognition

results.  The content types applicable to each MRCPv2 resource-type

are specified in the corresponding section of the document.  The

multi-part content type "multi-part/mixed" is supported to

communicate multiple of the above mentioned contents, in which case

the body parts MUST NOT contain any MRCPv2 specific headers.

6.2.7.  Content-ID

This header contains an ID or name for the content by which it can be

referenced.  This header operates according to the specification in

RFC2392 [14] and is required for content disambiguation in multi-part

messages.  In MRCPv2 whenever the associated content is stored, by

either the client or the server, it MUST be retrievable using this

ID.  Such content can be referenced later in a session by addressing

it with the ""session:"" URI scheme described in Section 13.6.

6.2.8.  Content-Base

The content-base entity-header may be used to specify the base URI

for resolving relative URLs within the entity.

Shanmugham & Burnett    Expires September 6, 2007              [Page 32]

Internet-Draft                   MRCPv2                       March 2007

content-base      = "Content-Base" ":" absoluteURI CRLF

Note, however, that the base URI of the contents within the entity-

body may be redefined within that entity-body.  An example of this

would be a multi-part MIME entity, which in turn can have multiple

entities within it.

6.2.9.  Content-Encoding

The content-encoding entity-header is used as a modifier to the

media-type.  When present, its value indicates what additional

content encoding has been applied to the entity-body, and thus what

decoding mechanisms must be applied in order to obtain the media-type

referenced by the content-type header.  Content-encoding is primarily

used to allow a document to be compressed without losing the identity

of its underlying media type.

content-encoding  = "Content-Encoding" ":"

*WSP content-coding

*(*WSP "," *WSP content-coding *WSP )

CRLF

Content-coding is defined in [H3.5].  An example of its use is

Content-Encoding:gzip

If multiple encodings have been applied to an entity, the content

encodings MUST be listed in the order in which they were applied.

6.2.10.  Content-Location

The content-location entity-header MAY be used to supply the resource

location for the entity enclosed in the message when that entity is

accessible from a location separate from the requested resource's

URI.  Refer to [H14.14].

content-location  =  "Content-Location" ":"

( absoluteURI / relativeURI ) CRLF

The content-location value is a statement of the location of the

resource corresponding to this particular entity at the time of the

request.  This header is provided for optimization purposes only.

The receiver of this header MAY assume that the entity being sent is

identical to what would have been retrieved or might already have

been retrieved from the content-location URI.

For example, if the client provided a grammar markup inline, and it

Shanmugham & Burnett    Expires September 6, 2007              [Page 33]

Internet-Draft                   MRCPv2                       March 2007

had previously retrieved it from a certain URI, that URI can be

provided as part of the entity, using the content-location header.

This allows a resource like the recognizer to look into its cache to

see if this grammar was previously retrieved, compiled and cached.

In this case, it might optimize by using the previously compiled

grammar object.

If the content-location is a relative URI, the relative URI is

interpreted relative to the content-base URI.

6.2.11.  Content-Length

This header contains the length of the content of the message body

(i.e. after the double CRLF following the last header field).  Unlike

HTTP, it MUST be included in all messages that carry content beyond

the header portion of the message.  If it is missing, a default value

of zero is assumed.  Otherwise, it is interpreted according to

[H14.13].  When a message having no use for a message body contains

one, i.e. the Content-Length is non-zero, the receiver MAY ignore the

content of the message body.

6.2.12.  Fetch Timeout

When the recognizer or synthesizer needs to fetch documents or other

resources this header controls the corresponding URI access

properties.  This defines the timeout for content that the server may

need to fetch over the network.  The value is interpreted to be in

milliseconds and ranges from 0 to an implementation-specific maximum

value.  The default value for this header is implementation-specific.

This header MAY occur in "DEFINE-GRAMMAR", "RECOGNIZE", "SPEAK",

"SET-PARAMS" or "GET-PARAMS".

fetch-timeout       =   "Fetch-Timeout" ":" 1*DIGIT CRLF

6.2.13.  Cache-Control

If the server implements content caching, it MUST adhere to the cache

correctness rules of HTTP 1.1 [6] when accessing and caching stored

content.  In particular, the "expires" and "cache-control" headers of

the cached URI or document MUST be honored and take precedence over

the Cache-Control defaults set by this header.  The cache-control

directives are used to define the default caching algorithms on the

server for the session or request.  The scope of the directive is

based on the method it is sent on.  If the directives are sent on a

"SET-PARAMS" method, it applies for all requests for external

documents the server makes during that session, unless overridden by

a cache-control header on an individual request.  If the directives

are sent on any other requests they apply only to external document

Shanmugham & Burnett    Expires September 6, 2007              [Page 34]

Internet-Draft                   MRCPv2                       March 2007

requests the server makes for that request.  An empty cache-control

header on the "GET-PARAMS" method is a request for the server to

return the current cache-control directives setting on the server.

cache-control       = "Cache-Control" ":" cache-directive

*("," *LWS cache-directive) CRLF

cache-directive     = "max-age" "=" delta-seconds

/ "max-stale" [ "=" delta-seconds ]

/ "min-fresh" "=" delta-seconds

delta-seconds       = 1*DIGIT

Here delta-seconds is a decimal time value specifying the number of

seconds since the instant the message response or data was received

by the server.

The cache-directives allow the client to ask the server to override

the default cache expiration mechanisms.

max-age        Indicates that the client can tolerate the server

using content whose age is no greater than the

specified time in seconds.  Unless a max-stale

directive is also included, the client is not willing

to accept a response based on stale data.

min-fresh      Indicates that the client is willing to accept a

server response with cached data whose expiration is

no less than its current age plus the specified time

in seconds.  If the server's cache time to live

exceeds the client-supplied min-fresh value, the

server MUST NOT utilize cached content.

max-stale      Indicates that the client is willing to allow a server

to utilize cached data that has exceeded its

expiration time.  If max-stale is assigned a value,

then the client is willing to allow the server to use

cached data that has exceeded its expiration time by

no more than the specified number of seconds.  If no

value is assigned to max-stale, then the client is

willing to allow the server to use stale data of any

age.

The server cache MAY be requested to use stale response/data without

validation, but only if this does not conflict with any "MUST"-level

requirements concerning cache validation (e.g., a "must-revalidate"

cache-control directive in the HTTP 1.1 specification pertaining to

the corresponding URI).

If both the MRCPv2 cache-control directive and the cached entry on

Shanmugham & Burnett    Expires September 6, 2007              [Page 35]

Internet-Draft                   MRCPv2                       March 2007

the server include "max-age" directives, then the lesser of the two

values is used for determining the freshness of the cached entry for

that request.

6.2.14.  Logging-Tag

This header MAY be sent as part of a "SET-PARAMS"/"GET-PARAMS" method

to set or retrieve the logging tag for logs generated by the server.

Once set, the value persists until a new value is set or the session

ends.  The MRCPv2 server MAY provide a mechanism to subset its output

logs so that system administrators can examine or extract only the

log file portion during which the logging tag was set to a certain

value.

It is RECOMMENDED that clients have some identifying information in

the logging tag, so that one can determine which client request

generated a given log message at the server.

logging-tag    = "Logging-Tag" ":" 1*UTFCHAR CRLF

6.2.15.  Set-Cookie and Set-Cookie2

Since the associated HTTP client on an MRCPv2 server fetches

documents for processing on behalf of the MRCPv2 client, the cookie

store in the HTTP client of the MRCPv2 server is treated as an

extension of the cookie store in the HTTP client of the MRCPv2

client.  This requires that the MRCPv2 client and server be able to

synchronize their common cookie store as needed.  To enable the

MRCPv2 client to push its stored cookies to the MRCPv2 server and get

new cookies from the MRCPv2 server stored back to the MRCPv2 client,

the set-cookie and set-cookie2 entity-header fields MAY be included

in MRCPv2 requests to update the cookie store on a server and be

returned in final MRCPv2 responses or events to subsequently update

the client's own cookie store.  The stored cookies on the server

persist for the duration of the MRCPv2 session and MUST be destroyed

at the end of the session.  To ensure support for the type of cookie

header dictated by the HTTP origin server, MRCPv2 clients and servers

MUST support both the set-cookie and set-cookie2 entity header

fields.

Shanmugham & Burnett    Expires September 6, 2007              [Page 36]

Internet-Draft                   MRCPv2                       March 2007

set-cookie      =       "Set-Cookie:" cookies CRLF

cookies         =       cookie *("," *LWS cookie)

cookie          =       attribute "=" value *(";" cookie-av)

cookie-av       =       "Comment" "=" value

/       "Domain" "=" value

/       "Max-Age" "=" value

/       "Path" "=" value

/       "Secure"

/       "Version" "=" 1*DIGIT

/       "Age" "=" delta-seconds

set-cookie2     =       "Set-Cookie2:" cookies2 CRLF

cookies2        =       cookie2 *("," *LWS cookie2)

cookie2         =       attribute "=" value *(";" cookie-av2)

cookie-av2      =       "Comment" "=" value

/       "CommentURL" "=" <"> http_URL <">

/       "Discard"

/       "Domain" "=" value

/       "Max-Age" "=" value

/       "Path" "=" value

/       "Port" [ "=" <"> portlist <"> ]

/       "Secure"

/       "Version" "=" 1*DIGIT

/       "Age" "=" delta-seconds

portlist        =       portnum *("," *LWS portnum)

portnum         =       1*DIGIT

The set-cookie and set-cookie2 headers are specified in RFC2109 [15]

and RFC2965 [16], respectively.  The "Age" attribute is introduced in

this specification to indicate the age of the cookie and is optional.

An MRCPv2 client or server MUST calculate the age of the cookie

according to the age calculation rules in the HTTP/1.1 specification

[6] and append the "Age" attribute accordingly.

The MRCPv2 client or server MUST supply defaults for the Domain and

Path attributes if omitted by the HTTP origin server as specified in

RFC2109 (set-cookie) and RFC2965 (set-cookie2).  Note that there is

no leading dot present in the Domain attribute value in this case.

Although an explicitly specified Domain value received via the HTTP

protocol may be modified to include a leading dot, an MRCPv2 client

or server MUST NOT modify the Domain value when received via the

MRCPv2 protocol.

An MRCPv2 client or server MAY combine multiple cookie headers of the

same type into a single "field-name:field-value" pair as described in

Section 6.2.

The set-cookie and set-cookie2 headers MAY be specified in any

Shanmugham & Burnett    Expires September 6, 2007              [Page 37]

Internet-Draft                   MRCPv2                       March 2007

request that subsequently results in the server performing an HTTP

access.  When a server receives new cookie information from an HTTP

origin server, and assuming the cookie store is modified according to

RFC2109 or RFC2965, the server MUST return the new cookie information

in the MRCPv2 COMPLETE response or event as appropriate to allow the

client to update its own cookie store.

The "SET-PARAMS" request MAY specify the set-cookie and set-cookie2

headers to update the cookie store on a server.  The GET-PARAMS

request MAY be used to return the entire cookie store of "Set-Cookie"

or "Set-Cookie2" type cookies to the client.

6.2.16.  Vendor Specific Parameters

This set of headers allows for the client to set or retrieve Vendor

Specific parameters.

vendor-specific          =    "Vendor-Specific-Parameters" ":"

vendor-specific-av-pair

*[";" vendor-specific-av-pair] CRLF

vendor-specific-av-pair  = vendor-av-pair-name "="

value

Headers of this form MAY be sent in any method and are used to manage

implementation-specific parameters on the server side.  The vendor-

av-pair-name follows the reverse Internet Domain Name convention (see

Section 13.1.6 for syntax and registration information).  The value

of the vendor attribute is specified after the "=" symbol and MAY be

quoted.  For example:

com.example.companyA.paramxyz=256

com.example.companyA.paramabc=High

com.example.companyB.paramxyz=Low

When used in GET-PARAMS to get the current value of these parameters

from the server, this header value may contain a semicolon-separated

list of implementation-specific attribute names.

6.3.  Generic Result Structure

Result data from the server for the Recognizer and Verification

resources is carried as a MIME entity in the MRCPv2 message body of

various events.  The Natural Language Semantics Markup Language

(NLSML), an XML markup based on an early draft from the W3C, is the

default standard for returning results back to the client.  Hence,

Shanmugham & Burnett    Expires September 6, 2007              [Page 38]

Internet-Draft                   MRCPv2                       March 2007

all servers implementing these resource types MUST support the MIME-

type application/nlsml+xml.  When the Extensible MultiModal

Annotation [33] being developed at the W3C has reached a stable

standards state, it can be used to return results as well.  This can

be done by negotiating the format at session establishment time with

SDP (a=resultformat:application/emma-xml) or with SIP (Allow/Accept).

With SIP, for example, if a client wants results in EMMA, an MRCPv2

proxy can route the request to a server that supports EMMA by

inspecting the SIP headers, rather than having to introspect in to

the SDP.

MRCPv2 uses this representation to convey content among the clients

and servers that generate and make use of the markup.  MRCPv2 uses

NSLML specifically to convey recognition, enrollment, and

verification results between the corresponding resource on the MRCPv2

server and the MRCPv2 client.  Details of this result format are

fully described in Section 6.3.1.

Content-Type:application/nlsml+xml

Content-Length:104

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="http://theYesNoGrammar">

<interpretation>

<instance>

<ex:response>yes</ex:response>

</instance>

<input>ok</input>

</interpretation>

</result>

Result Example

6.3.1.  Natural Language Semantics Markup Language

The Natural Language Semantics Markup Language (NLSML) is an XML data

structure with elements and attributes designed to carry result

information from recognizer (including enrollment) and verfication

resources.  The normative definition of NLSML is the RelaxNG schema

in Section 16.1.  Note that the elements and attributes of this

format are defined in the MRCPv2 namespace.  In the result structure,

they must either be prefixed by a namespace prefix declared within

the result or must be children of an element identified as belonging

to the respective namespace.  For details on how to use XML

Namespaces, see [27].  Section 2 of [27] provides details on how to

declare namespaces and namespace prefixes.

Shanmugham & Burnett    Expires September 6, 2007              [Page 39]

Internet-Draft                   MRCPv2                       March 2007

The root element of NLSML is <result>.  Optional child elements are

<interpretation>, <enrollment-result>, and <verification-result>, at

least one of which must be present.  A single <result> may contain

all of the optional child elements.  Details of the <result> and

<interpretation> elements and their subelements and attributes can be

found in Section 9.6.  Details of the <enrollment-result> element and

its subelements can be found in Section 9.7.  Details of the

<veriifcation-result> element and its subelements can be found in

Section 11.5.2.

7.  Resource Discovery

Server resources may be discovered and their capabilities learned by

clients through standard SIP machinery.  The client can issue a SIP

OPTIONS transaction to a server, which has the effect of requesting

the capabilities of the server.  The server MUST respond to such a

request with an SDP-encoded description of its capabilities according

to RFC3264 [7].  The MRCPv2 capabilities are described by a single

m-line containing the media type "application" and transport type

"TCP/TLS/MRCPv2" or "TCP/MRCPv2".  There MUST be one "resource"

attribute for each media resource that the server supports with the

resource type identifier as its value.

The SDP description MUST also contain m-lines describing the audio

capabilities and the coders the server supports.

Shanmugham & Burnett    Expires September 6, 2007              [Page 40]

Internet-Draft                   MRCPv2                       March 2007

In this example, the client uses the SIP OPTIONS method to query the

capabilities of the MRCPv2 server.

C->S:

OPTIONS sip:mrcp@server.example.com SIP/2.0

Max-Forwards:6

To:<sip:mrcp@server.example.com>

From:Sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:63104 OPTIONS

Contact:<sip:sarvi@example.com>

Accept:application/sdp

Content-Length:0

S->C:

SIP/2.0 200 OK

To:<sip:mrcp@server.example.com>;tag=93810874

From:Sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:63104 OPTIONS

Contact:<sip:mrcp@server.example.com>

Allow:INVITE, ACK, CANCEL, OPTIONS, BYE

Accept:application/sdp

Accept-Encoding:gzip

Accept-Language:en

Supported:foo

Content-Type:application/sdp

Content-Length:274

v=0

o=sarvi 2890844526 2890842807 IN IP4 192.168.64.4

s=SDP Seminar

i=A session for processing media

c=IN IP4 10.2.17.12/127

m=application 0 TCP/MRCPv2 1

a=resource:speechsynth

a=resource:speechrecog

a=resource:speakverify

m=audio 0 RTP/AVP 0 1 3

a=rtpmap:0 PCMU/8000

a=rtpmap:1 1016/8000

a=rtpmap:3 GSM/8000

Example of using SIP OPTIONS for MRCPv2 Server Capability Discovery

Shanmugham & Burnett    Expires September 6, 2007              [Page 41]

Internet-Draft                   MRCPv2                       March 2007

8.  Speech Synthesizer Resource

This resource processes text markup provided by the client and

generates a stream of synthesized speech in real-time.  Depending

upon the server implementation and capability of this resource, the

client can also dictate parameters of the synthesized speech such as

voice characteristics, speaker speed, etc.

The synthesizer resource is controlled by MRCPv2 requests from the

client.  Similarly, the resource can respond to these requests or

generate asynchronous events to the client to indicate conditions of

interest to the client during the generation of the synthesized

speech stream.

This section applies for the following resource types:

speechsynth

basicsynth

The capabilities of these resources are defined in Section 3.1.

8.1.  Synthesizer State Machine

The synthesizer maintains a state machine to process MRCPv2 requests

from the client.  The state transitions shown below describe the

states of the synthesizer and reflect the state of the request at the

head of the synthesizer resource queue.  A "SPEAK" request in the

PENDING state can be deleted or stopped by a "STOP" request without

affecting the state of the resource.

Shanmugham & Burnett    Expires September 6, 2007              [Page 42]

Internet-Draft                   MRCPv2                       March 2007

Idle                    Speaking                  Paused

State                   State                     State

|                        |                          |

|----------SPEAK-------->|                 |--------|

|<------STOP-------------|             CONTROL      |

|<----SPEAK-COMPLETE-----|                 |------->|

|<----BARGE-IN-OCCURRED--|                          |

|              |---------|                          |

|          CONTROL       |-----------PAUSE--------->|

|              |-------->|<----------RESUME---------|

|                        |               |----------|

|----------|             |              PAUSE       |

|    BARGE-IN-OCCURRED   |               |--------->|

|<---------|             |----------|               |

|                        |      SPEECH-MARKER       |

|                        |<---------|               |

|----------|             |----------|               |

|         STOP           |       RESUME             |

|          |             |<---------|               |

|<---------|             |                          |

|<---------------------STOP-------------------------|

|----------|             |                          |

|     DEFINE-LEXICON     |                          |

|          |             |                          |

|<---------|             |                          |

|<---------------BARGE-IN-OCCURRED------------------|

Synthesizer State Machine

8.2.  Synthesizer Methods

The synthesizer supports the following methods.

synthesizer-method   =  "SPEAK"

/  "STOP"

/  "PAUSE"

/  "RESUME"

/  "BARGE-IN-OCCURRED"

/  "CONTROL"

/  "DEFINE-LEXICON"

8.3.  Synthesizer Events

The synthesizer may generate the following events.

synthesizer-event    =  "SPEECH-MARKER"

/  "SPEAK-COMPLETE"

Shanmugham & Burnett    Expires September 6, 2007              [Page 43]

Internet-Draft                   MRCPv2                       March 2007

8.4.  Synthesizer Header Fields

A synthesizer method may contain headers containing request options

and information to augment the Request, Response or Event it is

associated with.

synthesizer-header  =  jump-size

/  kill-on-barge-in

/  speaker-profile

/  completion-cause

/  completion-reason

/  voice-parameter

/  prosody-parameter

/  speech-marker

/  speech-language

/  fetch-hint

/  audio-fetch-hint

/  failed-uri

/  failed-uri-cause

/  speak-restart

/  speak-length

/  load-lexicon

/  lexicon-search-order

8.4.1.  Jump-Size

This header MAY be specified in a CONTROL method and controls the

amount to jump forward or backward in an active "SPEAK" request.  A +

or - indicates a relative value to what is being currently played.

This header MAY also be specified in a "SPEAK" request as a desired

offset into the synthesized speech.  In this case, the synthesizer

MUST begin speaking from this amount of time into the speech markup.

Note that an offset that extends beyond the end of the produced

speech will result in audio of length zero.  The different speech

length units supported are dependent on the synthesizer

implementation.  If the synthesizer resource does not support a unit

or the operation, the resource MUST respond with a status code of 409

"Unsupported Header Value".

Shanmugham & Burnett    Expires September 6, 2007              [Page 44]

Internet-Draft                   MRCPv2                       March 2007

jump-size             =   "Jump-Size" ":" speech-length-value CRLF

speech-length-value   =   numeric-speech-length

/   text-speech-length

text-speech-length    =   1*UTFCHAR SP "Tag"

numeric-speech-length =    ("+" / "-") positive-speech-length

positive-speech-length =   1*DIGIT SP numeric-speech-unit

numeric-speech-unit   =   "Second"

/   "Word"

/   "Sentence"

/   "Paragraph"

8.4.2.  Kill-On-Barge-In

This header MAY be sent as part of the "SPEAK" method to enable kill-

on-barge-in support.  If enabled, the "SPEAK" method is interrupted

by DTMF input detected by a signal detector resource or by the start

of speech sensed or recognized by the speech recognizer resource.

kill-on-barge-in      =   "Kill-On-Barge-In" ":" boolean-value CRLF

boolean-value         =   "true" / "false"

The client MUST send a BARGE-IN-OCCURRED method to the synthesizer

resource when it receives a barge-in-able event from any source.

This source could be a synthesizer resource or signal detector

resource and MAY be either local or distributed.  If this header is

not specified in a "SPEAK" request or explicitly set by a

"SET-PARAMS", the default value for this header is "true".

If the recognizer or signal detector resource is on the same server

as the synthesizer and both are part of the same session, the server

MAY work with both to provide internal notification to the

synthesizer so that audio may be stopped without having to wait for

the client's BARGE-IN-OCCURRED event.

8.4.3.  Speaker Profile

This header MAY be part of the "SET-PARAMS"/"GET-PARAMS" or "SPEAK"

request from the client to the server and specifies a URI which

references the profile of the speaker.  Speaker profiles are

collections of voice parameters like gender, accent etc.

Shanmugham & Burnett    Expires September 6, 2007              [Page 45]

Internet-Draft                   MRCPv2                       March 2007

speaker-profile       =   "Speaker-Profile" ":" uri CRLF

8.4.4.  Completion Cause

This header MUST be specified in a "SPEAK-COMPLETE" event coming from

the synthesizer resource to the client.  This indicates the reason

the "SPEAK" request completed.

completion-cause      =   "Completion-Cause" ":" 1*DIGIT SP

1*VCHAR CRLF

+------------+-----------------------+------------------------------+

| Cause-Code | Cause-Name            | Description                  |

+------------+-----------------------+------------------------------+

| 000        | normal                | SPEAK completed normally.    |

| 001        | barge-in              | SPEAK request was terminated |

|            |                       | because of barge-in.         |

| 002        | parse-failure         | SPEAK request terminated     |

|            |                       | because of a failure to      |

|            |                       | parse the speech markup      |

|            |                       | text.                        |

| 003        | uri-failure           | SPEAK request terminated     |

|            |                       | because access to one of the |

|            |                       | URIs failed.                 |

| 004        | error                 | SPEAK request terminated     |

|            |                       | prematurely due to           |

|            |                       | synthesizer error.           |

| 005        | language-unsupported  | Language not supported.      |

| 006        | lexicon-load-failure  | Lexicon loading failed.      |

| 007        | cancelled             | A prior SPEAK request failed |

|            |                       | while this one was still in  |

|            |                       | the queue.                   |

+------------+-----------------------+------------------------------+

Synthesizer Resource Compleion Cause Codes

8.4.5.  Completion Reason

This header MAY be specified in a "SPEAK-COMPLETE" event coming from

the synthesizer resource to the client.  This contains the reason

text behind the "SPEAK" request completion.  This header can be use

to communicate text describing the reason for the failure, such as an

error in parsing the speech markup text.

completion-reason   =   "Completion-Reason" ":"

quoted-string CRLF

Shanmugham & Burnett    Expires September 6, 2007              [Page 46]

Internet-Draft                   MRCPv2                       March 2007

The completion reason text is provided for client use in logs and for

debugging and instrumentation purposes.  Clients are NOT REQUIRED to

interpret the completion reason text.

8.4.6.  Voice- Parameters

This set of headers defines the voice of the speaker.

voice-parameters    =   voice-gender

/   voice-age

/   voice-variant

/   voice-name

voice-gender        =   "Voice-Gender:" voice-gender-value CRLF

voice-gender-value  =   "male"

/   "female"

/   "neutral"

voice-age           =   "Voice-Age:" 1*DIGIT CRLF

voice-variant       =   "Voice-Variant:" 1*DIGIT CRLF

voice-name          =   "Voice-Name:"

1*UTFCHAR *[1*WSP 1*UTFCHAR] CRLF

The Voice- parameters are derived from the similarly-named attributes

of the voice element specified in W3C's Speech Synthesis Markup

Language Specification [24].  Legal values for these parameters are

as defined in that specification.

These headers MAY be sent in "SET-PARAMS"/"GET-PARAMS" request to

define/get default values for the entire session or MAY be sent in

the "SPEAK" request to define default values for that speak request.

Note that SSML content can itself set these values internal to the

SSML document, of course.

Voice parameter headers MAY also be sent in a CONTROL method to

affect a "SPEAK" request in progress and change its behavior on the

fly.  If the synthesizer resource does not support this operation, it

MUST reject the request with a status of 403 "Unsupported Header".

8.4.7.  Prosody-Parameters

This set of headers defines the prosody of the speech.

prosody-parameter   =   "Prosody-" prosody-param-name ":"

prosody-param-value CRLF

prosody-param-name is any one of the attribute names under the

Shanmugham & Burnett    Expires September 6, 2007              [Page 47]

Internet-Draft                   MRCPv2                       March 2007

prosody element specified in W3C's Speech Synthesis Markup Language

Specification [24].  The prosody-param-value is any one of the value

choices of the corresponding prosody element attribute specified in

the above section.

These headers MAY be sent in "SET-PARAMS"/"GET-PARAMS" request to

define/get default values for the entire session or MAY be sent in

the "SPEAK" request to define default values for that speak request.

Furthermore, these attributes can be part of the speech text marked

up in SSML.

The prosody parameter headers in the "SET-PARAMS" or "SPEAK" request

only apply if the speech data is of type text/plain and does not use

a speech markup format.

These prosody parameter headers MAY also be sent in a CONTROL method

to affect a "SPEAK" request in progress and change its behavior on

the fly.  If the synthesizer resource does not support this

operation, it MUST respond back to the client with a status of 403

"Unsupported Header".

8.4.8.  Speech Marker

This header contains a timestamp, a marker, or both.  The markers are

bookmarks that are defined within the markup.  Most speech markup

formats provide mechanisms to embed marker fields within speech

texts.  The synthesizer generates SPEECH-MARKER events when it

reaches these marker fields.  This header MUST be part of the SPEECH-

MARKER event and contain the marker tag value.

The header value MAY also have timestamp information in a "timestamp"

field that precedes the marker value and is separated from it by a

semicolon.  This is an NTP timestamp, 64 bit number in decimal form,

marking the time the text corresponding to the marker was emitted as

speech by the synthesizer.  It therefore MUST be synced with the RTP

timestamp of the media stream through RTCP.

This header MUST also be returned in responses to STOP, CONTROL, and

BARGE-IN-OCCURRED methods, in the "SPEAK-COMPLETE" event, and in an

IN-PROGRESS SPEAK response.  In these messages the marker tag MUST be

the last embedded marker encountered or a null string if no marker

has yet been encountered.  Note than in these events the purpose of

this header is to provide timestamp information associated with

important events within the lifecycle of a request (start of SPEAK

processing, end of SPEAK processing, receipt of CONTROL/STOP/

BARGE-IN-OCCURRED).

Shanmugham & Burnett    Expires September 6, 2007              [Page 48]

Internet-Draft                   MRCPv2                       March 2007

timestamp           =   "timestamp" "=" time-stamp-value CRLF

time-stamp-value    =   1*DIGIT

speech-marker       =   "Speech-Marker" ":"

"timestamp=" [time-stamp-value]

[";" 1*(UTFCHAR / 0x20)] CRLF

8.4.9.  Speech Language

This header specifies the default language of the speech data if the

language is not specified in the markup.  The value of this header

MUST follow RFC4646 [17] for its values.  The header MAY occur in

"SPEAK", "SET-PARAMS" or "GET-PARAMS" requests.

speech-language     =   "Speech-Language" ":" 1*VCHAR CRLF

8.4.10.  Fetch Hint

When the synthesizer needs to fetch documents or other resources like

speech markup or audio files, this header controls the corresponding

URI access properties.  This provides client policy on when the

synthesizer should retrieve content from the server.  A value of

"prefetch" indicates the content MAY be downloaded when the request

is received, whereas "safe" indicates that content MUST NOT be

downloaded until actually referenced.  The default value is

"prefetch".  This header MAY occur in "SPEAK", "SET-PARAMS" or

"GET-PARAMS" requests.

fetch-hint          =   "Fetch-Hint" ":" 1*ALPHA CRLF

8.4.11.  Audio Fetch Hint

When the synthesizer needs to fetch documents or other resources like

speech audio files, this header controls the corresponding URI access

properties.  This provides client policy whether or not the

synthesizer may attempt to optimize speech by pre-fetching audio.

The value is either "safe" to say that audio is only fetched when it

is referenced, never before; "prefetch" to permit, but not require

the implementation to pre-fetch the audio; or "stream" to allow it to

stream the audio fetches.  The default value is "prefetch".  This

header MAY occur in "SPEAK", "SET-PARAMS" or "GET-PARAMS". requests.

audio-fetch-hint    =   "Audio-Fetch-Hint" ":" 1*ALPHA CRLF

Shanmugham & Burnett    Expires September 6, 2007              [Page 49]

Internet-Draft                   MRCPv2                       March 2007

8.4.12.  Failed URI

When a synthesizer method needs a synthesizer to fetch or access a

URI and the access fails, the server SHOULD provide the failed URI in

this header in the method response, unless there are multiple URI

failures, in which case one of the failed URIs MUST be provided in

this header in the method response.

failed-uri          =   "Failed-URI" ":" Uri CRLF

8.4.13.  Failed URI Cause

When a synthesizer method needs a synthesizer to fetch or access a

URI and the access fails the server MUST provide the URI specific or

protocol specific response code for the URI in the Failed-URI header

in the method response through this header.  The value encoding is

alphanumeric to accommodate all anticipated access protocols, some of

which might have a response string instead of a numeric response

code.

failed-uri-cause    =   "Failed-URI-Cause" ":" 1*alphanum CRLF

8.4.14.  Speak Restart

When a CONTROL request to jump backward is issued to a currently

speaking synthesizer resource, and the target jump point is before

the start of the current "SPEAK" request, the current "SPEAK" request

MUST restart from the beginning of its speech data and the response

to the CONTROL request MUST contain this header indicating a restart.

speak-restart       =   "Speak-Restart" ":" boolean-value CRLF

8.4.15.  Speak Length

This header MAY be specified in a CONTROL method to control the

length of speech to speak, relative to the current speaking point in

the currently active "SPEAK" request.  If numeric, the value MUST be

a positive integer.  If a header with a Tag unit is specified, then

the speech output continues until the tag is reached or the "SPEAK"

request complete, whichever comes first.  This header MAY be

specified in a "SPEAK" request to indicate the length to speak from

the speech data and is relative to the point in speech that the

"SPEAK" request starts.  The different speech length units supported

are synthesizer implementation dependent.  If a server does not

support the specified unit, the resource MUST respond with a status

code of 409 "Unsupported Header Value".

Shanmugham & Burnett    Expires September 6, 2007              [Page 50]

Internet-Draft                   MRCPv2                       March 2007

speak-length          =   "Speak-Length" ":" positive-length-value

CRLF

positive-length-value =   positive-speech-length

/   text-speech-length

text-speech-length    =   1*UTFCHAR SP "Tag"

positive-speech-length =  1*DIGIT SP numeric-speech-unit

numeric-speech-unit   =   "Second"

/   "Word"

/   "Sentence"

/   "Paragraph"

8.4.16.  Load-Lexicon

This header is used to indicate whether a lexicon has to be loaded or

unloaded.  The default value for this header is "true".  This header

MAY be specified in a DEFINE-LEXICON method.

load-lexicon       =   "Load-Lexicon" ":" Boolean-value CRLF

8.4.17.  Lexicon-Search-Order

This header is used to specify a list of active Lexicon URIs and the

search order among the active lexicons.  Lexicons specified within

the SSML document take precedence over the lexicons specified in this

header.  This header MAY be specified in the SPEAK, SET-PARAMS, and

GET-PARAMS methods.

lexicon-search-order =   "Lexicon-Search-Order" ":"

"<" absoluteURI ">" *[" " "<" absoluteURI ">"] CRLF

8.5.  Synthesizer Message Body

A synthesizer message may contain additional information associated

with the Request, Response or Event in its message body.

8.5.1.  Synthesizer Speech Data

Marked-up text for the synthesizer to speak is specified as a MIME

entity in the message body.  The speech data to be spoken by the

synthesizer can be specified inline by embedding the data in the

message body or by reference by providing a URI for accessing the

data.  In either case the data and the format used to markup the

speech needs to be of a content type supported by the server.

Shanmugham & Burnett    Expires September 6, 2007              [Page 51]

Internet-Draft                   MRCPv2                       March 2007

All MRCPv2 servers containing synthesizer resources MUST support both

plain text speech data and W3C's Speech Synthesis Markup Language

[24] and hence MUST support the MIME types text/plain and

application/ssml+xml.  Other formats MAY be supported.

If the speech data is to be fetched by URI reference, the MIME type

text/uri-list is used to indicate one or more URIs that, when

dereferenced, will contain the content to be spoken.  If a list of

speech URIs is specified, speech data provided by each URI MUST be

spoken in the order in which the URIs are specified in the MIME

content.

A mix of URI and inline speech data may be indicated through the

multipart/mixed MIME-type.  Embedded within the multipart there MAY

be MIME content for text/uri-list, application/ssml+xml and/or text/

plain.  The character set and encoding used in the speech data is

specified according to standard MIME-type definitions.  The multi-

part MIME-block MAY also contain actual audio data in .wav or sun

audio format.  Clients may have recorded audio clips stored in memory

or on a local device and it wish to play it as part of the "SPEAK"

request.  The audio MIME-parts, MAY be sent by the client as part of

the multi-part MIME-block.  This audio is referenced in the speech

markup data that is another part in the multi-part MIME-block

according to the multipart/mixed MIME-type specification.

Content-Type:text/uri-list

Content-Length:176

http://www.example.com/ASR-Introduction.ssml

http://www.example.com/ASR-Document-Part1.ssml

http://www.example.com/ASR-Document-Part2.ssml

http://www.example.com/ASR-Conclusion.ssml

URI List Example

Shanmugham & Burnett    Expires September 6, 2007              [Page 52]

Internet-Draft                   MRCPv2                       March 2007

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams

and arrived at <break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is <prosody

rate="-20%">ski trip</prosody></s>

</p>

</speak>

SSML Example

Shanmugham & Burnett    Expires September 6, 2007              [Page 53]

Internet-Draft                   MRCPv2                       March 2007

Content-Type:multipart/mixed; boundary="break"

--break

Content-Type:text/uri-list

Content-Length:176

http://www.example.com/ASR-Introduction.ssml

http://www.example.com/ASR-Document-Part1.ssml

http://www.example.com/ASR-Document-Part2.ssml

http://www.example.com/ASR-Conclusion.ssml

--break

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams

and arrived at <break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is <prosody

rate="-20%">ski trip</prosody></s>

</p>

</speak>

--break--

Multipart Example

8.5.2.  Lexicon Data

Synthesizer lexicon data from the client to the server can be

provided inline or by reference.  Either way they are carried as MIME

entities in the message body of the MRCPv2 request message.

When a lexicon is specified in-line in the message, the client MUST

provide a Content-ID for that lexicon as part of the content headers.

The server MUST store the lexicon associated with that Content-ID for

the duration of the session.  A stored lexicon can be overwritten by

defining a new lexicon with the same Content-ID.  Lexicons that have

been associated with a Content-ID can be referenced through the

Shanmugham & Burnett    Expires September 6, 2007              [Page 54]

Internet-Draft                   MRCPv2                       March 2007

""session:"" URI scheme (see Section 13.6).

If lexicon data is specified by external URI reference, the MIME-type

text/uri-list is used to list the one or more URIs that may be

dereferenced to obtain the lexicon data.  All MRCPv2 servers MUST

support the HTTP and HTTPS uri access mechanisms, and MAY support

other mechanisms.

If the data in the MIME body consists of a mix of URI and inline

lexicon data the multipart/mixed MIME-type is used.  The character

set and encoding used in the lexicon data may be specified according

to standard MIME-type definitions.

8.6.  SPEAK Method

The "SPEAK" Request provides the synthesizer resource with the speech

text and initiates speech synthesis and streaming.  The "SPEAK"

method can carry voice and prosody headers that alter the behavior of

the voice being synthesized, as well as a MIME body containing the

actual marked-up text to be spoken.

The SPEAK method implementation MUST do a fetch of all external URIs

that are part of that operation.  If caching is implemented, this URI

fetching MUST conform to the cache control hints and parameter

headers associated with the method in deciding whether it is to be

fetched from cache or from the external server.  If these hints/

parameters are not specified in the method, the values set for the

session using SET-PARAMS/GET-PARAMS apply.  If it was not set for the

session their default values apply.

When applying voice parameters there are 3 levels of precedence.  The

highest precedence are those specified within the speech markup text,

followed by those specified in the headers of the "SPEAK" request and

hence apply for that "SPEAK" request only, followed by the session

default values which can be set using the "SET-PARAMS" request and

apply for subsequent methods invoked during the session.

If the resource was idle at the time the "SPEAK" request arrived at

the server and the "SPEAK" method is being actively processed, the

resource responds immediately with a success status code and a

request-state of IN-PROGRESS.

If the resource is in the speaking or paused state when the "SPEAK"

method arrives at the server, i.e. it is in the middle of processing

a previous "SPEAK" request, the status returns success with a

request-state of PENDING.  The server places the "SPEAK" request in

the synthesizer resource request queue.  The request queue operates

strictly FIFO: requests are processed serially in order of receipt.

Shanmugham & Burnett    Expires September 6, 2007              [Page 55]

Internet-Draft                   MRCPv2                       March 2007

If the current SPEAK fails, all SPEAK methods in the pending queue

are cancelled and each generates a SPEAK-COMPLETE event with a

Completion-Cause of "cancelled".

For the synthesizer resource, "SPEAK" is the only method that can

return a request-state of IN-PROGRESS or PENDING.  When the text has

been synthesized and played into the media stream, the resource

issues a "SPEAK-COMPLETE" event with the request-id of the "SPEAK"

request and a request-state of COMPLETE.

C->S: MRCP/2.0 489 SPEAK 543257

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:neutral

Voice-Age:25

Prosody-volume:medium

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams and arrived at

<break/>

<say-as interpret-as="vxml:time">0345p</say-as>.

</s>

<s>The subject is

<prosody rate="-20%">ski trip</prosody>

</s>

</p>

</speak>

S->C: MRCP/2.0 28 543257 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857206027059

S->C: MRCP/2.0 79 SPEAK-COMPLETE 543257 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Completion-Cause:000 normal

Speech-Marker:timestamp=857206027059

Shanmugham & Burnett    Expires September 6, 2007              [Page 56]

Internet-Draft                   MRCPv2                       March 2007

SPEAK Example

8.7.  STOP

The "STOP" method from the client to the server tells the synthesizer

resource to stop speaking if it is speaking something.

The "STOP" request can be sent with an active-request-id-list header

to stop the zero or more specific "SPEAK" requests that may be in

queue and return a response code of 200 (Success).  If no active-

request-id-list header is sent in the "STOP" request the server

terminates all outstanding "SPEAK" requests.

If a "STOP" request successfully terminated one or more PENDING or

IN-PROGRESS "SPEAK" requests, then the response MUST contain an

active-request-id-list header enumerating the "SPEAK" request-ids

that were terminated.  Otherwise there is no active-request-id-list

header in the response.  No "SPEAK-COMPLETE" events are sent for such

terminated requests.

If a "SPEAK" request that was IN-PROGRESS and speaking was stopped,

the next pending "SPEAK" request, if any, becomes IN-PROGRESS at the

resource and enters the speaking state.

If a "SPEAK" request that was IN-PROGRESS and paused was stopped, the

next pending "SPEAK" request, if any, becomes IN-PROGRESS and enters

the paused state.

Shanmugham & Burnett    Expires September 6, 2007              [Page 57]

Internet-Draft                   MRCPv2                       March 2007

C->S: MRCP/2.0 423 SPEAK 543258

Channel-Identifier:32AECB23433802@speechsynth

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams and arrived at

<break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is

<prosody rate="-20%">ski trip</prosody></s>

</p>

</speak>

S->C: MRCP/2.0 48 543258 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857206027059

C->S: MRCP/2.0 44 STOP 543259

Channel-Identifier:32AECB23433802@speechsynth

S->C: MRCP/2.0 66 543259 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Active-Request-Id-List:543258

Speech-Marker:timestamp=857206039059

STOP Example

8.8.  BARGE-IN-OCCURED

The BARGE-IN-OCCURRED method, when used with the synthesizer

resource, provides a client which has detected a barge-in-able event

a means to communicate the occurrence of the event to the synthesizer

resource.

This method is useful in two scenarios,

1.  The client has detected DTMF digits in the input media or some

other barge-in-able event and wants to communicate that to the

synthesizer resource.

Shanmugham & Burnett    Expires September 6, 2007              [Page 58]

Internet-Draft                   MRCPv2                       March 2007

2.  The recognizer resource and the synthesizer resource are in

different servers.  In this case the client acts as an

intermediary for the two servers.  It receives an event from the

recognition resource and sends a BARGE-IN-OCCURRED request to the

synthesizer.  In such cases, the BARGE-IN-OCCURRED method would

also have a proxy-sync-id header received from the resource

generating the original event.

If a "SPEAK" request is active with kill-on-barge-in enabled, and the

BARGE-IN-OCCURRED event is received, the synthesizer MUST immediately

stop streaming out audio.  It MUST also terminate any speech requests

queued behind the current active one, irrespective of whether they

have barge-in enabled or not.  If a barge-in-able "SPEAK" request was

playing and it was terminated, the response MUST contain the an

active-request-list header listing the request-ids of all "SPEAK"

requests that were terminated.  The server generates no

"SPEAK-COMPLETE" events for these requests.

If there were no "SPEAK" requests terminated by the synthesizer

resource as a result of the BARGE-IN-OCCURRED method, the server

responds to the BARGE-IN-OCCURRED with a 200 success which MUST NOT

contain an active-request-id-list header.

If the synthesizer and recognizer resources are part of the same

MRCPv2 session, they can be optimized for a quicker kill-on-barge-in

response if the recognizer and synthesizer interact directly.  In

these cases, the client MUST still react to a START-OF-INPUT event

from the recognizer by invoking the BARGE-IN-OCCURRED method to the

synthesizer.  The client MUST invoke the BARGE-IN-OCCURRED if it has

any outstanding requests to the synthesizer resource in either the

PENDING or IN-PROGRESS state.

Shanmugham & Burnett    Expires September 6, 2007              [Page 59]

Internet-Draft                   MRCPv2                       March 2007

C->S: MRCP/2.0 433 SPEAK 543258

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:neutral

Voice-Age:25

Prosody-volume:medium

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams and arrived at

<break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is

<prosody rate="-20%">ski trip</prosody></s>

</p>

</speak>

S->C: MRCP/2.0 47 543258 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857206027059

C->S: MRCP/2.0 69 BARGE-IN-OCCURRED 543259

Channel-Identifier:32AECB23433802@speechsynth

Proxy-Sync-Id:987654321

S->C:MRCP/2.0 72 543259 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Active-Request-Id-List:543258

Speech-Marker:timestamp=857206039059

BARGE-IN-OCCURED Example

8.9.  PAUSE

The PAUSE method from the client to the server tells the synthesizer

resource to pause speech output if it is speaking something.  If a

PAUSE method is issued on a session when a "SPEAK" is not active the

server MUST respond with a status of 402 "Method not valid in this

state".  If a PAUSE method is issued on a session when a "SPEAK" is

active and paused the server MUST respond with a status of 200

Shanmugham & Burnett    Expires September 6, 2007              [Page 60]

Internet-Draft                   MRCPv2                       March 2007

"Success".  If a "SPEAK" request was active the server MUST return an

active-request-id-list header with the request-id of the "SPEAK"

request that was paused.

C->S: MRCP/2.0 434 SPEAK 543258

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:neutral

Voice-Age:25

Prosody-volume:medium

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams and arrived at

<break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is

<prosody rate="-20%">ski trip</prosody></s>

</p>

</speak>

S->C: MRCP/2.0 48 543258 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857206027059

C->S: MRCP/2.0 43 PAUSE 543259

Channel-Identifier:32AECB23433802@speechsynth

S->C: MRCP/2.0 68 543259 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Active-Request-Id-List:543258

PAUSE Example

8.10.  RESUME

The RESUME method from the client to the server tells a paused

synthesizer resource to resume speaking.  If a RESUME request is

issued on a session with no active "SPEAK" request, the server MUST

Shanmugham & Burnett    Expires September 6, 2007              [Page 61]

Internet-Draft                   MRCPv2                       March 2007

respond with a status of 402 "Method not valid in this state".  If a

RESUME request is issued on a session with an active "SPEAK" request

that is speaking (i.e., not paused) the server MUST respond with a

status of 200 "Success".  If a "SPEAK" request was active the server

MUST return an active-request-id-list header with the request-id of

the "SPEAK" request that was resumed.

C->S: MRCP/2.0 434 SPEAK 543258

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:neutral

Voice-age:25

Prosody-volume:medium

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams and arrived at

<break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is

<prosody rate="-20%">ski trip</prosody></s>

</p>

</speak>

S->C: MRCP/2.0 48 543258 200 IN-PROGRESS@speechsynth

Channel-Identifier:32AECB23433802

Speech-Marker:timestamp=857206027059

C->S: MRCP/2.0 44 PAUSE 543259

Channel-Identifier:32AECB23433802@speechsynth

S->C: MRCP/2.0 47 543259 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Active-Request-Id-List:543258

C->S: MRCP/2.0 44 RESUME 543260

Channel-Identifier:32AECB23433802@speechsynth

S->C: MRCP/2.0 66 543260 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Shanmugham & Burnett    Expires September 6, 2007              [Page 62]

Internet-Draft                   MRCPv2                       March 2007

Active-Request-Id-List:543258

RESUME Example

8.11.  CONTROL

The CONTROL method from the client to the server tells a synthesizer

that is speaking to modify what it is speaking on the fly.  This

method is used to request the synthesizer to jump forward or backward

in what it is speaking, change speaker rate, speaker parameters, etc.

It affects only the currently IN-PROGRESS "SPEAK" request.  Depending

on the implementation and capability of the synthesizer resource it

may or may not support the various modifications indicated by headers

in the CONTROL request.

When a client invokes a CONTROL method to jump forward and the

operation goes beyond the end of the active "SPEAK" method's text,

the CONTROL request still succeeds.  The active "SPEAK" request

completes and returns a "SPEAK-COMPLETE" event following the response

to the CONTROL method.  If there are more "SPEAK" requests in the

queue, the synthesizer resource starts at the beginning of the next

"SPEAK" request in the queue.

When a client invokes a CONTROL method to jump backward and the

operation jumps to the beginning or beyond the beginning of the

speech data of the active "SPEAK" method, the CONTROL request still

succeeds.  The response to the CONTROL request contains the speak-

restart header, and the active "SPEAK" request restarts from the

beginning of its speech data.

These two behaviors can be used to rewind or fast-forward across

multiple speech requests, if the client wants to break up a speech

markup text to multiple "SPEAK" requests.

If a "SPEAK" request was active when the CONTROL method was received

the server MUST return an active-request-id-list header with the

Request-id of the "SPEAK" request that was active.

Shanmugham & Burnett    Expires September 6, 2007              [Page 63]

Internet-Draft                   MRCPv2                       March 2007

C->S: MRCP/2.0 434 SPEAK 543258

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:neutral

Voice-age:25

Prosody-volume:medium

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams

and arrived at <break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is <prosody

rate="-20%">ski trip</prosody></s>

</p>

</speak>

S->C: MRCP/2.0 47 543258 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857205016059

C->S: MRCP/2.0 63 CONTROL 543259

Channel-Identifier:32AECB23433802@speechsynth

Prosody-rate:fast

S->C: MRCP/2.0 67 543259 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Active-Request-Id-List:543258

Speech-Marker:timestamp=857206027059

C->S: MRCP/2.0 68 CONTROL 543260

Channel-Identifier:32AECB23433802@speechsynth

Jump-Size:-15 Words

S->C: MRCP/2.0 69 543260 200 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Active-Request-Id-List:543258

Speech-Marker:timestamp=857206039059

Shanmugham & Burnett    Expires September 6, 2007              [Page 64]

Internet-Draft                   MRCPv2                       March 2007

CONTROL Example

8.12.  SPEAK-COMPLETE

This is an Event message from the synthesizer resource to the client

indicating that the corresponding "SPEAK" request was completed.  The

request-id header matches the request-id of the "SPEAK" request that

initiated the speech that just completed.  The request-state field is

set to COMPLETE by the server, indicating that this is the last event

with the corresponding request-id.  The completion-cause header

specifies the cause code pertaining to the status and reason of

request completion such as the "SPEAK" completed normally or because

of an error, kill-on-barge-in etc.

C->S: MRCP/2.0 434 SPEAK 543260

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:neutral

Voice-age:25

Prosody-volume:medium

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams

and arrived at <break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is

<prosody rate="-20%">ski trip</prosody></s>

</p>

</speak>

S->C: MRCP/2.0 48 543260 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857206027059

S->C: MRCP/2.0 73 SPEAK-COMPLETE 543260 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Completion-Cause:000 normal

Speech-Marker:timestamp=857206039059

Shanmugham & Burnett    Expires September 6, 2007              [Page 65]

Internet-Draft                   MRCPv2                       March 2007

SPEAK-COMPLETE Example

8.13.  SPEECH-MARKER

This is an event generated by the synthesizer resource to the client

when the synthesizer encounters a marker tag in the speech markup it

is currently processing.  The request-id field in the header matches

the corresponding "SPEAK" request.  The request-state field indicates

IN-PROGRESS as the speech is still not complete.  The value of the

speech marker tag hit, describing where the synthesizer is in the

speech markup, is returned in the speech-marker header, along with an

NTP timestamp indicating the instant in the output speech stream that

the marker was encountered.  The SPEECH-MARKER event is also

generated with a null marker value and output NTP timestamp, when a

SPEAK request in Pending-State (i.e. in the queue) changes state to

IN-PROGRESS and starts speaking.  The NTP timestamp MUST be

synchronized with the RTP timestamp used to generate the speech

stream through standard RTCP machinery.

Shanmugham & Burnett    Expires September 6, 2007              [Page 66]

Internet-Draft                   MRCPv2                       March 2007

C->S: MRCP/2.0 434 SPEAK 543261

Channel-Identifier:32AECB23433802@speechsynth

Voice-gender:neutral

Voice-age:25

Prosody-volume:medium

Content-Type:synthesis+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams

and arrived at <break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<mark name="here"/>

<s>The subject is

<prosody rate="-20%">ski trip</prosody>

</s>

<mark name="ANSWER"/>

</p>

</speak>

S->C: MRCP/2.0 48 543261 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857205015059

S->C: MRCP/2.0 73 SPEECH-MARKER 543261 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857206027059;here

S->C: MRCP/2.0 74 SPEECH-MARKER 543261 IN-PROGRESS

Channel-Identifier:32AECB23433802@speechsynth

Speech-Marker:timestamp=857206039059;ANSWER

S->C: MRCP/2.0 73 SPEAK-COMPLETE 543261 COMPLETE

Channel-Identifier:32AECB23433802@speechsynth

Completion-Cause:000 normal

Speech-Marker:timestamp=857207689259;ANSWER

SPEECH-MARKER Example

Shanmugham & Burnett    Expires September 6, 2007              [Page 67]

Internet-Draft                   MRCPv2                       March 2007

8.14.  DEFINE-LEXICON

The DEFINE-LEXICON method, from the client to the server, provides a

lexicon and tells the server to load, unload, activate or deactivate

the lexicon.

If the server resource is in the speaking or paused state, the server

MUST respond 402 (Method not valid in this state) failure status .

If the resource is in the idle state and is able to successfully

load/unload/activate/deactivate the lexicon the status MUST return a

success code and the request-state MUST be COMPLETE.

If the synthesizer could not define the lexicon for some reason, for

example because the download failed or the lexicon was in an

unsupported form, the server MUST respond with a failure status code

of 407, and a Completion-Cause header describing the failure reason.

9.  Speech Recognizer Resource

The speech recognizer resource receives an incoming voice stream and

provides the client with an interpretation of what was spoken in

textual form.

The recognizer resource is controlled by MRCPv2 requests from the

client.  The recognizer resource can both respond to these requests

and generate asynchronous events to the client to indicate conditions

of interest during the processing of the method.

This section applies to the following resource types.

1.  speechrecog

2.  dtmfrecog

The difference between the above two resources is in their level of

support for recognition grammars.  The "dtmfrecog" resource type is

capable of recognizing only DTMF digits and hence accepts only DTMF

grammars.  It only generates barge-in for DTMF inputs and ignores

speech.  The "speechrecog" resource type can recognize regular speech

as well as DTMF digits and hence MUST support grammars describing

either speech or DTMF.  This resource generates barge-in events for

speech and/or DTMF.  By analyzing the grammars that are activated by

the RECOGNIZE method, it determines if a barge-in should occur for

speech and/or DTMF.  When the recognizer decides it needs to generate

barge-in it also generates a START-OF-INPUT event to the client.  The

recognition resource may support recognition in the normal or hotword

modes or both (although note that a single speechrecog resource does

not perform normal and hotword mode recognition simultaneously).  For

Shanmugham & Burnett    Expires September 6, 2007              [Page 68]

Internet-Draft                   MRCPv2                       March 2007

implementations where a single recognition resource does not support

both modes, or simultaneous normal and hotword recognition is

desired, the two modes can be invoked through separate resources

allocated to the same SIP dialog (with different MRCP session

identifiers) and share the RTP audio feed.

The capabilities of the recognition resource are enumerated below:

Normal Mode Recognition  Normal mode recognition tries to match all

of the speech or DTMF against the grammar and returns a no-match

status if the input fails to match or the method times out.

Hotword Mode Recognition  Hotword mode is where the recognizer looks

for a match against specific speech grammar or DTMF sequence and

ignores speech or DTMF that does not match.  The recognition

completes only for a successful match of grammar or if the client

cancels the request or if there is a a non-input or recognition

timeout.

Voice Enrolled Grammars  A recognition resource may optionally

support Voice Enrolled Grammars.  With this functionality,

enrollment is performed using a person's voice.  For example, a

list of contacts can be created and maintained by recording the

person's names using the caller's voice.  This technique is

sometimes also called speaker-dependent recognition.

Interpretation  A recognition resource may be employed strictly for

its natural language interpretation capabilities by supplying it

with a text string as input instead of speech.  In this mode the

resource takes text as input and produces an "interpretation" of

the input according to the supplied grammar.

Voice Enrollment has the concept of an enrollment session.  A session

to add a new phrase to a personal grammar involves the initial

enrollment followed by a repeat of enough utterances before

committing the new phrase to the personal grammar.  Each time an

utterance is recorded, it is compared for similarity with the other

samples and a clash test is performed against other entries in the

personal grammar to ensure there are no similar and confusable

entries.

Enrollment is done using a recognizer resource.  Controlling which

utterances are to be considered for enrollment of a new phrase is

done by setting a header (see Section 9.4.39) in the Recognize

request.

Interpretation is accomplished through the INTERPRET method

(Section 9.20) and the interpret-text header (Section 9.4.30).

Shanmugham & Burnett    Expires September 6, 2007              [Page 69]

Internet-Draft                   MRCPv2                       March 2007

9.1.  Recognizer State Machine

The recognizer resource maintains a state machine to process MRCPv2

requests from the client.

Idle                   Recognizing               Recognized

State                  State                     State

|                       |                          |

|---------RECOGNIZE---->|---RECOGNITION-COMPLETE-->|

|<------STOP------------|<-----RECOGNIZE-----------|

|                       |                          |

|                       |              |-----------|

|              |--------|       GET-RESULT         |

|       START-OF-INPUT  |              |---------->|

|------------| |------->|                          |

|            |          |----------|               |

|      DEFINE-GRAMMAR   | START-INPUT-TIMERS       |

|<-----------|          |<---------|               |

|                       |                          |

|                       |------|                   |

|-------|               |   RECOGNIZE              |

|      STOP             |<-----|                   |

|<------|                                          |

|                                                  |

|<-------------------STOP--------------------------|

|<-------------------DEFINE-GRAMMAR----------------|

Recognizer State Machine

If a recognition resource supports voice enrolled grammars, starting

an enrollment session does not change the state of the recognizer

resource.  Once an enrollment session is started, then utterances are

enrolled by calling the RECOGNIZE method repeatedly.  The state of

the speech recognizer resource goes from IDLE to RECOGNIZING state

each time RECOGNIZE is called.

9.2.  Recognizer Methods

The recognizer supports the following methods.

recognizer-method    =  recog-only-method

/  enrollment-method

recog-only-method    =  "DEFINE-GRAMMAR"

/  "RECOGNIZE"

/  "INTERPRET"

/  "GET-RESULT"

/  "START-INPUT-TIMERS"

Shanmugham & Burnett    Expires September 6, 2007              [Page 70]

Internet-Draft                   MRCPv2                       March 2007

/  "STOP"

It is OPTIONAL for a recognizer resource to support voice enrolled

grammars.  If the recognizer resource does support voice enrolled

grammars it MUST support the following methods.

enrollment-method    =  "START-PHRASE-ENROLLMENT"

/  "ENROLLMENT-ROLLBACK"

/  "END-PHRASE-ENROLLMENT"

/  "MODIFY-PHRASE"

/  "DELETE-PHRASE"

9.3.  Recognizer Events

The recognizer may generate the following events.

recognizer-event     =  "START-OF-INPUT"

/  "RECOGNITION-COMPLETE"

/  "INTERPRETATION-COMPLETE"

9.4.  Recognizer Header Fields

A recognizer message may contain headers containing request options

and information to augment the Method, Response or Event message it

is associated with.

Shanmugham & Burnett    Expires September 6, 2007              [Page 71]

Internet-Draft                   MRCPv2                       March 2007

recognizer-header    =  recog-only-header

/  enrollment-header

recog-only-header    =  confidence-threshold

/  sensitivity-level

/  speed-vs-accuracy

/  n-best-list-length

/  no-input-timeout

/  input-type

/  recognition-timeout

/  waveform-uri

/  input-waveform-uri

/  completion-cause

/  completion-reason

/  recognizer-context-block

/  start-input-timers

/  speech-complete-timeout

/  speech-incomplete-timeout

/  dtmf-interdigit-timeout

/  dtmf-term-timeout

/  dtmf-term-char

/  failed-uri

/  failed-uri-cause

/  save-waveform

/  media-type

/  new-audio-channel

/  speech-language

/  ver-buffer-utterance

/  recognition-mode

/  cancel-if-queue

/  hotword-max-duration

/  hotword-min-duration

/  interpret-text

/  dtmf-buffer-time

/  clear-dtmf-buffer

/  early-no-match

If a recognition resource supports voice enrolled grammars, the

following headers are also used.

Shanmugham & Burnett    Expires September 6, 2007              [Page 72]

Internet-Draft                   MRCPv2                       March 2007

enrollment-header    =  num-min-consistent-pronunciations

/  consistency-threshold

/  clash-threshold

/  personal-grammar-uri

/  enroll-utterance

/  phrase-id

/  phrase-nl

/  weight

/  save-best-waveform

/  new-phrase-id

/  confusable-phrases-uri

/  abort-phrase-enrollment

For enrollment-specific headers that can appear as part of

"SET-PARAMS" or "GET-PARAMS" methods, the following general rule

applies: the START-PHRASE-ENROLLMENT method must be invoked before

these headers may be set through the "SET-PARAMS" method or retrieved

through the "GET-PARAMS" method.

Note that the waveform-uri header of the Recognizer resource can also

appear in the response to the END-PHRASE-ENROLLMENT method.

9.4.1.  Confidence Threshold

When a recognition resource recognizes or matches a spoken phrase

with some portion of the grammar, it associates a confidence level

with that match.  The confidence-threshold header tells the

recognizer resource what confidence level the client considers a

successful match.  This is a float value between 0.0-1.0 indicating

the recognizer's confidence in the recognition.  If the recognizer

determines that there is no candidate match with a confidence that is

greater than the confidence threshold, then it MUST return no-match

as the recognition result.  This header MAY occur in RECOGNIZE,

"SET-PARAMS" or "GET-PARAMS".  The default value for this header is

implementation specific.

confidence-threshold     =  "Confidence-Threshold" ":" FLOAT CRLF

9.4.2.  Sensitivity Level

To filter out background noise and not mistake it for speech, the

recognizer may support a variable level of sound sensitivity.  The

sensitivity-level header is a float value between 0.0 and 1.0 and

allows the client to set the sensitivity level for the recognizer.

This header MAY occur in RECOGNIZE, "SET-PARAMS" or "GET-PARAMS".  A

higher value for this header means higher sensitivity.  The default

value for this header is implementation specific.

Shanmugham & Burnett    Expires September 6, 2007              [Page 73]

Internet-Draft                   MRCPv2                       March 2007

sensitivity-level        =  "Sensitivity-Level" ":" FLOAT CRLF

9.4.3.  Speed Vs Accuracy

Depending on the implementation and capability of the recognizer

resource it may be tunable towards Performance or Accuracy.  Higher

accuracy may mean more processing and higher CPU utilization, meaning

fewer active sessions per server and vice versa.  The value is a

float between 0.0 and 1.0.  A value of 0.0 means fastest recognition.

A value of 1.0 means best accuracy.  This header MAY occur in

RECOGNIZE, "SET-PARAMS" or "GET-PARAMS".  The default value for this

header is implementation specific.

speed-vs-accuracy        =  "Speed-Vs-Accuracy" ":" FLOAT CRLF

9.4.4.  N Best List Length

When the recognizer matches an incoming stream with the grammar, it

may come up with more than one alternative match because of

confidence levels in certain words or conversation paths.  If this

header is not specified, by default, the recognition resource returns

only the best match above the confidence threshold.  The client, by

setting this header, can ask the recognition resource to send it more

than 1 alternative.  All alternatives must still be above the

confidence-threshold.  A value greater than one does not guarantee

that the recognizer will provide the requested number of

alternatives.  This header MAY occur in RECOGNIZE, "SET-PARAMS" or

"GET-PARAMS".  The minimum value for this header is 1.  The default

value for this header is 1.

n-best-list-length       =  "N-Best-List-Length" ":" 1*DIGIT CRLF

9.4.5.  Input Type

When the recognizer detects barge-in-able input and generates a

START-OF-INPUT event, that event MUST carry this header field to

specify where the input that caused the barge-in was DTMF or speech.

.

input-type         =  "Input-Type" ":"  inputs CRLF

inputs             =  "speech" / "dtmf"

9.4.6.  No Input Timeout

When recognition is started and there is no speech detected for a

certain period of time, the recognizer can send a RECOGNITION-

COMPLETE event to the client with a Completion-Status of "002 no-

input-timeout" and terminate the recognition operation.  The client

Shanmugham & Burnett    Expires September 6, 2007              [Page 74]

Internet-Draft                   MRCPv2                       March 2007

can use the no-input-timeout header to set this timeout.  The value

is in milliseconds and may range from 0 to an implementation specific

maximum value.  This header MAY occur in RECOGNIZE, "SET-PARAMS" or

"GET-PARAMS".  The default value is implementation specific.

no-input-timeout         =  "No-Input-Timeout" ":" 1*DIGIT CRLF

9.4.7.  Recognition Timeout

When recognition is started and there is no match for a certain

period of time, the recognizer can send a RECOGNITION-COMPLETE event

to the client and terminate the recognition operation.  For regular

recognition, this timer is started when a START-OF-INPUT event is

generated by the resource.  When this timer expires and there is a

partial match to a grammar the recognition request completes with a

status code of "008 success-maxtime".  For hotword mode recognition,

this timer is started when the user begins speaking.  Note that for

Hotword mode recognition the START-OF-INPUT event is not generated.

When this timer expires the recognition request completes with a

status code of "003 recognition-timeout".  The recognition-timeout

header allows the client to set this timeout value.  The value is in

milliseconds.  The value for this header ranges from 0 to an

implementation specific maximum value.  The default value is 10

seconds.  This header MAY occur in RECOGNIZE, SET-PARAMS or GET-

PARAMS.  """"

recognition-timeout      =  "Recognition-Timeout" ":" 1*DIGIT CRLF

9.4.8.  Waveform URI

If the save-waveform header is set to true, the recognizer MUST

record the incoming audio stream of the recognition into a stored

form and provide a URI for the client to access it.  This header MUST

be present in the RECOGNITION-COMPLETE event if the save-waveform

header was set to true.  The URI value of the header MUST be NULL if

there was some error condition preventing the server from recording.

Otherwise, the URI generated by the server MUST be unambiguous across

the server and all its recognition sessions.  The content associated

with the URI MUST be available to the client until the MRCPv2 session

terminates.

Similarly, if the save-best-waveform header is set to true, the

recognizer MUST save the audio stream for the best repetition of the

phrase that was used during the enrollment session.  The recognizer

MUST then record the recognized audio and make it available to the

client in the form of a URI returned in the waveform-uri header in

the response to the END-PHRASE-ENROLLMENT method.  The URI value of

the header MUST be NULL if there was some error condition preventing

Shanmugham & Burnett    Expires September 6, 2007              [Page 75]

Internet-Draft                   MRCPv2                       March 2007

the server from recording.  Otherwise, the URI generated by the

server MUST be unambiguous across the server and all its recognition

sessions.  The content associated with the URI MUST be available to

the client until the MRCPv2 session terminates.

The server MUST also return the size in bytes and the duration in

milliseconds of the recorded audio wave-form as parameters associated

with the header.

waveform-uri             =  "Waveform-URI" ":" "<" Uri ">"

";" "size" "=" 1*DIGIT

";" "duration" "=" 1*DIGIT CRLF

9.4.9.  Media Type

This header MAY be specified in the SET-PARAMS, GET-PARAMS or the

RECOGNIZE methods and tells the server resource the MIME content type

in which to store captured audio or video such as the one captured

and returned by the Waveform-URI header.

Media-type               =  "Media-Type" ":" media-type-value

CRLF

9.4.10.  Input-Waveform-URI

This optional header specifies a URI pointing to audio content to be

processed by the RECOGNIZE operation.  This enables the client to

request recognition from a specified buffer or audio file.

input-waveform-uri       =  "Input-Waveform-URI" ":" Uri CRLF

9.4.11.  Completion Cause

This header MUST be part of a RECOGNITION-COMPLETE, event coming from

the recognizer resource to the client.  It indicates the reason

behind the RECOGNIZE method completion.  This header MUST be sent in

the DEFINE-GRAMMAR and RECOGNIZE responses, if they return with a

failure status and a COMPLETE state.

completion-cause         =  "Completion-Cause" ":" 1*DIGIT SP

1*VCHAR CRLF

Shanmugham & Burnett    Expires September 6, 2007              [Page 76]

Internet-Draft                   MRCPv2                       March 2007

+---------+--------------------------+------------------------------+

| Cause-C | Cause-Name               | Description                  |

| ode     |                          |                              |

+---------+--------------------------+------------------------------+

| 000     | success                  | RECOGNIZE completed with a   |

|         |                          | match or DEFINE-GRAMMAR      |

|         |                          | succeeded in downloading and |

|         |                          | compiling the grammar        |

| 001     | no-match                 | RECOGNIZE completed, but no  |

|         |                          | match was found              |

| 002     | no-input-timeout         | RECOGNIZE completed without  |

|         |                          | a match due to a             |

|         |                          | no-input-timeout             |

| 003     | hotword-maxtime          | RECOGNIZE in hotword mode    |

|         |                          | completed without a match    |

|         |                          | due to a recognition-timeout |

| 004     | grammar-load-failure     | RECOGNIZE failed due grammar |

|         |                          | load failure.                |

| 005     | grammar-compilation-fail | RECOGNIZE failed due to      |

|         | ure                      | grammar compilation failure. |

| 006     | recognizer-error         | RECOGNIZE request terminated |

|         |                          | prematurely due to a         |

|         |                          | recognizer error.            |

| 007     | speech-too-early         | RECOGNIZE request terminated |

|         |                          | because speech was too       |

|         |                          | early.  This happens when    |

|         |                          | the audio stream is already  |

|         |                          | "in-speech" when the         |

|         |                          | RECOGNIZE request was        |

|         |                          | received.                    |

| 008     | success-maxtime          | RECOGNIZE request terminated |

|         |                          | because speech was too long  |

|         |                          | but whatever was spoken till |

|         |                          | that point was a full match. |

| 009     | uri-failure              | Failure accessing a URI.     |

| 010     | language-unsupported     | Language not supported.      |

| 011     | cancelled                | A new RECOGNIZE cancelled    |

|         |                          | this one, or a prior         |

|         |                          | RECOGNIZE failed while this  |

|         |                          | one was still in the queue.  |

| 012     | semantics-failure        | Recognition succeeded but    |

|         |                          | semantic interpretation of   |

|         |                          | the recognized input failed. |

|         |                          | The RECOGNITION-COMPLETE     |

|         |                          | event MUST contain the       |

|         |                          | Recognition result with only |

|         |                          | input text and no            |

|         |                          | interpretation.              |

Shanmugham & Burnett    Expires September 6, 2007              [Page 77]

Internet-Draft                   MRCPv2                       March 2007

| 013     | partial-match            | Speech Incomplete timeout    |

|         |                          | expired before there was a   |

|         |                          | full match.  But whatever    |

|         |                          | that was spoken till that    |

|         |                          | point was a partial match to |

|         |                          | one or more grammars.        |

| 014     | partial-match-maxtime    | The Recognition-Timer        |

|         |                          | expired before full match    |

|         |                          | was achieved.  But whatever  |

|         |                          | was spoken till that point   |

|         |                          | was a partial match to one   |

|         |                          | or more grammars.            |

| 015     | no-match-maxtime         | The Recognition-Timer        |

|         |                          | expired.  Whatever was       |

|         |                          | spoken till that point       |

|         |                          | either did not match any of  |

|         |                          | the grammars.  This cause    |

|         |                          | could also be returned if    |

|         |                          | the recognizer does not      |

|         |                          | support detecting partial    |

|         |                          | grammar matches.             |

| 016     | grammar-definition-failu | any DEFINE-GRAMMAR error     |

|         | re                       | other than                   |

|         |                          | grammar-load-failure and     |

|         |                          | grammar-compilation-failure. |

+---------+--------------------------+------------------------------+

9.4.12.  Completion Reason

This header MAY be specified in a RECOGNITION-COMPLETE event coming

from the recognizer resource to the client.  This contains the reason

text behind the RECOGNIZE request completion.  This header can be use

to communicate text describing the reason for the failure, such as

the specific error encountered in parsing a grammar markup.

The completion reason text is provided for client use in logs and for

debugging and instrumentation purposes.  Clients are NOT REQUIRED to

interpret the completion reason text.

completion-reason        =  "Completion-Reason" ":"

quoted-string CRLF

9.4.13.  Recognizer Context Block

This header MAY be sent as part of the "SET-PARAMS" or "GET-PARAMS"

request.  If the "GET-PARAMS" method contains this header with no

value, then it is a request to the recognizer to return the

recognizer context block.  The response to such a message MAY contain

Shanmugham & Burnett    Expires September 6, 2007              [Page 78]

Internet-Draft                   MRCPv2                       March 2007

a recognizer context block as a MIME message body.  If the server

returns a recognizer context block, the response MUST contain this

header and its value MUST match the Content-ID of the corresponding

MIME body.

If the "SET-PARAMS" method contains this header, it MUST also contain

a message body containing the recognizer context data, and a

Content-ID matching this header value.  This Content-ID MUST match

the Content-ID that came with the context data during the

"GET-PARAMS" operation.

An implementation choosing to use this mechanism to hand off

recognizer context data between servers MUST distinguish its

implementation-specific block of data by using an IANA-registered

content type in the IANA MIME vendor tree.

recognizer-context-block  =  "Recognizer-Context-Block" ":"

1*VCHAR CRLF

9.4.14.  Start Input Timers

This header MAY be sent as part of the RECOGNIZE request.  A value of

false tells the recognizer to start recognition, but not to start the

no-input timer yet.  The recognizer MUST NOT start the timers until

the client sends a START-INPUT-TIMERS request to the recognizer.

This is useful in the scenario when the recognizer and synthesizer

engines are not part of the same session.  In such configurations,

when a kill-on-barge-in prompt is being played, the client wants the

RECOGNIZE request to be simultaneously active so that it can detect

and implement kill-on-barge-in.  However, the recognizer ought not

start the no-input timers until the prompt is finished.  The default

value is "true".

start-input-timers  =  "Start-Input-Timers" ":" boolean-value CRLF

9.4.15.  Speech Complete Timeout

This header specifies the length of silence required following user

speech before the speech recognizer finalizes a result (either

accepting it or generating a nomatch event).  The speech-complete-

timeout value applies when the recognizer currently has a complete

match against an active grammar, and specifies how long the

recognizer MUST wait for more input before declaring a match.  By

contrast, the incomplete timeout is used when the speech is an

incomplete match to an active grammar.  The value is in milliseconds.

speech-complete-timeout = "Speech-Complete-Timeout" ":" 1*DIGIT CRLF

Shanmugham & Burnett    Expires September 6, 2007              [Page 79]

Internet-Draft                   MRCPv2                       March 2007

A long speech-complete-timeout value delays the result to the client

and therefore makes the application's response to a user slow.  A

short speech-complete-timeout may lead to an utterance being broken

up inappropriately.  Reasonable speech complete timeout values are

typically in the range of 0.3 seconds to 1.0 seconds.  The value for

this header ranges from 0 to an implementation specific maximum

value.  The default value for this header is implementation specific.

This header MAY occur in RECOGNIZE, "SET-PARAMS" or "GET-PARAMS".

9.4.16.  Speech Incomplete Timeout

This header specifies the required length of silence following user

speech after which a recognizer finalizes a result.  The incomplete

timeout applies when the speech prior to the silence is an incomplete

match of all active grammars.  In this case, once the timeout is

triggered, the partial result is rejected (with a Completion-Cause of

"partial-match").  The value is in milliseconds.  The value for this

header ranges from 0 to an implementation specific maximum value.

The default value for this header is implementation specific.

speech-incomplete-timeout = "Speech-Incomplete-Timeout" ":" 1*DIGIT

CRLF

The speech-incomplete-timeout also applies when the speech prior to

the silence is a complete match of an active grammar, but where it is

possible to speak further and still match the grammar.  By contrast,

the complete timeout is used when the speech is a complete match to

an active grammar and no further spoken words can continue to

represent a match.

A long speech-incomplete-timeout value delays the result to the

client and therefore makes the application's response to a user slow.

A short speech-incomplete-timeout may lead to an utterance being

broken up inappropriately.

The speech-incomplete-timeout is usually longer than the speech-

complete-timeout to allow users to pause mid-utterance (for example,

to breathe).  This header MAY occur in RECOGNIZE, "SET-PARAMS" or

"GET-PARAMS".

9.4.17.  DTMF Interdigit Timeout

This header specifies the inter-digit timeout value to use when

recognizing DTMF input.  The value is in milliseconds.  The value for

this header ranges from 0 to an implementation specific maximum

value.  The default value is 5 seconds.  This header MAY occur in

RECOGNIZE, "SET-PARAMS" or "GET-PARAMS".

Shanmugham & Burnett    Expires September 6, 2007              [Page 80]

Internet-Draft                   MRCPv2                       March 2007

dtmf-interdigit-timeout = "DTMF-Interdigit-Timeout" ":" 1*DIGIT CRLF

9.4.18.  DTMF Term Timeout

This header specifies the terminating timeout to use when recognizing

DTMF input.  The DTMF-Term-Timeout applies only when no additional

input is allowed by the grammar; otherwise, the DTMF-Interdigit-

Timeout applies.  The value is in milliseconds.  The value for this

header ranges from 0 to an implementation specific maximum value.

The default value is 10 seconds.  This header MAY occur in RECOGNIZE,

"SET-PARAMS" or "GET-PARAMS".

dtmf-term-timeout        =  "DTMF-Term-Timeout" ":" 1*DIGIT CRLF

9.4.19.  DTMF-Term-Char

This header specifies the terminating DTMF character for DTMF input

recognition.  The default value is NULL which is indicated by an

empty header value.  This header MAY occur in RECOGNIZE, "SET-PARAMS"

or "GET-PARAMS".

dtmf-term-char           =  "DTMF-Term-Char" ":" VCHAR CRLF

9.4.20.  Failed URI

When a recognizer needs to fetch or access a URI and the access fails

the server SHOULD provide the failed URI in this header in the method

response, unless there are multiple URI failures, in which case one

of the failed URIs MUST be provided in this header in the method

response.

failed-uri               =  "Failed-URI" ":" Uri CRLF

9.4.21.  Failed URI Cause

When a recognizer method needs a recognizer to fetch or access a URI

and the access fails the server MUST provide the URI specific or

protocol specific response code for the URI in the Failed-URI header

through this header in the method response.  The value encoding is

alphanumeric to accommodate all anticipated access protocols, some of

which might have a response string instead of a numeric response

code.

failed-uri-cause         =  "Failed-URI-Cause" ":" 1*alphanum CRLF

Shanmugham & Burnett    Expires September 6, 2007              [Page 81]

Internet-Draft                   MRCPv2                       March 2007

9.4.22.  Save Waveform

This header allows the client to request the recognizer resource to

save the audio input to the recognizer.  The recognizer resource MUST

then attempt to record the recognized audio, without end-pointing,

and make it available to the client in the form of a URI returned in

the waveform-uri header in the RECOGNITION-COMPLETE event.  If there

was an error in recording the stream or the audio content is

otherwise not available, the recognizer MUST return an empty

waveform-uri header.  The default value for this field is "false".

save-waveform            =  "Save-Waveform" ":" boolean-value CRLF

9.4.23.  New Audio Channel

This header MAY be specified in a RECOGNIZE request and allows the

client to tell the server that, from this point on, further input

audio comes from a different audio source, channel or speaker.  If

the recognition resource had collected any input statistics or

adaptation state, the recognition resource MUST do what is

appropriate for the specific recognition technology, which includes

but is not limited to discarding any collected input statistics or

adaptation state before starting the RECOGNIZE request.  Note that if

there are multiple resources that are sharing a media pipe and are

collecting or using this data, and the client issues this header to

one of the resources, the reset operation applies to all resources

that use the shared media stream.  This helps in a number of use

cases, including where the client wishes to reuse an open recognition

session with an existing media session for multiple telephone calls.

new-audio-channel        =  "New-Audio-Channel" ":" boolean-value

CRLF

9.4.24.  Speech-Language

This header specifies the language of recognition grammar data within

a session or request, if it is not specified within the data.  The

value of this header MUST follow RFC4646 [17] for its values.  This

MAY occur in DEFINE-GRAMMAR, RECOGNIZE, "SET-PARAMS" or "GET-PARAMS"

request.

speech-language          =  "Speech-Language" ":" 1*VCHAR CRLF

9.4.25.  Ver-Buffer-Utterance

This header lets the client request the server to buffer the

utterance associated with this recognition request into a buffer

available to a co-resident verification resource.  The buffer is

Shanmugham & Burnett    Expires September 6, 2007              [Page 82]

Internet-Draft                   MRCPv2                       March 2007

shared across resources within a session and is allocated when a

verification resource is added to this session.  The client MUST NOT

send this header unless a verification resource is instantiated for

the session.  The buffer is released when the verification resource

is released from the session.

9.4.26.  Recognition-Mode

This header specifies what mode the RECOGNIZE method will operate in.

The value choices are "normal" or "hotword".  If the value is

"normal", the RECOGNIZE starts matching speech and DTMF to the

grammars specified in the RECOGNIZE request.  If any portion of the

speech does not match the grammar, the RECOGNIZE command completes

with a no-match status.  Timers may be active to detect speech in the

audio (see Section 9.4.14), so the RECOGNIZE method may complete

because of a timeout waiting for speech.  If the value of this header

is "hotword", the RECOGNIZE method operates in hotword mode, where it

only looks for the particular keywords or DTMF sequences specified in

the grammar and ignores silence or other speech in the audio stream.

The default value for this header is "normal".

recognition-mode         =  "Recognition-Mode" ":" 1*ALPHA CRLF

9.4.27.  Cancel-If-Queue

This header specifies what will happen if the client attempts to

invoke another RECOGNIZE method when this RECOGNIZE request is

already in progress for the resource.  The value for this header is

Boolean.  A value of "true" means the server MUST terminate this

RECOGNIZE request, with a Completion-Cause of "cancelled", if the

client issues another RECOGNIZE request for the same resource.  A

value of "false" for this header indicates to the server that this

RECOGNIZE request will continue to completion and if the client

issues more RECOGNIZE requests to the same resource, they are queued.

When the currently active RECOGNIZE request is stopped or completes

with a successful match, the first RECOGNIZE method in the queue

becomes active.  If the current RECOGNIZE fails, all RECOGNIZE

methods in the pending queue are cancelled and each generates a

RECOGNITION-COMPLETE event with a Completion-Cause of "cancelled".

This header MUST be present in every RECOGNIZE request.  There is no

default value.

cancel-if-queue          =  "Cancel-If-Queue" ":" Boolean-value CRLF

Shanmugham & Burnett    Expires September 6, 2007              [Page 83]

Internet-Draft                   MRCPv2                       March 2007

9.4.28.  Hotword-Max-Duration

This header MAY be sent in a hotword mode RECOGNIZE request.  It

specifies the maximum length of an utterance (in seconds) that will

be considered for Hotword recognition.  This header, along with

Hotword-Min-Duration, can be used to tune performance by preventing

the recognizer from evaluating utterances that are too short or too

long to be one of the hotwords in the grammar(s).  The value is in

milliseconds.  The default is implementation dependent.  If present

in a RECOGNIZE request specifying a mode other than "hotword", the

header is ignored.

hotword-max-duration     =  "Hotword-Max-Duration" ":" 1*DIGIT

CRLF

9.4.29.  Hotword-Min-Duration

This header MAY be sent in a hotword mode RECOGNIZE request.  It

specifies the minimum length of an utterance (in seconds) that will

be considered for Hotword recognition.  This header, along with

Hotword-Max-Duration, can be used to tune performance by preventing

the recognizer from evaluating utterances that are too short or too

long to be one of the hotwords in the grammar(s).  The value is in

milliseconds.  The default value is implementation dependent.  If

present in a RECOGNIZE request specifying a mode other than

"hotword", the header is ignored.

hotword-min-duration     =  "Hotword-Min-Duration" ":" 1*DIGIT CRLF

9.4.30.  Interpret-Text

This header is used to provide a pointer to the text for which a

natural language interpretation is desired.  The value is a

Content-ID that refers to a MIME entity of type plain/text in the

body of the message.  This header MUST be used when invoking the

INTERPRET method.

interpret-text           =  "Interpret-Text" ":" 1*VCHAR CRLF

9.4.31.  DTMF-Buffer-Time

This header MAY be specified in a GET-PARAMS or SET-PARAMS method and

is used to specify the size in time, in milliseconds, of the

typeahead buffer for the recognizer.  This is the buffer that

collects DTMF digits as they are pressed even when there is no

RECOGNIZE command active.  When a subsequent RECOGNIZE method is

received it MAY look to this buffer to match the RECOGNIZE request.

If the digits in the buffer is not sufficient then it can continue to

Shanmugham & Burnett    Expires September 6, 2007              [Page 84]

Internet-Draft                   MRCPv2                       March 2007

listen to more digits to match the grammar.  The default size of this

DTMF buffer is platform specific.

dtmf-buffer-time  =  "DTMF-Buffer-Time" ":" 1*DIGIT CRLF

9.4.32.  Clear-DTMF-Buffer

This header MAY be specified in a RECOGNIZE method and is used to

tell the recognizer to clear the DTMF type-ahead buffer before

starting the recognize.  The default value of this header is FALSE,

which does not clear the typeahead buffer before starting the

RECOGNIZE method.  If this header is specified to be TRUE, then the

recognize will clear the DTMF buffer before starting recognition.

This means digits pressed by the caller before the RECOGNIZE command

was issued are discarded.

clear-dtmf-buffer  = "Clear-DTMF-Buffer" ":" boolean-value CRLF

9.4.33.  Early-No-Match

This header MAY be specified in a RECOGNIZE method and is used to

tell the recognizer that it MUST not wait for the end of speech

before processing the collected speech to match active grammars.  A

value of TRUE indicates the recognizer MUST do early matching.  The

default value for this header if not specified is FALSE.  If the

recognizer does not support the processing of the collected audio

before the end of speech this header field can be safely ignored.

early-no-match  = "Early-No-Match" ":" boolean-value CRLF

9.4.34.  Num-Min-Consistent-Pronunciations

This header MAY be specified in a START-PHRASE-ENROLLMENT,

"SET-PARAMS", or "GET-PARAMS" method and is used to specify the

minimum number of consistent pronunciations that must be obtained to

voice enroll a new phrase.  The minimum value is 1.  The default

value is implementation specific and MAY be greater than 1.

num-min-consistent-pronunciations  =

"Num-Min-Consistent-Pronunciations" ":" 1*DIGIT CRLF

9.4.35.  Consistency-Threshold

This header MAY be sent as part of the START-PHRASE-ENROLLMENT,

"SET-PARAMS", or "GET-PARAMS" method.  Used during voice-enrollment,

this header specifies how similar to a previously enrolled

pronunciation of the same phrase an utterance needs to be in order to

be considered "consistent."  The higher the threshold, the closer the

Shanmugham & Burnett    Expires September 6, 2007              [Page 85]

Internet-Draft                   MRCPv2                       March 2007

match between an utterance and previous pronunciations must be for

the pronunciation to be considered consistent.  The range for this

threshold is a float value between is 0.0 to 1.0.  The default value

for this header is implementation specific.

consistency-threshold    =  "Consistency-Threshold" ":" FLOAT CRLF

9.4.36.  Clash-Threshold

This header MAY be sent as part of the START-PHRASE-ENROLLMENT, SET-

PARAMS, or "GET-PARAMS" method.  Used during voice-enrollment, this

header specifies how similar the pronunciations of two different

phrases can be before they are considered to be clashing.  For

example, pronunciations of phrases such as "John Smith" and "Jon

Smits" may be so similar that they are difficult to distinguish

correctly.  A smaller threshold reduces the number of clashes

detected.  The range for this threshold is float value between 0.0

and 1.0.  The default value for this header is implementation

specific.  Clash testing can be turned off completely by setting the

Clash-Threshold header value to 0.

clash-threshold          =  "Clash-Threshold" ":" 1*DIGIT CRLF

9.4.37.  Personal-Grammar-URI

This header specifies the speaker-trained grammar to be used or

referenced during enrollment operations.  Phrases are added to this

grammar during enrollment.  For example, a contact list for user

"Jeff" could be stored at the Personal-Grammar-URI

"http://myserver.example.com/myenrollmentdb/jeff-list".  The

generated grammar syntax MAY be implementation specific.  There is no

default value for this header.

personal-grammar-uri     =  "Personal-Grammar-URI" ":" Uri CRLF

9.4.38.  Enroll-Utterance

This header MAY be specified in the RECOGNIZE method.  If this header

is set to "true" and an Enrollment is active, the RECOGNIZE command

MUST add the collected utterance to the personal grammar that is

being enrolled.  The default value for this header is "false".

enroll-utterance     =  "Enroll-Utterance" ":" Boolean-Value CRLF

Shanmugham & Burnett    Expires September 6, 2007              [Page 86]

Internet-Draft                   MRCPv2                       March 2007

9.4.39.  Phrase-Id

This header in a request identifies a phrase in an existing personal

grammar for which enrollment is desired.  It is also returned to the

client in the RECOGNIZE complete event.  This header MAY occur in

START-PHRASE-ENROLLMENT, MODIFY-PHRASE or DELETE-PHRASE requests.

There is no default value for this header.

phrase-id                =  "Phrase-ID" ":" 1*VCHAR CRLF

9.4.40.  Phrase-NL

This string specifies the interpreted text to be returned when the

phrase is recognized.  This header MAY occur in START-PHRASE-

ENROLLMENT and MODIFY-PHRASE requests.  There is no default value for

this header.

phrase-nl                =  "Phrase-NL" ":" 1*UTFCHAR CRLF

9.4.41.  Weight

The value of this header represents the occurrence likelihood of a

phrase in an enrolled grammar.  When using grammar enrollment, the

system is essentially constructing a grammar segment consisting of a

list of possible match phrases.  This can be thought of to be similar

to the dynamic construction of a <one-of> tag in the W3C grammar

specification.  Each enrolled-phrase becomes an item in the list that

can be matched against spoken input similar to the <item> within a

<one-of> list.  This header allows you to assign a wait to the

phrase(i.e <item> entry) in the <one-of> list that is enrolled.

Grammar weights are normalized to a sum of one at grammar compilation

time, so a weight value of 1 for each phrase in an enrolled grammar

list indicates all items in that list have the same weight.  This

header MAY occur in START-PHRASE-ENROLLMENT and MODIFY-PHRASE

requests.  The default value for this header is implementation

specific.

weight                   =  "Weight" ":" weight-value CRLF

9.4.42.  Save-Best-Waveform

This header allows the client to request the recognizer resource to

save the audio stream for the best repetition of the phrase that was

used during the enrollment session.  The recognizer MUST attempt to

record the recognized audio and make it available to the client in

the form of a URI returned in the waveform-uri header in the response

to the END-PHRASE-ENROLLMENT method.  If there was an error in

recording the stream or the audio data is otherwise not available,

Shanmugham & Burnett    Expires September 6, 2007              [Page 87]

Internet-Draft                   MRCPv2                       March 2007

the recognizer MUST return an empty waveform-uri header.

save-best-waveform  =  "Save-Best-Waveform" ":" Boolean-value CRLF

9.4.43.  New-Phrase-Id

This header replaces the id used to identify the phrase in a personal

grammar.  The recognizer returns the new id when using an enrollment

grammar.  This header MAY occur in MODIFY-PHRASE requests.

new-phrase-id            =  "New-Phrase-ID" ":" 1*VCHAR CRLF

9.4.44.  Confusable-Phrases-URI

This header specifies a grammar that defines invalid phrases for

enrollment.  For example, typical applications do not allow an

enrolled phrase that is also a command word.  This header MAY occur

in RECOGNIZE requests that are part of an enrollment session.

confusable-phrases-uri   =  "Confusable-Phrases-URI" ":" Uri CRLF

9.4.45.  Abort-Phrase-Enrollment

This header can optionally be specified in the END-PHRASE-ENROLLMENT

method to abort the phrase enrollment, rather than committing the

phrase to the personal grammar.

abort-phrase-enrollment  =  "Abort-Phrase-Enrollment" ":"

Boolean-value CRLF

9.5.  Recognizer Message Body

A recognizer message may carry additional data associated with the

request, response or event.  The client may provide the grammar to be

recognized in DEFINE-GRAMMAR or RECOGNIZE requests.  When one or more

grammars are specified using the DEFINE-GRAMMAR method, the server

MUST attempt to fetch, compile and optimize the grammar before

returning a response to the DEFINE-GRAMMAR method.  A RECOGNIZE

request MUST completely specify the grammars to be active during the

recognition operation, except when the RECOGNIZE method is being used

to enroll a grammar.  During grammar enrollment, such grammars are

optional.  The server resource may send the recognition results in

the RECOGNITION-COMPLETE event or the GET-RESULT response.  Grammars

and recognition results are carried in the message body of the

corresponding MRCPv2 messages.

Shanmugham & Burnett    Expires September 6, 2007              [Page 88]

Internet-Draft                   MRCPv2                       March 2007

9.5.1.  Recognizer Grammar Data

Recognizer grammar data from the client to the server can be provided

inline or by reference.  Either way, grammar data is carried as MIME

entities in the message body of the RECOGNIZE or DEFINE-GRAMMAR

request.  All MRCPv2 servers MUST accept grammars in the XML form

(MIME-type application/srgs+xml) of the W3C's XML-based Speech

Grammar Markup Format (SRGS) [25] and MAY accept grammars in other

formats.  Examples include but are not limited to:

o  the ABNF form (MIME-type application/srgs) of SRGS

o  Sun's Java Speech Grammar Format [32]

Additionally, MRCPv2 servers MAY support the Semantic Interpretation

for Speech Recognition (SISR) [26] specification.

When a grammar is specified inline in the request, the client MUST

provide a Content-ID for that grammar as part of the content headers.

If there is no space on the server to store the inline grammar, the

request MUST return with a Completion-Cause code of 016 grammar-

definition-failure.  Otherwise, the server MUST associate the inline

grammar block with that Content-ID and MUST store it on the server

for the duration of the session.  However, if the Content-ID is

redefined later in the session through a subsequent DEFINE-GRAMMAR,

the inline grammar previously associated with the Content-ID MUST be

freed.  If the Content-ID is redefined through a subsequent DEFINE-

GRAMMAR with an empty message body (i.e. no grammar definition), then

in addition to freeing any grammar previously associated with the

Content-ID the server MUST clear all bindings and associations to the

Content-ID.  Unless and until subsequently redefined, this URI MUST

be interpreted by the server as one that has never been set.

Grammars that have been associated with a Content-ID can be

referenced through the ""session:"" URI scheme (see Section 13.6).

For example:

session:help@root-level.store

Grammar data MAY be specified using external URI references.  To do

so, the client uses a MIME body of type text/uri-list to list the one

or more URIs that point to the grammar data.  The client can use MIME

body of type text/grammar-ref-list if it wants to assign weights to

the list of grammar URI.  All MRCPv2 servers MUST support grammar

access using the HTTP and HTTPS uri schemes.

If the grammar data the client wishes to be used on a request

consists of a mix of URI and inline grammar data the client uses the

multipart/mixed MIME-type to embed the MIME-blocks for text/uri-list,

application/srgs or application/srgs+xml.  The character set and

encoding used in the grammar data are specified using to standard

MIME-type definitions.

Shanmugham & Burnett    Expires September 6, 2007              [Page 89]

Internet-Draft                   MRCPv2                       March 2007

When more than one grammar URI or inline grammar block is specified

in a message body of the RECOGNIZE request, the server interprets

this as a list of grammar alternatives to match against.

Content-Type:application/srgs+xml

Content-ID:<request1@form-level.store>

Content-Length:104

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0" root="request">

<!-- single language attachment to tokens -->

<rule id="yes">

<one-of>

<item xml:lang="fr-CA">oui</item>

<item xml:lang="en-US">yes</item>

</one-of>

</rule>

<!-- single language attachment to a rule expansion -->

<rule id="request">

may I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

<!-- multiple language attachment to a token -->

<rule id="people1">

<token lexicon="en-US,fr-CA"> Robert </token>

</rule>

<!-- the equivalent single-language attachment expansion -->

<rule id="people2">

<one-of>

<item xml:lang="en-US">Robert</item>

<item xml:lang="fr-CA">Robert</item>

</one-of>

</rule>

</grammar>

SRGS Grammar Example

Shanmugham & Burnett    Expires September 6, 2007              [Page 90]

Internet-Draft                   MRCPv2                       March 2007

Content-Type:text/uri-list

Content-Length:176

session:help@root-level.store

http://www.example.com/Directory-Name-List.grxml

http://www.example.com/Department-List.grxml

http://www.example.com/TAC-Contact-List.grxml

session:menu1@menu-level.store

Grammar Reference Example

Content-Type:multipart/mixed; boundary="break"

--break

Content-Type:text/uri-list

Content-Length:176

http://www.example.com/Directory-Name-List.grxml

http://www.example.com/Department-List.grxml

http://www.example.com/TAC-Contact-List.grxml

--break

Content-Type:application/srgs+xml

Content-ID:<request1@form-level.store>

Content-Length:104

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0">

<!-- single language attachment to tokens -->

<rule id="yes">

<one-of>

<item xml:lang="fr-CA">oui</item>

<item xml:lang="en-US">yes</item>

</one-of>

</rule>

<!-- single language attachment to a rule expansion -->

<rule id="request">

may I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

Shanmugham & Burnett    Expires September 6, 2007              [Page 91]

Internet-Draft                   MRCPv2                       March 2007

<!-- multiple language attachment to a token -->

<rule id="people1">

<token lexicon="en-US,fr-CA"> Robert </token>

</rule>

<!-- the equivalent single-language attachment expansion -->

<rule id="people2">

<one-of>

<item xml:lang="en-US">Robert</item>

<item xml:lang="fr-CA">Robert</item>

</one-of>

</rule>

</grammar>

--break--

Mixed Grammar Reference Example

9.5.2.  Recognizer Result Data

Recognition results are returned to the client in the message body of

the RECOGNITION-COMPLETE event or the GET-RESULT response message as

described in Section 6.3).  Element and attribute descriptions for

the recognition portion of the NLSML format are provided in

Section 9.6 with a normative definition of the schema in

Section 16.1.

Content-Type:application/nlsml+xml

Content-Length:104

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="http://theYesNoGrammar">

<interpretation>

<instance>

<ex:response>yes</ex:response>

</instance>

<input>ok</input>

</interpretation>

</result>

Result Example

Shanmugham & Burnett    Expires September 6, 2007              [Page 92]

Internet-Draft                   MRCPv2                       March 2007

9.5.3.  Enrollment Result Data

Enrollment results are returned to the client in the message body of

the RECOGNITION-COMPLETE event as described in Section 6.3).  Element

and attribute descriptions for the enrollment portion of the NLSML

format are provided in Section 9.7 with a normative definition of the

schema in Section 16.2.

9.5.4.  Recognizer Context Block

When a client changes servers while operating on the behalf of the

same incoming communication session, this header allows the client to

collect a block of opaque data from one server and provide it to

another server.  This capability is desirable if the client needs

different language support or because the server issued a redirect.

Here the first recognizer resource may have collected acoustic and

other data during its execution of recognition methods.  After a

server switch, communicating this data may allow the recognition

resource on the new server to provide better recognition.  This block

of data is implementation-specific and MUST be carried as MIME-type

application/octets in the body of the message.

This block of data is communicated in the "SET-PARAMS" and

"GET-PARAMS" method/response messages.  In the "GET-PARAMS" method,

if an empty recognizer-context-block header is present, then the

recognizer SHOULD return its vendor-specific context block, if any,

in the message body as a MIME-entity with a specific Content-ID.  The

Content-ID value MUST also be specified in the recognizer-context-

block header in the "GET-PARAMS" response.  The "SET-PARAMS" request

wishing to provide this vendor-specific data MUST send it in the

message body as a MIME-entity with the same Content-ID that it

received from the "GET-PARAMS".  The Content-ID MUST also be sent in

the recognizer-context-block header of the "SET-PARAMS" message.

Each speech recognition implementation choosing to use this mechanism

to hand off recognizer context data among servers MUST distinguish

its implementation-specific block of data from other implementations

by choosing a Content-ID that is recognizable among the participating

servers and unlikely to collide with values chosen by another

implementation.

9.6.  Recognizer Results

The recognizer portion of NLSML (see Section 6.3.1) represents

information automatically extracted from a user's utterances by a

semantic interpretation component, where "utterance" is to be taken

in the general sense of a meaningful user input in any modality

supported by the MRCPv2 implementation.

Shanmugham & Burnett    Expires September 6, 2007              [Page 93]

Internet-Draft                   MRCPv2                       March 2007

9.6.1.  Markup Functions

MRCPv2 recognition resources employ the Natural Language Semantics

Markup Language to interpret natural language speech input and to

format the interpretation for consumption by an MRCPv2 client.

The elements of the markup fall into the following general functional

categories: Interpretation, Side Information, and Multi-Modal

Integration.

9.6.1.1.  Interpretation

Elements and attributes represent the semantics of a user's

utterance, including the <result>, <interpretation>, and <instance>

elements.  The <result> element contains the full result of

processing one utterance.  It may contain multiple <interpretation>

elements if the interpretation of the utterance results in multiple

alternative meanings due to uncertainty in speech recognition or

natural language understanding.  There are at least two reasons for

providing multiple interpretations:

1.  the client application might have additional information, for

example, information from a database, that would allow it to

select a preferred interpretation from among the possible

interpretations returned from the semantic interpreter.

2.  a client-based dialog manager (e.g.  VXML) that was unable to

select between several competing interpretations could use this

information to go back to the user and find out what was

intended.  For example, it could issue a "SPEAK" request to a

synthesizer resource to emit "Did you say 'Boston' or 'Austin'?"

9.6.1.2.  Side Information

These are elements and attributes representing additional information

about the interpretation, over and above the interpretation itself.

Side information includes:

1.  Whether an interpretation was achieved (the <nomatch> element)

and the system's confidence in an interpretation (the

"confidence" attribute of <interpretation>).

2.  Alternative interpretations (<interpretation>)

3.  Input formats and ASR information: the <input> element,

representing the input to the semantic interpreter.

9.6.1.3.  Multi-Modal Integration

When more than one modality is available for input, the

interpretation of the inputs need to be coordinated.  The "mode"

attribute of <input> supports this by indicating whether the

utterance was input by speech, dtmf, pointing, etc.  The

Shanmugham & Burnett    Expires September 6, 2007              [Page 94]

Internet-Draft                   MRCPv2                       March 2007

"timestamp_start" and "timestamp_end" attributes of <interpretation>

also provide for temporal coordination by indicating when inputs

occurred.

9.6.2.  Overview of Recognizer Result Elements and their Relationships

The recognizer elements in NLSML fall into two categories:

1.  description of the input that was processed.

2.  description of the meaning which was extracted from the input.

Next to each element are its attributes.  In addition, some elements

can contain multiple instances of other elements.  For example, a

<result> can contain multiple <interpretations>, each of which is

taken to be an alternative.  Similarly, <input> can contain multiple

child <input> elements which are taken to be cumulative.  To

illustrate the basic usage of these elements, as a simple example,

consider the utterance "ok" (interpreted as "yes").  The example

illustrates how that utterance and its interpretation would be

represented in the NL Semantics markup.

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="http://theYesNoGrammar">

<interpretation>

<instance>

<ex:response>yes</ex:response>

</instance>

<input>ok</input>

</interpretation>

</result>

This example includes only the minimum required information.  There

is an overall <result> element which includes one interpretation and

an input element.  The interpretation contains the application-

specific element "<response>" which is the semantically interpreted

result.

9.6.3.  Elements and Attributes

9.6.3.1.  RESULT Root Element

The root element of the markup is <result>.  The <result> element

includes one or more <interpretation> elements.  Multiple

interpretations can result from ambiguities in the input or in the

semantic interpretation.  If the "grammar" attribute does not apply

to all of the interpretations in the result it can be overridden for

individual interpretations at the <interpretation> level.

Shanmugham & Burnett    Expires September 6, 2007              [Page 95]

Internet-Draft                   MRCPv2                       March 2007

Attributes:

1.  grammar: The grammar or recognition rule matched by this result.

The format of the grammar attribute will match the rule reference

semantics defined in the grammar specification.  Specifically,

the rule reference is in the external XML form for grammar rule

references.  The markup interpreter needs to know the grammar

rule that is matched by the utterance because multiple rules may

be simultaneously active.  The value is the grammar URI used by

the markup interpreter to specify the grammar.  The grammar can

be overridden by a grammar attribute in the <interpretation>

element if the input was ambiguous as to which grammar it

matched.  If all interpretation elements within the result

element contain carry their own grammar attributes, the attribute

can be dropped from the result element.

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

grammar="http://grammar">

<interpretation>

....

</interpretation>

</result>

9.6.3.2.  INTERPRETATION Element

An <interpretation> element contains a single semantic

interpretation.

Attributes:

1.  confidence: A float value from 0.0-1.0 indicating the semantic

analyzer's confidence in this interpretation.  A value of 1.0

indicates maximum confidence.  The values are implementation-

dependent, but are intended to align with the value

interpretation for the confidence MRCPv2 header defined in

Section 9.4.1.  This attribute is optional.

2.  grammar: The grammar or recognition rule matched by this

interpretation (if needed to override the grammar specification

at the <interpretation> level.)  This attribute is only needed

under <interpretation> if it is necessary to override a grammar

that was defined at the <result> level.)  Note that the grammar

attribute for the interpretation element is OPTIONAL if and only

if the grammar attribute is specified in the result element.

Interpretations MUST be sorted best-first by some measure of

"goodness".  The goodness measure is "confidence" if present,

otherwise, it is some implementation-specific indication of quality.

The grammar is expected to be specified most frequently at the

Shanmugham & Burnett    Expires September 6, 2007              [Page 96]

Internet-Draft                   MRCPv2                       March 2007

<result> level.  However, it can be overridden at the

<interpretation> level because it is possible that different

interpretations may match different grammar rules.

The <interpretation> element includes an optional <input> element

which contains the input being analyzed, and an <instance> element

containing the interpretation of the utterance.

<interpretation confidence="0.75" grammar="http://grammar">

...

</interpretation>

9.6.3.3.  INSTANCE Element

The <instance> element contains the interpretation of the utterance.

When the Semantic Interpretation for Speech Recognition format is

used, the <instance> element contains the XML serialization of the

ECMAScript result using the approach defined in that specification.

"When there is semantic markup in the grammar that does not create

semantic objects, but instead only does a semantic translation of a

portion of the input, such as translating "coke" to "coca-cola", the

instance contains the whole input but with the translation applied.

The NLSML looks like the markup in Figure 128 below.  If there are no

semantic objects created, nor any semantic translation the instance

value is the same as the input value.

Attributes:

1.  confidence: Each element of the instance may have a confidence

attribute, defined in the NL semantics namespace.  The confidence

attribute contains an float value in the range from 0.0-1.0

reflecting the system's confidence in the analysis of that slot.

A value of 1.0 indicates maximum confidence.  The values are

implementation-dependent, but are intended to align with the

value interpretation for the confidence MRCPv2 header defined in

Section 9.4.1.  This attribute is optional.

<instance>

<nameAddress>

<street confidence="75">123 Maple Street</street>

<city>Mill Valley</city>

<state>CA</state>

<zip>90952</zip>

</nameAddress>

</instance>

<input>

My address is 123 Maple Street,

Mill Valley, California, 90952

</input>

Shanmugham & Burnett    Expires September 6, 2007              [Page 97]

Internet-Draft                   MRCPv2                       March 2007

<instance>

I would like to buy a coca-cola

</instance>

<input>

I would like to buy a coke

</input>

Figure 128

9.6.3.4.  INPUT Element

The <input> element is the text representation of a user's input.  It

includes an optional "confidence" attribute which indicates the

recognizer's confidence in the recognition result (as opposed to the

confidence in the interpretation, which is indicated by the

"confidence" attribute of <interpretation>).  Optional "timestamp-

start" and "timestamp-end" attributes indicate the start and end

times of a spoken utterance, in ISO 8601 format.

Attributes:

1.  timestamp-start: The time at which the input began. (optional)

2.  timestamp-end: The time at which the input ended. (optional)

3.  mode: The modality of the input, for example, speech, dtmf, etc.

(optional)

4.  confidence: the confidence of the recognizer in the correctness

of the input in the range 0.0 to 1.0 (optional)

Note that it may not make sense for temporally overlapping inputs to

have the same mode; however, this constraint is not expected to be

enforced by implementations.

When there is no time zone designator, ISO 8601 time representations

default to local time.

There are three possible formats for the <input> element.

1.  The <input> element can contain simple text:

<input>onions</input>

A future possibility is for <input> to contain not only text but

additional markup that represents prosodic information that was

contained in the original utterance and extracted by the speech

recognizer.  This depends on the availability of ASR's that are

capable of producing prosodic information.  MRCPv2 clients MUST

be prepared to receive such markup but are NOT REQUIRED to act on

it.

2.  An <input> tag can also contain additional <input> tags.  Having

additional input elements allows the representation to support

future multi-modal inputs as well as finer-grained speech

information, such as timestamps for individual words and word-

level confidences.

Shanmugham & Burnett    Expires September 6, 2007              [Page 98]

Internet-Draft                   MRCPv2                       March 2007

<input>

<input mode="speech" confidence="0.5"

timestamp-start="2000-04-03T0:00:00"

timestamp-end="2000-04-03T0:00:00.2">fried</input>

<input mode="speech" confidence="1.0"

timestamp-start="2000-04-03T0:00:00.25"

timestamp-end="2000-04-03T0:00:00.6">onions</input>

</input>

3.  Finally, the <input> element can contain <nomatch> and <noinput>

elements, which describe situations in which the speech

recognizer received input that it was unable to process, or did

not receive any input at all, respectively.

9.6.3.5.  NOMATCH Element

The <nomatch> element under <input> is used to indicate that the

semantic interpreter was unable to successfully match any input with

confidence above the threshold.  It can optionally contain the text

of the best of the (rejected) matches.

<interpretation>

<instance/>

<input confidence="0.1">

<nomatch/>

</input>

</interpretation>

<interpretation>

<instance/>

<input mode="speech" confidence="0.1">

<nomatch>I want to go to New York</nomatch>

</input>

</interpretation>

9.6.3.6.  NOINPUT Element

<noinput> indicates that there was no input - a timeout occurred in

the speech recognizer due to silence.

<interpretation>

<instance/>

<input>

<noinput/>

</input>

</interpretation>

If there are multiple levels of inputs, the most natural place for

<nomatch> and <noinput> elements to appear is under the highest level

of <input> for <no input>, and under the appropriate level of

<interpretation> for <nomatch>.  So <noinput> means "no input at all"

Shanmugham & Burnett    Expires September 6, 2007              [Page 99]

Internet-Draft                   MRCPv2                       March 2007

and <nomatch> means "no match in speech modality" or "no match in

dtmf modality".  For example, to represent garbled speech combined

with dtmf "1 2 3 4", the markup would be:

<input>

<input mode="speech"><nomatch/></input>

<input mode="dtmf">1 2 3 4</input>

</input>

Note: while <noinput> could be represented as an attribute of input,

<nomatch> cannot, since it could potentially include PCDATA content

with the best match.  For parallelism, <noinput> is also an element.

9.7.  Enrollment Results

All enrollment elements are contained within a single <enrollment-

result> element under <result>.  The elements are described below and

have the schema defined in Section 16.2.  The following elements are

defined:

1.  num-clashes

2.  num-good-repetitions

3.  num-repetitions-still-needed

4.  consistency-status

5.  clash-phrase-ids

6.  transcriptions

7.  confusable-phrases

9.7.1.  NUM-CLASHES Element

The <num-clashes> element contains the number of clashes that this

pronunciation has with other pronunciations in an active enrollment

session.  The associated Clash-Threshold header determines the

sensitivity of the clash measurement.  Note that clash testing can be

turned off completely by setting the Clash-Threshold header value to

0.

9.7.2.  NUM-GOOD-REPETITIONS Element

The <num-good-repetitions> element contains the number of consistent

pronunciations obtained so far in an active enrollment session.

9.7.3.  NUM-REPETITIONS-STILL-NEEDED Element

The <num-repetitions-still-needed> element contains the number of

consistent pronunciations that must still be obtained before the new

phrase can be added to the enrollment grammar.  The number of

consistent pronunciations required is specified by the client in the

request header Num-Min-Consistent-Pronunciations.  The returned value

Shanmugham & Burnett    Expires September 6, 2007             [Page 100]

Internet-Draft                   MRCPv2                       March 2007

must be 0 before the client can successfully commit a phrase to the

grammar by ending the enrollment session.

9.7.4.  CONSISTENCY-STATUS Element

The <consistency-status> element is used to indicate how consistent

the repetitions are when learning a new phrase.  It can have the

values of consistent, inconsistent, and undecided.

9.7.5.  CLASH-PHRASE-IDS Element

The <clash-phrase-ids> element contains the phrase ids of clashing

pronunciation(s), if any.  This element is absent if there are no

clashes.

9.7.6.  TRANSCRIPTIONS Element

The <transcriptions> element contains the transcriptions returned in

the last repetition of the phrase being enrolled.

9.7.7.  CONFUSABLE-PHRASES Element

The <confusable-phrases> element contains a list of phrases from a

command grammar that are confusable with the phrase being added to

the personal grammar.  This element may be absent if there are no

confusable phrases.

9.8.  DEFINE-GRAMMAR

The DEFINE-GRAMMAR method, from the client to the server, provides

one or more grammars and requests the server to access, fetch, and

compile the grammars as needed.  The DEFINE-GRAMMAR method

implementation MUST do a fetch of all external URIs that are part of

that operation.  If caching is implemented, this URI fetching MUST

conform to the cache control hints and parameter headers associated

with the method in deciding whether it should be fetched from cache

or from the external server.  If these hints/parameters are not

specified in the method, the values set for the session using SET-

PARAMS/GET-PARAMS apply.  If it was not set for the session their

default values apply.

If the server resource is in the recognition state, the DEFINE-

GRAMMAR request MUST respond with a failure status.

If the resource is in the idle state and is able to successfully

process the supplied grammars the server the returned status MUST be

a success code and the request-state MUST be COMPLETE.

Shanmugham & Burnett    Expires September 6, 2007             [Page 101]

Internet-Draft                   MRCPv2                       March 2007

If the recognizer resource could not define the grammar for some

reason, for example if the download failed, the grammar failed to

compile, or the grammar was in an unsupported form, the MRCPv2

response for the DEFINE-GRAMMAR method MUST contain a failure status

code of 407, and contain a completion-cause header describing the

failure reason.

C->S:MRCP/2.0 589 DEFINE-GRAMMAR 543257

Channel-Identifier:32AECB23433801@speechrecog

Content-Type:application/srgs+xml

Content-ID:<request1@form-level.store>

Content-Length:104

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0">

<!-- single language attachment to tokens -->

<rule id="yes">

<one-of>

<item xml:lang="fr-CA">oui</item>

<item xml:lang="en-US">yes</item>

</one-of>

</rule>

<!-- single language attachment to a rule expansion -->

<rule id="request">

may I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

</grammar>

S->C:MRCP/2.0 73 543257 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

C->S:MRCP/2.0 334 DEFINE-GRAMMAR 543258

Channel-Identifier:32AECB23433801@speechrecog

Content-Type:application/srgs+xml

Content-ID:<helpgrammar@root-level.store>

Content-Length:104

Shanmugham & Burnett    Expires September 6, 2007             [Page 102]

Internet-Draft                   MRCPv2                       March 2007

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0">

<rule id="request">

I need help

</rule>

S->C:MRCP/2.0 73 543258 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

C->S:MRCP/2.0 723 DEFINE-GRAMMAR 543259

Channel-Identifier:32AECB23433801@speechrecog

Content-Type:application/srgs+xml

Content-ID:<request2@field-level.store>

Content-Length:104

<?xml version="1.0" encoding="UTF-8"?>

<!DOCTYPE grammar PUBLIC "-//W3C//DTD GRAMMAR 1.0//EN"

"http://www.w3.org/TR/speech-grammar/grammar.dtd">

<grammar xmlns="http://www.w3.org/2001/06/grammar" xml:lang="en"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/06/grammar

http://www.w3.org/TR/speech-grammar/grammar.xsd"

version="1.0" mode="voice" root="basicCmd">

<meta name="author" content="Stephanie Williams"/>

<rule id="basicCmd" scope="public">

<example> please move the window </example>

<example> open a file </example>

<ruleref

uri="http://grammar.example.com/politeness.grxml#startPolite"/>

<ruleref uri="#command"/>

<ruleref

uri="http://grammar.example.com/politeness.grxml#endPolite"/>

</rule>

<rule id="command">

<ruleref uri="#action"/> <ruleref uri="#object"/>

</rule>

Shanmugham & Burnett    Expires September 6, 2007             [Page 103]

Internet-Draft                   MRCPv2                       March 2007

<rule id="action">

<one-of>

<item weight="10"> open   <tag>open</tag>   </item>

<item weight="2">  close  <tag>close</tag>  </item>

<item weight="1">  delete <tag>delete</tag> </item>

<item weight="1">  move   <tag>move</tag>   </item>

</one-of>

</rule>

<rule id="object">

<item repeat="0-1">

<one-of>

<item> the </item>

<item> a </item>

</one-of>

</item>

<one-of>

<item> window </item>

<item> file </item>

<item> menu </item>

</one-of>

</rule>

</grammar>

S->C:MRCP/2.0 69 543259 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

C->S:MRCP/2.0 155 RECOGNIZE 543260

Channel-Identifier:32AECB23433801@speechrecog

N-Best-List-Length:2

Content-Type:text/uri-list

Content-Length:176

session:request1@form-level.store

session:request2@field-level.store

session:helpgramar@root-level.store

S->C:MRCP/2.0 48 543260 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

S->C:MRCP/2.0 48 START-OF-INPUT 543260 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

S->C:MRCP/2.0 486 RECOGNITION-COMPLETE 543260 COMPLETE

Shanmugham & Burnett    Expires September 6, 2007             [Page 104]

Internet-Draft                   MRCPv2                       March 2007

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

Waveform-URI:<http://web.media.com/session123/audio.wav>;

size=124535;duration=2340

Content-Type:applicationt/x-nlsml

Content-Length:276

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="session:request1@form-level.store">

<interpretation>

<instance name="Person">

<ex:Person>

<ex:Name> Andre Roy </ex:Name>

</ex:Person>

</instance>

<input>   may I speak to Andre Roy </input>

</interpretation>

</result>

Define Grammar Example

9.9.  RECOGNIZE

The RECOGNIZE method from the client to the server requests the

recognizer to start recognition and provides it with one or more

grammar references for grammars to match against the input media.

The RECOGNIZE method can carry headers to control the sensitivity,

confidence level and the level of detail in results provided by the

recognizer.  These header values override the current values set by a

previous "SET-PARAMS" method.

The RECOGNIZE method can request the recognizer resource to operate

in normal or hotword mode as specified by the Recognition-Mode

header.  The default value is "normal".  If the resource could not

start a recognition, the server MUST respond with a failure status

code of 407 and a completion-cause header in the response describing

the cause of failure.

The RECOGNIZE request uses the message body to specify the grammars

applicable to the request.  The active grammar(s) for the request can

be specified in one of 3 ways.  If the client needs to explicitly

control grammar weights for the recognition operation, it must employ

method 3 below.  The order of these grammars specifies the precedence

of the grammars which is used when more than one grammar in the list

matches the speech; in this case, the grammar with the higher

precedence is returned as a match.  This precedence capability is

Shanmugham & Burnett    Expires September 6, 2007             [Page 105]

Internet-Draft                   MRCPv2                       March 2007

useful in applications like VoiceXML browsers to order grammars

specified at the dialog, document and root level of a VoiceXML

application.

1.  The grammar may be placed directly in the message body using MIME

content.  If more than one grammar is included in the body, the

order of inclusion controls the corresponding precedence for the

grammars during recognition, with earlier grammars in the body

having a higher precedence than later ones.

2.  The body may contain a list of grammar URIs specified in a mime-

content of type text/uri-list.  The order of the URIs determines

the corresponding precedence for the grammars during recognition,

with highest-precedence first and decreasing for each URI

thereafter.

3.  The body may contain a list of grammar URIs specified in a mime-

content of type text/grammar-ref-list.  This mime type defines a

list of grammar URIs and allows each grammar URI to be assigned a

weight in the list.  This weight has the same meaning as the W3C

grammar weights.

In addition to performing recognition on the input, the recognizer

may also enroll the collected utterance in a personal grammar if the

Enroll-Utterance header is set to true and an Enrollment is active

(via an earlier execution of the START-PHRASE-ENROLLMENT method).  If

so, and if the RECOGNIZE request contains a Content-ID header, then

the resulting grammar (which includes the personal grammar as a sub-

grammar) can be referenced through the ""session:"" URI scheme (see

Section 13.6).

If the resource was able to successfully start the recognition, the

server MUST return a success code and a request-state of IN-PROGRESS.

This means that the recognizer is active and that the client MUST be

prepared to receive further events with this request-id.

If the resource was able to queue the request the server MUST return

a success code and request-state of PENDING.  This means that the

recognizer is currently active with another request and that this

request has been queued for processing.

If the resource could not start a recognition, the server MUST

respond with a failure status code of 407 and a completion-cause

header in the response describing the cause of failure.

For the recognizer resource, RECOGNIZE is the only request that

returns a request-state of IN-PROGRESS, meaning that recognition is

in progress.  When the recognition completes by matching one of the

grammar alternatives or by a time-out without a match or for some

other reason, the recognizer resource MUST send the client a

RECOGNITION-COMPLETE event with the result of the recognition and a

request-state of COMPLETE.

Shanmugham & Burnett    Expires September 6, 2007             [Page 106]

Internet-Draft                   MRCPv2                       March 2007

Large grammars can take a long time for the server to compile.  For

grammars which are used repeatedly, the client can improve server

performance by issuing a DEFINE-GRAMMAR request with the grammar

ahead of time.  In such a case the client can issue the RECOGNIZE

request and reference the grammar through the ""session:"" URI scheme

(see Section 13.6.  This also applies in general if the client wants

to repeat recognition with a previous inline grammar.

The RECOGNIZE method implementation MUST do a fetch of all external

URIs that are part of that operation.  If caching is implemented,

this URI fetching MUST conform to the cache control hints and

parameter headers associated with the method in deciding whether it

should be fetched from cache or from the external server.  If these

hints/parameters are not specified in the method, the values set for

the session using SET-PARAMS/GET-PARAMS apply.  If it was not set for

the session their default values apply.

Note that since the audio and the messages are carried over separate

communication paths there may be a race condition between the start

of the flow of audio and the receipt of the RECOGNIZE method.  For

example, if an audio flow is started by the client at the same time

as the RECOGNIZE method is sent, either the audio or the RECOGNIZE

can arrive at the recognizer first.  As another example, the client

may choose to continuously send audio to the Server and signal the

Server to recognize using the RECOGNIZE method.  A number of

mechanisms exist to resolve this condition and the mechanism chosen

is left to the implementers of recognition resource.  The recognizer

can expect the media to start flowing when it receives the recognize

request, but MUST NOT buffer anything it receives beforehand.

Non-Hotword mode recognition:

When a RECOGNIZE method has been received the recognition is

initiated on the stream.  The No-Input-Timer MUST BE started at this

time if the Start-Input-Timers header is specified as "true".  If

this header is set to "false", the No-Input-Timer MUST be started

when it receives the START-INPUT-TIMERS method from the client.  The

Recognition-Timer MUST be started when the START-OF-INPUT event is

sent.  When enough speech has been collected to be able to process,

the recognizer can try to match the collected speech with the active

grammars.  If the speech collected at this point fully matches with

any of the active grammars, the Speech-Complete-Timer is started.  If

it matches partially with one or more of the active grammars, with

more speech needed before a full match is achieved, then the Speech-

Incomplete-Timer is started.

1.  When the No-Input-Timer expires, the recognizer must complete

with a Completion-Cause code of "no-input-timeout".

Shanmugham & Burnett    Expires September 6, 2007             [Page 107]

Internet-Draft                   MRCPv2                       March 2007

2.  The recognizer MUST support detecting a no-match condition upon

detecting end of speech.  The recognizer MAY support detecting a no-

match condition before waiting for end-of-speech.  If this is

supported, this capability is enabled by setting the "Early-No-Match"

header to "true".  Upon detecting a no-match condition the RECOGNIZE

MUST return with "no-match".

3.  When the Speech-Incomplete-Timer expires the recognizer SHOULD

complete with a Completion-Cause code of "partial-match", unless the

recognizer cannot differentiate a partial-match in which case it MUST

return a Completion-Cause code of "no-match".  The recognizer MAY

return results for the partially matched grammar.

4.  When the Speech-Complete-Timer expires the recognizer MUST

complete with a Completion-Cause code of "success".

5.  When the Recognition-Timer expires one of the following MUST

happen:

5.1 If there was a partial-match the recognizer SHOULD complete with

a Completion-Cause code of "partial-match-maxtime", unless the

recognizer cannot differentiate a partial-match in which case it MUST

complete with a Completion-Cause code of "no-match-maxtime".  The

recognizer MAY return results for the partially matched grammar.

5.2 If there was a full-match the recognizer MUST complete with a

Completion-Cause code of "success-maxtime".

5.3 If there was a no match the recognizer MUST complete with a

Completion-Cause code of "no-match-maxtime".

For the Hotword mode recognition:

1.  The Recognition-Timer gets started at the beginning of RECOGNIZE.

2.  When there is match at anytime, the RECOGNIZE completes with a

Completion-Cause code of "success".

3.  When the Recognition-Timer expires and there is not a match, the

RECOGNIZE MUST complete with a Completion-Cause code of "hotword-

maxtime"

4.  When the Recognition-Timer expires and there is a match, the

RECOGNIZE MUST complete with a Completion-Cause code of "success-

maxtime".

C->S:MRCP/2.0 479 RECOGNIZE 543257

Channel-Identifier:32AECB23433801@speechrecog

Shanmugham & Burnett    Expires September 6, 2007             [Page 108]

Internet-Draft                   MRCPv2                       March 2007

Confidence-Threshold:0.9

Content-Type:application/srgs+xml

Content-ID:<request1@form-level.store>

Content-Length:104

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0" root="request">

<!-- single language attachment to tokens -->

<rule id="yes">

<one-of>

<item xml:lang="fr-CA">oui</item>

<item xml:lang="en-US">yes</item>

</one-of>

</rule>

<!-- single language attachment to a rule expansion -->

<rule id="request">

may I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

</grammar>

S->C: MRCP/2.0 48 543257 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

S->C:MRCP/2.0 49 START-OF-INPUT 543257 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

S->C:MRCP/2.0 467 RECOGNITION-COMPLETE 543257 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

Waveform-URI:<http://web.media.com/session123/audio.wav>;

size=424252;duration=2543

Content-Type:application/nlsml+xml

Content-Length:276

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="session:request1@form-level.store">

Shanmugham & Burnett    Expires September 6, 2007             [Page 109]

Internet-Draft                   MRCPv2                       March 2007

<interpretation>

<instance name="Person">

<ex:Person>

<ex:Name> Andre Roy </ex:Name>

</ex:Person>

</instance>

<input>   may I speak to Andre Roy </input>

</interpretation>

</result>

RECOGNIZE Example

C->S:   MRCP/2.0 479 RECOGNIZE 543257

Channel-Identifier:32AECB23433801@speechrecog

Confidence-Threshold:0.9

Fetch-Timeout:20

Content-Type:application/srgs+xml

Content-Length:176

<?xml version="1.0"? Version="1.0" mode="voice"

root="Basic md">

<rule id="rule_list" scope="public">

<one-of>

<item weight=10>

<ruleref uri=

"http://grammar.example.com/world-cities.grxml#canada"/>

</item>

<item weight=1.5>

<ruleref uri=

"http://grammar.example.com/world-cities.grxml#america"/>

</item>

<item weight=0.5>

<ruleref uri=

"http://grammar.example.com/world-cities.grxml#india"/>

</item>

</one-of>

</rule>

Second RECOGNIZE Example

9.10.  STOP

The "STOP" method from the client to the server tells the resource to

stop recognition if a request is active.  If a RECOGNIZE request is

active and the "STOP" request successfully terminated it, then the

response header contains an active-request-id-list header containing

the request-id of the RECOGNIZE request that was terminated.  In this

Shanmugham & Burnett    Expires September 6, 2007             [Page 110]

Internet-Draft                   MRCPv2                       March 2007

case, no RECOGNITION-COMPLETE event is sent for the terminated

request.  If there was no recognition active, then the response MUST

NOT contain an active-request-id-list header.  Either way the

response MUST contain a status of 200 (Success).

C->S:   MRCP/2.0 573 RECOGNIZE 543257

Channel-Identifier:32AECB23433801@speechrecog

Confidence-Threshold:0.9

Content-Type:application/srgs+xml

Content-ID:<request1@form-level.store>

Content-Length:104

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0" root="request">

<!-- single language attachment to tokens -->

<rule id="yes">

<one-of>

<item xml:lang="fr-CA">oui</item>

<item xml:lang="en-US">yes</item>

</one-of>

</rule>

<!-- single language attachment to a rule expansion -->

<rule id="request">

may I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

</grammar>

S->C:   MRCP/2.0 47 543257 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

C->S:   MRCP/2.0 28 STOP 543258 200

Channel-Identifier:32AECB23433801@speechrecog

S->C:   MRCP/2.0 67 543258 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Active-Request-Id-List:543257

Shanmugham & Burnett    Expires September 6, 2007             [Page 111]

Internet-Draft                   MRCPv2                       March 2007

9.11.  GET-RESULT

The GET-RESULT method from the client to the server may be issued

when the recognizer resource is in the recognized state.  This

request allows the client to retrieve results for a completed

recognition.  This is useful if the client decides it wants more

alternatives or more information.  When the server receives this

request it re-computes and returns the results according to the

recognition constraints provided in the GET-RESULT request.

The GET-RESULT request can specify constraints such as a different

confidence-threshold, or n-best-list-length.  This capability is

optional for MRCPv2 servers and the automatic speech recognition

engine in the server MAY return a status of unsupported feature.

C->S:   MRCP/2.0 73 GET-RESULT 543257

Channel-Identifier:32AECB23433801@speechrecog

Confidence-Threshold:0.9

S->C:   MRCP/2.0 487 543257 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Content-Type:application/nlsml+xml

Content-Length:276

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="session:request1@form-level.store">

<interpretation>

<instance name="Person">

<ex:Person>

<ex:Name> Andre Roy </ex:Name>

</ex:Person>

</instance>

<input>   may I speak to Andre Roy </input>

</interpretation>

</result>

9.12.  START-OF-INPUT

This is an event from the server to the client indicating that the

recognition resource has detected speech or a DTMF digit in the media

stream.  This event is useful in implementing kill-on-barge-in

scenarios when a synthesizer resource is in a different session from

the recognizer resource and hence is not aware of an incoming audio

source.  In these cases, it is up to the client to act as a

intermediary and respond to this event by issuing a BARGE-IN-OCCURRED

Shanmugham & Burnett    Expires September 6, 2007             [Page 112]

Internet-Draft                   MRCPv2                       March 2007

event to the synthesizer resource.  The recognizer resource also MUST

send a Proxy-Sync-Id header with a unique value for this event.

This event MUST be generated by the server irrespective of whether

the synthesizer and recognizer are on the same server or not.

9.13.  START-INPUT-TIMERS

This request is sent from the client to the recognition resource when

it knows that a kill-on-barge-in prompt has finished playing.  This

is useful in the scenario when the recognition and synthesizer

engines are not in the same session.  When a kill-on-barge-in prompt

is being played, the client may want a RECOGNIZE request to be

simultaneously active so that it can detect and implement kill on

barge-in.  But at the same time the client doesn't want the

recognizer to start the no-input timers until the prompt is finished.

The Start-Input-Timers header in the RECOGNIZE request allows the

client to say whether the timers should be started immediately or

not.  If not, the recognizer resource MUST NOT start the timers until

the client sends a START-INPUT-TIMERS method to the recognizer.

9.14.  RECOGNITION-COMPLETE

This is an Event from the recognizer resource to the client

indicating that the recognition completed.  The recognition result is

sent in the body of the MRCPv2 message.  The request-state field MUST

be COMPLETE indicating that this is the last event with that

request-id, and that the request with that request-id is now

complete.  The server MUST maintain the recognizer context containing

the results and the audio waveform input of that recognition until

the next RECOGNIZE request is issued for that resource or the session

terminates.  A URI to the audio waveform MAY be returned to the

client in a waveform-uri header in the RECOGNITION-COMPLETE event.

The client can use this URI to retrieve or playback the audio.

Note if an enrollment session was active, the RECOGNITION-COMPLETE

event can contain either recognition or enrollment results depending

on what was spoken.

C->S:   MRCP/2.0 487 RECOGNIZE 543257

Channel-Identifier:32AECB23433801@speechrecog

Confidence-Threshold:0.9

Content-Type:application/srgs+xml

Content-ID:<request1@form-level.store>

Content-Length:104

<?xml version="1.0"?>

Shanmugham & Burnett    Expires September 6, 2007             [Page 113]

Internet-Draft                   MRCPv2                       March 2007

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0" root="request">

<!-- single language attachment to tokens -->

<rule id="yes">

<one-of>

<item xml:lang="fr-CA">oui</item>

<item xml:lang="en-US">yes</item>

</one-of>

</rule>

<!-- single language attachment to a rule expansion -->

<rule id="request">

may I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

</grammar>

S->C:   MRCP/2.0 48 543257 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

S->C:   MRCP/2.0 49 START-OF-INPUT 543257 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

S->C:   MRCP/2.0 465 RECOGNITION-COMPLETE 543257 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

Waveform-URI:<http://web.media.com/session123/audio.wav>;

size=342456;duration=25435

Content-Type:application/nlsml+xml

Content-Length:276

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="session:request1@form-level.store">

<interpretation>

<instance name="Person">

<ex:Person>

<ex:Name> Andre Roy </ex:Name>

</ex:Person>

</instance>

<input>   may I speak to Andre Roy </input>

</interpretation>

Shanmugham & Burnett    Expires September 6, 2007             [Page 114]

Internet-Draft                   MRCPv2                       March 2007

</result>

S->C:   MRCP/2.0 465 RECOGNITION-COMPLETE 543257 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

Content-Type:application/nlsml+xml

Content-Length:123

<?xml version= "1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

grammar="Personal-Grammar-URI">

<enrollment-result>

<num-clashes> 2 </num-clashes>

<num-good-repetitions> 1 </num-good-repetitions>

<num-repetitions-still-needed>

1

</num-repetitions-still-needed>

<consistency-status> consistent </consistency-status>

<clash-phrase-ids>

<item> Jeff </item> <item> Andre </item>

</clash-phrase-ids>

<transcriptions>

<item> m ay b r ow k er </item>

<item> m ax r aa k ah </item>

</transcriptions>

<confusable-phrases>

<item>

<phrase> call </phrase>

<confusion-level> 10 </confusion-level>

</item>

</confusable-phrases>

</enrollment-result>

</result>

9.15.  START-PHRASE-ENROLLMENT

The START-PHRASE-ENROLLMENT method from the client to the server

starts a new phrase enrollment session during which the client may

call RECOGNIZE multiple times to enroll a new utterance in a grammar.

An enrollment session consists of a set of calls to RECOGNIZE in

which the caller speaks a phrase several times so the system can

"learn" it.  The phrase is then added to a personal grammar (speaker-

trained grammar), so that the system can recognize it later.

Only one phrase enrollment session may be active at a time for a

resource.  The Personal-Grammar-URI identifies the grammar that is

used during enrollment to store the personal list of phrases.  Once

Shanmugham & Burnett    Expires September 6, 2007             [Page 115]

Internet-Draft                   MRCPv2                       March 2007

RECOGNIZE is called, the result is returned in a RECOGNITION-COMPLETE

event and may contain either an enrollment result OR a recognition

result for a regular recognition.

Calling END-PHRASE-ENROLLMENT ends the ongoing phrase enrollment

session, which is typically done after a sequence of successful calls

to RECOGNIZE.  This method can be called to commit the new phrase to

the personal grammar or to abort the phrase enrollment session.

The Personal-Grammar-URI, which specifies the grammar to contain the

new enrolled phrase, is created if it does not exist.  Also, the

personal grammar may ONLY contain phrases added via a phrase

enrollment session.

The Phrase-ID passed to this method is used to identify this phrase

in the grammar and will be returned as the speech input when doing a

RECOGNIZE on the grammar.  The Phrase-NL similarly is returned in a

RECOGNITION-COMPLETE event in the same manner as other NL in a

grammar.  The tag-format of this NL is implementation specific.

If the client has specified Save-Best-Waveform as true, then the

response after ending the phrase enrollment session MUST contain the

location/URI of a recording of the best repetition of the learned

phrase.

C->S:     MRCP/2.0 123 START-PHRASE-ENROLLMENT 543258

Channel-Identifier:32AECB23433801@speechrecog

Num-Min-Consistent-Pronunciations:2

Consistency-Threshold:30

Clash-Threshold:12

Personal-Grammar-URI:<personal grammar uri>

Phrase-Id:<phrase id>

Phrase-NL:<NL phrase>

Weight:1

Save-Best-Waveform:true

S->C:    MRCP/2.0 49 543258 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

9.16.  ENROLLMENT-ROLLBACK

The ENROLLMENT-ROLLBACK method discards the last live utterance from

the RECOGNIZE operation.  The client can invoke this method when the

caller provides undesirable input such as non-speech noises, side-

speech, commands, utterance from the RECOGNIZE grammar, etc.  Note

that this method does not provide a stack of rollback states.

Executing ENROLLMENT-ROLLBACK twice in succession without an

intervening recognition operation has no effect on the second

Shanmugham & Burnett    Expires September 6, 2007             [Page 116]

Internet-Draft                   MRCPv2                       March 2007

attempt.

C->S:   MRCP/2.0 49 ENROLLMENT-ROLLBACK 543261

Channel-Identifier:32AECB23433801@speechrecog

S->C:    MRCP/2.0 49 543261 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

9.17.  END-PHRASE-ENROLLMENT

The END-PHRASE-ENROLLMENT method may be called ONLY during an active

phrase enrollment session.  It MUST NOT be called during an ongoing

RECOGNIZE operation.  To commit the new phrase in the grammar, the

client MAY call this method once successive calls to RECOGNIZE have

succeeded and Num-Repetitions-Still-Needed has been returned as 0 in

the RECOGNITION-COMPLETE event.  Alternatively, the client can abort

the phrase enrollment session by calling this method with the Abort-

Phrase-Enrollment header.

If the client has specified Save-Best-Waveform as true in the START-

PHRASE-ENROLLMENT request, then the response MUST contain the

location/URI of a recording of the best repetition of the learned

phrase.

C->S:     MRCP/2.0 49 END-PHRASE-ENROLLMENT 543262

Channel-Identifier:32AECB23433801@speechrecog

S->C:    MRCP/2.0 123 543262 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Waveform-URI:<http://mediaserver.com/recordings/file1324.wav>;

size=242453;duration=25432

9.18.  MODIFY-PHRASE

The MODIFY-PHRASE method sent from the client to the server is used

to change the phrase ID, NL phrase and/or weight for a given phrase

in a personal grammar.

If no fields are supplied then calling this method has no effect.

Shanmugham & Burnett    Expires September 6, 2007             [Page 117]

Internet-Draft                   MRCPv2                       March 2007

C->S:     MRCP/2.0 123 MODIFY-PHRASE 543265

Channel-Identifier:32AECB23433801@speechrecog

Personal-Grammar-URI:<personal grammar uri>

Phrase-Id:<phrase id>

New-Phrase-Id:<new phrase id>

Phrase-NL:<NL phrase>

Weight:1

S->C:    MRCP/2.0 49 543265 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

9.19.  DELETE-PHRASE

The DELETE-PHRASE method sent from the client to the server is used

to delete a phase in a personal grammar added through voice

enrollment or text enrollment.  If the specified phrase does not

exist, this method has no effect.

C->S:     MRCP/2.0 123 DELETE-PHRASE 543266

Channel-Identifier:32AECB23433801@speechrecog

Personal-Grammar-URI:<personal grammar uri>

Phrase-Id:<phrase id>

S->C:    MRCP/2.0 49 543266 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

9.20.  INTERPRET

The INTERPRET method from the client to the server takes as input an

interpret-text header containing the text for which the semantic

interpretation is desired, and returns, via the INTERPRETATION-

COMPLETE event, an interpretation result which is very similar to the

one returned from a RECOGNIZE method invocation.  Only portions of

the result relevant to acoustic matching are excluded from the

result.  The interpret-text header MUST be included in the INTERPRET

request.

Recognizer grammar data is treated in the same way as it is when

issuing a RECOGNIZE method call.

If a RECOGNIZE, RECORD or another INTERPRET operation is already in

progress for the resource, the server MUST reject the request a

response having a status code of 402, "Method not valid in this

state", and a COMPLETE request state.

C->S:    MRCP/2.0 123 INTERPRET 543266

Channel-Identifier:32AECB23433801@speechrecog

Interpret-Text:may I speak to Andre Roy

Shanmugham & Burnett    Expires September 6, 2007             [Page 118]

Internet-Draft                   MRCPv2                       March 2007

Content-Type:application/srgs+xml

Content-ID:<request1@form-level.store>

Content-Length:104

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0" root="request">

<!-- single language attachment to tokens -->

<rule id="yes">

<one-of>

<item xml:lang="fr-CA">oui</item>

<item xml:lang="en-US">yes</item>

</one-of>

</rule>

<!-- single language attachment to a rule expansion -->

<rule id="request">

may I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

</grammar>

S->C:    MRCP/2.0 49 543266 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

S->C:    MRCP/2.0 49 543267 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

Content-Type:application/nlsml+xml

Content-Length:276

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="session:request1@form-level.store">

<interpretation>

<instance name="Person">

<ex:Person>

<ex:Name> Andre Roy </ex:Name>

</ex:Person>

</instance>

<input>   may I speak to Andre Roy </input>

</interpretation>

</result>

Shanmugham & Burnett    Expires September 6, 2007             [Page 119]

Internet-Draft                   MRCPv2                       March 2007

9.21.  INTERPRETATION-COMPLETE

This event from the recognition resource to the client indicates that

the INTERPRET operation is complete.  The interpretation result is

sent in the body of the MRCP message.  The request state MUST be set

to COMPLETE.

The completion-cause header MUST be included in this event and MUST

be set to an appropriate value from the list of cause codes.

C->S:    MRCP/2.0 123 INTERPRET 543266

Channel-Identifier:32AECB23433801@speechrecog

Interpret-Text:may I speak to Andre Roy

Content-Type:application/srgs+xml

Content-ID:<request1@form-level.store>

Content-Length:104

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0" root="request">

<!-- single language attachment to tokens -->

<rule id="yes">

<one-of>

<item xml:lang="fr-CA">oui</item>

<item xml:lang="en-US">yes</item>

</one-of>

</rule>

<!-- single language attachment to a rule expansion -->

<rule id="request">

may I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

</grammar>

S->C:    MRCP/2.0 49 543266 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

S->C:    MRCP/2.0 49 543267 200 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

Content-Type:application/nlsml+xml

Content-Length:276

Shanmugham & Burnett    Expires September 6, 2007             [Page 120]

Internet-Draft                   MRCPv2                       March 2007

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="session:request1@form-level.store">

<interpretation>

<instance name="Person">

<ex:Person>

<ex:Name> Andre Roy </ex:Name>

</ex:Person>

</instance>

<input>   may I speak to Andre Roy </input>

</interpretation>

</result>

9.22.  DTMF Detection

Digits received as DTMF tones are delivered to the recognition

resource in the MRCPv2 server in the RTP stream according to RFC2833

[29].  The automatic speech recognizer (ASR) MUST support RFC2833 to

recognize digits and it MAY support recognizing DTMF tones [28] in

the audio.

10.  Recorder Resource

This resource captures received audio and video and stores it as

content pointed to by a URI.  The main usages of recorders are

1.  to capture speech audio that may be submitted for recognition at

a later time, and

2.  recording voice or video mails.

Both these applications require functionality above and beyond those

specified by protocols such as RTSP.  This includes Audio End-

pointing (i.e., detecting speech or silence).  The support for video

is optional and is mainly capturing video mails that may require the

speech or audio processing mentioned above.

A recorder MUST provide some end-pointing capabilities for

suppressing silence at the beginning and end of a recording, and MAY

also suppress silence in the middle of a recording.  If such

suppression is done, the recorder MUST maintain timing metadata to

indicate the actual time stamps of the recorded media.

Shanmugham & Burnett    Expires September 6, 2007             [Page 121]

Internet-Draft                   MRCPv2                       March 2007

10.1.  Recorder State Machine

Idle                   Recording

State                  State

|                       |

|---------RECORD------->|

|                       |

|<------STOP------------|

|                       |

|<--RECORD-COMPLETE-----|

|                       |

|              |--------|

|       START-OF-INPUT  |

|              |------->|

|                       |

|              |--------|

|    START-INPUT-TIMERS |

|              |------->|

|                       |

Recorder State Machine

10.2.  Recorder Methods

The recorder resource supports the following methods.

recorder-Method      =  "RECORD"

/  "STOP"

/  "START-INPUT-TIMERS"

10.3.  Recorder Events

The recorder resource may generate the following events.

recorder-Event       =  "START-OF-INPUT"

/  "RECORD-COMPLETE"

10.4.  Recorder Header Fields

Method invocations for the recorder resource may contain resource-

specific headers containing request options and information to

augment the Method, Response or Event message it is associated with.

Shanmugham & Burnett    Expires September 6, 2007             [Page 122]

Internet-Draft                   MRCPv2                       March 2007

recorder-header      =  sensitivity-level

/  no-input-timeout

/  completion-cause

/  completion-reason

/  failed-uri

/  failed-uri-cause

/  record-uri

/  media-type

/  max-time

/  trim-length

/  final-silence

/  capture-on-speech

/  ver-buffer-utterance

/  start-input-timers

/  new-audio-channel

10.4.1.  Sensitivity Level

To filter out background noise and not mistake it for speech, the

recorder may support a variable level of sound sensitivity.  The

sensitivity-level header is a float value between 0.0 and 1.0 and

allows the client to set the sensitivity level for the recorder.

This header MAY occur in RECORD, "SET-PARAMS" or "GET-PARAMS".  A

higher value for this header means higher sensitivity.  The default

value for this header is implementation specific.

sensitivity-level    =     "Sensitivity-Level" ":" FLOAT CRLF

10.4.2.  No Input Timeout

When recording is started and there is no speech detected for a

certain period of time, the recorder can send a RECORD-COMPLETE event

to the client and terminate the record operation.  The no-input-

timeout header can set this timeout value.  The value is in

milliseconds.  This header MAY occur in RECORD, "SET-PARAMS" or

"GET-PARAMS".  The value for this header ranges from 0 to an

implementation specific maximum value.  The default value for this

header is implementation specific.

no-input-timeout    =     "No-Input-Timeout" ":" 1*DIGIT CRLF

10.4.3.  Completion Cause

This header MUST be part of a RECORD-COMPLETE event from the recorder

resource to the client.  This indicates the reason behind the RECORD

method completion.  This header MUST be sent in the RECORD responses

if they return with a failure status and a COMPLETE state.

Shanmugham & Burnett    Expires September 6, 2007             [Page 123]

Internet-Draft                   MRCPv2                       March 2007

completion-cause         =  "Completion-Cause" ":" 1*DIGIT SP

1*VCHAR CRLF

+------------+-----------------------+------------------------------+

| Cause-Code | Cause-Name            | Description                  |

+------------+-----------------------+------------------------------+

| 000        | success-silence       | RECORD completed with a      |

|            |                       | silence at the end           |

| 001        | success-maxtime       | RECORD completed after       |

|            |                       | reaching maximum recording   |

|            |                       | time specified in record     |

|            |                       | method.                      |

| 002        | noinput-timeout       | RECORD failed due to no      |

|            |                       | input                        |

| 003        | uri-failure           | Failure accessing the record |

|            |                       | URI.                         |

| 004        | error                 | RECORD request terminated    |

|            |                       | prematurely due to a         |

|            |                       | recorder error.              |

+------------+-----------------------+------------------------------+

10.4.4.  Completion Reason

This header MAY be present in a RECORD-COMPLETE event coming from the

recorder resource to the client.  It contains the reason text behind

the RECORD request completion.  This header can be use to communicate

text describing the reason for the failure.

The completion reason text is provided for client use in logs and for

debugging and instrumentation purposes.  Clients are NOT REQUIRED to

interpret the completion reason text.

completion-reason        =  "Completion-Reason" ":"

quoted-string CRLF

10.4.5.  Failed URI

When a recorder method needs to post the audio to an URI and access

to the URI fails, the server MUST provide the failed URI in this

header in the method response.

failed-uri               =  "Failed-URI" ":" Uri CRLF

10.4.6.  Failed URI Cause

When a recorder method needs to post the audio to an URI and access

to the URI fails, the server MUST provide the URI specific or

protocol specific response code through this header in the method

Shanmugham & Burnett    Expires September 6, 2007             [Page 124]

Internet-Draft                   MRCPv2                       March 2007

response.  The value encoding is alphanumeric to accommodate all

anticipated access protocols, some of which might have a response

string instead of a numeric response code.

failed-uri-cause         =  "Failed-URI-Cause" ":" 1*alphanum

CRLF

10.4.7.  Record URI

When a recorder method contains this header the server must capture

the audio and store it.  If the header is present but specified with

no value, the server MUST store the content locally and generate a

URI that points to it.  This URI is then returned in either the

"STOP" response or the RECORD-COMPLETE event.  If the header in the

RECORD method specifies a URI, the server MUST attempt to capture and

store the audio at that location.  If this header is not specified in

the RECORD request, the server MUST capture the audio and send it in

the "STOP" response or the RECORD-COMPLETE event as a message body.

In this case, the response carrying the audio content would have this

header with a cid value pointing to the Content-ID in the message

body.

The server MUST also return the size in bytes and the duration in

milliseconds of the recorded audio wave-form as parameters associated

with the header.

record-uri               =  "Record-URI" ":" ["<" Uri ">"

";" "size" "=" 1*DIGIT

";" "duration" "=" 1*DIGIT] CRLF

10.4.8.  Media Type

A RECORD method MUST contain this header, which specifies to the

server the MIME content type in which to store the captured audio or

video.

media-type               =  "Media-Type" ":" media-type-value

CRLF

10.4.9.  Max Time

When recording is started this specifies the maximum length of the

recording in milliseconds, calculated from the time the actual

capture and store begins and is not necessarily the time the RECORD

method is received.  It specifies the duration before silence

suppression, if any, has been applied by the recorder resource.

After this time, the recording stops and the server MUST return a

RECORD-COMPLETE event to the client having a request-state of

Shanmugham & Burnett    Expires September 6, 2007             [Page 125]

Internet-Draft                   MRCPv2                       March 2007

"COMPLETE".  This header MAY occur in RECORD, "SET-PARAMS" or

"GET-PARAMS".  The value for this header ranges from 0 to an

implementation specific maximum value.  A value of zero means

infinity and hence the recording continues until one or more of the

other stop conditions are met.  The default value for this header is

0.

max-time                 =  "Max-Time" ":" 1*DIGIT CRLF

10.4.10.  Trim-Length

This header MAY be sent on a STOP method and specifies the length of

audio to be trimmed from the end of the recording after the stop.

The length is interpreted to be in milliseconds.  The default value

for this header is 0.

trim-length                 =  "Trim-Length" ":" 1*DIGIT CRLF

10.4.11.  Final Silence

When recorder is started and the actual capture begins, this header

specifies the length of silence in the audio that is to be

interpreted as the end of the recording.  This header MAY occur in

RECORD, "SET-PARAMS" or "GET-PARAMS".  The value for this header

ranges from 0 to an implementation specific maximum value and is

interpreted to be in milliseconds.  A value of zero means infinity

and hence the recording will continue until one of the other stop

conditions are met.  The default value for this header is

implementation specific.

final-silence            =  "Final-Silence" ":" 1*DIGIT CRLF

10.4.12.  Capture On Speech

If false, the recorder MUST start capturing immediately when started.

If true, the recorder MUST wait for the end-pointing functionality to

detect speech before it starts capturing.  This header MAY occur in

the RECORD, "SET-PARAMS" or "GET-PARAMS".  The value for this header

is a Boolean.  The default value for this header is false.

capture-on-speech        =  "Capture-On-Speech " ":" boolean-value CRLF

10.4.13.  Ver-Buffer-Utterance

This header is the same as the one described for the Verification

resource (see Section 11.4.14).  This tells the server to buffer the

utterance associated with this recording request into the

verification buffer.  Sending this header is permitted only if the

Shanmugham & Burnett    Expires September 6, 2007             [Page 126]

Internet-Draft                   MRCPv2                       March 2007

verification buffer is for the session.  This buffer is shared across

resources within a session.  It gets instantiated when a verification

resource is added to this session and is released when the

verification resource is released from the session.

10.4.14.  Start Input Timers

This header MAY be sent as part of the RECORD request.  A value of

false tells the recorder resource to start the operation, but not to

start the no-input timer until the client sends a START-INPUT-TIMERS

request to the recorder resource.  This is useful in the scenario

when the recorder and synthesizer resources are not part of the same

session.  When a kill-on-barge-in prompt is being played, the client

may want the RECORD request to be simultaneously active so that it

can detect and implement kill-on-barge-in.  But at the same time the

client doesn't want the recorder resource to start the no-input

timers until the prompt is finished.  The default value is "true".

start-input-timers       =  "Start-Input-Timers" ":"

boolean-value CRLF

10.4.15.  New Audio Channel

This header is the same as the one described for the Recognizer

resource (see Section 9.4.23).

10.5.  Recorder Message Body

If the RECORD request did not have a Record-Uri header, the "STOP"

response or the RECORD-COMPLETE event MUST contain a message body

carrying the captured audio.  In this case, the message carrying the

audio content has a Record-Uri header with a cid value pointing to

the message MIME body that contains the recorded audio.

10.6.  RECORD

The RECORD request places the recorder resource in the Recording

state.  Depending on the headers specified in the RECORD method, the

resource may start recording the audio immediately or wait for the

end pointing functionality to detect speech in the audio.  The audio

is then made available to the client either in the message body or as

specified by Record-URI.

The server MUST support the HTTPS URI scheme and MAY support other

schemes.  Note that due to the sensitive nature of voice recordings,

any other URI schemes supported by the server SHOULD employ integrity

and confidentiality on the data transfer (e.g.  FTPS).

Shanmugham & Burnett    Expires September 6, 2007             [Page 127]

Internet-Draft                   MRCPv2                       March 2007

If a RECORD operation is already in progress, invoking this method

causes the server to issue a response having a status code of 402,

"Method not valid in this state", and a COMPLETE request state.

If the recording-uri is not valid, a status code of 404, "Illegal

Value for Header", is returned in the response.  If it is impossible

for the server to create the requested stored content, a status code

of 407, "Method or Operation Failed", is returned.

If the type specified in the Media-Type header is not supported, the

server MUST respond with a status code of 409, "Unsupported Header

Value", with the Media-Type header in its response.

When the recording operation is initiated, the response indicates an

IN-PROGRESS request state.  The server MAY generate a subsequent

START-OF-INPUT event when speech is detected.  Upon completion of the

recording operation, the server generates a RECORD-COMPLETE event.

C->S:  MRCP/2.0 386 RECORD 543257

Channel-Identifier:32AECB23433802@recorder

Record-URI:<file://mediaserver/recordings/myfile.wav>

Capture-On-Speech:true

Final-Silence:300

Max-Time:6000

S->C:  MRCP/2.0 48 456234 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@recorder

S->C:  MRCP/2/0 49 START-OF-INPUT 456234 IN-PROGRESS

Channel-Identifier:32AECB23433802@recorder

S->C:  MRCP/2.0 54 RECORD-COMPLETE 456234 COMPLETE

Channel-Identifier:32AECB23433802@recorder

Completion-Cause:000 success-silence

Record-URI:<file://mediaserver/recordings/myfile.wav>;

size=242552;duration=25645

RECORD Example

10.7.  STOP

The "STOP" method moves the recorder from the recording state back to

the idle state.  If a RECORD request is active and the "STOP" request

successfully terminated it, then the STOP response MUST contain an

active-request-id-list header containing the "RECORD" request-id that

was terminated.  In this case, no RECORD-COMPLETE event is sent for

the terminated request.  If there was no recording active, then the

response MUST NOT contain an active-request-id-list header.  If the

Shanmugham & Burnett    Expires September 6, 2007             [Page 128]

Internet-Draft                   MRCPv2                       March 2007

recording was a success the "STOP" response MUST contain a Record-URI

header pointing to the recorded audio content or to a MIME part in

the body of the "STOP" response containing the recorded audio.  The

"STOP" method may have a Trim-Length header, in which case the

specified length of audio is trimmed from the end of the recording

after the stop.  In any case, the response MUST contain a status of

200 (Success).

C->S:  MRCP/2.0 386 RECORD 543257

Channel-Identifier:32AECB23433802@recorder

Record-URI:<file://mediaserver/recordings/myfile.wav>

Capture-On-Speech:true

Final-Silence:300

Max-Time:6000

S->C:  MRCP/2.0 48 456234 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@recorder

S->C:  MRCP/2/0 49 START-OF-INPUT 456234 IN-PROGRESS

Channel-Identifier:32AECB23433802@recorder

C->S:  MRCP/2.0 386 STOP 543257

Channel-Identifier:32AECB23433802@recorder

Trim-Length:200

S->C:  MRCP/2.0 48 456234 200 COMPLETE

Channel-Identifier:32AECB23433802@recorder

Record-URI:<file://mediaserver/recordings/myfile.wav>;

size=324253;duration=24561

Active-Request-Id-List:543257

STOP Example

10.8.  RECORD-COMPLETE

If the recording completes due to no-input, silence after speech or

max-time the server MUST generate the RECORD-COMPLETE event to the

client with a request-state of "COMPLETE".  If the recording was a

success the RECORD-COMPLETE event contains a Record-URI header

pointing to the recorded audio file on the server or to a MIME part

containing the recorded audio in the body of the message .

Shanmugham & Burnett    Expires September 6, 2007             [Page 129]

Internet-Draft                   MRCPv2                       March 2007

C->S:  MRCP/2.0 386 RECORD 543257

Channel-Identifier:32AECB23433802@recorder

Record-URI:<file://mediaserver/recordings/myfile.wav>

Capture-On-Speech:true

Final-Silence:300

Max-Time:6000

S->C:  MRCP/2.0 48 456234 200 IN-PROGRESS

Channel-Identifier:32AECB23433802@recorder

S->C:  MRCP/2/0 49 START-OF-INPUT 456234 IN-PROGRESS

Channel-Identifier:32AECB23433802@recorder

S->C:  MRCP/2.0 48 RECORD-COMPLETE 456234 COMPLETE

Channel-Identifier:32AECB23433802@recorder

Completion-Cause:000 success

Record-URI:<file://mediaserver/recordings/myfile.wav>;

size=325325;duration=24652

RECORD-COMPLETE Example

10.9.  START-INPUT-TIMERS

This request is sent from the client to the recorder resource when it

discovers that a kill-on-barge-in prompt has finished playing.  This

is useful in the scenario when the recorder and synthesizer resources

are not in the same MRCPv2 session.  When a kill-on-barge-in prompt

is being played, the client wants the RECORD request to be

simultaneously active so that it can detect and implement kill on

barge-in.  But at the same time the client doesn't want the recorder

resource to start the no-input timers until the prompt is finished.

The Start-Input-Timers header in the RECORD request allows the client

to say if the timers should be started or not.  In the above case the

recorder resource does not start the timers until the client sends a

START-INPUT-TIMERS method to the recorder.

10.10.  START-OF-INPUT

The START-OF-INPUT event is returned from the server to the client

once the server has detected speech.  This event is always returned

by the recording resource when speech has been detected.  The

recorder resource also MUST send a Proxy-Sync-Id header with a unique

value for this event.

S->C:  MRCP/2.0 49 START-OF-INPUT 543259 IN-PROGRESS

Channel-Identifier:32AECB23433801@recorder

Proxy-Sync-Id:987654321

Shanmugham & Burnett    Expires September 6, 2007             [Page 130]

Internet-Draft                   MRCPv2                       March 2007

11.  Speaker Verification and Identification

This section describes the methods, responses and events employed by

MRCPv2 for doing Speaker Verification / Identification.

Speaker verification is a voice authentication methodology that can

be used to identify the speaker in order to grant the user access to

sensitive information and transactions.  Because speech is a

biometric, a number of essential security considerations related to

biometric authentication technologies apply to its implementation and

usage.  Implementers should carefully read Section 12 in this

document and the corresponding section of Speechsc Requirements [1].

In speaker verification, a recorded utterance is compared to a

previously stored voiceprint which is in turn associated with a

claimed identity for that user.  Verification typically consists of

two phases: a designation phase to establish the claimed identity of

the caller and an execution phase in which a voiceprint is either

created (training) or used to authenticate the claimed identity

(verification).

Speaker identification identifies the speaker among a set of users by

matching against a set of voiceprints.  (This function is also called

Multi-Verification).  Speaker identification can be performed on a

small set of users or for a large population.  This capability is

useful for applications where multiple users share the same access

privileges to some data or application, but where the individual

speaker must be uniquely identified from the group.  It is also

useful for real time or post processing of recorded content to

ascertain who was speaking when.  Speaker identification is also done

in two phases, a designation phase and an execution phase.

It is possible for a speaker verification resource to share the same

session with a recognizer resource or to operate independently.  In

order to share the same session, the verification and recognizer

resources MUST be allocated from within the same SIP dialog.

Otherwise, an independent verification resource, running on the same

physical server or a separate one, will be set up.  Note that in

addition to allowing both resources to be allocated in the same

INVITE, it is possible to allocate one initially and the other later

via a re-INVITE.

Some of the speaker verification methods, described below, apply only

to a specific mode of operation.

The verification resource has a verification buffer associated with

it (see Section 11.4.14).  This allows the storage of speech

utterances for the purposes of verification, identification or

Shanmugham & Burnett    Expires September 6, 2007             [Page 131]

Internet-Draft                   MRCPv2                       March 2007

training from the buffered speech.  This buffer is owned by the

verification resource but other input resources such as the

recognition resource or recorder resource may write to it.  This

allows the speech received as part of a recognition or recording

operation to be later used for verification, identification or

training.  Access to the buffer is limited to one operation at time.

Hence when the resource is doing read, write or delete operation such

as a RECOGNIZE with ver-buffer-utterance turned on, another operation

involving the buffer fails with a status of 402.  The verification

buffer can be cleared by a CLEAR-BUFFER request from the client and

is freed when the verification resource is deallocated or the session

with the server terminates.

The verification buffer is different from collecting waveforms and

processing them using either the real time audio stream or stored

audio, because this buffering mechanism does not simply accumulate

speech to a buffer.  The verification buffer may contain additional

information gathered by the recognition resource that serves to

improve verification performance.

11.1.  Speaker Verification State Machine

Speaker verification may operate in a training or a verification

session.  Starting one of these sessions does not change the state of

the verification resource, i.e. it remains idle.  Once a verification

or training session is started, then utterances are trained or

verified by calling the VERIFY or VERIFY-FROM-BUFFER method.  The

state of the verification resources goes from IDLE to VERIFYING state

each time VERIFY or VERIFY-FROM-BUFFER is called.

Idle              Session Opened       Verifying/Training

State             State                State

|                   |                         |

|--START-SESSION--->|                         |

|                   |                         |

|                   |----------|              |

|                   |     START-SESSION       |

|                   |<---------|              |

|                   |                         |

|<--END-SESSION-----|                         |

|                   |                         |

|                   |---------VERIFY--------->|

|                   |                         |

|                   |---VERIFY-FROM-BUFFER--->|

|                   |                         |

|                   |----------|              |

|                   |  VERIFY-ROLLBACK        |

|                   |<---------|              |

Shanmugham & Burnett    Expires September 6, 2007             [Page 132]

Internet-Draft                   MRCPv2                       March 2007

|                   |                         |

|                   |                |--------|

|                   | GET-INTERMEDIATE-RESULT |

|                   |                |------->|

|                   |                         |

|                   |                |--------|

|                   |     START-INPUT-TIMERS  |

|                   |                |------->|

|                   |                         |

|                   |                |--------|

|                   |         START-OF-INPUT  |

|                   |                |------->|

|                   |                         |

|                   |<-VERIFICATION-COMPLETE--|

|                   |                         |

|                   |<--------STOP------------|

|                   |                         |

|                   |----------|              |

|                   |         STOP            |

|                   |<---------|              |

|                   |                         |

|----------|        |                         |

|         STOP      |                         |

|<---------|        |                         |

|                   |----------|              |

|                   |    CLEAR-BUFFER         |

|                   |<---------|              |

|                   |                         |

|----------|        |                         |

|   CLEAR-BUFFER    |                         |

|<---------|        |                         |

|                   |                         |

|                   |----------|              |

|                   |   QUERY-VOICEPRINT      |

|                   |<---------|              |

|                   |                         |

|----------|        |                         |

| QUERY-VOICEPRINT  |                         |

|<---------|        |                         |

|                   |                         |

|                   |----------|              |

|                   |  DELETE-VOICEPRINT      |

|                   |<---------|              |

|                   |                         |

|----------|        |                         |

| DELETE-VOICEPRINT |                         |

|<---------|        |                         |

Shanmugham & Burnett    Expires September 6, 2007             [Page 133]

Internet-Draft                   MRCPv2                       March 2007

Verification Resource State Machine

11.2.  Speaker Verification Methods

The verification resource supports the following methods.

verification-method      =  "START-SESSION"

/ "END-SESSION"

/ "QUERY-VOICEPRINT"

/ "DELETE-VOICEPRINT"

/ "VERIFY"

/ "VERIFY-FROM-BUFFER"

/ "VERIFY-ROLLBACK"

/ "STOP"

/ "CLEAR-BUFFER"

/ "START-INPUT-TIMERS"

/ "GET-INTERMEDIATE-RESULT"

These methods allow the client to control the mode and target of

verification or identification operations within the context of a

session.  All the verification input operations that occur within a

session may be used to create, update, or validate against the

voiceprint specified during the session.  At the beginning of each

session the verification resource is reset to the state it had prior

to any previous verification session.

Verification/identification operations can be executed against live

or buffered audio.  The verification resource provides methods for

collecting and evaluating live audio data, and methods for

controlling the verification resource and adjusting its configured

behavior.

There are no dedicated methods for collecting buffered audio data.

This is accomplished by calling VERIFY, RECOGNIZE or RECORD as

appropriate for the resource, with the header ver-buffer-utterance.

Then, when the following method is called verification is performed

using the set of buffered audio.

1.  VERIFY-FROM-BUFFER

The following methods are used for verification of live audio

utterances :

1.  VERIFY

2.  START-INPUT-TIMERS

The following methods are used for configuring the verification

resource and for establishing resource states :

Shanmugham & Burnett    Expires September 6, 2007             [Page 134]

Internet-Draft                   MRCPv2                       March 2007

1.  START-SESSION

2.  END-SESSION

3.  QUERY-VOICEPRINT

4.  DELETE-VOICEPRINT

5.  VERIFY-ROLLBACK

6.  "STOP"

7.  CLEAR-BUFFER

The following method allows the polling a Verification in progress

for intermediate results.

1.  GET-INTERMEDIATE-RESULT

11.3.  Verification Events

The verification resource generates the following events.

verification-event       =  "VERIFICATION-COMPLETE"

/  "START-OF-INPUT"

11.4.  Verification Header Fields

A verification resource message may contain headers containing

request options and information to augment the Request, Response or

Event message it is associated with.

verification-header      =  repository-uri

/  voiceprint-identifier

/  verification-mode

/  adapt-model

/  abort-model

/  min-verification-score

/  num-min-verification-phrases

/  num-max-verification-phrases

/  no-input-timeout

/  save-waveform

/  media-type

/  waveform-uri

/  voiceprint-exists

/  ver-buffer-utterance

/  input-waveform-uri

/  completion-cause

/  completion-reason

/  speech-complete-timeout

/  new-audio-channel

/  abort-verification

/  start-input-timers

Shanmugham & Burnett    Expires September 6, 2007             [Page 135]

Internet-Draft                   MRCPv2                       March 2007

11.4.1.  Repository-URI

This header specifies the voiceprint repository to be used or

referenced during speaker verification or identification operations.

This header is required in START-SESSION, QUERY-VOICEPRINT and

DELETE-VOICEPRINT methods.

repository-uri           =  "Repository-URI" ":" Uri CRLF

11.4.2.  Voiceprint-Identifier

This header specifies the claimed identity for verification

applications.  The claimed identity may be used to specify an

existing voiceprint or to establish a new voiceprint.  This header is

required in QUERY-VOICEPRINT and DELETE-VOICEPRINT methods.  The

Voiceprint-Identifier is required in the START-SESSION method for

verification operations.  For Identification or Multi-Verification

operations this header may contain a list of voiceprint identifiers

separated by semi-colons.  For identification operations the client

can also specify a voiceprint group identifier instead of a list of

voiceprint identifiers.

voiceprint-identifier        =  "Voiceprint-Identifier" ":"

1*VCHAR "." 1*VCHAR

*[";" 1*VCHAR "." 1*VCHAR] CRLF

11.4.3.  Verification-Mode

This header specifies the mode of the verification resource and is

set by the START-SESSION method.  Acceptable values indicate whether

the verification session will train a voiceprint ("train") or verify/

identify using an existing voiceprint ("verify").

Training and verification sessions both require the voiceprint

Repository-URI to be specified in the START-SESSION.  In many usage

scenarios, however, the system does not know the speaker's claimed

identity until a recognition operation has, for example, recognized a

an account number to which the user desires access.  In order to

allow the first few utterances of a dialog to be both recognized and

verified, the verification resource on the MRCPv2 server retains a

buffer.  In this buffer, the MRCPv2 server accumulates recognized

utterances.  The client can later execute a verification method and

apply the buffered utterances to the current verification session.

Some voice user interfaces may require additional user input that

should not be subject to verification.  For example, the user's input

may have been recognized with low confidence and thus require a

confirmation cycle.  In such cases, the client should not execute the

Shanmugham & Burnett    Expires September 6, 2007             [Page 136]

Internet-Draft                   MRCPv2                       March 2007

VERIFY or VERIFY-FROM-BUFFER methods to collect and analyze the

caller's input.  A separate recognizer resource can analyze the

caller's response without any participation by the verification

resource.

Once the following conditions have been met:

1.  Voiceprint identity has been successfully established through the

voiceprint identifier headers of the START-SESSION method, and

2.  the verification mode has been set to one of "train" or "verify",

the verification resource may begin providing verification

information during verification operations.  If the verification

resource does not reach one of the two major states ("train" or

"verify") , it MUST report an error condition in the MRCPv2 status

code to indicate why the verification resource is not ready for the

corresponding usage.

The value of verification-mode is persistent within a verification

session.  If the client attempts to change the mode during a

verification session, the verification resource reports an error and

the mode retains its current value.

verification-mode            =  "Verification-Mode" ":"

verification-mode-string

verification-mode-string     =  "train"

/  "verify"

11.4.4.  Adapt-Model

This header indicates the desired behavior of the verification

resource after a successful verification operation.  If the value of

this header is "true", the audio collected during the verification

session MAY be used by the server to update the voiceprint to account

for ongoing changes in a speaker's incoming speech characteristics.

If the value is "false" (the default), the voiceprint MUST NOT be

updated from the latest audio.  This header MAY only occur in the

START-SESSION method.

adapt-model              = "Adapt-Model" ":" Boolean-value CRLF

11.4.5.  Abort-Model

The Abort-Model header indicates the desired behavior of the

verification resource upon session termination.  If the value of this

header is "true", any pending changes to a voiceprint due to

verification training or verification adaptation are discarded.  If

the value is "false" (the default), the pending changes for a

training session or a successful verification session are committed

Shanmugham & Burnett    Expires September 6, 2007             [Page 137]

Internet-Draft                   MRCPv2                       March 2007

to the voiceprint repository.  A value of "true" for Abort-Model

overrides a value of "true" for the Adapt-Model header.  This header

MAY only occur in END-SESSION method.

abort-model             = "Abort-Model" ":" Boolean-value CRLF

11.4.6.  Min-Verification-Score

The Min-Verification-Score header, when used with a verification

resource through a "SET-PARAMS", "GET-PARAMS" or START-SESSION

method, determines the minimum verification score for which a

verification decision of "accepted" may be declared by the server.

This is a float value between -1.0 and 1.0 determines the minimum

verification score for which a verification decision of "accepted"

may be declared by the server.  The default value for this header is

implementation specific.

min-verification-score  = "Min-Verification-Score" ":"

[ %2D ] Float-value CRLF

11.4.7.  Num-Min-Verification-Phrases

The Num-Min-Verification-Phrases header is used to specify the

minimum number of valid utterances before a positive decision is

given for verification.  The value syntax for this header is integer

and the default value is 1.  The verification resource MUST NOT

declare a verification 'accepted' unless Num-Min-Verification-Phrases

valid utterances have been received.  The minimum value is 1.

num-min-verification-phrases =  "Num-Min-Verification-Phrases" ":"

1*DIGIT CRLF

11.4.8.  Num-Max-Verification-Phrases

The Num-Max-Verification-Phrases header is used to specify the number

of valid utterances required before a decision is forced for

verification.  The verification resource MUST NOT return a decision

of 'undecided' once Num-Max-Verification-Phrases have been collected

and used to determine a verification score.  The value for this

header is integer and the minimum value is 1.

num-min-verification-phrases =  "Num-Max-Verification-Phrases" ":"

1*DIGIT CRLF

Shanmugham & Burnett    Expires September 6, 2007             [Page 138]

Internet-Draft                   MRCPv2                       March 2007

11.4.9.  No-Input-Timeout

The No-Input-Timeout header sets the length of time from the start of

the verification timers (see START-INPUT-TIMERS) until the

declaration of a no-input event in the VERIFICATION-COMPLETE server

event message.  The value is in milliseconds.  This header MAY occur

in VERIFY, "SET-PARAMS" or "GET-PARAMS".  The value for this header

ranges from 0 to an implementation specific maximum value.  The

default value for this header is implementation specific.

no-input-timeout         = "No-Input-Timeout" ":" 1*DIGIT CRLF

11.4.10.  Save-Waveform

This header allows the client to request the verification resource to

save the audio stream that was used for verification/identification.

The verification resource MUST attempt to record the audio and make

it available to the client in the form of a URI returned in the

waveform-uri header in the VERIFICATION-COMPLETE event.  If there was

an error in recording the stream or the audio content is otherwise

not available, the verification resource MUST return an empty

waveform-uri header.  The default value for this header is "false".

This header MAY appear in the VERIFY method, but NOT in the VERIFY-

FROM-BUFFER method since it can control whether or not to save the

waveform for live verification / identification operations only.

save-waveform            =  "Save-Waveform" ":" boolean-value CRLF

11.4.11.  Media Type

This header MAY be specified in the SET-PARAMS, GET-PARAMS or the

VERIFY methods and tells the server resource the MIME content type in

which to store captured audio or video such as the one captured and

returned by the Waveform-URI header.

media-type               =  "Media-Type" ":" media-type-value

CRLF

11.4.12.  Waveform-URI

If the save-waveform header is set to true, the verification resource

MUST attempt to record the incoming audio stream of the verification

into a file and provide a URI for the client to access it.  This

header MUST be present in the VERIFICATION-COMPLETE event if the

save-waveform header was set to true by the client.  The URI value of

the header MUST be NULL if there was some error condition preventing

the server from recording.  Otherwise, the URI generated by the

server MUST be globally unique across the server and all its

Shanmugham & Burnett    Expires September 6, 2007             [Page 139]

Internet-Draft                   MRCPv2                       March 2007

verification sessions.  The content MUST be available via the URI

until the verification session ends.  Since the save-waveform header

applies only to live verification / identification operations, the

waveform-uri is only be returned in the VERIFICATION-COMPLETE event

for live verification / identification operations.

The server MUST also return the size in bytes and the duration in

milliseconds of the recorded audio wave-form as parameters associated

with the header.

waveform-uri             =  "Waveform-URI" ":" "<" Uri ">"

";" "size" "=" 1*DIGIT

";" "duration" "=" 1*DIGIT CRLF

11.4.13.  Voiceprint-Exists

This header is returned in a QUERY-VOICEPRINT or DELETE-VOICEPRINT

response.  This is the status of the voiceprint specified in the

QUERY-VOICEPRINT method.  For the DELETE-VOICEPRINT method this

header indicates the status of the voiceprint at the moment the

method execution started.

voiceprint-exists    =  "Voiceprint-Exists" ":" Boolean-value CRLF

11.4.14.  Ver-Buffer-Utterance

This header is used to indicate that this utterance could be later

considered for Speaker Verification.  This way, a client can request

the server to buffer utterances while doing regular recognition or

verification activities and speaker verification can later be

requested on the buffered utterances.  This header is OPTIONAL in the

RECOGNIZE, VERIFY and RECORD methods.  The default value for this

header is "false".

ver-buffer-utterance     = "Ver-Buffer-Utterance" ":" Boolean-value

CRLF

11.4.15.  Input-Waveform-Uri

This optional header specifies stored audio content that the client

requests the server to fetch and process according to the current

verification mode, either to train the voiceprint or verify a claimed

identity.  This header enables the client to implement the buffering

use case where the recognizer and verification resources are in

different sessions and the verification buffer technique cannot be

used.  It MAY specified on the VERIFY request.

input-waveform-uri           =  "Input-Waveform-URI" ":" Uri CRLF

Shanmugham & Burnett    Expires September 6, 2007             [Page 140]

Internet-Draft                   MRCPv2                       March 2007

11.4.16.  Completion-Cause

This header MUST be part of a VERIFICATION-COMPLETE event from the

verification resource to the client.  This indicates the cause of

VERIFY or VERIFY-FROM-BUFFER method completion.  This header MUST be

sent in the VERIFY, VERIFY-FROM-BUFFER, QUERY-VOICEPRINT responses,

if they return with a failure status and a COMPLETE state.

completion-cause         = "Completion-Cause" ":" 1*DIGIT SP

1*VCHAR CRLF

+------------+--------------------------+---------------------------+

| Cause-Code | Cause-Name               | Description               |

+------------+--------------------------+---------------------------+

| 000        | success                  | VERIFY or                 |

|            |                          | VERIFY-FROM-BUFFER        |

|            |                          | request completed         |

|            |                          | successfully.  The verify |

|            |                          | decision can be           |

|            |                          | "accepted", "rejected",   |

|            |                          | or "undecided".           |

| 001        | error                    | VERIFY or                 |

|            |                          | VERIFY-FROM-BUFFER        |

|            |                          | request terminated        |

|            |                          | prematurely due to a      |

|            |                          | verification resource or  |

|            |                          | system error.             |

| 002        | no-input-timeout         | VERIFY request completed  |

|            |                          | with no result due to a   |

|            |                          | no-input-timeout.         |

| 003        | too-much-speech-timeout  | VERIFY request completed  |

|            |                          | result due to too much    |

|            |                          | speech.                   |

| 004        | speech-too-early         | VERIFY request completed  |

|            |                          | with no result due to     |

|            |                          | spoke too soon.           |

| 005        | buffer-empty             | VERIFY-FROM-BUFFER        |

|            |                          | request completed with no |

|            |                          | result due to empty       |

|            |                          | buffer.                   |

| 006        | out-of-sequence          | Verification operation    |

|            |                          | failed due to             |

|            |                          | out-of-sequence method    |

|            |                          | invocations.  For example |

|            |                          | calling VERIFY before     |

|            |                          | QUERY-VOICEPRINT.         |

| 007        | repository-uri-failure   | Failure accessing         |

|            |                          | Repository URI.           |

Shanmugham & Burnett    Expires September 6, 2007             [Page 141]

Internet-Draft                   MRCPv2                       March 2007

| 008        | repository-uri-missing   | Repository-uri is not     |

|            |                          | specified.                |

| 009        | voiceprint-id-missing    | Voiceprint-identification |

|            |                          | is not specified.         |

| 010        | voiceprint-id-not-exist  | Voiceprint-identification |

|            |                          | does not exist in the     |

|            |                          | voiceprint repository.    |

+------------+--------------------------+---------------------------+

11.4.17.  Completion Reason

This header MAY be specified in a VERIFICATION-COMPLETE event coming

from the verifier resource to the client.  It contains the reason

text behind the VERIFY request completion.  This header can be use to

communicate text describing the reason for the failure.

The completion reason text is provided for client use in logs and for

debugging and instrumentation purposes.  Clients are NOT REQUIRED to

interpret the completion reason text.

completion-reason        =  "Completion-Reason" ":"

quoted-string CRLF

11.4.18.  Speech Complete Timeout

This header is the same as the one described for the Recognizer

resource.  See Section 9.4.15.

11.4.19.  New Audio Channel

This header is the same as the one described for the Recognizer

resource.  See Section 9.4.23

11.4.20.  Abort-Verification

This header MUST be sent in a "STOP" request to indicate whether or

not to abort a VERIFY method in progress.  A value of "true" requests

the server to discard the results.  A value of "false" requests the

server to return in the "STOP" response the verification results

obtained up to the point it received the "STOP" request.

Abort-verification   =  "Abort-Verification " ":" Boolean-value CRLF

11.4.21.  Start Input Timers

This header MAY be sent as part of a VERIFY request.  A value of

false tells the verification resource to start the VERIFY operation,

but not to start the no-input timer yet.  The verification resource

Shanmugham & Burnett    Expires September 6, 2007             [Page 142]

Internet-Draft                   MRCPv2                       March 2007

MUST NOT start the timers until the client sends a START-INPUT-TIMERS

request to the resource.  This is useful in the scenario when the

verifier and synthesizer resources are not part of the same session.

in this scenario, when a kill-on-barge-in prompt is being played, the

client may want the VERIFY request to be simultaneously active so

that it can detect and implement kill-on-barge-in.  But at the same

time the client doesn't want the verification resource to start the

no-input timers until the prompt is finished.  The default value is

"true".

start-input-timers       =  "Start-Input-Timers" ":"

boolean-value CRLF

11.5.  Verification Message Body

A verification response or event message may carry additional data as

described in the following subsection.

11.5.1.  Verification Result Data

Verification results are returned to the client in the message body

of the VERIFICATION-COMPLETE event or the GET-INTERMEDIATE-RESULT

response message as described in Section 6.3).  Element and attribute

descriptions for the verification portion of the NLSML format are

provided in Section 11.5.2 with a normative definition of the schema

in Section 16.3.

11.5.2.  Verification Result Elements

All verification elements are contained within a single

<verification-result> element under <result>.  The elements are

described below and have the schema defined in Section 16.2.  The

following elements are defined:

1.   Voiceprint

2.   Incremental

3.   Cumulative

4.   Decision

5.   Utterance-Length

6.   Device

7.   Gender

8.   Adapted

9.   Verification-Score

10.  Vendor-Specific-Results

Shanmugham & Burnett    Expires September 6, 2007             [Page 143]

Internet-Draft                   MRCPv2                       March 2007

11.5.2.1.  Voiceprint

This element in the verification results provides information on how

the speech data matched a single voiceprint.  The result data

returned may have more than one such entity in the case of

Identification or Multi-Verification.  Each "<voiceprint>" element

and the XML data within the element describe verification result

information for how well the speech data matched that particular

voiceprint.  The list of voiceprint element data are ordered

according to their cumulative verification match scores, with the

highest score first.

11.5.2.2.  Cumulative

Within each "<voiceprint>" element there MUST be a "<cumulative>"

element with the cumulative scores of how well multiple utterances

matched the voiceprint.

11.5.2.3.  Incremental

The first "<voiceprint>" element MAY contain an "<incremental>"

element with the incremental scores of how well the last utterance

matched the voiceprint.

11.5.2.4.  Decision

This element is found within the "<incremental>" or "<cumulative>"

element within the verification results.  Its value indicates the

verification decision.  It can have the values of "accepted",

"rejected" or "undecided".

11.5.2.5.  Utterance-Length

This element MAY occur within either the "<incremental>" or

"<cumulative>" elements within the first "<voiceprint>" element.  Its

value indicates the size in milliseconds, respectively, of the last

utterance or the cumulated set of utterances.

11.5.2.6.  Device

This element is found within the incremental or cumulative element

within the verification results.  Its value indicates the apparent

type of device used by the caller as determined by the verification

resource.  It can have the values of "cellular-phone", "electret-

phone", "carbon-button-phone", or "unknown".

Shanmugham & Burnett    Expires September 6, 2007             [Page 144]

Internet-Draft                   MRCPv2                       March 2007

11.5.2.7.  Gender

This element is found within the incremental or cumulative element

within the verification results.  Its value indicates the apparent

gender of the speaker as determined by the verification resource.  It

can have the values of "male", "female" or "unknown".

11.5.2.8.  Adapted

This element is found within the "<voiceprint>" element within the

verification results.  When verification is trying to confirm the

voiceprint, this indicates if the voiceprint has been adapted as a

consequence of analyzing the source utterances.  It is not returned

during verification training.  The value can be "true" or "false".

11.5.2.9.  Verification-Score

This element is found within the incremental or cumulative element

within the verification results.  Its value indicates the score of

the last utterance as determined by verification.

During verification, the higher the score the more likely it is that

the speaker is the same one as the one who spoke the voiceprint

utterances.  During training, the higher the score the more likely

the speaker is to have spoken all of the analyzed utterances.  The

value is a floating point between -1.0 and 1.0.  If there are no such

utterances the score is -1.  Note that the verification score is not

a probability value.

11.5.2.10.  Vendor-Specific-Results

Verification results may contain implementation specific data which

augment the information provided by the MRCPv2-defined elements.

These may be useful to clients who have private knowledge of how to

interpret these schema extensions.  Implementation specific additions

to the verification results schema MUST belong to the vendor's own

namespace.  In the result structure, they must either be indicated by

a namespace prefix declared within the result or must be children of

an element identified as belonging to the respective namespace.

The following example shows the results of three voiceprints.  Note

that the first one has crossed the verification score threshold, and

the speaker has been accepted.  The voiceprint was also adapted with

the most recent utterance.

Shanmugham & Burnett    Expires September 6, 2007             [Page 145]

Internet-Draft                   MRCPv2                       March 2007

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

grammar="What-Grammar-URI">

<verification-result>

<voiceprint id="johnsmith">

<adapted> true </adapted>

<incremental>

<utterance-length> 500 </utterance-length>

<device> cellular-phone </device>

<gender> male </gender>

<decision> accepted </decision>

<verification-score> 0.98514 </verification-score>

</incremental>

<cumulative>

<utterance-length> 10000 </utterance-length>

<device> cellular-phone </device>

<gender> male </gender>

<decision> accepted </decision>

<verification-score> 0.96725</verification-score>

</cumulative>

</voiceprint>

<voiceprint id="marysmith">

<cumulative>

<verification-score> 0.93410 </verification-score>

</cumulative>

</voiceprint>

<voiceprint uri="juniorsmith">

<cumulative>

<verification-score> 0.74209 </verification-score>

</cumulative>

</voiceprint>

</verification-result>

</result>

Verification Results Example 1

In this next example, the verifier has enough information to decide

to reject the speaker.

Shanmugham & Burnett    Expires September 6, 2007             [Page 146]

Internet-Draft                   MRCPv2                       March 2007

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:xmpl="http://www.example.org/2003/12/mrcpv2"

grammar="What-Grammar-URI">

<verification-result>

<voiceprint id="johnsmith">

<incremental>

<utterance-length> 500 </utterance-length>

<device> cellular-phone </device>

<gender> male </gender>

<verification-score> 0.88514 </verification-score>

<xmpl:raspiness> high </xmpl:raspiness>

<xmpl:emotion> sadness </xmpl:emotion>

</incremental>

<cumulative>

<utterance-length> 10000 </utterance-length>

<device> cellular-phone </device>

<gender> male </gender>

<decision> rejected </decision>

<verification-score> 0.9345 </verification-score>

</cumulative>

</voiceprint>

</verification-result>

</result>

Verification Results Example 2

11.6.  START-SESSION

The START-SESSION method starts a Speaker Verification or

Identification session.  Execution of this method places the

verification resource into its initial state.  If this method is

called during an ongoing verification session, the previous session

is implicitly aborted.  If this method is invoked when VERIFY or

VERIFY-FROM-BUFFER is active, the method fails and the server returns

a status code of 402.

Upon completion of the START-SESSION method, the verification

resource MUST have terminated any ongoing verification session, and

cleared any voiceprint designation.

A verification session is associated with the voiceprint repository

to be used during the session.  This is specified through the

"Repository-URI" header (see Section 11.4.1).

The START-SESSION method also establishes, through the Voiceprint-

Identifier header, which voiceprints are to be matched or trained

during the verification session.  If this is an Identification

Shanmugham & Burnett    Expires September 6, 2007             [Page 147]

Internet-Draft                   MRCPv2                       March 2007

session or if the client wants to do Multi-Verification, the

Voiceprint-Identifier header contains a list of semi-colon separated

voiceprint identifiers.

The header "Adapt-Model" may also be present in the START-SESSION

request to indicate whether or not to adapt a voiceprint based on

data collected during the session (if the voiceprint verification

phase succeeds).  By default, the voiceprint model MUST NOT be

adapted with data from a verification session.

The START-SESSION also determines whether the session is for a train

or verify of a voiceprint.  Hence the Verification-Mode header MUST

be sent in every START-SESSION request.  The value of the

Verification-Mode header MUST be one of either "train" or "verify".

Before a verification/identification session is started, only VERIFY-

ROLLBACK and generic "SET-PARAMS" and "GET-PARAMS" operations may be

performed on the verification resource.  The server MUST return 402

"Method not valid in this state" for all other verification

operations.

A verification resource may only have a single session active at one

time.

C->S:  MRCP/2.0 123 START-SESSION 314161

Channel-Identifier:32AECB23433801@speakverify

Repository-URI:http://www.example.com/voiceprintdbase/

Voiceprint-Mode:verify

Voiceprint-Identifier:johnsmith.voiceprint

Adapt-Model:true

S->C:  MRCP/2.0 49 314161 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

11.7.  END-SESSION

The END-SESSION method terminates an ongoing verification session and

releases the verification voiceprint resources.  The session may

terminate in one of three ways:

a.  abort - the voiceprint adaptation or creation may be aborted so

that the voiceprint remains unchanged (or is not created).

b.  commit - when terminating a voiceprint training session, the new

voiceprint is committed to the repository.

c.  adapt - an existing voiceprint is modified using a successful

verification.

The header "Abort-Model" MAY be included in the END-SESSION to

control whether or not to abort any pending changes to the

Shanmugham & Burnett    Expires September 6, 2007             [Page 148]

Internet-Draft                   MRCPv2                       March 2007

voiceprint.  The default behavior is to commit (not abort) any

pending changes to the designated voiceprint.

The END-SESSION method may be safely executed multiple times without

first executing the START-SESSION method.  Any additional executions

of this method without an intervening use of the START-SESSION method

have no effect on the verification resource.

The following example assumes there is either a training session or a

verification session in progress.

C->S:  MRCP/2.0 123 END-SESSION 314174

Channel-Identifier:32AECB23433801@speakverify

Abort-Model:true

S->C:  MRCP/2.0 49 314174 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

11.8.  QUERY-VOICEPRINT

The QUERY-VOICEPRINT method is used to get status information on a

particular voiceprint and can be used by the client to ascertain if a

voiceprint or repository exists and if it contains trained

voiceprints.

The response to the QUERY-VOICEPRINT request contains an indication

of the status of the designated voiceprint in the "Voiceprint-Exists"

header, allowing the client to determine whether to use the current

voiceprint for verification, train a new voiceprint, or choose a

different voiceprint.

A Voiceprint is completely specified by providing a repository

location and a voiceprint identifier.  The particular voiceprint or

identity within the repository is specified by string identifier

unique within the repository.  The "Voiceprint-Identifier" header

carries this unique voiceprint identifier within a given repository.

The following example assumes a verification session is in progress

and the voiceprint exists in the voiceprint repository.

Shanmugham & Burnett    Expires September 6, 2007             [Page 149]

Internet-Draft                   MRCPv2                       March 2007

C->S:  MRCP/2.0 123 QUERY-VOICEPRINT 314168

Channel-Identifier:32AECB23433801@speakverify

Repository-URI:http://www.example.com/voiceprints/

Voiceprint-Identifier:johnsmith.voiceprint

S->C:  MRCP/2.0 123 314168 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

Repository-URI:http://www.example.com/voiceprints/

Voiceprint-Identifier:johnsmith.voiceprint

Voiceprint-Exists:true

The following example assumes that the URI provided in the

'Repository-URI' header is a bad URI.

C->S:  MRCP/2.0 123 QUERY-VOICEPRINT 314168

Channel-Identifier:32AECB23433801@speakverify

Repository-URI:http://www.example.com/bad-uri/

Voiceprint-Identifier:johnsmith.voiceprint

S->C:  MRCP/2.0 123 314168 405 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

Repository-URI:http://www.example.com/bad-uri/

Voiceprint-Identifier:johnsmith.voiceprint

Completion-Cause:007 repository-uri-failure

11.9.  DELETE-VOICEPRINT

The DELETE-VOICEPRINT method removes a voiceprint from a repository.

This method MUST carry the Repository-URI and Voiceprint-Identifier

header fields.

If the corresponding voiceprint does not exist, the DELETE-VOICEPRINT

method still returns a 200 status code.

The following example demonstrates a DELETE-VOICEPRINT operation to

remove a specific voiceprint.

C->S:  MRCP/2.0 123 DELETE-VOICEPRINT 314168

Channel-Identifier:32AECB23433801@speakverify

Repository-URI:http://www.example.com/bad-uri/

Voiceprint-Identifier:johnsmith.voiceprint

S->C:  MRCP/2.0 49 314168 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

Shanmugham & Burnett    Expires September 6, 2007             [Page 150]

Internet-Draft                   MRCPv2                       March 2007

11.10.  VERIFY

The VERIFY method is used to request the verification resource to

either train/adapt the voiceprint or to verify/identify a claimed

identity.  If the voiceprint is new or was deleted by a previous

DELETE-VOICEPRINT method, the VERIFY method trains the voiceprint.

If the voiceprint already exits, it is adapted and not re-trained by

the VERIFY command..

C->S:  MRCP/2.0 49 VERIFY 543260

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 49 543260 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speakverify

When the VERIFY request is completes, the MRCPv2 server sends a

'VERIFICATION-COMPLETE' event to the client.

11.11.  VERIFY-FROM-BUFFER

The VERIFY-FROM-BUFFER method directs the verification resource to

verify buffered audio against a voiceprint.  Only one VERIFY or

VERIFY-FROM-BUFFER method may be active for a verification resource

at a time.

The buffered audio is not consumed by this method and thus VERIFY-

FROM-BUFFER may be invoked multiple times by the client to attempt

verification against different voiceprints.

For VERIFY-FROM-BUFFER method, the server MAY optionally return an

"IN-PROGRESS" response before the "VERIFICATION-COMPLETE" event.

When the VERIFY-FROM-BUFFER method is invoked and the verification

buffer is in use by another resource sharing it, the server MUST

return an IN-PROGRESS response and wait until the buffer is available

to it.  The verification buffer is owned by the verification resource

but is shared with write access from other input resources on the

same session.  Hence, it is considered to be in use if there is a

read or write operation such as, a RECORD or RECOGNIZE with the ver-

buffer-utterance header set to "true", on a resource that shares this

buffer.  Note that if a RECORD or RECOGNIZE method returns with a

failure cause code, the VERIFY-FROM-BUFFER request waiting to process

that buffer MUST also fail with a Completion-Cause of 005 (buffer-

empty).

The following example illustrates the usage of some buffering

methods.  In this scenario the client first performed a live

verification, but the utterance had been rejected.  In the meantime,

Shanmugham & Burnett    Expires September 6, 2007             [Page 151]

Internet-Draft                   MRCPv2                       March 2007

the utterance is also saved to the audio buffer.  Then, another

voiceprint is used to do verification against the audio buffer and

the utterance is accepted.  For the example, we assume both 'num-min-

verification-phrases' and 'num-max-verification-phrases' are 1.

C->S:  MRCP/2.0 123 START-SESSION 314161

Channel-Identifier:32AECB23433801@speakverify

Verification-Mode:verify

Adapt-Model:true

Repository-URI:http://www.example.com/voiceprints

Voiceprint-Identifier:johnsmith.voiceprint

S->C:  MRCP/2.0 49 314161 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

C->S:  MRCP/2.0 123 VERIFY 314162

Channel-Identifier:32AECB23433801@speakverify

Ver-buffer-utterance:true

S->C:  MRCP/2.0 49 314164 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 123 VERIFICATION-COMPLETE 314162 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

Completion-Cause:000 success

Content-Type:application/nlsml+xml

Content-Length:123

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

grammar="What-Grammar-URI">

<verification-result>

<voiceprint id="johnsmith">

<incremental>

<utterance-length> 500 </utterance-length>

<device> cellular-phone </device>

<gender> female </gender>

<decision> rejected </decision>

<verification-score> 0.05465 </verification-score>

</incremental>

<cumulative>

<utterance-length> 500 </utterance-length>

<device> cellular-phone </device>

<gender> female </gender>

<decision> rejected </decision>

<verification-score> 0.05465 </verification-score>

</cumulative>

</voiceprint>

Shanmugham & Burnett    Expires September 6, 2007             [Page 152]

Internet-Draft                   MRCPv2                       March 2007

</verification-result>

</result>

C->S:  MRCP/2.0 123 QUERY-VOICEPRINT 314163

Channel-Identifier:32AECB23433801@speakverify

Repository-URI:http://www.example.com/voiceprints/

Voiceprint-Identifier:johnsmith

S->C:  MRCP/2.0 123 314163 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

Repository-URI:http://www.example.com/voiceprints/

Voiceprint-Identifier:johnsmith.voiceprint

Voiceprint-Exists:true

C->S:  MRCP/2.0 123 START-SESSION 314164

Channel-Identifier:32AECB23433801@speakverify

Verification-Mode:verify

Adapt-Model:true

Repository-URI:http://www.example.com/voiceprints

Voiceprint-Identifier:marysmith.voiceprint

S->C:  MRCP/2.0 49 314164 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

C->S:  MRCP/2.0 123 VERIFY-FROM-BUFFER 314165

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 49 314165 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 123 VERIFICATION-COMPLETE 314165 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

Completion-Cause:000 success

Content-Type:application/nlsml+xml

Content-Length:123

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

grammar="What-Grammar-URI">

<verification-result>

<voiceprint id="marysmith">

<incremental>

<utterance-length> 1000 </utterance-length>

<device> cellular-phone </device>

<gender> female </gender>

<decision> accepted </decision>

<verification-score> 0.98 </verification-score>

</incremental>

Shanmugham & Burnett    Expires September 6, 2007             [Page 153]

Internet-Draft                   MRCPv2                       March 2007

<cumulative>

<utterance-length> 1000 </utterance-length>

<device> cellular-phone </device>

<gender> female </gender>

<decision> accepted </decision>

<verification-score> 0.98 </verification-score>

</cumulative>

</voiceprint>

</verification-result>

</result>

C->S:  MRCP/2.0 49 END-SESSION 314166

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 49 314166 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

VERIFY-FROM-BUFFER example

11.12.  VERIFY-ROLLBACK

The VERIFY-ROLLBACK method discards the last buffered utterance or

discards the last live utterances (when the mode is "train" or

"verify").  The client should invoke this method when the user

provides undesirable input such as non-speech noises, side-speech,

out-of-grammar utterances, commands, etc.  Note that this method does

not provide a stack of rollback states.  Executing VERIFY-ROLLBACK

twice in succession without an intervening recognition operation has

no effect on the second attempt.

C->S:  MRCP/2.0 49 VERIFY-ROLLBACK 314165

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 49 314165 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

VERFY-ROLLBACK Example

11.13.  STOP

The "STOP" method from the client to the server tells the

verification resource to stop the VERIFY or VERIFY-FROM-BUFFER

request if one is active.  If such a request is active and the "STOP"

request successfully terminated it, then the response header contains

an active-request-id-list header containing the request-id of the

VERIFY or VERIFY-FROM-BUFFER request that was terminated.  In this

case, no VERIFICATION-COMPLETE event is sent for the terminated

Shanmugham & Burnett    Expires September 6, 2007             [Page 154]

Internet-Draft                   MRCPv2                       March 2007

request.  If there was no verify request active, then the response

MUST NOT contain an active-request-id-list header.  Either way the

response MUST contain a status of 200 (Success).

The "STOP" method can carry a "Abort-Verification" header which

specifies if the verification result until that point should be

discarded or returned.  If this header is not present or if the value

is "true", the verification result is discarded and the "STOP"

response does not contain any result data.  If the header is present

and its value is "false", the "STOP" response MUST contain a

"Completion-Cause" header and carry the Verification result data in

its body.

An aborted VERIFY request does an automatic roll-back and hence does

not affect the cumulative score.  A VERIFY request that was stopped

with no "Abort-Verification" header or with the "Abort-Verification"

header set to "false" does affect cumulative scores and would need to

be explicitly rolled-back if the client does not want the

verification result considered in the cumulative scores.

The following example assumes a voiceprint identity has already been

established.

C->S:  MRCP/2.0 123 VERIFY 314177

Channel-Identifier:32AECB23433801@speakverify

Verification-Mode:verify

S->C:  MRCP/2.0 49 314177 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speakverify

C->S:  MRCP/2.0 49 STOP 314178

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 123 314178 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

Active-Request-Id-List:314177

STOP verification Example

11.14.  START-INPUT-TIMERS

This request is sent from the client to the verification resource to

start the no-input timer, usually once the client has ascertained

that any audio prompts to the user have played to completion.

Shanmugham & Burnett    Expires September 6, 2007             [Page 155]

Internet-Draft                   MRCPv2                       March 2007

C->S:  MRCP/2.0 49 START-INPUT-TIMERS 543260

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 49 543260 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

11.15.  VERIFICATION-COMPLETE

The VERIFICATION-COMPLETE event follows a call to VERIFY or VERIFY-

FROM-BUFFER and is used to communicate the verification results to

the client.  The event message body contains only verification

results.

S->C:  MRCP/2.0 123 VERIFICATION-COMPLETE 543259 COMPLETE

Completion-Cause:000 success

Content-Type:application/nlsml+xml

Content-Length:123

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

grammar="What-Grammar-URI">

<verification-result>

<voiceprint id="johnsmith">

<incremental>

<utterance-length> 500 </utterance-length>

<device> cellular-phone </device>

<gender> male </gender>

<decision> accepted </decision>

<verification-score> 0.85 </verification-score>

</incremental>

<cumulative>

<utterance-length> 1500 </utterance-length>

<device> cellular-phone </device>

<gender> male </gender>

<decision> accepted </decision>

<verification-score> 0.75 </verification-score>

</cumulative>

</voiceprint>

</verification-result>

</result>

11.16.  START-OF-INPUT

The START-OF-INPUT event is returned from the server to the client

once the server has detected speech.  This event is always returned

by the verification resource when speech has been detected,

irrespective of whether the recognizer and verification resources

share the same session or not.

Shanmugham & Burnett    Expires September 6, 2007             [Page 156]

Internet-Draft                   MRCPv2                       March 2007

S->C:  MRCP/2.0 49 START-OF-INPUT 543259 IN-PROGRESS

Channel-Identifier:32AECB23433801@speakverify

11.17.  CLEAR-BUFFER

The CLEAR-BUFFER method can be used to clear the verification buffer.

This buffer is used to buffer speech during a recognition, record or

verification operations that may later be used VERIFY-FROM-BUFFER.

As noted before, the buffer associated with the verification resource

is shared by other input resources like recognizers and recorders.

Hence, a CLEAR-BUFFER request fails if the verification buffer is in

use.  This can happen when any one of the input resources that shares

this buffer has an active read or write operation such as RECORD,

RECOGNIZE or VERIFY with the ver-buffer-utterance header set to

"true".

C->S:  MRCP/2.0 49 CLEAR-BUFFER 543260

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 49 543260 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

11.18.  GET-INTERMEDIATE-RESULT

A client can use the GET-INTERMEDIATE-RESULT method to poll for

intermediate results of a verification request that is in progress.

Invoking this method does not change the state of the resource.  The

verification resource collects the accumulated verification results

and returns the information in the method response.  The message body

in the response to a GET-INTERMEDIATE-RESULT REQUEST contains only

verification results.  The method response MUST NOT contain a

Completion-Cause header as the request is not yet complete.  If the

resource does not have a verification in progress the response has a

402 failure code and no result in the body.

Shanmugham & Burnett    Expires September 6, 2007             [Page 157]

Internet-Draft                   MRCPv2                       March 2007

C->S:  MRCP/2.0 49 GET-INTERMEDIATE-RESULT 543260

Channel-Identifier:32AECB23433801@speakverify

S->C:  MRCP/2.0 49 543260 200 COMPLETE

Channel-Identifier:32AECB23433801@speakverify

Content-Type:application/nlsml+xml

Content-Length:123

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

grammar="What-Grammar-URI">

<verification-result>

<voiceprint id="marysmith">

<incremental>

<utterance-length> 50 </utterance-length>

<device> cellular-phone </device>

<gender> female </gender>

<decision> undecided </decision>

<verification-score> 0.85 </verification-score>

</incremental>

<cumulative>

<utterance-length> 150 </utterance-length>

<device> cellular-phone </device>

<gender> female </gender>

<decision> undecided </decision>

<verification-score> 0.65 </verification-score>

</cumulative>

</voiceprint>

</verification-result>

</result>

12.  Security Considerations

MRCPv2 is designed to comply with the security-related requirements

documented in SpeechSC Requirements [1].  Implementers and users of

MRCPv2 are strongly encouraged to read the Security Considerations

section of [1], because that document contains discussion of a number

of important security issues associated with the utilization of

speech as biometric authentication technology, and on the threats

against systems which store recorded speech, contain large corpora of

voiceprints, and send and receive sensitive information based on

voice input to a recognizer or speech output from a synthesizer.

Specific security measures employed by MRCPv2 are summarized in the

following subsections.  See the corresponding sections of this

specification for how the security-related machinery is invoked by

individual protocol operations.

Shanmugham & Burnett    Expires September 6, 2007             [Page 158]

Internet-Draft                   MRCPv2                       March 2007

12.1.  Rendezvous and Session Establishment

MRCPv2 control sessions are established as media sessions described

by SDP within the context of a SIP dialog.  In order to ensure secure

rendezvous between MRCPv2 clients and servers, the following are

required:

1.  The SIP implementation in MRCPv2 clients and servers MUST support

digest authentication.

2.  The SIP implementation in MRCPv2 clients and servers SHOULD

employ SIPS: URIs,

3.  If media stream cryptographic keying is done through SDP (e.g.

using Security Descriptions [23]), the MRCPv2 clients and servers

MUST employ SIPS:.

12.2.  Control channel protection

Sensitive data is carried over the MRCPv2 control channel.  This

includes things like the output of speech recognition operations,

speaker verification results, input to text-to-speech conversion,

etc.  For this reason MRCPv2 servers must be properly authenticated

and the control channel must permit the use of both confidentiality

and integrity for the data.  To ensure control channel protection,

MRCPv2 clients and servers MUST support TLS and SHOULD utilize it by

default unless alternative control channel protection is used.

Alternative control channel protection MAY be used if desired (e.g.

IPSEC).

12.3.  Media session protection

Sensitive data is also carried on media sessions terminating on

MRCPv2 servers (the other end of a media channel may or may not be on

the MRCPv2 client).  This data includes the user's spoken utterances

and the output of text-to-speech operations.  MRCPv2 servers MUST

support SRTP for protection of audio media sessions.  MRCPv2 clients

that originate or consume audio similarly MUST support SRTP.

Alternative media channel protection MAY be used if desired (e.g.

IPSEC).

12.4.  Indirect Content Access

MCRPv2 employs content indirection extensively.  Content may be

fetched and/or stored based on URI-addressing on systems other than

the MRCPv2 client or server.  Not all of the stored content is

necessarily sensitive (e.g. grammar definitions, XML schemas), but

the majority generally needs protection, and some indirect content,

such as voice recordings and voiceprints, are extremely sensitive and

must always be protected.  MRCPv2 clients and servers MUST implement

Shanmugham & Burnett    Expires September 6, 2007             [Page 159]

Internet-Draft                   MRCPv2                       March 2007

HTTPS for indirect content access, and SHOULD employ secure access

for all sensitive indirect content.  Other secure URI-schemes, such

as FTPS or SIPS MAY also be used.

12.5.  Protection of stored media

MRCPv2 applications often require the use of stored media.  Voice

recordings are both stored (e.g. for diagnosis and system tuning),

and fetched (for replaying utterances into multiple MRCPv2

resources).  Voiceprints are fundamental to the speaker

identification and verification functions.  This data can be

extremely sensitive and can present substantial privacy and

impersonation risks if stolen.  Systems employing MRCPv2 should be

deployed in ways that minimize these risks.  The SpeechSC

Requirements [1] contains a more extensive discussion of these risks

and ways they may be mitigated.

13.  IANA Considerations

13.1.  New registries

This section describes the name spaces (registries) for MRCPv2 that

IANA is requested to create and maintain.  Assignment/registration

policies are described in RFC2434 [18].

13.1.1.  MRCPv2 resource types

IANA SHALL create a new name space of "MRCPv2 resource types" with

the initial values that are defined in section 4.2.  All maintenance

within and additions to the contents of this name space MUST be

according to the "Standards Action" registration policy.

13.1.2.  MRCPv2 methods and events

IANA SHALL create a new name space of "MRCPv2 methods and events"

with the initial values that are defined by the "method-name" BNF in

section 5.1 and the "event-name" BNF in section 5.3.  All maintenance

within and additions to the contents of this name space MUST be

according to the "Standards Action" registration policy.

13.1.3.  MRCPv2 headers

IANA SHALL create a new name space of "MRCPv2 headers" with the

initial values that are defined by the "message-header" BNF in

section 5.  All maintenance within and additions to the contents of

this name space MUST be according to the "Standards Action"

registration policy.  Note that the values permitted for the "Vendor-

Shanmugham & Burnett    Expires September 6, 2007             [Page 160]

Internet-Draft                   MRCPv2                       March 2007

Specific-Parameters" parameter are managed according to a different

policy.  See "MRCPv2 vendor-specific parameters", below.

13.1.4.  MRCPv2 status codes

IANA SHALL create a new name space of "MRCPv2 status codes" with the

initial values that are defined in section 5.2.  All maintenance

within and additions to the contents of this name space MUST be

according to the "Specification Required with Expert Review"

registration policy.

13.1.5.  Grammar Reference List Parameters

IANA SHALL create a new name space of "Grammar Reference List

Parameters" with the initial values that are defined in section 13.6.

All maintenance within and additions to the contents of this name

space MUST be according to the "Specification Required with Expert

Review" registration policy.

13.1.6.  MRCPv2 vendor-specific parameters

IANA SHALL create a new name space of "MRCPv2 vendor-specific

parameters".  All maintenance within and additions to the contents of

this name space MUST be according to the "Hierarchical Allocation"

registration policy as follows.  Each name (corresponding to the

"vendor-av-pair-name" ABNF production) MUST satisfy the syntax

requirements of Internet Domain Names as described in section 2.3.1

of RFC1035 [19] (and as updated or obsoleted by successive RFCs),

with one exception, the order of the domain names is reversed.  For

example, a vendor-specific parameter "foo" by example.com would have

the form "com.example.foo".  The first, or top-level domain, is

restricted to exactly the set of Top-Level Internet Domains defined

by IANA and will be updated by IANA when and only when that set

changes.  The second-level and all subdomains within the parameter

name MUST be allocated according to the "Expert Review" policy.  The

Designated Expert MAY advise IANA to allow delegation of subdomains

to the requester.  As a general guideline, the Designated Expert is

encouraged to manage the allocation of corporate, organizational, or

institutional names and delegate all subdomains accordingly.  For

example, the Designated Expert MAY allocate "com.example" and

delegate all subdomains of that name to the organization represented

by the Internet domain name "example.com".  For simplicity, the

Designated Expert is encouraged to perform allocations according to

the existing allocations of Internet domain names to organizations,

institutions, corporations, etc.

Shanmugham & Burnett    Expires September 6, 2007             [Page 161]

Internet-Draft                   MRCPv2                       March 2007

13.2.  NLSML-related registrations

13.2.1.  application/nlsml+xml MIME type registration

IANA is requested to register the following MIME type according to

the process defined in RFC4288 [20].

To ietf-types@iana.org

Subject  Registration of MIME media type application/nlsml+xml

MIME media type name  application

MIME subtype name  nlsml+xml

Required parameters  none

Optional parameters

charset  All of the considerations described in RFC3023 also apply

to the application/nlsml+xml media type.

Encoding considerations  All of the considerations described in

RFC3023 also apply to the application/nlsml+xml media type.

Security considerations  As with HTML, NLSML documents contain links

to other data stores (grammars, verification resources, etc.).

Unlike HTML, however, the data stores are not treated as media to

be rendered.  Nevertheless, linked files may themselves have

security considerations, which would be those of the individual

registered types.  Additionally, this media type has all of the

security considerations described in RFC3023.

Interoperability considerations  Although an NLSML document is itself

a complete XML document, for a fuller interpretation of the

content a receiver of an NLSML document may wish to access

resources linked to by the document.  The inability of an NLSML

processor to access or process such linked resources could result

in different behavior by the ultimate consumer of the data.

Published specification  RFCXXXX

Applications which use this media type  MRCPv2 clients and servers

Additional information  none

Magic number(s)  There is no single initial byte sequence that is

always present for NLSML files.

Person & email address to contact for further information  Sarvi

Shanmugham, sarvi@cisco.com

Intended usage  This media type is expected to be used only in

conjunction with MRCPv2.

13.3.  NLSML XML Schema registration

IANA is requested to register and maintain the following XML Schema.

Information provided follows the template in RFC3688 [21].

XML element type  schema

Shanmugham & Burnett    Expires September 6, 2007             [Page 162]

Internet-Draft                   MRCPv2                       March 2007

URI  http://www.ietf.org/xml/schema/mrcpv2

Registrant Contact  IESG

XML  See Section 16.1.

13.4.  MRCPv2 XML Namespace registration

IANA is requested to register and maintain the following XML Name

space.  Information provided follows the template in RFC3688 [21].

XML element type  ns

URI  http://www.ietf.org/xml/ns/mrcpv2

Registrant Contact  IESG

XML  RFCXXXX

13.5.  text/grammar-ref-list Mime Type Registration

IANA is requested to register the following MIME type according to

the process defined in RFC 4288. [20]

To ietf-types@iana.org

Subject  Registration of MIME media type text/grammar-ref-list

MIME media type name  application

MIME subtype name  text/grammar-ref-list

Required parameters  none

Optional parameters  none

Encoding considerations  Depending on the transfer protocol, a

transfer encoding may be necessary to deal with very long lines.

Security considerations  This media type contains URIs which may

represent references to external resources.  As these resources

are assumed to be speech recognition grammars, similar

considerations as for the media types "application/srgs" and

"application/srgs+xml" [1] apply.

Interoperability considerations  We make the assumption that '>' is

not a valid character in a URI according to RFC3986.

Published specification  The RECOGNIZE method of the MRCP protocol

performs a recognition operation that matches input against a set

of grammars.  When matching against more than one grammar, it is

sometimes necessary to use different weights for the individual

grammars.  These weights are not a property of the grammar

resource itself but qualify the reference to that grammar for the

particular recognition operation initiated by the RECOGNIZE

method.  The format of the proposed text/grammar-ref-list media

type is as follows: body = *reference where reference = "<" uri

">" [parameters] CRLF parameters = ";" parameter *(";" parameter)

and parameter = attribute "=" value.  This specification currently

only defines a 'weight' parameter, but new parameters may be added

through the "Grammar Reference List Parameters" IANA registry

established through this specification.  Example:

<http://example.com/grammars/field1.gram>

<http://example.com/grammars/field2.gram>;weight="0.85"

Shanmugham & Burnett    Expires September 6, 2007             [Page 163]

Internet-Draft                   MRCPv2                       March 2007

<session:field3@form-level.store>;weight="0.9"

<http://example.com/grammars/universals.gram>;weight="0.75"

Applications which use this media type  MRCPv2 clients and servers

Additional information  none

Magic number(s)  none

Person & email address to contact for further information  Sarvi

Shanmugham, sarvi@cisco.com

Intended usage  This media type is expected to be used only in

conjunction with MRCPv2.

13.6.  session URL scheme registration

IANA is requested to register the following new URI scheme.  The

information below follows the template given in RFC4395 [22].

URL scheme name  "session"

URL scheme syntax  The syntax of this scheme is identical to that

defined for the "cid" scheme in section 2 of RFC2392.

Character encoding considerations  URL values are limited to the US-

ASCII character set.

Intended usage  The URL is intended to identify a data resource

previously given to the network computing resource.  The purpose

of this scheme is to permit access to the specific resource for

the lifetime of the session with the entity storing the resource.

The media type of the resource CAN vary.  There is no explicit

mechanism for communication of the media type.

Applications and/or protocols which use this URL scheme name  This

scheme name is used by MRCPv2 clients and servers.

Interoperability considerations

The character set for URLs is restricted to US-ASCII.  Note that

none of the resources are accessible after the MCRPv2 session

ends, hence the name of the scheme.  For clients who establish one

MRCPv2 session only for the entire speech application being

implemented this is sufficient, but clients who create, terminate,

and recreate MRCP sessions for performance or scalability reasons

will lose access to resources established in the earlier

session(s).

Security considerations  The URLs defined here provide an addressing

or referencing mechanism only.  Given that the communication

channel between client and server is secure, that the server

correctly accesses the resource associated with the URL, and that

the server ensures session-only lifetime and access for each URL,

the only remaining security issues are those of the types of media

referred to by the URL.

Relevant publications  This specification, particularly sections 6.1

"Content-ID", 8.5 "Lexicon Data", 9.5 "Recognizer Grammar Data",

and 9.9 "RECOGNIZE".

Shanmugham & Burnett    Expires September 6, 2007             [Page 164]

Internet-Draft                   MRCPv2                       March 2007

Contact for further information  Sarvi Shanmugham, sarvi@cisco.com

Author/Change controller  IESG

13.7.  SDP parameter registrations

IANA is requested to register the following SDP parameter values.

The information for each follows the template given in RFC4566 [4],

Appendix B.

"TCP/MRCPv2" value of the "proto" parameter

Contact name, email address and telephone number  Sarvi Shanmugham,

sarvi@cisco.com, +1.408.902.3875

Name being registered (as it will appear in SDP)  TCP/MRCPv2

Long-form name in English  MCRPv2 over TCP

Type of name  proto

Explanation of name  This name represents the MCRPv2 protocol carried

over TCP.

Reference to specification of name  RFCXXXX

"TCP/TLS/MRCPv2" value of the "proto" parameter

Contact name, email address and telephone number  Sarvi Shanmugham,

sarvi@cisco.com, +1.408.902.3875

Name being registered (as it will appear in SDP)  TCP/TLS/MRCPv2

Long-form name in English  MCRPv2 over TLS over TCP

Type of name  proto

Explanation of name  This name represents the MCRPv2 protocol carried

over TLS over TCP.

Reference to specification of name  RFCXXXX

"resource" value of the "att-field" parameter

Contact name, email address and telephone number  Sarvi Shanmugham,

sarvi@cisco.com, +1.408.902.3875

Attribute name (as it will appear in SDP)  resource

Long-form attribute name in English  MRCPv2 resource type

Type of attribute  session-level

Subject to charset attribute?  no

Explanation of attribute  See section 4.2 of RFCXXXX for description

and examples

Specification of appropriate attribute values  See section 13.1,

"MRCPv2 resource types" of RFCXXXX.

"channel" value of the "att-field" parameter

Contact name, email address and telephone number  Sarvi Shanmugham,

sarvi@cisco.com, +1.408.902.3875

Shanmugham & Burnett    Expires September 6, 2007             [Page 165]

Internet-Draft                   MRCPv2                       March 2007

Attribute name (as it will appear in SDP)  channel

Long-form attribute name in English  MRCPv2 resource channel

identifier

Type of attribute  session-level

Subject to charset attribute?  no

Explanation of attribute  See section 4.2 of RFCXXXX for description

and examples

Specification of appropriate attribute values  See section 4.2 and

the "channel-id" ABNF production rules of RFCXXXX.

14.  Examples

14.1.  Message Flow

The following is an example of a typical MRCPv2 session of speech

synthesis and recognition between a client and a server.

The figure below illustrates opening a session to the MRCPv2 server.

This is exchange does not allocate a resource or setup media.  It

simply establishes a SIP session with the MRCPv2 server.

Shanmugham & Burnett    Expires September 6, 2007             [Page 166]

Internet-Draft                   MRCPv2                       March 2007

C->S:

INVITE sip:mresources@server.example.com SIP/2.0

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314159 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length:142

v=0

o=sarvi 2890844526 2890842807 IN IP4 192.168.64.4

s=SDP Seminar

i=A session for processing media

c=IN IP4 10.2.17.12

S->C:

SIP/2.0 200 OK

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314159 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length:131

v=0

o=sarvi 2890844526 2890842807 IN IP4 192.168.64.4

s=SDP Seminar

i=A session for processing media

c=IN IP4 10.2.17.11

C->S:

ACK sip:mrcp@server.example.com SIP/2.0

Max-Forwards:6

To:MediaServer <sip:mrcp@server.example.com>;tag=a6c85cf

From:Sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314160 ACK

Content-Length:0

The client requests the server to create synthesizer resource control

channel to do speech synthesis.  This also adds a media pipe to send

the generated speech.  Note that in this example, the client request

the reuse of an existing MRCPv2 TCP pipe between the client and the

Shanmugham & Burnett    Expires September 6, 2007             [Page 167]

Internet-Draft                   MRCPv2                       March 2007

server.

C->S:

INVITE sip:mresources@server.example.com SIP/2.0

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314161 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length:142

v=0

o=sarvi 2890844526 2890842808 IN IP4 192.168.64.4

s=SDP Seminar

i=A session for processing media

c=IN IP4 10.2.17.12

m=application 9  TCP/MRCPv2 1

a=setup:active

a=connection:existing

a=resource:speechsynth

a=cmid:1

m=audio 49170 RTP/AVP 0 96

a=rtpmap:0 pcmu/8000

a=recvonly

a=mid:1

S->C:

SIP/2.0 200 OK

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314161 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length:131

v=0

o=sarvi 2890844526 2890842808 IN IP4 192.168.64.4

s=SDP Seminar

i=A session for processing media

c=IN IP4 10.2.17.11

m=application 32416  TCP/MRCPv2 1

a=setup:passive

a=connection:existing

a=channel:32AECB23433801@speechsynth

Shanmugham & Burnett    Expires September 6, 2007             [Page 168]

Internet-Draft                   MRCPv2                       March 2007

a=cmid:1

m=audio 48260 RTP/AVP 0

a=rtpmap:0 pcmu/8000

a=sendonly

a=mid:1

C->S:

ACK sip:mrcp@server.example.com SIP/2.0

Max-Forwards:6

To:MediaServer <sip:mrcp@server.example.com>;tag=a6c85cf

From:Sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314162 ACK

Content-Length:0

This exchange allocates an additional resource control channel for a

recognizer.  Since a recognizer would need to receive an audio stream

for recognition, this interaction also updates the audio stream to

sendrecv making it a 2-way audio stream.

C->S:

INVITE sip:mresources@server.example.com SIP/2.0

Max-Forwards:6

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314163 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length:142

v=0

o=sarvi 2890844526 2890842809 IN IP4 192.168.64.4

s=SDP Seminar

i=A session for processing media

c=IN IP4 10.2.17.12

m=application 9  TCP/MRCPv2 1

a=setup:active

a=connection:existing

a=resource:speechsynth

a=cmid:1

m=audio 49170 RTP/AVP 0 96

a=rtpmap:0 pcmu/8000

a=recvonly

a=mid:1

m=application 9  TCP/MRCPv2 1

a=setup:active

Shanmugham & Burnett    Expires September 6, 2007             [Page 169]

Internet-Draft                   MRCPv2                       March 2007

a=connection:existing

a=resource:speechrecog

a=cmid:2

m=audio 49180 RTP/AVP 0 96

a=rtpmap:0 pcmu/8000

a=rtpmap:96 telephone-event/8000

a=fmtp:96 0-15

a=sendonly

a=mid:2

S->C:

SIP/2.0 200 OK

To:MediaServer <sip:mresources@server.example.com>

From:sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314163 INVITE

Contact:<sip:sarvi@example.com>

Content-Type:application/sdp

Content-Length:131

v=0

o=sarvi 2890844526 2890842809 IN IP4 192.168.64.4

s=SDP Seminar

i=A session for processing media

c=IN IP4 10.2.17.11

m=application 32416  TCP/MRCPv2 1

a=channel:32AECB23433801@speechsynth

a=cmid:1

m=audio 48260 RTP/AVP 0

a=rtpmap:0 pcmu/8000

a=sendonly

a=mid:1

m=application 32416  TCP/MRCPv2 1

a=channel:32AECB23433801@speechrecog

a=cmid:2

m=audio 48260 RTP/AVP 0

a=rtpmap:0 pcmu/8000

a=rtpmap:96 telephone-event/8000

a=fmtp:96 0-15

a=recvonly

a=mid:2

C->S:

ACK sip:mrcp@server.example.com SIP/2.0

Max-Forwards:6

To:MediaServer <sip:mrcp@server.example.com>;tag=a6c85cf

Shanmugham & Burnett    Expires September 6, 2007             [Page 170]

Internet-Draft                   MRCPv2                       March 2007

From:Sarvi <sip:sarvi@example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:314164 ACK

Content-Length:0

A MRCPv2 "SPEAK" request initiates speech.

C->S:

MRCP/2.0 386 SPEAK 543257

Channel-Identifier:32AECB23433801@speechsynth

Kill-On-Barge-In:false

Voice-gender:neutral

Voice-age:25

Prosody-volume:medium

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>You have 4 new messages.</s>

<s>The first is from Stephanie Williams

<mark name="Stephanie"/>

and arrived at <break/>

<say-as interpret-as="vxml:time">0345p</say-as>.</s>

<s>The subject is <prosody

rate="-20%">ski trip</prosody></s>

</p>

</speak>

S->C:

MRCP/2.0 49 543257 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechsynth

Speech-Marker:timestamp=857205015059

The synthesizer hits the special marker in the message to be spoken

and faithfully informs the client of the event.

S->C:  MRCP/2.0 46 SPEECH-MARKER 543257 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechsynth

Speech-Marker:timestamp=857206027059;Stephanie

Shanmugham & Burnett    Expires September 6, 2007             [Page 171]

Internet-Draft                   MRCPv2                       March 2007

The synthesizer finishes with the "SPEAK" request.

S->C:  MRCP/2.0 48 SPEAK-COMPLETE 543257 COMPLETE

Channel-Identifier:32AECB23433801@speechsynth

Speech-Marker:timestamp=857207685213;Stephanie

The recognizer is issued a request to listen for the customer

choices.

C->S:  MRCP/2.0 343 RECOGNIZE 543258

Channel-Identifier:32AECB23433801@speechrecog

Content-Type:application/srgs+xml

Content-Length:104

<?xml version="1.0"?>

<!-- the default grammar language is US English -->

<grammar xmlns="http://www.w3.org/2001/06/grammar"

xml:lang="en-US" version="1.0" root="request">

<!-- single language attachment to a rule expansion -->

<rule id="request">

Can I speak to

<one-of xml:lang="fr-CA">

<item>Michel Tremblay</item>

<item>Andre Roy</item>

</one-of>

</rule>

</grammar>

S->C:  MRCP/2.0 49 543258 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

The client issues the next MRCPv2 "SPEAK" method.  It is generally

RECOMMENDED when playing a prompt to the user with kill-on-barge-in

and asking for input, that the client issue the RECOGNIZE request

ahead of the "SPEAK" request for optimum performance and user

experience.  This way, it is guaranteed that the recognizer is online

before the prompt starts playing and the user's speech will not be

truncated at the beginning (especially for power users).

Shanmugham & Burnett    Expires September 6, 2007             [Page 172]

Internet-Draft                   MRCPv2                       March 2007

C->S:  MRCP/2.0 289 SPEAK 543259

Channel-Identifier:32AECB23433801@speechsynth

Kill-On-Barge-In:true

Content-Type:application/ssml+xml

Content-Length:104

<?xml version="1.0"?>

<speak version="1.0"

xmlns="http://www.w3.org/2001/10/synthesis"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.w3.org/2001/10/synthesis

http://www.w3.org/TR/speech-synthesis/synthesis.xsd"

xml:lang="en-US">

<p>

<s>Welcome to ABC corporation.</s>

<s>Who would you like Talk to.</s>

</p>

</speak>

S->C:  MRCP/2.0 52 543259 200 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechsynth

Speech-Marker:timestamp=857207696314

Since the last "SPEAK" request had Kill-On-Barge-In set to "true",

the speech synthesizer is interrupted when the user starts speaking.

And the client is notified.

Now, since the recognition and synthesizer resources are on the same

session, they may have worked with each other to deliver kill-on-

barge-in.  Whether the synthesizer and recognizer are in the same

session or not the recognizer MUST generate the START-OF-INPUT event

to the client.

The client MUST then blindly turn around and issued a BARGE-IN-

OCCURRED method to the synthesizer resource (if a "SPEAK" request was

active).  The synthesizer, if kill-on-barge-in was enabled on the

current "SPEAK" request, would have then interrupted it and issued a

"SPEAK"-COMPLETE event to the client.

The completion-cause code differentiates if this is normal completion

or a kill-on-barge-in interruption.

Shanmugham & Burnett    Expires September 6, 2007             [Page 173]

Internet-Draft                   MRCPv2                       March 2007

S->C:  MRCP/2.0 49 START-OF-INPUT 543258 IN-PROGRESS

Channel-Identifier:32AECB23433801@speechrecog

Proxy-Sync-Id:987654321

C->S:  MRCP/2.0 69 BARGE-IN-OCCURRED 543259

Channel-Identifier:32AECB23433801@speechsynth

Proxy-Sync-Id:987654321

S->C:  MRCP/2.0 72 543259 200 COMPLETE

Channel-Identifier:32AECB23433801@speechsynth

Active-Request-Id-List:543258

Speech-Marker:timestamp=857206096314

S->C:  MRCP/2.0 73 SPEAK-COMPLETE 543259 COMPLETE

Channel-Identifier:32AECB23433801@speechsynth

Completion-Cause:001 barge-in

Speech-Marker:timestamp=857207685213

The recognition resource matched the spoken stream to a grammar and

generated results.  The result of the recognition is returned by the

server as part of the RECOGNITION-COMPLETE event.

S->C:  MRCP/2.0 412 RECOGNITION-COMPLETE 543258 COMPLETE

Channel-Identifier:32AECB23433801@speechrecog

Completion-Cause:000 success

Waveform-URI:<http://web.media.com/session123/audio.wav>;

size=423523;duration=25432

Content-Type:application/nlsml+xml

Content-Length:104

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="session:request1@form-level.store">

<interpretation>

<instance name="Person">

<ex:Person>

<ex:Name> Andre Roy </ex:Name>

</ex:Person>

</instance>

<input>   may I speak to Andre Roy </input>

</interpretation>

</result>

When the client wants to tear down the whole session and all its

Shanmugham & Burnett    Expires September 6, 2007             [Page 174]

Internet-Draft                   MRCPv2                       March 2007

resources, it MUST issue a SIP BYE to close the SIP session.  This

will de-allocate all the control channels and resources allocated

under the session.

C->S:  BYE sip:mrcp@server.example.com SIP/2.0

Max-Forwards:6

From:Sarvi <sip:sarvi@example.com>;tag=a6c85cf

To:MediaServer <sip:mrcp@server.example.com>;tag=1928301774

Call-ID:a84b4c76e66710

CSeq:231 BYE

Content-Length:0

14.2.  Recognition Result Examples

14.2.1.  Simple ASR Ambiguity

System: To which city will you be traveling?

User:   I want to go to Pittsburgh.

<?xml version="1.0"?>

<result xmlns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns:ex="http://www.example.com/example"

grammar="http://flight">

<interpretation confidence="0.6">

<instance>

<ex:airline>

<ex:to_city>Pittsburgh</ex:to_city>

<ex:airline>

<instance>

<input mode="speech">

I want to go to Pittsburgh

</input>

</interpretation>

<interpretation confidence="0.4"

<instance>

<ex:airline>

<ex:to_city>Stockholm</ex:to_city>

</ex:airline>

</instance>

<input>I want to go to Stockholm</input>

</interpretation>

</result>

Shanmugham & Burnett    Expires September 6, 2007             [Page 175]

Internet-Draft                   MRCPv2                       March 2007

14.2.2.  Mixed Initiative

System: What would you like?

User:   I would like 2 pizzas, one with pepperoni and cheese,

one with sausage and a bottle of coke, to go.

This example includes an order object which in turn contains objects

named "food_item", "drink_item" and "delivery_method".  The

representation assumes there are no ambiguities in the speech or

natural language processing.  Note that this representation also

assumes some level of intra-sentential anaphora resolution, i.e., to

resolve the two "one's" as "pizza".

<?xml version="1.0"?>

<nl:result xmlns:nl="http://www.ietf.org/xml/ns/mrcpv2"

xmlns="http://www.example.com/example"

grammar="http://foodorder">

<nl:interpretation confidence="1.0" >

<nl:instance>

<order>

<food_item confidence="1.0">

<pizza>

<ingredients confidence="1.0">

pepperoni

</ingredients>

<ingredients confidence="1.0">

cheese

</ingredients>

</pizza>

<pizza>

<ingredients>sausage</ingredients>

</pizza>

</food_item>

<drink_item confidence="1.0">

<size>2-liter</size>

</drink_item>

<delivery_method>to go</delivery_method>

</order>

</nl:instance>

<nl:input mode="speech">I would like 2 pizzas,

one with pepperoni and cheese, one with sausage

and a bottle of coke, to go.

</nl:input>

</nl:interpretation>

</nl:result>

Shanmugham & Burnett    Expires September 6, 2007             [Page 176]

Internet-Draft                   MRCPv2                       March 2007

14.2.3.  DTMF Input

A combination of DTMF input and speech is represented using nested

input elements.  For example:

User: My pin is (dtmf 1 2 3 4)

<input>

<input mode="speech" confidence ="1.0"

timestamp-start="2000-04-03T0:00:00"

timestamp-end="2000-04-03T0:00:01.5">My pin is

</input>

<input mode="dtmf" confidence ="1.0"

timestamp-start="2000-04-03T0:00:01.5"

timestamp-end="2000-04-03T0:00:02.0">1 2 3 4

</input>

</input>

Note that grammars that recognize mixtures of speech and DTMF are not

currently possible in VoiceXML; however this representation may be

needed for other applications of NLSML, and it may be introduced in

future versions of VoiceXML.

14.2.4.  Interpreting Meta-Dialog and Meta-Task Utterances

The natural language requires that the semantics specification must

be capable of representing a number of types of meta-dialog and meta-

task utterances (Task-Specific Information/Meta-task Information

Requirements 1-8 and Generic Information about the Communication

Process Requirements 1-6).  This specification is flexible enough so

that meta utterances can be represented on an application-specific

basis without defining specific formats in this specification.

Here are two examples of how meta-task and meta-dialog utterances

might be represented.

Shanmugham & Burnett    Expires September 6, 2007             [Page 177]

Internet-Draft                   MRCPv2                       March 2007

System: What toppings do you want on your pizza?

User:   What toppings do you have?

<interpretation grammar="http://toppings">

<instance>

<question>

<questioned_item>toppings<questioned_item>

<questioned_property>

availability

</questioned_property>

</question>

</instance>

<input mode="speech">

what toppings do you have?

</input>

</interpretation>

User:   slow down.

<interpretation grammar="http://generalCommandsGrammar">

<instance>

<command>

<action>reduce speech rate</action>

<doer>system</doer>

</command>

</instance>

<input mode="speech">slow down</input>

</interpretation>

14.2.5.  Anaphora and Deixis

This specification can be used on an application-specific basis to

represent utterances that contain unresolved anaphoric and deictic

references.  Anaphoric references, which include pronouns and

definite noun phrases that refer to something that was mentioned in

the preceding linguistic context, and deictic references, which refer

to something that is present in the non-linguistic context, present

similar problems in that there may not be sufficient unambiguous

linguistic context to determine what their exact role in the

interpretation should be.  In order to represent unresolved anaphora

and deixis using this specification, one strategy would be for the

developer to define a more surface-oriented representation that

leaves the specific details of the interpretation of the reference

open.  (This assumes that a later component is responsible for

actually resolving the reference).

Shanmugham & Burnett    Expires September 6, 2007             [Page 178]

Internet-Draft                   MRCPv2                       March 2007

Example: (ignoring the issue of representing the input from the

pointing gesture.)

System: What do you want to drink?

User:   I want this (clicks on picture of large root beer.)

<?xml version="1.0"?>

<nl:result xmlns:nl="http://www.ietf.org/xml/ns/mrcpv2"

xmlns="http://www.example.com/example"

grammar="http://www.example.com/beverages.grxml">

<nl:interpretation>

<nl:instance>

<doer>I</doer>

<action>want</action>

<object>this</object>

</nl:instance>

<nl:input mode="speech">I want this</nl:input>

</nl:interpretation>

</nl:result>

Future versions of the W3C Speech Interface Framework may address

issues of representing resolved anaphora.

14.2.6.  Distinguishing Individual Items from Sets with One Member

For programming convenience, it is useful to be able to distinguish

between individual items and sets containing one item in the XML

representation of semantic results.  For example, a pizza order might

consist of exactly one pizza, but a pizza might contain zero or more

toppings.  Since there is no standard way of marking this distinction

directly in XML, in the current framework, the developer is free to

adopt any conventions that would convey this information in the XML

markup.  One strategy would be for the developer to wrap the set of

items in a grouping element, as in the following example.

<order>

<pizza>

<topping-group>

<topping>mushrooms</topping>

</topping-group>

</pizza>

<drink>coke</drink>

</order>

In this example, the programmer can assume that there is supposed to

be exactly one pizza and one drink in the order, but the fact that

there is only one topping is an accident of this particular pizza

order.

Shanmugham & Burnett    Expires September 6, 2007             [Page 179]

Internet-Draft                   MRCPv2                       March 2007

14.2.7.  Extensibility

One of the natural language requirements states that the

specification must be extensible.  The specification supports this

requirement because of its flexibility, as discussed in the

discussions of meta utterances and anaphora.  NLSML can easily be

used in sophisticated systems to convey application-specific

information that more basic systems would not make use of, for

example defining speech acts.  Defining standard representations for

items such as dates, times, etc. could also be done.

15.  ABNF Normative Definition

LWS    =    [*WSP CRLF] 1*WSP ; linear whitespace

SWS    =    [LWS] ; sep whitespace

UTF8-NONASCII    =    %xC0-DF 1UTF8-CONT

/    %xE0-EF 2UTF8-CONT

/    %xF0-F7 3UTF8-CONT

/    %xF8-FB 4UTF8-CONT

/    %xFC-FD 5UTF8-CONT

UTF8-CONT        =    %x80-BF

VCHAR            =    %x21-7E

UTFCHAR          =    %x21-7E

/    UTF8-NONASCII

param            =    *pchar

quoted-string    =    SWS DQUOTE *(qdtext / quoted-pair )

DQUOTE

qdtext           =    LWS / %x21 / %x23-5B / %x5D-7E

/    UTF8-NONASCII

quoted-pair      =    "\" (%x00-09 / %x0B-0C / %x0E-7F)

token            =    1*(alphanum / "-" / "." / "!" / "%" / "*"

/ "_" / "+" / "`" / "'" / "~" )

reserved         =    ";" / "/" / "?" / ":" / "@" / "&" / "="

/ "+" / "$" / ","

mark             =    "-" / "_" / "." / "!" / "~" / "*" / "'"

/    "(" / ")"

unreserved       =    alphanum / mark

Shanmugham & Burnett    Expires September 6, 2007             [Page 180]

Internet-Draft                   MRCPv2                       March 2007

pchar            =    unreserved / escaped

/    ":" / "@" / "&" / "=" / "+" / "$" / ","

alphanum         =    ALPHA / DIGIT

escaped          =    "%" HEXDIG HEXDIG

fragment         =    *uric

uri              =    [ absoluteURI / relativeURI ]

[ "#" fragment ]

absoluteURI      =    scheme ":" ( hier-part / opaque-part )

relativeURI      =    ( net-path / abs-path / rel-path )

[ "?" query ]

hier-part        =    ( net-path / abs-path ) [ "?" query ]

net-path         =    "//" authority [ abs-path ]

abs-path         =    "/" path-segments

rel-path         =    rel-segment [ abs-path ]

rel-segment      =    1*( unreserved / escaped / ";" / "@"

/    "&" / "=" / "+" / "$" / "," )

opaque-part      =    uric-no-slash *uric

uric             =    reserved / unreserved / escaped

uric-no-slash    =    unreserved / escaped / ";" / "?" / ":"

/ "@" / "&" / "=" / "+" / "$" / ","

path-segments    =    segment *( "/" segment )

segment          =    *pchar *( ";" param )

scheme           =    ALPHA *( ALPHA / DIGIT / "+" / "-" / "." )

authority        =    srvr / reg-name

srvr             =    [ [ userinfo "@" ] hostport ]

reg-name         =    1*( unreserved / escaped / "$" / ","

/     ";" / ":" / "@" / "&" / "=" / "+" )

Shanmugham & Burnett    Expires September 6, 2007             [Page 181]

Internet-Draft                   MRCPv2                       March 2007

query            =    *uric

userinfo         =    ( user ) [ ":" password ] "@"

user             =    1*( unreserved / escaped

/    user-unreserved )

user-unreserved  =    "&" / "=" / "+" / "$" / "," / ";"

/    "?" / "/"

password         =    *( unreserved / escaped

/    "&" / "=" / "+" / "$" / "," )

hostport         =    host [ ":" port ]

host             =    hostname / IPv4address / IPv6reference

hostname         =    *( domainlabel "." ) toplabel [ "." ]

domainlabel      =    alphanum / alphanum *( alphanum / "-" )

alphanum

toplabel         =    ALPHA / ALPHA *( alphanum / "-" )

alphanum

IPv4address      =    1*3DIGIT "." 1*3DIGIT "." 1*3DIGIT "."

1*3DIGIT

IPv6reference    =    "[" IPv6address "]"

IPv6address      =    hexpart [ ":" IPv4address ]

hexpart          =    hexseq / hexseq "::" [ hexseq ] / "::"

[ hexseq ]

hexseq           =    hex4 *( ":" hex4)

hex4             =    1*4HEXDIG

port             =    1*DIGIT

cmid-attribute   =    "a=cmid:" identification-tag

identification-tag =    token

generic-message  =    start-line message-header CRLF

[ message-body ]

Shanmugham & Burnett    Expires September 6, 2007             [Page 182]

Internet-Draft                   MRCPv2                       March 2007

message-body     =    *OCTET

start-line       =    request-line / status-line / event-line

request-line     =    mrcp-version SP message-length SP method-name

SP request-id CRLF

status-line      =    mrcp-version SP message-length SP request-id

SP status-code SP request-state CRLF

event-line       =    mrcp-version SP message-length SP event-name

SP request-id SP request-state CRLF

method-name      =    generic-method

/    synthesizer-method

/    recorder-method

/    recognizer-method

/    verifier-method

generic-method   =    "SET-PARAMS</spanx>"

/    "GET-PARAMS"

request-state    =    "COMPLETE"

/    "IN-PROGRESS"

/    "PENDING"

event-name       =    synthesizer-event

/    recognizer-event

/    recorder-event

/    verifier-event

message-header   =    1*(generic-header / resource-header)

resource-header  =    recognizer-header

/    synthesizer-header

/    recorder-header

/    verifier-header

generic-header   =    channel-identifier

/    accept

/    active-request-id-list

/    proxy-sync-id

/    accept-charset

/    content-type

/    content-id

/    content-base

/    content-encoding

/    content-location

Shanmugham & Burnett    Expires September 6, 2007             [Page 183]

Internet-Draft                   MRCPv2                       March 2007

/    content-length

/    fetch-timeout

/    cache-control

/    logging-tag

/    set-cookie

/    set-cookie2

/    vendor-specific

; -- content-id is as defined in RFC2392, RFC2046 and RFC2822

; -- accept-charset is as defined in RFC2616

mrcp-version     =    "MRCP" "/" 1*DIGIT "." 1*DIGIT

message-length   =    1*DIGIT

request-id       =    1*DIGIT

status-code      =    1*DIGIT

channel-identifier =  "Channel-Identifier" ":"

channel-id CRLF

channel-id       =    1*VCHAR "@" 1*VCHAR

active-request-id-list = "Active-Request-Id-List" ":"

request-id *("," request-id) CRLF

proxy-sync-id    =    "Proxy-Sync-Id" ":" 1*VCHAR CRLF

content-length   =    "Content-Length" ":" 1*DIGIT CRLF

content-base     =    "Content-Base" ":" absoluteURI CRLF

content-type     =    "Content-Type" ":" media-type-value

media-type-value =    type "/" subtype *( ";" parameter )

type             =    token

subtype          =    token

parameter        =    attribute "=" value

attribute        =    token

value            =    token / quoted-string

content-encoding =    "Content-Encoding" ":"

Shanmugham & Burnett    Expires September 6, 2007             [Page 184]

Internet-Draft                   MRCPv2                       March 2007

*WSP content-coding

*(*WSP "," *WSP content-coding *WSP )

CRLF

content-coding   =    token

content-location =    "Content-Location" ":"

( absoluteURI / relativeURI )  CRLF

cache-control    =    "Cache-Control" ":"

[*WSP cache-directive

*( *WSP "," *WSP cache-directive *WSP )]

CRLF

fetch-timeout    =    "Fetch-Timeout" ":" [1*DIGIT] CRLF

cache-directive  =    "max-age" "=" delta-seconds

/    "max-stale" "=" [ delta-seconds ]

/    "min-fresh" "=" delta-seconds

logging-tag      =    "Logging-Tag" ":" 1*UTFCHAR CRLF

vendor-specific  =    "Vendor-Specific-Parameters" ":"

[vendor-specific-av-pair

*[";" vendor-specific-av-pair]] CRLF

vendor-specific-av-pair = vendor-av-pair-name "="

value

vendor-av-pair-name     = 1*UTFCHAR

set-cookie       =    "Set-Cookie:" cookies CRLF

cookies          =    cookie *("," *LWS cookie)

cookie           =    attribute "=" value *(";" cookie-av)

cookie-av        =    "Comment" "=" value

/    "Domain" "=" value

/    "Max-Age" "=" value

/    "Path" "=" value

/    "Secure"

/    "Version" "=" 1*DIGIT

/    "Age" "=" delta-seconds

set-cookie2      =    "Set-Cookie2:" cookies2 CRLF

Shanmugham & Burnett    Expires September 6, 2007             [Page 185]

Internet-Draft                   MRCPv2                       March 2007

cookies2         =    cookie2 *("," *LWS cookie2)

cookie2          =    attribute "=" value *(";" cookie-av2)

cookie-av2       =    "Comment" "=" value

/    "CommentURL" "=" DQUOTE uri DQUOTE

/    "Discard"

/    "Domain" "=" value

/    "Max-Age" "=" value

/    "Path" "=" value

/    "Port" [ "=" DQUOTE portlist DQUOTE ]

/    "Secure"

/    "Version" "=" 1*DIGIT

/    "Age" "=" delta-seconds

portlist         =    portnum *("," *LWS portnum)

portnum          =    1*DIGIT

; Synthesizer ABNF

synthesizer-method    =    "SPEAK"

/    "STOP"

/    "PAUSE"

/    "RESUME"

/    "BARGE-IN-OCCURRED"

/    "CONTROL"

/    "DEFINE-LEXICON"

synthesizer-event     =    "SPEECH-MARKER"

/    "SPEAK-COMPLETE"

synthesizer-header    =    jump-size

/    kill-on-barge-in

/    speaker-profile

/    completion-cause

/    completion-reason

/    voice-parameter

/    prosody-parameter

/    speech-marker

/    speech-language

/    fetch-hint

/    audio-fetch-hint

/    failed-uri

/    failed-uri-cause

/    speak-restart

/    speak-length

/    load-lexicon

Shanmugham & Burnett    Expires September 6, 2007             [Page 186]

Internet-Draft                   MRCPv2                       March 2007

/    lexicon-search-order

jump-size             =    "Jump-Size" ":" speech-length-value CRLF

speech-length-value   =    numeric-speech-length

/    text-speech-length

text-speech-length    =    1*UTFCHAR SP "Tag"

numeric-speech-length =    ("+" / "-") positive-speech-length

positive-speech-length =   1*DIGIT SP numeric-speech-unit

numeric-speech-unit   =    "Second"

/    "Word"

/    "Sentence"

/    "Paragraph"

delta-seconds         =    1*DIGIT

kill-on-barge-in      =    "Kill-On-Barge-In" ":" boolean-value

CRLF

boolean-value         =    "true" / "false"

speaker-profile       =    "Speaker-Profile" ":" absoluteURI

CRLF

completion-cause      =    "Completion-Cause" ":" 1*DIGIT SP

1*VCHAR CRLF

completion-reason     =    "Completion-Reason" ":"

quoted-string CRLF

voice-parameter       =    voice-gender

/    voice-age

/    voice-variant

/    voice-name

voice-gender          =    "Voice-Gender:" voice-gender-value CRLF

voice-gender-value    =    "male"

/    "female"

/    "neutral"

voice-age             =    "Voice-Age:" 1*DIGIT CRLF

Shanmugham & Burnett    Expires September 6, 2007             [Page 187]

Internet-Draft                   MRCPv2                       March 2007

voice-variant         =    "Voice-Variant:" 1*DIGIT CRLF

voice-name            =    "Voice-Name:"

1*UTFCHAR *[1*WSP 1*UTFCHAR] CRLF

prosody-parameter     =    "Prosody-" prosody-param-name ":"

[prosody-param-value] CRLF

prosody-param-name    =    1*VCHAR

prosody-param-value   =    1*VCHAR

timestamp             =    "Timestamp" "=" time-stamp-value CRLF

time-stamp-value      =    1*DIGIT

speech-marker         =    "Speech-Marker" ":"

"timestamp=" [time-stamp-value]

[";" 1*(UTFCHAR / 0x20)] CRLF

speech-language       =    "Speech-Language" ":" [1*VCHAR] CRLF

fetch-hint            =    "Fetch-Hint" ":" [1*ALPHA] CRLF

audio-fetch-hint      =    "Audio-Fetch-Hint" ":" [1*ALPHA] CRLF

failed-uri            =    "Failed-URI" ":" absoluteURI CRLF

failed-uri-cause      =    "Failed-URI-Cause" ":" 1*alphanum CRLF

speak-restart         =    "Speak-Restart" ":" boolean-value CRLF

speak-length          =    "Speak-Length" ":" positive-length-value

CRLF

positive-length-value   =  positive-speech-length

/  text-speech-length

load-lexicon          =    "Load-Lexicon" ":" boolean CRLF

lexicon-search-order  =    "Lexicon-Search-Order" ":"

"<" absoluteURI ">" *[" " "<" absoluteURI ">"] CRLF

; Recognizer ABNF

recognizer-method     =    recog-only-method

/    enrollment-method

Shanmugham & Burnett    Expires September 6, 2007             [Page 188]

Internet-Draft                   MRCPv2                       March 2007

recog-only-method     =    "DEFINE-GRAMMAR"

/    "RECOGNIZE"

/    "INTERPRET"

/    "GET-RESULT"

/    "START-INPUT-TIMERS"

/    "STOP"

enrollment-method     =    "START-PHRASE-ENROLLMENT"

/    "ENROLLMENT-ROLLBACK"

/    "END-PHRASE-ENROLLMENT"

/    "MODIFY-PHRASE"

/    "DELETE-PHRASE"

recognizer-event      =    "START-OF-INPUT"

/    "RECOGNITION-COMPLETE"

/    "INTERPRETATION-COMPLETE"

recognizer-header     =    recog-only-header

/    enrollment-header

recog-only-header     =    confidence-threshold

/    sensitivity-level

/    speed-vs-accuracy

/    n-best-list-length

/    input-type

/    no-input-timeout

/    recognition-timeout

/    waveform-uri

/    input-waveform-uri

/    completion-cause

/    completion-reason

/    recognizer-context-block

/    start-input-timers

/    speech-complete-timeout

/    speech-incomplete-timeout

/    dtmf-interdigit-timeout

/    dtmf-term-timeout

/    dtmf-term-char

/    failed-uri

/    failed-uri-cause

/    save-waveform

/    media-type

/    new-audio-channel

/    speech-language

/    ver-buffer-utterance

/    recognition-mode

/    cancel-if-queue

Shanmugham & Burnett    Expires September 6, 2007             [Page 189]

Internet-Draft                   MRCPv2                       March 2007

/    hotword-max-duration

/    hotword-min-duration

/    interpret-text

/    dtmf-buffer-time

/    clear-dtmf-buffer

/    early-no-match

enrollment-header     =    num-min-consistent-pronunciations

/    consistency-threshold

/    clash-threshold

/    personal-grammar-uri

/    enroll-utterance

/    phrase-id

/    phrase-nl

/    weight

/    save-best-waveform

/    new-phrase-id

/    confusable-phrases-uri

/    abort-phrase-enrollment

confidence-threshold  =    "Confidence-Threshold" ":"

[1*DIGIT] CRLF

sensitivity-level     =    "Sensitivity-Level" ":" FLOAT

CRLF

speed-vs-accuracy     =    "Speed-Vs-Accuracy" ":" [1*DIGIT]

CRLF

n-best-list-length    =    "N-Best-List-Length" ":" [1*DIGIT]

CRLF

input-type            =  "Input-Type" ":"  [ "speech" / "dtmf" ] CRLF

no-input-timeout      =    "No-Input-Timeout" ":" [1*DIGIT]

CRLF

recognition-timeout   =    "Recognition-Timeout" ":" [1*DIGIT]

CRLF

waveform-uri          =    "Waveform-URI" ":" "<" absoluteURI ">"

";" "size" "=" 1*DIGIT

";" "duration" "=" 1*DIGIT CRLF

recognizer-context-block = "Recognizer-Context-Block" ":"

[1*VCHAR] CRLF

Shanmugham & Burnett    Expires September 6, 2007             [Page 190]

Internet-Draft                   MRCPv2                       March 2007

start-input-timers    =    "Start-Input-Timers" ":"

boolean-value CRLF

speech-complete-timeout =  "Speech-Complete-Timeout" ":"

[1*DIGIT] CRLF

speech-incomplete-timeout = "Speech-Incomplete-Timeout" ":"

[1*DIGIT] CRLF

dtmf-interdigit-timeout = "DTMF-Interdigit-Timeout" ":"

[1*DIGIT] CRLF

dtmf-term-timeout     =    "DTMF-Term-Timeout" ":" [1*DIGIT]

CRLF

dtmf-term-char        =    "DTMF-Term-Char" ":" [VCHAR] CRLF

save-waveform         =    "Save-Waveform" ":" [boolean-value] CRLF

new-audio-channel     =    "New-Audio-Channel" ":"

boolean-value CRLF

recognition-mode      =    "Recognition-Mode" ":" 1*ALPHA CRLF

cancel-if-queue       =    "Cancel-If-Queue" ":" boolean-value CRLF

hotword-max-duration  =    "Hotword-Max-Duration" ":"

1*DIGIT CRLF

hotword-min-duration  =    "Hotword-Min-Duration" ":"

1*DIGIT CRLF

dtmf-buffer-time      =    "DTMF-Buffer-Time" ":" 1*DIGIT CRLF

clear-dtmf-buffer     =    "Clear-DTMF-Buffer" ":" boolean-value CRLF

early-no-match        =    "Early-No-Match" ":" boolean-value CRLF

num-min-consistent-pronunciations    =

"Num-Min-Consistent-Pronunciations" ":" 1*DIGIT CRLF

consistency-threshold =    "Consistency-Threshold" ":" 1*DIGIT

CRLF

clash-threshold       =    "Clash-Threshold" ":" 1*DIGIT CRLF

personal-grammar-uri  =    "Personal-Grammar-URI" ":" uri CRLF

Shanmugham & Burnett    Expires September 6, 2007             [Page 191]

Internet-Draft                   MRCPv2                       March 2007

enroll-utterance      =    "Enroll-Utterance" ":" boolean-value CRLF

phrase-id             =    "Phrase-ID" ":" 1*VCHAR CRLF

phrase-nl             =    "Phrase-NL" ":" 1*UTFCHAR CRLF

weight                =    "Weight" ":" weight-value CRLF

weight-value          =    1*DIGIT

save-best-waveform    =    "Save-Best-Waveform" ":"

boolean-value CRLF

new-phrase-id         =    "New-Phrase-ID" ":" 1*VCHAR CRLF

confusable-phrases-uri =   "Confusable-Phrases-URI" ":"

uri CRLF

abort-phrase-enrollment =  "Abort-Phrase-Enrollment" ":"

boolean-value CRLF

; Verifier ABNF

verifier-method       =    "START-SESSION"

/    "END-SESSION"

/    "QUERY-VOICEPRINT"

/    "DELETE-VOICEPRINT"

/    "VERIFY"

/    "VERIFY-FROM-BUFFER"

/    "VERIFY-ROLLBACK"

/    "STOP"

/    "START-INPUT-TIMERS"

/    "GET-INTERMEDIATE-RESULT"

verifier-event        =    "VERIFICATION-COMPLETE"

/    "START-OF-INPUT"

verifier-header       =    repository-uri

/    voiceprint-identifier

/    verification-mode

/    adapt-model

/    abort-model

/    min-verification-score

/    num-min-verification-phrases

/    num-max-verification-phrases

Shanmugham & Burnett    Expires September 6, 2007             [Page 192]

Internet-Draft                   MRCPv2                       March 2007

/    no-input-timeout

/    save-waveform

/    media-type

/    waveform-uri

/    voiceprint-exists

/    ver-buffer-utterance

/    input-waveform-uri

/    completion-cause

/    completion-reason

/    speech-complete-timeout

/    new-audio-channel

/    abort-verification

/    start-input-timers

/    input-type

repository-uri        =    "Repository-URI" ":" uri CRLF

voiceprint-identifier =    "Voiceprint-Identifier" ":"

1*VCHAR "." 3VCHAR

[";" 1*VCHAR "." 3VCHAR] CRLF

verification-mode     =    "Verification-Mode" ":"

verification-mode-string

verification-mode-string = "train" / "verify"

adapt-model           =    "Adapt-Model" ":" boolean-value CRLF

abort-model           =    "Abort-Model" ":" boolean-value CRLF

min-verification-score  =  "Min-Verification-Score" ":"

[ %2D ] float-value CRLF

num-min-verification-phrases = "Num-Min-Verification-Phrases"

":" 1*DIGIT CRLF

num-max-verification-phrases = "Num-Max-Verification-Phrases"

":" 1*DIGIT CRLF

voiceprint-exists     =    "Voiceprint-Exists" ":"

boolean-value CRLF

ver-buffer-utterance  =    "Ver-Buffer-Utterance" ":"

boolean-value CRLF

input-waveform-uri    =    "Input-Waveform-URI" ":" uri CRLF

Shanmugham & Burnett    Expires September 6, 2007             [Page 193]

Internet-Draft                   MRCPv2                       March 2007

abort-verification    =    "Abort-Verification " ":"

boolean-value CRLF

; Recorder ABNF

recorder-method       =    "RECORD"

/    "STOP"

recorder-event        =    "START-OF-INPUT"

/    "RECORD-COMPLETE"

recorder-header       =    sensitivity-level

/    no-input-timeout

/    completion-cause

/    completion-reason

/    failed-uri

/    failed-uri-cause

/    record-uri

/    media-type

/    max-time

/    trim-length

/    final-silence

/    capture-on-speech

/    new-audio-channel

/    start-input-timers

/    input-type

record-uri            =    "Record-URI" ":" [ "<" uri ">"

";" "size" "=" 1*DIGIT

";" "duration" "=" 1*DIGIT] CRLF

media-type            =    "Media-Type" ":" media-type-value CRLF

max-time              =    "Max-Time" ":" 1*DIGIT CRLF

trim-length           =    "Trim-Length" ":" 1*DIGIT CRLF

final-silence         =    "Final-Silence" ":" 1*DIGIT CRLF

capture-on-speech     =    "Capture-On-Speech " ":"

boolean-value CRLF

Shanmugham & Burnett    Expires September 6, 2007             [Page 194]

Internet-Draft                   MRCPv2                       March 2007

16.  XML Schemas

16.1.  NLSML Schema Definition

<?xml version="1.0" encoding="UTF-8"?>

<xs:schema  xmlns:xs="http://www.w3.org/2001/XMLSchema"

targetNamespace="http://www.ietf.org/xml/ns/mrcpv2"

xmlns="http://www.ietf.org/xml/ns/mrcpv2"

elementFormDefault="qualified"

attributeFormDefault="unqualified" >

<xs:element name="result">

<xs:annotation>

<xs:documentation> Natural Language Semantic Markup Schema

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element name="interpretation" maxOccurs="unbounded">

<xs:complexType>

<xs:sequence>

<xs:element name="instance" minOccurs="0">

<xs:complexType mixed="true">

<xs:sequence minOccurs="0">

<xs:any namespace="##other" processContents="lax"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="input">

<xs:complexType mixed="true">

<xs:choice>

<xs:element name="noinput" minOccurs="0"/>

<xs:element name="nomatch" minOccurs="0"/>

<xs:element name="input" minOccurs="0"/>

</xs:choice>

<xs:attribute name="mode"

type="xs:string"

default="speech"/>

<xs:attribute name="confidence"

type="confidenceinfo"

default="1.0"/>

<xs:attribute name="timestamp-start"

type="xs:string"/>

<xs:attribute name="timestamp-end"

type="xs:string"/>

</xs:complexType>

</xs:element>

</xs:sequence>

<xs:attribute name="confidence" type="confidenceinfo"

Shanmugham & Burnett    Expires September 6, 2007             [Page 195]

Internet-Draft                   MRCPv2                       March 2007

default="1.0"/>

<xs:attribute name="grammar" type="xs:anyURI"

use="optional"/>

</xs:complexType>

</xs:element>

<xs:include schemaLocation="enrollment-schema.rng"/>

<xs:include schemaLocation="verification-schema.rng"/>

</xs:sequence>

<xs:attribute name="grammar" type="xs:anyURI"

use="optional"/>

</xs:complexType>

</xs:element>

<xs:simpleType name="confidenceinfo">

<xs:restriction base="xs:float">

<xs:minInclusive value="0.0"/>

<xs:maxInclusive value="1.0"/>

</xs:restriction>

</xs:simpleType>

</xs:schema>

16.2.  Enrollment Results Schema Definition

<!-- MRCP Enrollment Schema

(See http://www.oasis-open.org/committees/relax-ng/spec.html)

-->

<element name="enrollment-result"

datatypeLibrary="http://www.w3.org/2001/XMLSchema-datatypes"

ns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns="http://relaxng.org/ns/structure/1.0">

<interleave>

<element name="num-clashes">

<data type="nonNegativeInteger"/>

</element>

<element name="num-good-repetitions">

<data type="nonNegativeInteger"/>

</element>

<element name="num-repetitions-still-needed">

<data type="nonNegativeInteger"/>

</element>

<element name="consistency-status">

<choice>

<value>consistent</value>

<value>inconsistent</value>

<value>undecided</value>

</choice>

</element>

Shanmugham & Burnett    Expires September 6, 2007             [Page 196]

Internet-Draft                   MRCPv2                       March 2007

<optional>

<element name="clash-phrase-ids">

<oneOrMore>

<element name="item">

<data type="token"/>

</element>

</oneOrMore>

</element>

</optional>

<optional>

<element name="transcriptions">

<oneOrMore>

<element name="item">

<text/>

</element>

</oneOrMore>

</element>

</optional>

<optional>

<element name="confusable-phrases">

<oneOrMore>

<element name="item">

<text/>

</element>

</oneOrMore>

</element>

</optional>

</interleave>

</element>

16.3.  Verification Results Schema Definition

<!--    MRCP Verification Results Schema

(See http://www.oasis-open.org/committees/relax-ng/spec.html)

-->

<grammar datatypeLibrary="http://www.w3.org/2001/XMLSchema-datatypes"

ns="http://www.ietf.org/xml/ns/mrcpv2"

xmlns="http://relaxng.org/ns/structure/1.0">

<start>

<element name="verification-result">

<element name="voiceprint">

<ref name="firstVoiceprintContent"/>

</element>

<zeroOrMore>

<element name="voiceprint">

<ref name="restVoiceprintContent"/>

Shanmugham & Burnett    Expires September 6, 2007             [Page 197]

Internet-Draft                   MRCPv2                       March 2007

</element>

</zeroOrMore>

</element>

</start>

<define name="firstVoiceprintContent">

<attribute name="id">

<data type="string"/>

</attribute>

<interleave>

<optional>

<element name="adapted">

<data type="boolean"/>

</element>

<element name="needmoredata">

<ref name="needmoredataContent"/>

</element>

</optional>

<element name="incremental">

<ref name="firstCommonContent"/>

</element>

<element name="cumulative">

<ref name="firstCommonContent"/>

</element>

</interleave>

</define>

<define name="restVoiceprintContent">

<attribute name="id">

<data type="string"/>

</attribute>

<interleave>

<optional>

<element name="incremental">

<ref name="restCommonContent"/>

</element>

</optional>

<element name="cumulative">

<ref name="restCommonContent"/>

</element>

</interleave>

</define>

<define name="firstCommonContent">

<interleave>

<choice>

<element name="decision">

<ref name="decisionContent"/>

Shanmugham & Burnett    Expires September 6, 2007             [Page 198]

Internet-Draft                   MRCPv2                       March 2007

</element>

</choice>

<element name="device">

<ref name="deviceContent"/>

</element>

<element name="gender">

<ref name="genderContent"/>

</element>

<zeroOrMore>

<element name="verification-score">

<ref name="verification-scoreContent"/>

</element>

</zeroOrMore>

</interleave>

</define>

<define name="restCommonContent">

<interleave>

<optional>

<element name="decision">

<ref name="decisionContent"/>

</element>

</optional>

<optional>

<element name="utterance-length">

<ref name="utterance-lengthContent"/>

</element>

</optional>

<optional>

<element name="device">

<ref name="deviceContent"/>

</element>

</optional>

<optional>

<element name="gender">

<ref name="genderContent"/>

</element>

</optional>

<zeroOrMore>

<element name="verification-score">

<ref name="verification-scoreContent"/>

</element>

</zeroOrMore>

</interleave>

</define>

<define name="decisionContent">

<choice>

Shanmugham & Burnett    Expires September 6, 2007             [Page 199]

Internet-Draft                   MRCPv2                       March 2007

<value>accepted</value>

<value>rejected</value>

<value>undecided</value>

</choice>

</define>

<define name="needmoredataContent">

<data type="boolean"/>

</define>

<define name="utterance-lengthContent">

<data type="nonNegativeInteger"/>

</define>

<define name="deviceContent">

<choice>

<value>cellular-phone</value>

<value>electret-phone</value>

<value>carbon-button-phone</value>

<value>unknown</value>

</choice>

</define>

<define name="genderContent">

<choice>

<value>male</value>

<value>female</value>

<value>unknown</value>

</choice>

</define>

<define name="verification-scoreContent">

<data type="float">

<param name="minInclusive">-1</param>

<param name="maxInclusive">1</param>

</data>

</define>

</grammar>

17.  References

17.1.  Normative References

[1]   Oran, D., "Requirements for Distributed Control of Automatic

Speech Recognition (ASR), Speaker Identification/Speaker

Verification (SI/SV), and Text-to-Speech (TTS) Resources",

Shanmugham & Burnett    Expires September 6, 2007             [Page 200]

Internet-Draft                   MRCPv2                       March 2007

RFC 4313, December 2005.

[2]   Schulzrinne, H., Casner, S., Frederick, R., and V. Jacobson,

"RTP: A Transport Protocol for Real-Time Applications", STD 64,

RFC 3550, July 2003.

[3]   Rosenberg, J., Schulzrinne, H., Camarillo, G., Johnston, A.,

Peterson, J., Sparks, R., Handley, M., and E. Schooler, "SIP:

Session Initiation Protocol", RFC 3261, June 2002.

[4]   Handley, M., Jacobson, V., and C. Perkins, "SDP: Session

Description Protocol", RFC 4566, July 2006.

[5]   Bradner, S., "Key words for use in RFCs to Indicate Requirement

Levels", BCP 14, RFC 2119, March 1997.

[6]   Fielding, R., Gettys, J., Mogul, J., Frystyk, H., Masinter, L.,

Leach, P., and T. Berners-Lee, "Hypertext Transfer Protocol --

HTTP/1.1", RFC 2616, June 1999.

[7]   Rosenberg, J. and H. Schulzrinne, "An Offer/Answer Model with

Session Description Protocol (SDP)", RFC 3264, June 2002.

[8]   Yergeau, F., "UTF-8, a transformation format of ISO 10646",

STD 63, RFC 3629, November 2003.

[9]   Crocker, D., Ed. and P. Overell, "Augmented BNF for Syntax

Specifications: ABNF", RFC 4234, October 2005.

[10]  Yon, D., "Connection-Oriented Media Transport in the Session

Description Protocol  (SDP)", draft-ietf-mmusic-sdp-comedia-10

(work in progress), November 2004.

[11]  Lennox, J., "Connection-Oriented Media Transport over the

Transport Layer Security (TLS) Protocol in the Session

Description Protocol (SDP)", RFC 4572, July 2006.

[12]  Camarillo, G., Eriksson, G., Holler, J., and H. Schulzrinne,

"Grouping of Media Lines in the Session Description Protocol

(SDP)", RFC 3388, December 2002.

[13]  Resnick, P., "Internet Message Format", RFC 2822, April 2001.

[14]  Levinson, E., "Content-ID and Message-ID Uniform Resource

Locators", RFC 2392, August 1998.

[15]  Kristol, D. and L. Montulli, "HTTP State Management Mechanism",

RFC 2109, February 1997.

Shanmugham & Burnett    Expires September 6, 2007             [Page 201]

Internet-Draft                   MRCPv2                       March 2007

[16]  Kristol, D. and L. Montulli, "HTTP State Management Mechanism",

RFC 2965, October 2000.

[17]  Phillips, A. and M. Davis, "Tags for Identifying Languages",

BCP 47, RFC 4646, September 2006.

[18]  Narten, T. and H. Alvestrand, "Guidelines for Writing an IANA

Considerations Section in RFCs", BCP 26, RFC 2434,

October 1998.

[19]  Mockapetris, P., "Domain names - implementation and

specification", STD 13, RFC 1035, November 1987.

[20]  Freed, N. and J. Klensin, "Media Type Specifications and

Registration Procedures", BCP 13, RFC 4288, December 2005.

[21]  Mealling, M., "The IETF XML Registry", BCP 81, RFC 3688,

January 2004.

[22]  Hansen, T., Hardie, T., and L. Masinter, "Guidelines and

Registration Procedures for New URI Schemes", BCP 115,

RFC 4395, February 2006.

[23]  Andreasen, F., "Session Description Protocol Security

Descriptions for Media Streams",

draft-ietf-mmusic-sdescriptions-12 (work in progress),

September 2005.

[24]  Hunt, A., Walker, M., and D. Burnett, "Speech Synthesis Markup

Language (SSML) Version 1.0", World Wide Web Consortium

Recommendation REC-speech-synthesis-20040907, September 2004,

<http://www.w3.org/TR/2004/REC-speech-synthesis-20040907>.

[25]  Hunt, A. and S. McGlashan, "Speech Recognition Grammar

Specification Version 1.0", World Wide Web Consortium

Recommendation REC-speech-grammar-20040316, March 2004,

<http://www.w3.org/TR/2004/REC-speech-grammar-20040316>.

[26]  Tichelen, L. and D. Burke, "Semantic Interpretation for Speech

Recognition (SISR) Version 1.0", World Wide Web Consortium

CR CR-semantic-interpretation-20060111, January 2006,

<http://www.w3.org/TR/2006/

CR-semantic-interpretation-20060111>.

[27]  Hollander, D., Tobin, R., Layman, A., and T. Bray, "Namespaces

in XML 1.1", World Wide Web Consortium FirstEdition REC-xml-

names11-20040204, February 2004,

<http://www.w3.org/TR/2004/REC-xml-names11-20040204>.

Shanmugham & Burnett    Expires September 6, 2007             [Page 202]

Internet-Draft                   MRCPv2                       March 2007

17.2.  Informative References

[28]  International Telecommunications Union, "Technical Features of

Push-Button Telephone Sets", ITU-T Q.23, 1993.

[29]  Schulzrinne, H. and S. Petrack, "RTP Payload for DTMF Digits,

Telephony Tones and Telephony Signals", RFC 2833, May 2000.

[30]  Carter, J., Danielsen, P., Ferrans, J., Lucas, B., McGlashan,

S., Rehor, K., Porter, B., Hunt, A., Tryphonas, S., and D.

Burnett, "Voice Extensible Markup Language (VoiceXML) Version

2.0", World Wide Web Consortium Recommendation REC-voicexml20-

20040316, March 2004,

<http://www.w3.org/TR/2004/REC-voicexml20-20040316>.

[31]  Shanmugham, S., Monaco, P., and B. Eberman, "A Media Resource

Control Protocol (MRCP) Developed by Cisco, Nuance, and

Speechworks", RFC 4463, April 2006.

[32]  Sun Microsystems, "Java Speech Grammar Format Version 1.0",

October 1998.

[33]  Johnston, M., Chou, W., Dahl, A., McCobb, G., and D. Raggett,

"EMMA: Extensible MultiModal Annotation markup language", W3C

REC WD-emma-20050916, September 2005.

Shanmugham & Burnett    Expires September 6, 2007             [Page 203]

Internet-Draft                   MRCPv2                       March 2007

Appendix A.  Contributors

Pierre Forgues

Nuance Communications Ltd.

111 Duke Street

Suite 4100

Montreal, Quebec

Canada H3C 2M1

Email:  forgues@nuance.com

Charles Galles

Intervoice, Inc.

17811 Waterview Parkway

Dallas, Texas 75252

Email:  charles.galles@intervoice.com

Klaus Reifenrath

Scansoft, Inc

Guldensporenpark 32

Building D

9820 Merelbeke

Belgium

Email: klaus.reifenrath@scansoft.com

Shanmugham & Burnett    Expires September 6, 2007             [Page 204]

Internet-Draft                   MRCPv2                       March 2007

Appendix B.  Acknowledgements

Andre Gillet (Nuance Communications)

Andrew Hunt (ScanSoft)

Andrew Wahbe (Genesys)

Aaron Kneiss (ScanSoft)

Brian Eberman (ScanSoft)

Corey Stohs (Cisco Systems Inc)

Dave Burke (VoxPilot)

Jeff Kusnitz (IBM Corp)

Ganesh N Ramaswamy (IBM Corp)

Klaus Reifenrath (ScanSoft)

Kristian Finlator (ScanSoft)

Magnus Westerlund (Ericsson)

Martin Dragomirecky (Cisco Systems Inc)

Paolo Baggia (Loquendo)

Peter Monaco (Nuance Communications)

Pierre Forgues (Nuance Communications)

Ran Zilca (IBM Corp)

Suresh Kaliannan (Cisco Systems Inc.)

Skip Cave (Intervoice Inc)

Thomas Gal (LumenVox)

The chairs of the speechsc work group are Eric Burger (Brooktrout

Technology, Inc.) and Dave Oran (Cisco Systems, Inc.).

Authors' Addresses

Saravanan Shanmugham

Cisco Systems, Inc.

170 W. Tasman Dr.

San Jose, CA  95134

USA

Email: sarvi@cisco.com

Daniel C. Burnett

Nuance Communications

1 Wayside Road

Burlington, MA  01803

USA

Email: Daniel.Burnett@nuance.com

Shanmugham & Burnett    Expires September 6, 2007             [Page 205]

Internet-Draft                   MRCPv2                       March 2007

Full Copyright Statement

Copyright (C) The IETF Trust (2007).

This document is subject to the rights, licenses and restrictions

contained in BCP 78, and except as set forth therein, the authors

retain all their rights.

This document and the information contained herein are provided on an

"AS IS" basis and THE CONTRIBUTOR, THE ORGANIZATION HE/SHE REPRESENTS

OR IS SPONSORED BY (IF ANY), THE INTERNET SOCIETY, THE IETF TRUST AND

THE INTERNET ENGINEERING TASK FORCE DISCLAIM ALL WARRANTIES, EXPRESS

OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF

THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED

WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

Intellectual Property

The IETF takes no position regarding the validity or scope of any

Intellectual Property Rights or other rights that might be claimed to

pertain to the implementation or use of the technology described in

this document or the extent to which any license under such rights

might or might not be available; nor does it represent that it has

made any independent effort to identify any such rights.  Information

on the procedures with respect to rights in RFC documents can be

found in BCP 78 and BCP 79.

Copies of IPR disclosures made to the IETF Secretariat and any

assurances of licenses to be made available, or the result of an

attempt made to obtain a general license or permission for the use of

such proprietary rights by implementers or users of this

specification can be obtained from the IETF on-line IPR repository at

http://www.ietf.org/ipr.

The IETF invites any interested party to bring to its attention any

copyrights, patents or patent applications, or other proprietary

rights that may cover technology that may be required to implement

this standard.  Please address the information to the IETF at

ietf-ipr@ietf.org.

Acknowledgment

Funding for the RFC Editor function is provided by the IETF

Administrative Support Activity (IASA).

Shanmugham & Burnett    Expires September 6, 2007             [Page 206]